## Slide 1: Geography
http://goo.gl/ZjVJO
TOP
SVD
ECL
Groups (INFN+University)
Torino
Padova
Trieste
TIFPA
Pisa
Perugia
Laboratori Nazionali di Frascati
Roma 3
Enea Casaccia/Roma 1
Napoli
COMP

## Slide 2: Gli afferenti @RomaTre (2016)
P. Branchini 0.5
A. Baroncelli 0.3
E. Bernieri 0.5
A. Budano 0.5
M. Ciuchini 0.2
E. Graziani 0.5
A. Passeri 0.5
S. Bussino 0.3
Totale: 3.3
Very strong support and interest from Electronic (D. Tagnani, F. Budano)

## Slide 3: Introduction
Beast experiment
News from Belle2 (KLM)

## Slide 4: Introduction
The R&D on the Forward Calorimeter is over.
Several papers concerning test beam are being written.
RM3 developped the front-end electronics in this framework and
the daq system.
Collaboration will take a decision on what to do as soon as we’have final
results from beast
In 2014-2016 we have focused on the possibility to take
Part to the EMC forward upgrade. Moreover in 2015-2016 we have
Also taken part to the beast phase 1 experiment to measure
radiation back ground in the experiment.

## Slide 5: Beast phase 1:
Crystal box contains: Lyso, CsI CsI (Tl) equipped to monitor T and H
Idea: To measure irradiation spectra and rate and correlate it with machine optical function.

## Slide 6: Beam blow up evidence in LER:

## Slide 7: HER Touscheck study:

## Slide 8: Touscheck study

## Slide 9: LER Collimation Study

## Slide 11
Injection study

## Slide 12: New scheme of daq adopted (and made it work)

## Slide 19: Why KLM
Semileptonic decays are fundamental for B physics.
KLM detector detects and tiggers on muons.
By the end of 2015 beginning 2016 it was clear KLM fe would not
have been ready by the end of 2017.
The spokesman asked us (LNF and RM3) if we could take care
of this problem.
We analyzed the problem and acted.

## Slide 20: INFN KLM system review, board production
KLM system overview
KLM board production in Italy
results

## Slide 21: The Sytem
Front-end Board
INFN
LNF-RM3
13 RPC Front-End boards connect to a Data Concentrator in the barrel
2 Scintillator Motherboards connect to a Data Concentrator in the barrel
7 Scintillator Motherboards connect to a Data Concentrator in the end-cap
The Data Concentrator connects to the detector interface (HSLB, UT3, FTSW)

## Slide 22: Data Concentrator Board

## Slide 23: Data Concentrator Functions

## Slide 24: RPC front-end functions

## Slide 25: Custom backplane

## Slide 26: RPC Signals

## Slide 27: RPC front end board

## Slide 28: Test results
2 board were perfect
1 board has a broken multiplexer a broken diode and
transformer badly soldered.
This board has been reworked and it’s working now.

## Slide 29: Board:

## Slide 30: What was visible @microscope
A rotation occurred when it was
soldered

## Slide 31: Quotation
The 3 boards produced worked fine from the start now we are running a bid to assign the production.

## Slide 32: Next STEP on KLM
We are building a setup facility@LNF. (We need space)
We want to get the production done by the end of march 2017.
We want to test all the board in our facility by 30 th june 2017.
In this case installation will occur by end of october 2017.

## Slide 33: Backup slides

## Slide 34: Beast results (vacum scrubbing):

## Slide 39: Indiana test setup description
External pulser with variable amplitude connects to Z and Phi connectors
to pulse every channel while data is analyzed with COPPER readout.
Threshold and built-in pulser are manipulated with and data is analyzed
with COPPER readout .
Configure FPGAs with Data Concentrator.
It is a complicated setup and needs a lot of hw

## Slide 40: Hw needed for standard test setup
Home made Pulser
(1 board at the time!!
very slow)
2 optical concentrator (one is needed to
Teminate the bus) MANDATORY!
Copper link and pocket daq

## Slide 41: What we have:
To setup the very same test bed they
have in Indiana we should order 2 VME 64X
crate (lots of time and money)

## Slide 42: A different strategy:
Use ChipScope VIO to assert built-in test pulser channel, monitor associated channel with ChipScope ILA
Use ChipScope VIO to program threshold with low threshold, monitor associated channels with ChipScope ILA
Configure FPGA with Data Concentrator
Benefit: what we have is enough.

## Slide 43: And…
We developped this strategy when we were in Indiana (thanks Brandon) and
made it work….
Moreover we discovered that:
We could have been much faster if we could pulse the system
one crate at the time (13 boards)….
Therefore we are designing a pulse system we can use in Italy and Japan
To drive the RPC single crate and make debugging much faster.

## Slide 44: Proposed strategy:
Test analog part at the firm level using a scope and the proper hw
we are developping.
Test the digital part using chipscope at the crate level in italy.
Test the board with the pulser in Italy and send everything pulser
Included in Japan.
Cosmic test in Japan on KLM

## Slide 45: Situazione 2016
La commissione 1 ha appena approvato 210 keuro di finanziamento
per lo svolgimento delle gare per l’acquisto di FE boards per il KLM.
Queste gare dovrebbero avere luogo entro il corrente anno.
Per il prossimo anno si prevedono attivita’ di test ed installazione

## Slide 46: Richieste 2017
Missioni estere per metabolismo 23 keuro
Missioni estere per installazione 27 keuro
Missioni per contatti 2 keuro
Consumo metabolismo 5 keuro
Inventariabile 12 keuro

## Slide 47: Architettura proposta
Architettura di validazione del sistema EMC in avanti
Il sistema costituisce la dorsale DAQ per tutti i test svolti in italia durante la costruzione
E’ contemporaneamente uno studio di fattibilità di funzioni di SLOW control con capacita’ di DAQ e TRIGGER integrate.
In questo quadro RM3 seguirebbe lo sviluppo del pre-amp e scheda di gestione del very front-end (PTD power threshold digital). Il PTD e’ interfacciato con elettronica di Napoli.
Pre-Amps
PTD
uSOP

## Slide 48: Gerarchia di Aggregazione
<# | Crystal | LA APD | Preamp | PTD | uSOP
# | 72 | 144 | 144 | 5 | 1
mod | - | 2x Crystal | 1x LAAPD | 1x 32 Pre | 1x 5 PTD
costo | - | - | 65€/chan | 2k€/board | 4k€/board
totale | - | - | 10k€ | 10k€ | 4k€
uSOP
PTD
PTD
PTD
32 LA-APD
PTD
PTD
To Belle2 Network D
 | Forward | 
 | # | costo
spicchi | 16 | -
Crystal | ~1150 | -
LA-APD | ~1150 | -
PreAmp | ~2300 | 160 k€
PTD | 80 | 160 k€
uSOP | 16 | 64 k€
Totale | - | 384 k€

## Slide 49: Costi di Sviluppo 2013-2015
 | NRE costs (k€) |  | 
 | 2013 | 2014 | 2015
Napoli | 12.5 k€ | 42 k€ | ?
Roma3 | 12 k€ | 22 k€ | 22 k€
I costi di sviluppo devono considerarsi in aggiunta ai costi di produzione

## Slide 50
Shaper
Pre-amp
S
Pulse
Encoder
LVDS
Analog
Range (0,1)
n
Trigger Fast Path
X Ncryst
EMC energy, slow and Trigger path
Energy accurate measurement, trigger and slow control path
Slow control
and monitor

## Slide 51: Front end undoped CsI EMC BELLE 2
2 or 4 LAAPS Si APD S8664-1010 and Front& cards
Ultra LowNoise Charge Preamplifier
Power Regulator 500V
DAC SET Voltage
ADC READ Voltage
ADC READ Current APD
Q output
Front& cards
Pre-Amp G ̴ 1,4V/pC N < 0.6 MeV
Risoluzione@100MeV 4% and 1.6% @ 8 GeV
Range E = µ ( ̴168MeV) to 8 GeV
𝑄resolution = 2%/(𝑒)1/4 Dinamica massima = ? V (da decidere) Dissipazione massima = ? mW da vedere potrebbe non essere un problema Alimentazione singola = +6V
Dimensioni = 15 x 30 mm
Regolatore Alta Tensione Regolazione = 250V a 500V Lettura e scrittura regolazione alta tensione = 16bit tramite protocollo I2C Stabilità regolazione alta tensione = 0.1‰ Range temperatura = 0 a 60°C.
PTD con input da SLOW
Lavoro fatto ed in corso di implementazione nella matrice di CsI che stiamo costruendo

## Slide 52: PTD CSI EMC BELLE 2
uSOP (Na)
SLOW control interface
Set & Read Voltage single LAAPD (I2C protocol) la banda passante richiesta e’ qualche Mb/s.
Ethernet control
USB control
HV primary
HV generator 600V
Funzioni di DAQ
Processa signal
Somma signali for cristallo
Ecc..
PTD : paramteri di slow control
HV primaria
Soglie
Monitor in tensione
Monitor in corrente
Temperatura Digitalizzazione
Lettura adc
………..
FMC
…………..
From/to pre-amp
Single channel control units
Ognuna controlla il singolo
Pre-amp.
Lavoro fatto ed in corso di implementazione nella matrice di CsI che stiamo costruendo

## Slide 53: Tool Chain
Photodetector
APD
FrontEnd
PTD
Power
Threshold
Pre-Amp
Digital ReadOut
ARM
Cortex A8
LINUX
FMC
RAM
FLASH
USB
Ethernet
ZYNQ 7000
SPI
I2C
Parallel Digital
Timing
FPGA
KINTEX 7
Controls
Trig
DAQ
Aggregation switch
PC Server
uSOP: Service Oriented
Platform based on uP
Detetector, PreAmp, PTD
uSOP
File System
(P)NFS
Web Server
GUI
Web Services
Load Balancing
Run Control
Graphic Display
Network profiling

## Slide 54: Lavoro svolto a RM3
1
2
Start up system for the test beam
3
Single ended to differential converter
Front End
4
Conclusions and future development
Notes: Questa è un'altra opzione per creare una diapositiva introduttiva.

## Slide 55: Front End.
Charge pre-amp and detector
Voltage regulator.
TOP side.
Detector linear voltage regulator
BOTTOM side.
Charge pre-amp.
Notes: Aggiungere le diapositive necessarie per ogni sezione di argomento, incluse diapositive con tabelle, grafici e immagini.
Vedere la sezione successiva per un esempio di tabelle, grafici, immagini e video.

## Slide 56: Front End. Charge pre-amp
Charge – Preamplifier
Custom discrete amplifier at BJT transistor.
Gain = 1.4V/pC
Power dissipation = 16mW
Single power = 6V to GND
Dynamic Range 2.2V 50R
Tau IN = 40ns
40ns
420ns
40ns
Signal IN
Signal OUT
TIMING CsI PURE:
Protection
Pulse test IN
C
C
K
Signal OUT
KATODE

## Slide 57: Cosmic ray test stand 1.
Trigger Finger UP & Finger DOWN
TOP VIEW
Finger UP
Finger UP
CsI Pure
VIEW
Finger UP
CsI Pure
Finger DOWN
SCOPE
Electronics System
Pb
5cm
Pb
Logic NIM

## Slide 58: Front End. APD SET-UP.
Double APD Large Area read-out(S8664-1010).
Mechanical support for APDs.
Front end, mounted on APD.

## Slide 59: Front End. LAAPD Performance.
Standard analysis by Perugia.
Alessandro Rossi.

## Slide 60: Front End. PP 1inch SET-UP.
PP 1inch double rea-out (HAMAMATSU 1’’ UV PENTODE).
Mechanical support for 2 PP,voltage divider and front end electronics.

## Slide 61: Front End. 2PP 1inch Performance.
Signal/noise on ch1 = 49.
  Assuming a that muon delivers 30 MeV noise level is about 650 KeV
Signal to noise ratio on ch2 = 76
  Assuming a that muon delivers 30 MeV noise level is about 400 KeV
Signal/noise on
ch1+ch2 = 78.
  Assuming a that muon delivers 30 MeV noise level is about 400 KeV

## Slide 62: PP 1inch e 2inch voltage divider.
Pre Charge Amplifier
LV PW
HV PW

## Slide 63: In view of the next test beam
A test beam has been scheduled for next October.
We need:
  To sets and read back several parameters:
  HVs for each single channel.
  temperature for each channel.
  The uSOP platform (see Alberto Aloisio’s talk) will not be ready by then therefore we have developped a temporary solution.

## Slide 64: HV APD control system.
Front Panel NIM1U
Rear Panel NIM1U
16 Analog Signal Output
USB & Ethernet Connection
16 Analog Signal Input
16 line I2C.
Slow Control Front end
1-Ware protocol for external sensor:
- Temperature.
- Humidity.
High Voltage Generator.
Frequency: 250kHz.
Stability: 0,1%
Selectable Voltage:
- 50V
- 100V
- 600V
ON BOARD:
CPU (LPC1768FBD100)
HV for 16CH Front End
LV for 16CH Front End

## Slide 65: Front End control system for APDs.
Web panel.
  sets and reads back
  single channels HVs.
  Single channel temperature reading

## Slide 66: Attivita’ 2015
Pre-amp in carica con uscita differenziale e basati su JFET (vogliamo migliorare il rapporto
segnale fondo).
Sviluppo di una scheda di controllo per l’amplificatore e per l’HV che tenga conto delle
specifiche dell’esperimento piu’ restrittive di
quelle sulla base delle quali sono state sviluppate
le attuali distribuzioni di HV standard.

## Slide 67: Richieste Consumo EMC FE 2015
15 Keuro di consumo per produrre una catena di studio del EMC basata sui nuovi pre-amplificatori e Controller HV che seguono le specifiche dell’esperimento.
4 Montaggi radiografie saldature etc..
3 Connettori, componenti…

## Slide 68: Richieste Missioni 2015
Metabolismo: 1 m.u./FTE + 1.5ke/FTE *4 FTE=30
Assemblaggio modulo a KEK (1 m.u.) 5.5 keuro
Contatti tra gruppi italiani 4 keuro
Refurbishment ECL 12 keuro
2 sw e physics meeting 8.5 keuro

## Slide 69: Inventariabile
Impulsatore 10 keuro