## Slide 1: First look at test beam data
Mauro Raggi
PADME ECal meeting LNF, 8 september 2016

## Slide 2: Discharges in HZC PMTs
With naked dividers discharges were observed in the PMTs due to their very small distance (~1mm).

## Slide 3: The 25 crystal prototype
Uses 25 20x20x220 mm3 BGO crystals wrapped with Teflon. Coupled to XP911 HCZ photonics PMTs by using optical grease.
PMT high voltage set to the equalization values provided by firm.

## Slide 4: Analysis and data samples
By no means official reconstruction used
  Basic self made program with no sophisticated treatment of pedestals and saturations
Run 470: 450 MeV ~150K triggers collected
Run 471: 250 MeV ~1M triggers collected
Run 472: supposed to be 150 MeV is in fact 250 MeV

## Slide 5: Sample 250MeV event
Do we need some smoothing of the curves?
Seems Off

## Slide 6: Reconstruction of charge
Pedestal measurement averaging first 100 samples
After reconstructing pedestal average:
Qch=Qch-Ped()

## Slide 7: Sample of 450 MeV event
Seems Off

## Slide 8: Pedestal average example
QCh(i)=S(Sam(i)-PedAVG(i) )/50*1ns

## Slide 9: Qch in the pedestal region
Double peaks in the pedestal is a known issue. I get the maximum of this distribution Qped and I subtract it to Qch: Qch(i)=Qch(i)-Qped(i)

## Slide 10: Pedestal after Qch correction
Maximum of the pedestal is now at 0.
Few channels to be fixed

## Slide 11: Qch at 250 MeV

## Slide 12: Selection cuts
After reconstructing the charge the following cut are applied
  Zero suppression if(QCh(i)>0)
  Ncrystals>10
  Cluster center radius <5mm
Only events passing the selection enter the Qtot histograms
Can still apply timing cuts to remove accidental low energy photons

## Slide 13: 250MeV peaks fit

## Slide 14: Linearity for the 250MeV series
Good linearity up to 1 GeV!

## Slide 15: s(E)/E for the 250MeV run

## Slide 16: Qch at 450MeV

## Slide 17: Qtot at 450MeV run

## Slide 18: Linearity for 450MeV run
Higly non linear at E>1GeV as expected.
Need larger dynamic range (1V->2V) in the FADC.

## Slide 19: s(E)/E for the 450MeV run
Non linearity strongly affects energy resolution at E>1GeV as expected.
Can be corrected by fitting the signals?

## Slide 20: Linearity comparison
Perfect agreement in the linearity fit on blue dots only

## Slide 21: s(E)/E comparison
Perfect agreement resolution fit on blue dots only

## Slide 22: Comparison with old test beam
APD
Ham. S8664-1010
PMT
Ham. 1 inch
Preliminary 3x3

## Slide 23: Linearity comparison
Lower charge collected with respect to Hamamatsu: gain only??
PMT HCZ ~16pC /MeV
PMT Hama ~21pC /MeV
APD ~ 5.3pC /MeV

## Slide 24: DataMC comparison
Number of photo electrons: 640.
Minimum of the zero suppression in MC: 0.3MeV
Cell to Cell intercalibration errors: None

## Slide 25: Data Mc comparison tuning
Measurement of the Np.e.:
  NPE: from linearity plot: 16.4pC/MeV
  Gain from HZC data sheet ~9x105
  Np.e.= 16.4x10-12/(9x105 x 1.67x10-19)=110 p.e./MeV
  Greatest uncertainty on PMT gain (20%-30%)
Minimum of the zero suppression in MC
  Minimum visible energy (default per crystal in MC was 0.3 MeV)
  Moved to more realistic estimate from data ~1. MeV
Cell to Cell intercalibration
  Standard in MC includes no intercalibration errors in cell
  Energy scale of single cell in data are different

## Slide 26: Data MC after tuning
Number of photo electrons: 100.
Minimum of the zero suppression in MC: 1MeV
Cell to Cell intercalibration errors: None
Clear dependence introduced in the energy collection at low energy

## Slide 27: Calibration constant gaus at 10%
Introduced a random gaussian distributed Cij for each crystal.
When summing each single charge or energy value E=Eij*Cij
Result is a different behaviour at high energy where the number of involved cells increases. No changes at low energy.

## Slide 28: Conclusions
The test beam data provided a good sample of data to study the 5x5 crystals prototype.
  Missing glue and paintings. Partially calibrated crystals.
  One of the crystals off
The resolution obtained in ~ 1.9%/sqrt(E)+0.47%
  The resolution is understood in term of the PADME MC simulation
  Better measurements of minimum energy threshold will help improving the resolution in the low energy part of the spectrum.