## Slide 1
Massimiliano Scisciò
Varennes 6.9.2016
Examen Doctoral
Report of research activity
Doctoral school in Accelerator Physics (Year III)
-
Study and implementation of beamlines and devices
for the acceleration, transport and manipulation
of laser-accelerated particle beams
Massimiliano Scisciò
Rome, Oct. 17th 2016
Scientific supervisors: L. Palumbo, P. Antici

## Slide 2
Research activities - Summary
Laser driven acceleration mechanism
Laser driven electron beam line
Laser driven proton beam line
PIC simulations for ultra-thin targets
modeling of exploded targets with hydrodynamic codes
PIC simulations for CSA acceleration
particle tracking simulations of different transport lines
high- and low-energy electron beam
evaluation of acceptable initial beam
parameters
parametric study with particle tracking code (energy selector)
optimization with focusing elements
assembling
experimental calibration
20 MeV
  M. Scisciò, L. Lancia, M. Migliorati, A. Mostacci, L. Palumbo,
  Y. Papaphilippou, and P. Antici, J. Appl. Phys. 119, 094905 (2016)
  M. Scisciò, E. D'Humières, S. Fourmaux, J. C. Kieffer, L. Palumbo, and P. Antici, Phys. Plasmas 21, 123104 (2014)
  Paper on theoretic study in preparation
  P. Antici, E. Boella, S.N. Chen, M. Barberio, J. Böker, F. Cardelli, J.L. Feugeas, M. Glesser, P. Nicolaï, L. Romagnani, M. Scisciò, M.Starodubtsev, O. Willi, J.C. Kieffer, V. Tikhonchuk, H. Pépin, L. O. Silva, E. d’Humières, J. Fuchs, submitted to Phys. Rev. Lett., Oct. 2016

## Slide 3
TNSA acceleration mechanism
Dominant laser-driven acceleration mechanism on commercial TW-class lasers: Target Normal Sheath Acceleration (TNSA)
Energy selection device
Accelerating field up to TV/m
Proton energy up to a few tens of MeV
High bunch charge (up to hundreds of nC)
Energy spread of almost 100%
Protons are accelerated within a cone of tens of degrees
-
-
-
+ -
+ -
+ -
+ -
Surface contaminant (H2O)
H+ ion
Bulk Target (Al)
e-
E

## Slide 4
Energy selection device (ES)
Passive energy selection device based on magnetic dipoles
Displacement is a function of the
proton energy: spatial beam selection
Particle tracking simulations with TSTEP:
selection slit
Particle tracking simulations varying:
dipole length
magnetic field
slit aperture
entering beam divergence

## Slide 5
Optimization of the ES – particle tracking simulations
Data interpolation from numerous simulations: “working point maps”
Optimization for the range 1-20 MeV
final energy spread <20 %
compact dimensions
high efficiency
2 MeV
10 MeV selected energy
20 MeV
Length of the dipoles [cm]
Field strength
of the dipoles [T]
Energy spread of
the final beam [%]
Applications in material science: nano-structures and nano-crystals growth, IBA analysis, stress test of materials etc.

## Slide 6
Optimized ES – particle tracking simulations
dipole length
dipole width
magnetic field
slit aperture
dimensions
Optimized parameters for energy selection
Particle tracking simulation of the optimized ES
energy range from 1 to 20 MeV
energy spread % (FWHM)
efficiency %
beam transverse dimensions
in the mm range
Features

## Slide 7
ES efficiency
Optimized energy selection
TNSA proton source
5 mrad initial divergence
20% efficiency

## Slide 8
Laser driven proton beam line: Focusing + Energy selection
Proton beam line for beam focusing and energy selection
Focusing beam line stage based on
permanent magnet quadrupoles (PMQ)
compact dimensions (cm)
high focusing field gradient
(up to 500 T/m)
easy to implement
Energy selector
magnetic dipoles + slit
requires a few mrad initial divergence
T. Eichner et al., Pys. Rev. Spec. Topics – Accel. Beams 10, 082401 (2007)

## Slide 9
Permanent Magnet Quadrupoles: magnetic field simulations
Magnetic field simulations with PANDIRA (SuperFish)
Commercial rare-earth material
(NeFeB)
compact dimensions (cm)
Two types of PMQ:
160 T/m for low energy
350 T/m for high energy
Bx (Gauss)

## Slide 10
Focusing PMQ-line: beam optics + particle tracking simulations
Phase space E-x’ : the PMQ array collimates the beam at the central energy
PMQ focusing line for the 3 MeV central energy case
Proton beam
QF
QD
QD
QF
QF
Magnetic field gradient: ±160 T/m
Length: 3 cm
Bore radius: 1 cm
Outer radius: 4 cm
3.5 cm
2 mm
2 mm
1 cm
8 mm

## Slide 11
Laser driven proton beam line – Start-to-end simulation
Proton beam line for beam focusing and energy selection: case of 3 MeV central energy
Start-to-end particle tracking simulations
Focusing PMQ: improved efficiency
For different energies: same PMQs, different spacing
20 MeV focusing configuration: work in progress
Final energy spread < 20 %
Start-to-end efficiency 1%
3 MeV proton beam line

## Slide 12
Conclusions and future prospects
Numerical work for beam line optimization:
Beam optics and particle tracking simulations for the beam line analysis and optimization
Paper about the numerical results is in preparation
Manufacturing/assembling of the beam line components:
Energy selection device
PMQ for beam focusing
Experimental campaign:
PW laser TITAN @ LLNL (USA), August 2016 : first testing and calibration of the ES
500 TW laser ALLS @ INRS (Canada), winter 2016-17
@ LULI (France), April 2017

## Slide 13
Experimental run at LLNL: ES assembly
August 2016:
ES assembled and tested at the TITAN laser facility (LLNL, USA).

## Slide 14
Experimental run at LLNL: Exp. Setup
Experimental setup
Off-axis parabola
Un-focused
laser beam
Focused laser beam
Au foil 15µm
p+ beam
Energy selector
Thompson parabola
Laser parameters:
Wavelength
Energy
On-target spot size
On-target intensity
Pulse duration

## Slide 15
Experimental run at LLNL: Dipole calibration
RCF stack for monitoring beam dispersion between the 2nd and 3rd dipole
for beam dispersion measurements
3.6 cm
2.8 cm
2.4 cm
Simulation (TSTEP)
Experiment (RCF)

## Slide 16
Massimiliano Scisciò
Varennes 6.9.2016
Examen Doctoral
Thank you for the kind attention.
Massimiliano Scisciò