## Slide 1: High precision measurement of the radiative capture cross section of 238U at the n_TOF CERN facility
F. Mingrone on behalf of the n_TOF Collaboration

## Slide 2: Motivations: Nuclear Reactors
+ ADS
Advanced design of existing reactors to improve the safety standard and the efficiency.
Benefit of the new reactor concepts:
Fast reactors and ADS: multirecycling of the fuel, which leads to
  better use of the fuel (the energy production can be up to 60 times more efficient)
  Improving the waste management (reduction of the long-term radiotoxicity of the ultimate waste)
VHTRs: passive safety features and the ability to provide very-high-temperature process heat (used ad example in the massive production of hydrogen)

## Slide 3: Motivations: Role of the radiative capture of 238U
Fast and thermal reactor systems: uncertainties (%) due to 238U capture cross section
 | Reactor | keff (%) | Reactivity (%) | Power Peak (%)
Fast nuclear reactors | ABTR | 0.26 | – | –
 | SFR | 0.07 | 1.24 | –
 | GFR | 0.41 |  | 0.30
 | LFR | 0.25 | – | –
Thermal nuclear reactors | PWR | 0.26 | – | –
 | VHTR | 0.19 | – | –
Source: Final Report – Subgroup 26 of Organization for Economic Co-operation and Development (OECD) and Nuclear Energy Agency (NEA)
Uncertainty on Pu isotope density at the end of the fuel cycle:
1.1% for 239Pu
0.2% for 240Pu
0.1% for 241Pu

## Slide 4: Motivations: Role of the radiative capture of 238U
EXFOR DATABASE: more than 25 datasets in the resolved resonance region and a few less in the unresolved BUT still inconsistencies for the capture cross section up to 15%
ENDF/B-VII evaluation: some small (but higher than the uncertainty) modifications to the standards capture result in the high energy region
NEA High Priority Request List
UNCERTAINTY IN THE CROSS SECTION DOWN TO 1-5%
EC-JRC Gelina with C6D6 detection system (25 meV < En < 80 keV) Kim, H. I. et al., Eur. Phys. J. A 52, 170 (2016)
n_TOF with TAC detection system (1 eV < En < 90 keV)
n_TOF with C6D6 detection system (1 eV < En < 700 keV)
 | Neutron energy range | Current Accuracy | Target Accuracy
PWR | 22.6 – 454 eV | 2% | 1%
 | 9.12 – 24.8 keV | 9% | 5%
Fast reactors | 2.04 – 24.8 keV | 3-9% | 1.5-2%
EC-FP7
PROJECT ANDES

## Slide 5: Motivations: Role of the radiative capture of 238U
EXFOR DATABASE: more than 25 datasets in the resolved resonance region and a few less in the unresolved BUT still inconsistencies for the capture cross section up to 15%
ENDF/B-VII evaluation: some small (but higher than the uncertainty) modifications to the standards capture result in the high energy region
NEA High Priority Request List
UNCERTAINTY IN THE CROSS SECTION DOWN TO 1-5%
EC-JRC Gelina with C6D6 detection system (25 meV < En < 80 keV) Kim, H. I. et al., Eur. Phys. J. A 52, 170 (2016)
n_TOF with TAC detection system (1 eV < En < 90 keV)
n_TOF with C6D6 detection system (1 eV < En < 700 keV)
 | Neutron energy range | Current Accuracy | Target Accuracy
PWR | 22.6 – 454 eV | 2% | 1%
 | 9.12 – 24.8 keV | 9% | 5%
Fast reactors | 2.04 – 24.8 keV | 3-9% | 1.5-2%
EC-FP7
PROJECT ANDES

## Slide 6: The n_TOF CERN facility

## Slide 7: Experimental technique
Using a Time of Flight (TOF) technique, capture cross section is determined through the measurement of the reaction yield YR(En):
N: normalization factor
C: capture counts
B: background counts
F: incident neutron fluence
ε = k × Ec: detection efficiency
A: area of the sample
D ~ eV

## Slide 8: 238U(n,g): Experimental setup
2 different setups for capture measurements:
Total Absorption Calorimeter (TAC)
  40 BaF2 crystals in a 4p geometry
  Detects the entire g cascade
  Total Absorption Detection Technique
Two C6D6 scintillation detectors
  Optimized for a low neutron sensitivity (i.e. sensitivity to background from scattered n)
  Only one g-ray detected per event
  Total Energy Detection Technique with Pulse Height Weighting Technique (PHWT)
NEUTRON BEAM
C6D6

## Slide 9: 238U(n,g): Sample
Enriched metallic uranium rectangular plate (53.825 x 30.12 mm2, 235 mm thick) enveloped inside a 20 mm aluminum and a 25 mm kapton thick foils.
Provided by the EC-JRC Geel
Isotopic and physical analysis done @ EC-JRC Geel in 1984
Mass | 6.125 ± 0.002 g 9.56×10-4 atoms/barn
% 238U | 99.99 %
% 235U | < 11 ppm
% 233-234-236U | < 1 ppm each
Radioactivity | 12.4 kBq/g (76 kBq)

## Slide 10: 238U(n,g): Data reduction
Analysis from raw data to experimental yield
Stability of the detection system. The stability has been checked both for neutron flux and for the scintillators. Runs which show a deviation of more than the 3.5% have been rejected.
flash-ADC channels to energy calibration + energy resolution of C6D6. Weekly calibration measurements with 137Cs (661.7 keV), 88Y (0.898 and 1.836 MeV) and Am/Be (4.44 MeV). 6 calibration lines have been extracted to take into account small gain changes in the scintillators.
Weighting functions. The detector responses have been simulated with the GEANT4 toolkit, and convoluted with the experimental resolution. Two WF have been produced: one considering an homogenous z-emission, the other considering an exponential attenuation to take into account the the neutron transport within the sample.
Background subtraction.
Neutron flux evaluation. n_TOF evaluated flux (M. Barbagallo et al., The European Physics Journal A 49, 156 (2013))
Normalization.
FOR DETAILS SEE
F. Mingrone et al., Nuclear Data Sheets 119 (2014) 18-21
F. Mingrone et al., INPC 2013 - VOL. 1 Book Series: EPJ Web of Conferences 66 (2014) 03061
Notes: accurate study of the calibrations between the flash-ADC channels and the deposited energy was performed on a weekly basis using three standard sources: 137Cs (661.7 keV), 88Y (0.898 and 1.836 MeV) and Am/Be (4.44 MeV).
Comparing the different calibration spectra for each isotope, we notice that they are not stable, and for this reason we extracted six calibration lines from the different measurements made.

## Slide 11: 238U(n,g): Data reduction
Analysis from raw data to experimental yield
Stability of the detection system. The stability has been checked both for neutron flux and for the scintillators. Runs which show a deviation of more than the 3.5% have been rejected.
flash-ADC channels to energy calibration + energy resolution of C6D6. Weekly calibration measurements with 137Cs (661.7 keV), 88Y (0.898 and 1.836 MeV) and Am/Be (4.44 MeV). 6 calibration lines have been extracted to take into account small gain changes in the scintillators.
Weighting functions. The detector responses have been simulated with the GEANT4 toolkit, and convoluted with the experimental resolution. Two WF have been produced: one considering an homogenous z-emission, the other considering an exponential attenuation to take into account the the neutron transport within the sample.
Background subtraction. Validation of the background level through black-resonance filters.
Neutron flux evaluation. n_TOF evaluated flux (M. Barbagallo et al., The European Physics Journal A 49, 156 (2013)).
Normalization. Saturated-resonance method.
Notes: accurate study of the calibrations between the flash-ADC channels and the deposited energy was performed on a weekly basis using three standard sources: 137Cs (661.7 keV), 88Y (0.898 and 1.836 MeV) and Am/Be (4.44 MeV).
Comparing the different calibration spectra for each isotope, we notice that they are not stable, and for this reason we extracted six calibration lines from the different measurements made.

## Slide 12: 238U(n,g): Background subtraction
All the background components have been evaluated singularly:
  Beam off: time independent, from natural and sample radioactivity and air activation
  Sample out: main component of the beam-related background, evaluated without any sample in beam
  Scattered neutrons: g-rays coming from sample-scattered neutrons captured in the ambient material. Evaluated by GEANT4 simulations as in P. Zugec et al., NIM A 760, 57 (2014).
  In-beam g rays: very important in the keV energy region. Evaluated by means of a n+natPb measurement.
  g rays from fission events: prompt g-ray emission or from fission fragment decays. Evaluated with GEANT4 simulations

## Slide 13: 238U(n,g): Background subtraction
The background level has been evaluated exploiting Ag, W, Co and Al black-resonance filters in beam.
The resulting background has been properly scaled to take into account the attenuation of both the neutron beam and the in-beam photons.
The two background yields agree for 3 < En < 100 keV within the 5%
In the neighborhood of the Al resonances the estimation is not reliable because the amount of aluminum in the windows of the beam line is not precisely known

## Slide 14: 238U(n,g): Yield normalization
Saturated resonance technique applied to the first 3 resonances
DETECTOR | NORMALIZATION FACTOR |  |  | PERCENTAGE DEVIATION |  | 
 | N1 | N2 | N3 | N1/N2 | N2/N3 | N1/N3
BICRON | 0.842 | 0.843 | 0.850 | 0.03% | 0.9% | 1%
 | Nbic = 0.845 |  |  | DNbic/Nbic = 1% |  | 
FZK | 1.008 | 0.995 | 1.001 | 1% | 0.6% | 0.6%
 | Nfzk = 1.002 |  |  | DNfzk/Nfzk = 1% |  | 

## Slide 15: 238U(n,g): Correlated uncertainties
SOURCE OF UNCERTAINTY | UNCERTAINTY RRR | UNCERTAINTY URR
Sample mass | 0.1% | 0.1%
Neutron flux – shape* | 1-2% | 3 < En < 100 keV: 4-5% 100 < En < 480 keV: 2%
Normalization | 1% | 1%
Background subtraction | 1-2% | 3 < En < 100 keV: 3% 100 < En < 480 keV: 7%
Total | 2-3% | 3 < En < 100 keV: 5-6% 100 < En < 480 keV: 8%
*M. Barbagallo et al., The European Physics Journal A 49, 156 (2013)

## Slide 16: 238U(n,g): Capture yield

## Slide 17: 238U(n,g): Capture yield

## Slide 18: 238U(n,g): Resonance Shape Analysis
  RSA can be performed only up to 3 keV due to the degradation of the signal-to-background ratio with the neutron energy
  The multilevel multichannel R-matrix code SAMMY has been used to fit the resonances, starting from the parameters of JEFF-3.2.
  The resonance kernel has been used in the comparison with the evaluated libraries

## Slide 19: 238U(n,g): Unresolved Resonance Region
  The sample-related effects, i.e. self-shielding and multiple scattering followed by capture, are taken into account applying a correction factor obtained from MCNP6 simulations.

## Slide 20: 238U(n,g): Unresolved Resonance Region
  The sample-related effects, i.e. self-shielding and multiple scattering followed by capture, are taken into account applying a correction factor obtained from MCNP6 simulations.
  3 < En < 20 keV: fair agreement with libraries
50 bin/decade, dE/E~2%

## Slide 21: 238U(n,g): Unresolved Resonance Region
  The sample-related effects, i.e. self-shielding and multiple scattering followed by capture, are taken into account applying a correction factor obtained from MCNP6 simulations.
  3 < En < 20 keV: fair agreement with libraries
  20 < En < 80 keV: CS slightly below evaluated libraries and other measurements
  80 < En < 700 keV: CS 15 to 25% higher than the ENDF/B-VII.1 evaluation, and 21 to 32% higher than the JEFF-3.2 evaluation.
50 bin/decade, dE/E~2%

## Slide 22: Summary and conclusions
The radiative capture cross-section of 238U has been measured at the n_TOF facility using an array of two deuterated benzene scintillators.
The capture yield has been extracted with very low correlated uncertainties, which goes from 2-3% in the RRR to 5-8% in the URR, depending on the energy range.
The RSA has been performed up to 3 keV, showing a fair agreement with the evaluated libraries apart from few resonances.
In the URR the cross section has been extracted up to 700 keV. Results from this work are in fair agreement with evaluated libraries up to 20 keV, show minor differences from 20 to 80 keV, and yield to about a 20% increase in the cross section from 80 to 700 keV

## Slide 23: THANK YOU FOR YOU ATTENTION
Federica Mingrone
federica.mingrone@cern.ch

## Slide 24: BACKUP SLIDES

## Slide 25: Motivations: World energy outlook
Total Primary Energy Supply by resource
World Energy Council, World Energy Resources, 2013 Survey, London, 2013
Shares of global anthropogenic greenhouse-gas
International Energy Agency, CO2 Emissions from Fuel Combustion - Highlights,
Paris, 2014
IEA Energy Atlas
Data from IAEA, latest data available from 2013

## Slide 26: Motivations: Nuclear Reactors
+ ADS
Benefit of the new reactor concepts
Fast reactors and ADS: multirecycling of the fuel, which leads to
  better use of the fuel (the energy production can be up to 60 times more efficient)
  Improving the waste meanagement (reduction of the long-term radiotoxicity of the ultimate waste)
SCWR: higher efficiency and plant simplification, which lead to an improved economics
VHTRs: passive safety features and the ability to provide very-high-temperature process heat (used ad example in the massive production of hydrogen)

## Slide 27: Motivations: Nuclear Reactors
+ ADS
Deployment of Gen IV reactors: not before 2030
For many decades they will be deployed alongside Gen III+
R&D and demonstration projects needed to bring concepts towards commercialization, in particular in the areas of fuels and materials that can withstand higher temperatures, higher neutron fluxes or more corrosive environments.
Construction and operation of Gen IV prototypes in the period 2020-2030. Prototype development and testing is seen as particularly important.

## Slide 28: The n_TOF CERN facility
 | EAR-1 | EAR-2
Energy range | Thermal < En < 1 GeV | Thermal < En < 300 MeV
Instantaneous neutron flux | 105 n/cm2/pulse | 106 n/cm2/pulse
Repetition rate | <0.8 Hz (1 pulse/2.4 s maximum) | 
Proton pulse width | 7 ns | 
Cooling and moderation system | 1 cm water (cooling) + 4 cm borated water (moderator) | 5 cm water (cooling and moderator)
Energy resolution | DE/E=10-4 (En < 10 keV) | DE/E=10-3 (En < 10 keV)

## Slide 29: The n_TOF CERN facility
 | EAR-1 | EAR-2
Energy range | Thermal < En < 1 GeV | Thermal < En < 300 MeV
Instantaneous neutron flux | 105 n/cm2/pulse | 106 n/cm2/pulse
Repetition rate | <0.8 Hz (1 pulse/2.4 s maximum) | 
Proton pulse width | 7 ns | 
Cooling and moderation system | 1 cm water (cooling) + 4 cm borated water (moderator) | 5 cm water (cooling and moderator)
Energy resolution | DE/E=10-4 (En < 10 keV) | DE/E=10-3 (En < 10 keV)
Data from ENDF/B-VII.1
~15 keV

## Slide 30: n_TOF neutron flux
50 bin decade
Constant ratio @ 1.128 from 0.1 eV to 100 keV
Difference in the thermal region due to a change on the 10B density in the moderator

## Slide 31: 238U(n,g): Resonance Shape Analysis
  RSA can be performed only up to 3 keV due to the degradation of the signal-to-background ratio with the neutron energy
  The multilevel multichannel R-matrix code SAMMY has been used to fit the resonances, starting from the parameters of JEFF-3.2.
  The resonance kernel has been used in the comparison with the evaluated libraries
  For En>2.2keV kernel from this work are systematically higher than the ones reported in the evaluated libraries
2.2 keV

## Slide 32: 238U(n,g): Resonance Shape Analysis
  RSA can be performed only up to 3 keV due to the degradation of the signal-to-background ratio with the neutron energy
  The multilevel multichannel R-matrix code SAMMY has been used to fit the resonances, starting from the parameters of JEFF-3.2.
  The resonance kernel has been used in the comparison with the evaluated libraries
  3 resonances below 2.2 keV which differs from the evaluated libraries for more than 20%
2.2 keV
This work |  |  | ENDF/B-VII.1 | JEFF-3.2
Er (eV) | k(meV) | Dk/k (%) | k (meV) | k (meV)
721.68 | 1.45 0.09 | 6 | 1.12 | 1.36
1211.32 | 6.5 4 | 61 | 4.01 | 6.54
1565.54 | 6.1 0.7 | 12 | 4.71 | 4.71