## Slide 1: WP3 (status&update)
COSA f2f Meeting
INFN-CNAF Bologna
3/11/2016

## Slide 2: Outline
Cluster
Operations
Tests
Todo

## Slide 3: Boards@CNAF

## Slide 4: Cluster@CNAF (22 nodi!)
Xeon
Atom
Pentium
Broadwell
Q1/2015
14nm
Silvermont
Q3/2013
22nm
Airmont
Q1/2015
14nm
D-1540
8 core
90 W
151 HS06
C2750
8 core
25W
55 HS06
N3700
4 core
7W
28 HS06
X86_64
Tegra K1
Q2/2014
ARMv7
Tegra X1
Q2/2015
ARMv8
4 core
10W
28 HS06
4 core
15W
20/28 HS06
1.89
HS06/W
Nodo del cluster
2.20
HS06/W
4
HS06/W
2.8
HS06/W
<2.8
HS06/W

## Slide 5: Cluster low-power (operations)
CONFIGURATION
  Ansible
MONITORING
  Telegraf/InfluDB,Grafana
TEST SUITE
  Phoronix

## Slide 6: Osservazioni sull’HW lowpower
CPU ARM deludente dopo entusiasmo iniziale (solo Nvidia K1/X1…)
Intel sul low-power ha recuperato il gap su ARM (vedi Pentium N3700)
Intel copre ogni esigenza per cluster da laboratorio (da Pentium a Xeon-D)
Intel (tutto a parte Pentium) permette di utilizzare schede di rete a bassa latenza
Pentium N3700 conveniente come consumi, prezzo per board e ratio performance/consumo
Simulazioni tecnico-economiche hanno senso solo tra CPU Intel (in un mondo ideale per un datacenter sarebbe conveniente un economico Pentium N3700!!!)  no ECC, no multi PSU, no PCIe, no AVX2, etc.

## Slide 7: Il marketing Intel fa di tutto per complicare le cose…
E.G. Core-M hanno cambiato nome da Skylake a Kaby Lake (ora si chiamano di nuovo Core i5, Core i7)

## Slide 8: Tegra X1 vs K1
SORPRESA !!!!
X1 con CPU piu’ lenta (1.7Ghz vs 2.2GHz)
X1 ha interconnessioni ethernet 1GB con bridge USB !!!
  è orientata al mondo automotive/imaging non HPC
  installata scheda Planet 10Gb/s (ricompilato driver)
X1 sui test condotti (PI, Primes, CT reconstruction, staucc) fino ad ora non ci ha impressionato

## Slide 9: Tegra X1 vs K1
K1 2.2GHz, X1 1.7GHz
GPU very similar with the CT application

## Slide 10: Benchmarks
Risultati ed osservazioni in Google Drive
Sorgenti in github

## Slide 11: LHC offline benchmarks
HEPSPEC06
LHCb
Pentium N3700 16GB
=
130€ !!!
A.Falabella

## Slide 12: LHC online benchmarks
LHCb event building
  Sw designed to simulate the event building on a InfiniBand based network
D-1540@COSA vs E5-2600@Tier1
  Same performances (not shown)
  D-1540 requires a third of the power consumption of the E5-2600
M.Manzali

## Slide 13: Implementation of space-aware stochastic simulator on low-power architectures.
Implementig of a variant of a membrane system, called dynamical probabilistic P systems (DPPs), in which probabilities are associated with the rules , and such values vary during the evolution of the system according to a prescribed strategy.
Code Implementations:
Sequential
MPI
CUDA
E.Corni
L.Morganti

## Slide 14: Storage benchmarks
Test DAS (Direct Attached Storage) di HDD/SDD/eNVE
Test file system distribuiti

## Slide 15: Storage (test DAS)
WRITE (dd)
READ(dd)
XEOND WRITE/READ

## Slide 16: Preliminary distr. FS tests
Distributed FS to test:
HDFS (installed)
  10 Intel nodes
BEEGFS (installed, to reinstall)
  10 Intel nodes
LUSTRE (to install ???)
hadoop jar hadoop-mapreduce-client-jobclient-2.7.2-tests.jar TestDFSIO -read -nrFiles 10 -fileSize 1000MB
hadoop jar hadoop-mapreduce-client-jobclient-2.7.2-tests.jar TestDFSIO -write -nrFiles 10 -fileSize 1000MB
----- TestDFSIO ----- : write
Number of files: 10
Total MBytes processed: 10000.0
Throughput mb/sec: 20.2
Average IO rate mb/sec: 20.3
IO rate std deviation: 1.75
Test exec time sec: 80.8
----- TestDFSIO ----- : read
Number of files: 10
Total MBytes processed: 10000.0
Throughput mb/sec: 68.9
Average IO rate mb/sec: 121.2
IO rate std deviation: 2.7
Test exec time sec: 44.7
HDFS&BEEGFS convivono bene assieme

## Slide 17: Network latency
La network latency è alta per tutti (IB < 2micros)
Intel meglio di ARM
X1 molto peggio di K1!!!
Installata NIC 10Gb/s (latency <100micross)
10Gb/s for X1

## Slide 18: Not only CUDA (but not OpenCl)
U
AMD HIP

## Slide 19: TODO 2017
Previsione attività 2017 al CNAF
Continuazione porting applicazioni e benchmarking nuove architetture low power
Benchmarking XEON PHI (acquisto a settembre 2016 già finanziato)
Benchmarking GPU AMD HIP
Benchmarking GPU Pascal (acquisto 1H 2017 finanziato)
Benchmarking fabric OMNIPATH ( finanziato)