## Slide 1
Progress toward spin-polarized fusion: Performance of laser-polarized He-3 during permeation into tokamak pellets
Sina Tafti1, Alexandre Deur2, Jie Liu1, Michael Lowry2, Wilson Miller1, Andrew Sandorfi2, Kevin Wei3, Xiangdong Wei2, Xiaochao Zheng1
1University of Virginia, Charlottesville VA, USA
2Jefferson National Laboratory, Newport News VA, USA
3University of Connecticut, Storrs CT, USA

## Slide 2
Motivation and Background
Self-sustained fusion energy production has not yet been reached
  Energy spent sustaining the plasma > fusion output energy
50 % boost in fusion cross section!!
*Kulsrud, Furth, Valeo & Goldhaber, Phys Rev Lett 49 (1982) 1248.
  The possibility of spin-polarized nuclear fusion gained traction in 1982 with predicted time scales for polarization loss in a plasma that were much longer than the characteristic fuel burn-up period.*
At tokamak energies, fusion reaction of deuterium (D) and tritium (T) proceeds via spin 3/2 resonance state
Spin 1 D and spin 1/2 T will favorably fuse into a 3/2 spin state when their spins are aligned parallel to each other

## Slide 3
Motivation and Background
Self-sustained fusion energy production has not yet been reached
  Energy spent sustaining the plasma > fusion output energy
  The possibility of spin-polarized nuclear fusion gained traction in 1982 with predicted time scales for polarization loss in a plasma that were much longer than the characteristic fuel burn-up period.*
At tokamak energies, fusion reaction of deuterium (D) and tritium (T) proceeds via spin 3/2 resonance state
Spin 1 D and spin 1/2 T will favorably fuse into a 3/2 spin state when their spins are aligned parallel to each other
The same enhancement is achieved for isospin-mirrored reaction:
50 % boost in fusion cross section!!
*Kulsrud, Furth, Valeo & Goldhaber, Phys Rev Lett 49 (1982) 1248.

## Slide 4
The Challenge
Polarization survival in plasma temperatures of ~ K predicted* for fusion timescales but never experimentally tested!
Preparing and handling of polarized fuels
  lack of a method for delivering polarized fuel into the tokamak
Proposed method:
Polarized fusing elements can be delivered to the plasma using hollow polymer shells (~2 mm diameter ICF pellets)
D-III D Tokamak in San Diego
General Atomics
*M. Goldhaber, Proc. Cambridge Philos. Soc. 30, 561 (1934). A.M. Sandorfi et al., Springer Proc. Phys. 187, 115 (2016).

## Slide 5
Permeation time constant of gas into the ICF shells
2 ICF pellets placed inside tube
HD can be permeated into the pellet and polarized inside the shell
is polarized using hybrid alkali SEOP: Polarize first, then permeate into the pellet polarization loss

## Slide 6
Experimental Setup
d
Place pellets inside tube
Evacuate tube & pellets
Flood tube w/ 4-8 atms of polarized
Insert tube in custom built radio frequency coil inside a 1.5 T clinical MRI scanner
Image during permeation and decay of polarization

## Slide 7
Origin of the MR Signal
Classical picture
Imagine a spin initially aligned with the static magnetic field
If the spin is tipped away from the B axis
  The spin and its magnetic field precesses about the axis with frequency
Radiofrequency (RF) coil in the transverse plane
Precessing spin induces a changing voltage in the coil which is the MR signal
B
B
RF coil
MR Signal

## Slide 8
MRI Terminology
Longitudinal Magnetization
Transverse Magnetization
After application of RF pulse that tips the magnetization away from the static field axis:
Longitudinal signal exponentially approaches to thermal equilibrium
Transverse magnetization decays with effective time constant
Flip Angle
time
Using low flip angle RF pulses, make several measurements with very little polarization use
Less than 4% polarization loss for 100 excitations
θ
Polarized Gas

## Slide 9
ΔB
x
ΔB =
MRI Theory
Spatial Encoding using Magnetic Field Gradients
A gradient is a linear variation in the strength of the scanner’s magnetic field along a particular direction.
The gradient creates a linear mapping between position and resonant frequency:
X gradient

## Slide 10
ΔB
x
ΔB =
MRI Theory
Spatial Encoding using Magnetic Field Gradients
A gradient is a linear variation in the strength of the scanner’s magnetic field along a particular direction.
The gradient creates a linear mapping between position and resonant frequency:
Apply gradients in all three dimensions to have a 3D mapping between position and frequency.
++
Define k-space:

## Slide 11
𝜌 () ∝
MRI Theory
Image Reconstruction
There is a Fourier relationship between spin density 𝜌 () and k-space signal intensity :
Fourier transform properties:
  All k-space pixels contribute to every image space pixel intensity
  Central k-space pixels contribute the most

## Slide 12
Spin Exchange Optical Pumping
Hybrid alkali
Polarize 3He to ~ 60%
5 orders of magnitude higher polarization than thermal equilibrium at body temperature @ 1.5 T
Our polarizer produces ~ 2.5L of polarized gas per batch
Optics
Temperature Controllers and Laser Drivers
3He Gas Pluming
Electronics supplying static field and NMR measurement
Helmholtz Coils for Static Field
Oven (cell inside)
Our Polarizer
Rb + K + 3He

## Slide 13
2 ICF pellets placed inside tube
Image acquired ~10 min after tube was filled with polarized
Polarization survives permeation??
Can we get gas permeation into the pellets w/o complete polarization loss?

## Slide 14
2 ICF pellets placed inside tube
Image acquired ~10 min after tube was filled with polarized
Polarization survives permeation??
Polarization survives permeation!!
Image acquired after evacuating from tube
Yes, we can!

## Slide 15
NMR Theory and Imaging
Use slice-selective chemical shift imaging (SS-CSI) pulse sequence to measure polarization concentration in each image pixel
Imaging parameters:
  in-plane isotropic spatial resolution = 0.5 mm
  slice thickness = 2 mm
  and field-of-view = 5 mm
+
+
−
−
Move to each k-space location and acquire an NMR spectrum by measuring free induction decay (FID) after each excitation
Very fine resolution!!

## Slide 16
NMR Theory and Imaging
Use slice-selective chemical shift imaging (SS-CSI) pulse sequence to measure polarization concentration in each image pixel
Imaging parameters:
  in-plane isotropic spatial resolution = 0.5 mm
  slice thickness = 2 mm
  and field-of-view = 5 mm
+
+
−
−
Very fine resolution!!
Move to each k-space location and acquire an NMR spectrum by measuring free induction decay (FID) after each excitation

## Slide 17
NMR Theory and Imaging
+
+
−
−
Central location
SS-CSI makes maximum use of long
Boost in SNR
CSI allows us to make many measurements using low flip angles w/o using substantial polarization

## Slide 18
NMR Theory and Imaging
Take Fourier Transform
Gas outside the pellet
Gas inside the pellet
Presence of the tube and the pellets Susceptibility-induced off-resonance effects
Gas inside the pellet has a different precession frequency compared to the gas outside

## Slide 19
Calculation of Polarization Concentration
3D SS-CSI data matrix ()
  Take 3D Fourier transform of the matrix to get a matrix
Fourier transform of an FID is a complex Lorentzian
  Initial amplitude of the FID is proportional to the area under the Lorentzian in frequency spectrum
Fourier
0
Transform
If there are multiple species of gas, sum of Lorentizan curves represent the frequency spectrum data
FID
Complex Lorentzian

## Slide 20
Data Analysis
Tube
Pellet
Shoulder

## Slide 21
Data Analysis
Yellow Box Spectrum
Tube
Pellet
Shoulder
Red Box Spectrum

## Slide 22
Shoulder Peak
Pellet

## Slide 23
Shoulder Peak

## Slide 24
Tube
Pellet
Shoulder
Total Tube Signal
Pellet Signal
Tube + Shoulder
Polarization Maps

## Slide 25
Tube Signal
Pellet Signal
Track Permeation and Polarization Over Time

## Slide 26
Permeation and Polarization Evolution Model
Existing polarization in the pellet
Decay of polarization permeated into the pellet since last measurement
Permeation of polarization into the pellet since last measurement

## Slide 27
Tube Signal
Pellet Signal
Fit Results

## Slide 28
Pellet Wall Thickness and Polarization Loss
Thin wall ~ 90 % polarization retention
Thick wall ~ 80 % polarization retention

## Slide 29
Wall Thickness | 15 micron | 26 micron
Pin/Pout | 0.91 +/- 0.09 | 0.80 +/- 0.08
T1tube | 29 +/- 4 min | 47 +/- 5 min
T1pellet | 31 +/- 6 min | 59 +/- 13 min
Summary of Results

## Slide 30
Conclusion and Outlook
Permeation of 3He gas into the ICF pellets without loss of polarization is promising
We have developed a robust testbed for measuring polarization loss and decay time
  Chemical Shift Imaging: Magnetic susceptibility-induced frequency shifts are ideal for measuring polarization inside and outside the tube independently
Thicker pellet walls result in higher polarization loss
Goal is to perform in-situ test of SPF in General Atomics DIII-D tokamak reactor

## Slide 31
Thank You!