## Slide 1
New ideas for resonant cavities
David Alesini
(INFN-LNF, Frascati)
With the contribution of all QUAX collaboration
& OLD

## Slide 2
1) Design guidelines of high frequency (15-30 GHz) passive RF cavities in high magnetic fields (QUAX-type, ADMX-like cavities):
    -Modes of operation
    -coupling, tuning
    -quality factor
    -….
2) Superconducting, normal conducting and mixed cavities
3) Cavities with dielectrics
4) Few considerations on
active cavities (with power)
from Particle Accelerator world…
OUTLINE

## Slide 3
a) Resonant cavities in the range 10-30 GHz
b) Quality factor of the order of 106
c) Wide tunability range of the order of 1 GHz (to explore different axion masses)
d) Working in high magnetic field (5-10 T)
e) The magnetic field has to penetrate inside the volume of the cavity
f) With critical coupling
g) Uniformity of the magnetic field along the axis (QUAX)
h) Single mode cavity
i) Large resonating volumes (up to a 1 dm3)
Design requirements for passive cavities in high magnetic fields: the dream cavity
High frequency means small volumes, if we increase the volume of the cavity we have to work with higher order modes and the comb of resonant modes became very dense
Image: Ohjoon Kwon
AXION
search
Strong
magnet
High Q
cavity
Low noise Amplifier
Large
volume
cavity

## Slide 4
a) Resonant cavities in the range 10-30 GHz
b) Quality factor of the order of 106
c) Wide tunability range of the order of 1 GHz (to explore different axion masses)
d) Working in high magnetic field (5-10 T)
e) The magnetic field has to penetrate inside the volume of the cavity
f) With critical coupling
g) Uniformity of the magnetic field along the axis (QUAX)
h) Single mode cavity
i) Large resonating volumes (up to a 1 dm3)
High quality factors require, in principle, SC cavities that do not couple with high magnetic field and, moreover, the magnetic field is expelled from the cavity in the transition between the NC state and the SC state (with differences between zero field cooling ZFC and field cooling FC…)
AXION
search
Strong
magnet
High Q
cavity
Low noise Amplifier
Large
volume
cavity
Design requirements for passive cavities in high magnetic fields: the dream cavity
Image: Ohjoon Kwon

## Slide 5
This require the insertion of metallic plungers and/or dielectrics rods but avoiding perturbation of the field uniformity that is important for the QUAX experiment (uniformity on the region where magnetic materials are inserted)
AXION
search
Strong
magnet
High Q
cavity
Low noise Amplifier
Large
volume
cavity
Design requirements for passive cavities in high magnetic fields: the dream cavity
Image: Ohjoon Kwon
a) Resonant cavities in the range 10-30 GHz
b) Quality factor of the order of 106
c) Wide tunability range of the order of 1 GHz (to explore different axion masses)
d) Working in high magnetic field (5-10 T)
e) The magnetic field has to penetrate inside the volume of the cavity
f) With critical coupling
g) Uniformity of the magnetic field along the axis (QUAX)
h) Single mode cavity
i) Large resonating volumes (up to a 1 dm3)

## Slide 6
a) Resonant cavities in the range 10-30 GHz
b) Quality factor of the order of 106
c) Wide tunability range of the order of 1 GHz (to explore different axion masses)
d) Working in high magnetic field (5-10 T)
e) The magnetic field has to penetrate inside the volume of the cavity
f) With critical coupling
g) Uniformity of the magnetic field along the axis (QUAX)
h) Single mode cavity
i) Large resonating volumes (up to a 1 dm3)
If we work with SC cavities the quality factor depend on the temperature, frequency and applied magnetic field. In this case one has to have the possibility to tune the coupling in order to be always in critical one.
AXION
search
Strong
magnet
High Q
cavity
Low noise Amplifier
Large
volume
cavity
Design requirements for passive cavities in high magnetic fields: the dream cavity
Image: Ohjoon Kwon

## Slide 7
Basic Geometry: Cylindrical cavity working on TMxx0 mode
Simple design
RF field uniform along the longitudinal coordinate (0 no variation on z)
Resonant frequency fixed by the radius of the cell (a)
z
x
y

r
Bext
a
TM010
(ADMX-like)
TM110
(QUAX)
cylindrical symmetry of the structure ( cylindrical symmetry of DC induced currents in the SC)
L
DC Bext
RF Bcav
DC Bext
RF Ecav
H
E
H
E

## Slide 8
Cylindrical cavities working on TM110 mode:
NEAREST MODES AND MODE DEGENERATION REMOVAL
To increase the volume of the cavity (for YIG or other material insertion) we have to increase the cavity length.
This increase the number of nearest modes (hybridization can couple different modes?)
(D/L)20.26 in our case
Working mode
Mode frequencies in GHz
1 7.368 (D)
2 8.802 (TM010)
3 8.996 (D)
4 9.293
5 10.630
6 11.196 (D)
7 11.568 (D)
8 12.547
9 12.668 (D)
10 13.693 (D)
11 14.025 (TM110)
14.314 (D)
L=50.3 mm
D=26.1 mm
fres=14 GHz
There are, in principle, infinite TM110 dipole modes that can be excited with different tilted polarities.
It is necessary and useful to remove this degeneration for several reasons.
this can be done by cutting the structure
cut
Working mode
Other polarity
Separation with other modes

## Slide 9
COUPLING TO CAVITIES
Magnetic coupling
Electric coupling
Reflection coefficient for different 
Coupling coefficient

## Slide 10
Cylindrical cavities working on TM110 mode:
COUPLING
The coupling can be varied in a wide range changing the penetration of the antenna into the structure
Antenna penetration
We can couple to the mode in several ways
One of the two probe (or waveguides) is critically coupled while the other one is undercoupled and allow measuring the mode properties in transmission
Magnetic coupling
Electric coupling
NB not all nearest modes are coupled with the probe or waveguide but hybridization can introduce mode mixing if the modes are not sufficiently separated in frequency (?)

## Slide 11
Cylindrical cavities working on TM110 mode: RESONANT FREQUENCY TUNING
There are different possibilities to change the resonant frequency of the mode but the uniformity of the field has to be preserved
Sapphire Rod
Metallic tuner on the outer volume
Working mode
Working mode

## Slide 12
Cylindrical cavities: RESONANT FREQUENCY TUNING WORLDWIDE
Ohjoon Kwon, et al. KAIST, Korea
Tuning range: 2.1-2.5GHz
Ben Brubaker
Yale University 5.7 GHz
Dielectric rod: sapphire
ADMX experiment
Images taken from: http://depts.washington.edu/admx/cavity.shtml#
Metallic rod

## Slide 13
MATERIALS FOR CAVITY FABRICATION
The microwave surface resistance of a normal metals is expressed by:
At cryogenics temperatures and high frequency, the “anomalous skin depth effect” limits the quality factor.
For copper: =5.8x107 S/mRs(@1 GHz)3m, <1 m
Normal conducting materials
SUPER conducting materials
Courtesy J. Rosenzweig
Courtesy H. Safa,
Model valid for T<Tc/2 and below few GHz
Model not valid if the SC is inserted into high magnetic field!
Which is the correct model of the surface resistance for SC exposed to H field and RF field at 15-30 GHz? (R. Vaglio/S. Calatroni model to be implemented and properties of material such as Nb Ti or Nb3Sn to be measured)

## Slide 14
CHOICE OF MATERIAL FOR cavities working IN HIGH MAGNETIC FIELD
NC: Copper
Low quality factor even at cryogenic temperatures (6-8x104 because of the anomalous skin depth effect)
PROS
CONS
arbitrary H fields can be applied
H field (DC) can penetrate inside the cavity volume
Low cost, simple fabrication (brazing, welding,…)
SC: Nb Ti
High quality factor 106 (to be measured at 15 GHz)
PROS
CONS
H fields below Hc2 can be applied. Q-factor deterioration when H field are applied (between Hc1 and Hc2) (no model for Rs, measurements to be done, preliminary results on Nb).
external H field can, in principle, penetrate inside the cavity volume but measurements of the field penetration and uniformity have to be done (different regimes ZFC and FC can be explored).
POSSIBLE SOLUTIONS
Cut on the cavity wall to interrupt surface DC currents that obstacle the penetration of the H field into the cavity (measurements to be done)
Two copper plates to allow penetration of the H field
Bext
Bext

## Slide 15
Cylindrical cavities working on TM110 mode: CUT AND COPPER CUP TO ALLOW PENETRATION OF THE EXTERNAL H FIELD
Cut works for the RF field
Jsurf
No surface currents
Dissipation
To minimize the copper dissipation it is possible to increase the cavity length to increase the ratio W/Pdiss and/or introduce cones in which the field is below cutoff thus reducing the losses on Cu
SC
Cu
QCu_plates=4x107
50 mm
10% variation
13.69 GHz
14.02 GHz
14.31 GHz
13.76 GHz
14.02 GHz
14.10 GHz

## Slide 16
OPEN QUESTION: HOW TO CORRECTLY MODEL YIG MATERIAL AND THE FINAL FIELD CONFIGURATION OF HYBRID MODES?
If a uniform static magnetic field is applied along the z-axis of a cylindrical or Cartesian coordinate system, then the permeability tensor for this material takes the following form:
These type of materials are used for tunable microwave filters and the modeling of the e.m. field into the material is not trivial but would be very useful to understand the real configuration of the field into the cavity and sphere in case of hybridization.

## Slide 17
Cylindrical cavities: REALIZATION ISSUES
Ohjoon Kwon, et al., KAIST, Korea
5) Thin Coating on Cu or other substrates
2) Electron Beam Welding
3) Brazing (?)
1) Clamping
QUAX
Ian Stern, Hybrid cavities for ADMX
It can help in high magnetic field regime?
4) 3D printing

## Slide 18
EXPERIMENTAL ACTIVITIES ON SC CAVITIES IN HIGH MAGNETIC FIELD AT LNF (QUAX)
QUAX Experiment
LNF Activities: measurements of NC and SC properties (at cryogenics temperatures) under magnetic field (work in progress).
D. Di Gioacchino
Cavities fabricated and pre-tested at LNL
Nb
Cu

## Slide 19
Nb ZFC
FEW EXPERIMENTAL RESULTS
T
Tc
Hc1
Hc2
Hcrit
H
Q/104
H [T]
t [s]
Cu @ 6 K
WORKPLAN
B field measurements inside the Nb cavity (without closing cups) with and without the surface cut to avoid surface currents: meas. Of H field penetration and uniformity
Q map Nb cavity (FC and ZFC) with Cu cups and with cut
Effect of DC magnetic field on anomalous skin depth effect

## Slide 20
Cylindrical cavities working on TM010 mode:
ADMX-like cavities
The field uniformity is less stringent (frequency tuning with rods deforming the field configuration is possible).
All other considerations on Q factor, field penetration still works
cavities with dielectrics can be used (no needed space for magnetic material insertion): dielectrics with high r allow concentrating the RF field into the dielectrics thus reducing the dissipation on the magnetic walls.
DC Bext
RF Ecav
For QUAX experiment does not work properly.
Q0=106
S. Gallo/G. Ruoso
sapphire disks
High Q factors
Field concentrated in the dielectrics

## Slide 21
OTHER MORE “EXOTIC” CAVITIES:PBG
Photonic bandgap cavities PBG (Nathan Woollett, LLNL)
Considered for particle accelerators because the HOM can propagate and wakefields are reduced
Dielectrics Periodic structures can produce bandgaps in photon propagation like electrons in an atomic lattice.
Defects in the structure can be used to create waveguides, resonant cavities and other features.
With suitable choice of material Q’s similar to those of superconducting cavities can be achieved.
application of magnetic fields relatively straight forward.
Multiple cavities can be linked to create larger resonating structures (?).
Coupling into the structures and tuning the structure is non-trivial.
Small volume of the cavities.

## Slide 22
Multi-cell cavities are used in particle accelerator to accelerate (TM01-like modes) or to deflect (TM11-like modes)
Structures can be Standing Wave (SW) or Travelling Wave (TW).
N cell Multi-cell SW cavities have N Modes distributed in frequency on the dispersion curve of the “iris loaded waveguide”. The maximum number of cells is typically limited to 10-15 because of mode overlap.
Average dissipated power that can be easily managed are of the order of few kW/m.
Maximum electric field for copper cavities that can be reasonably sustained are of the order of 50-100 MV/m with ten of MW/structure in pulsed regime (klystron).
ACTIVE CAVITIES WORKING ON TM MODES…FROM PARTICLE ACCELERATOR WORLD (SW CASE)
Ez
z
P RF in
 mode
0 mode
fres
fres_
/2 mode
Ez
z
Ez
z
0 mode
 mode

## Slide 23
TW structures can be of hundred cells (meters)
The dispersion curve has limited bandwidth
The phase velocity of the field can be also equal to c (differently from uniform waveguides)
Average dissipated power and maximum electric field are similar to SW structures
Ez
z
P RF in
P RF out
P RF TW
RF
k*
k
/D

ACTIVE CAVITIES WORKING ON TM MODES…FROM PARTICLE ACCELERATOR WORLD (TW CASE)

## Slide 24
CONCLUSIONS
Main guidelines for design of high frequency cavities, working on magnetic field have been investigated: modes, frequency and coupling tuning, mode degeneration removal, dissipation,… problems and possible solutions in using SC cavities have been also addressed
Measurements of Q factors of SC cavities in high magnetic field (Nb, NbTi, cut on surface, Cu cups,…) started and are still in progress
Measurements of penetration of H field inside the material have to be done to guide the final electromagnetic design of the cavity
Dielectrics can be used for ADMX-like experiment but not for experiments that require field uniformity and space for insertion of magnetic material (like QUAX)
Main features of cavities from accelerator world for powered cavities have been illustrated

## Slide 25
ACKNOWLEDGEMENTS
All QUAX colleagues and in particular:
C. Gatti, D. Di Gioacchino, C. Ligi, M. Iannarelli, G. Lamanna (LNF)
G. Carugno, C. Braggio, C. S. Gallo (Padova)
A. Ortolan, N. Crescini, G. Ruoso (LNL)
U. Gambardella (Napoli)
THANK YOU FOR YOUR ATTENTION!