## Slide 1: Introduction to High-Level Synthesis with Vivado HLS

## Slide 2: Objectives
After completing this module, you will be able to:
  Describe the high level synthesis flow
  Understand the control and datapath extraction
  Describe scheduling and binding phases of the HLS flow
  List the priorities of directives set by Vivado HLS
  List comprehensive language support in Vivado HLS
  Identify steps involved in validation and verification flows

## Slide 3: Outline
Introduction to High-Level Synthesis
High-Level Synthesis with Vivado HLS
Language Support
Validation Flow
Summary

## Slide 4: Need for High-Level Synthesis
Algorithmic-based approaches are getting popular due to accelerated design time and time to market (TTM)
  Larger designs pose challenges in design and verification of hardware at HDL level
Industry trend is moving towards hardware acceleration to enhance performance and productivity
  CPU-intensive tasks can be offloaded to hardware accelerator in FPGA
  Hardware accelerators require a lot of time to understand and design
Vivado HLS tool converts algorithmic description written in C-based design flow into hardware description (RTL)
  Elevates the abstraction level from RTL to algorithms
High-level synthesis is essential for maintaining design productivity for large designs

## Slide 5: High-Level Synthesis: HLS
High-Level Synthesis
  Creates an RTL implementation from C, C++, System C, OpenCL API C kernel code
  Extracts control and dataflow from the source code
  Implements the design based on defaults and user applied directives
Many implementation are possible from the same source description
  Smaller designs, faster designs, optimal designs
  Enables design exploration

## Slide 6: Design Exploration with Directives
The same hardware is used for each iteration of the loop:
Small area
Long latency
Low throughput
Different iterations are executed concurrently:
Higher area
Short latency
Best throughput
…
loop: for (i=3;i>=0;i--) {
if (i==0) {
acc+=x*c[0];
shift_reg[0]=x;
} else {
shift_reg[i]=shift_reg[i-1];
acc+=shift_reg[i]*c[i];
}
}
….
Different hardware is used for each iteration of the loop:
Higher area
Short latency
Better throughput
Before we get into details, let’s look under the hood ….
One body of code:
Many hardware outcomes

## Slide 7: Introduction to High-Level Synthesis
How is hardware extracted from C code?
  Control and datapath can be extracted from C code at the top level
  The same principles used in the example can be applied to sub-functions
    At some point in the top-level control flow, control is passed to a sub-function
    Sub-function may be implemented to execute concurrently with the top-level and or other sub-functions
How is this control and dataflow turned into a hardware design?
  Vivado HLS maps this to hardware through scheduling and binding processes
How is my design created?
  How functions, loops, arrays and IO ports are mapped?

## Slide 8: HLS: Control Extraction
void fir (
data_t *y,
coef_t c[4],
data_t x
) {
static data_t shift_reg[4];
acc_t acc;
int i;
acc=0;
loop: for (i=3;i>=0;i--) {
if (i==0) {
acc+=x*c[0];
shift_reg[0]=x;
} else {
shift_reg[i]=shift_reg[i-1];
acc+=shift_reg[i]*c[i];
}
}
*y=acc;
}
Code
From any C code example ..
The loops in the C code correlated to states of behavior
Function Start
For-Loop Start
For-Loop End
Function End
0
2
Control Behavior
1
Finite State Machine (FSM) states
This behavior is extracted into a hardware state machine

## Slide 9: HLS: Control & Datapath Extraction
void fir (
data_t *y,
coef_t c[4],
data_t x
) {
static data_t shift_reg[4];
acc_t acc;
int i;
acc=0;
loop: for (i=3;i>=0;i--) {
if (i==0) {
acc+=x*c[0];
shift_reg[0]=x;
} else {
shift_reg[i]=shift_reg[i-1];
acc+=shift_reg[i]*c[i];
}
}
*y=acc;
}
Code
From any C code example ..
0
2
Control Behavior
1
Finite State Machine (FSM) states
The control is known
Operations
Operations are extracted…
-
==
+
>=
*
+
*
RDx
WRy
RDc
Control & Datapath Behavior
A unified control dataflow behavior is created.
Control Dataflow
>=
-
+
==
*
+
*
WRy
-
RDx
RDc

## Slide 10: High-Level Synthesis: Scheduling & Binding
Scheduling & Binding
  Scheduling and Binding are at the heart of HLS
Scheduling determines in which clock cycle an operation will occur
  Takes into account the control, dataflow and user directives
  The allocation of resources can be constrained
Binding determines which library cell is used for each operation
  Takes into account component delays, user directives
Design Source
(C, C++, SystemC)
Scheduling
Binding
RTL
(Verilog, VHDL, SystemC)
Technology
Library
User
Directives

## Slide 11: Scheduling
The operations in the control flow graph are mapped into clock cycles
The technology and user constraints impact the schedule
  A faster technology (or slower clock) may allow more operations to occur in the same clock cycle
The code also impacts the schedule
  Code implications and data dependencies must be obeyed
void foo (
…
t1 = a * b;
t2 = c + t1;
t3 = d * t2;
out = t3 – e;
}
+
*
a
b
c
-
*
d
e
out
*
-
*
+
Schedule 1
*
-
*
+
Schedule 2

## Slide 12: Binding
Binding is where operations are mapped to cores from the hardware library
  Operators map to cores
Binding Decision: to share
  Given this schedule:
    Binding must use 2 multipliers, since both are in the same cycle
    It can decide to use an adder and subtractor or share one addsub
Binding Decision: or not to share
  Given this schedule:
    Binding may decide to share the multipliers (each is used in a different cycle)
    Or it may decide the cost of sharing (muxing) would impact timing and it may decide not to share them
    It may make this same decision in the first example above too
*
-
*
+
*
-
*
+

## Slide 13: Outline
Introduction to High-Level Synthesis
High-Level Synthesis with Vivado HLS
Language Support
Validation Flow
Summary

## Slide 14: RTL vs High-Level Language
Notes: RTL design cycles typically consist of verification and design closure iterations for each block, as well as for the entire design. As a consequence of this methodology, the platform connectivity design never stabilizes, as any change in the differentiated logic can cause an I/O interface (e.g. DDR memory, Ethernet, or PCIe® core) to fail timing requirements. Also, RTL verification cycles no longer allow for exhaustive functional tests prior to hardware bring up.
A high-level design methodology turns the development effort on its head, allowing designers to spend more time designing the value-add logic and less time trying to make it work. This flow provides a 15X reduction in design cycle compared to an RTL design flow.
The main attributes of a high-level methodology are:
Separation of platform development and differentiated logic, allowing designers to focus on the company’s high-value functionality.
Rapid configuration, generation and closure of the platform connectivity, using the Vivado® IP Integrator with board awareness, as well as the Vivado IP systems.
C-based simulation for the differentiated logic, decreasing simulation times by orders of magnitude over traditional RTL simulation.
High-level synthesis with the Vivado HLS tool and C/C++ libraries, as well as the Vivado IP integrator for rapid implementation and system integration from C to silicon.

## Slide 15: Vivado HLS Benefits
Productivity
  Verification
    Functional
    Architectural
  Abstraction
    Datatypes
    Interface
    Classes
  Automation
Block level specification AND verification significantly reduced
Video Design Example |  |  | 
Input | C Simulation Time | RTL Simulation Time | Improvement
10 frames 1280x720 | 10s | ~2 days (ModelSim) | ~12000x
RTL (Spec)
RTL (Sim)
C (Spec/Sim)
RTL (Sim)

## Slide 16: Vivado HLS Benefits
Portability
  Processors and FPGAs
  Technology migration
  Cost reduction
  Power reduction
Design and IP reuse
RTL
RTL
RTL
RTL
RTL
RTL

## Slide 17: Vivado HLS Benefits
Permutability
  Architecture Exploration
    Timing
      Parallelization
      Pipelining
    Resources
      Sharing
  Better QoR
Rapid design exploration delivers QoR rivaling hand-coded RTL
Untimed C
Specification
Area
Performance
RTL
Insert Pipelines
RTL
Unroll Loops
RTL
Partition Arrays
Timed RTL
Architectures
RTL
Share Resources
RTL

## Slide 18: Understanding Vivado HLS Synthesis
Vivado HLS
  Determines in which cycle operations should occur (scheduling)
  Determines which hardware units to use for each operation (binding)
  Performs high-level synthesis by :
    Obeying built-in defaults
    Obeying user directives & constraints to override defaults
    Calculating delays and area using the specified technology/device
Priority of directives in Vivado HLS
  Meet Performance (clock & throughput)
    Vivado HLS will allow a local clock path to fail if this is required to meet throughput
    Often possible the timing can be met after logic synthesis
  Then minimize latency
  Then minimize area

## Slide 19: The Key Attributes of C code
void fir (
data_t *y,
coef_t c[4],
data_t x
) {
static data_t shift_reg[4];
acc_t acc;
int i;
acc=0;
loop: for (i=3;i>=0;i--) {
if (i==0) {
acc+=x*c[0];
shift_reg[0]=x;
} else {
shift_reg[i]=shift_reg[i-1];
acc+=shift_reg[i] * c[i];
}
}
*y=acc;
}
Functions: All code is made up of functions which represent the design hierarchy: the same in hardware
Loops: Functions typically contain loops. How these are handled can have a major impact on area and performance
Arrays: Arrays are used often in C code. They can influence the device IO and become performance bottlenecks
Operators: Operators in the C code may require sharing to control area or specific hardware implementations to meet performance
Types: All variables are of a defined type. The type can influence the area and performance
Let’s examine the default synthesis behavior of these …
Top Level IO : The arguments of the top-level function determine the hardware RTL interface ports

## Slide 20: Functions & RTL Hierarchy
Each function is translated into an RTL block
  Verilog module, VHDL entity
  By default, each function is implemented using a common instance
  Functions may be inlined to dissolve their hierarchy
    Small functions may be automatically inlined
void A() { ..body A..}
void B() { ..body B..}
void C() {
B();
}
void D() {
B();
}
void foo_top() {
A(…);
C(…);
D(…)
}
foo_top
A
C
B
D
B
Source Code
RTL hierarchy
Each function/block can be shared like any other component (add, sub, etc) provided it’s not in use at the same time
my_code.c

## Slide 21: Types = Operator Bit-sizes
void fir (
data_t *y,
coef_t c[4],
data_t x
) {
static data_t shift_reg[4];
acc_t acc;
int i;
acc=0;
loop: for (i=3;i>=0;i--) {
if (i==0) {
acc+=x*c[0];
shift_reg[0]=x;
} else {
shift_reg[i]=shift_reg[i-1];
acc+=shift_reg[i]*c[i];
}
}
*y=acc;
}
Code
From any C code example ...
Operations
Operations are extracted…
-
==
+
>=
*
+
*
RDx
WRy
RDc
Types
The C types define the size of the hardware used: handled automatically
long long (64-bit)
int (32-bit)
short (16-bit)
char (8-bit)
double (64-bit)
float (32-bit)
unsigned types
Standard C types
Arbitary Precision types
C: ap(u)int types (1-1024)
C++: ap_(u)int types (1-1024)
ap_fixed types
C++/SystemC: sc_(u)int types (1-1024)
sc_fixed types
Can be used to define any variable to be a specific bit-width (e.g. 17-bit, 47-bit etc).

## Slide 22: Loops
By default, loops are rolled
  Each C loop iteration  Implemented in the same state
  Each C loop iteration  Implemented with same resources
  Loops can be unrolled if their indices are statically determinable at elaboration time
    Not when the number of iterations is variable
  Unrolled loops result in more elements to schedule but greater operator mobility
    Let’s look at an example ….
void foo_top (…) {
...
Add: for (i=3;i>=0;i--) {
b = a[i] + b;
...
}
foo_top
+
Synthesis
N
a[N]
b
Loops require labels if they are to be referenced by Tcl directives
(GUI will auto-add labels)

## Slide 23: Data Dependencies: Good
Example of good mobility
  The read on data port X can occur anywhere from the start to iteration 4
    The only constraint on RDx is that it occur before the final multiplication
  Vivado HLS has a lot of freedom with this operation
    It waits until the read is required, saving a register
    There are no advantages to reading any earlier (unless you want it registered)
    Input reads can be optionally registered
  The final multiplication is very constrained…
void fir (
…
acc=0;
loop: for (i=3;i>=0;i--) {
if (i==0) {
acc+=x*c[0];
shift_reg[0]=x;
} else {
shift_reg[i]=shift_reg[i-1];
acc+=shift_reg[i]*c[i];
}
}
*y=acc;
}
+
==
-
>=
RDx
*
+
==
-
>=
*
+
==
-
>=
*
+
==
-
>=
*
WRy
Iteration 1
Iteration 2
Iteration 3
Iteration 4
-
-
-
RDc
RDc
RDc
RDc
The read X operation has good mobility
Default Schedule

## Slide 24: Data Dependencies: Bad
Example of bad mobility
  The final addition must occur before the final write and after the last multiplication and the previous addition
    It could occur in the same cycle if timing allows
  Loops are rolled by default
    Each iteration cannot start till the previous iteration completes
    The final addition (in iteration 4) must wait for earlier iterations to complete
  The structure of the code is forcing a particular schedule
    There is little mobility for most operations
  Optimizations allow loops to be unrolled giving greater freedom
void fir (
…
acc=0;
loop: for (i=3;i>=0;i--) {
if (i==0) {
acc+=x*c[0];
shift_reg[0]=x;
} else {
shift_reg[i]=shift_reg[i-1];
acc+=shift_reg[i]*c[i];
}
}
*y=acc;
}
+
==
-
>=
RDx
*
+
==
-
>=
*
+
==
-
>=
*
+
==
-
>=
*
WRy
Iteration 1
Iteration 2
Iteration 3
Iteration 4
-
-
-
RDc
RDc
RDc
RDc
Add is very constrained
Default Schedule

## Slide 25: Schedule after Loop Optimization
With the loop unrolled (completely)
  The dependency on loop iterations is gone
  Operations can now occur in parallel
    If data dependencies allow
    If operator timing allows
  Design finished faster but uses more operators
    2 multipliers & 2 Adders
Schedule Summary
  All the logic associated with the loop counters and index checking are now gone
  Two multiplications can occur at the same time
    All 4 could, but it’s limited by the number of input reads (2) on coefficient port C
  Why 2 reads on port C?
    The default behavior for arrays now limits the schedule…
+
RDx
*
+
*
*
*
WRy
RDc
RDc
+
RDc
RDc
void fir (
…
acc=0;
loop: for (i=3;i>=0;i--) {
if (i==0) {
acc+=x*c[0];
shift_reg[0]=x;
} else {
shift_reg[i]=shift_reg[i-1];
acc+=shift_reg[i]*c[i];
}
}
*y=acc;
}

## Slide 26: Arrays in HLS
An array in C code is implemented by a memory in the RTL
  By default, arrays are implemented as RAMs, optionally a FIFO
The array can be targeted to any memory resource in the library
  The ports (Address, CE active high, etc.) and sequential operation (clocks from address to data out) are defined by the library model
  All RAMs are listed in the Vivado HLS Library Guide
Arrays can be merged with other arrays and reconfigured
  To implement them in the same memory or one of different widths & sizes
Arrays can be partitioned into individual elements
  Implemented as smaller RAMs or registers
void foo_top(int x, …)
{
int A[N];
L1: for (i = 0; i < N; i++)
A[i+x] = A[i] + i;
}
N-1
N-2
…
1
0
Synthesis
foo_top
DOUT
DIN
ADDR
CE
WE
SPRAMB
A[N]
A_out
A_in

## Slide 27: Top-Level IO Ports
Top-level function arguments
  All top-level function arguments have a default hardware port type
When the array is an argument of the top-level function
  The array/RAM is “off-chip”
  The type of memory resource determines the top-level IO ports
  Arrays on the interface can be mapped & partitioned
    E.g. partitioned into separate ports for each element in the array
Default RAM resource
  Dual port RAM if performance can be improved otherwise Single Port RAM
Synthesis
foo_top
DOUT0
DIN0
ADDR0
CE0
WE0
DPRAMB
void foo_top( int A[3*N] , int x)
{
L1: for (i = 0; i < N; i++)
A[i+x] = A[i] + i;
}
+
Number of ports defined by the RAM resource
DIN1
ADDR1
CE1
WE1
DOUT1

## Slide 28: Schedule after an Array Optimization
With the existing code & defaults
  Port C is a dual port RAM
  Allows 2 reads per clock cycles
    IO behavior impacts performance
With the C port partitioned into (4) separate ports
  All reads and mults can occur in one cycle
  If the timing allows
    The additions can also occur in the same cycle
    The write can be performed in the same cycles
    Optionally the port reads and writes could be registered
+
RDx
*
+
*
*
*
WRy
RDc
RDc
+
RDc
RDc
+
RDx
*
+
*
*
*
WRy
RDc
+
RDc
RDc
RDc
Note: It could have performed 2 reads in the original rolled design but there was no advantage since the rolled loop forced a single read per cycle
loop: for (i=3;i>=0;i--) {
if (i==0) {
acc+=x*c[0];
shift_reg[0]=x;
} else {
shift_reg[i]=shift_reg[i-1];
acc+=shift_reg[i]*c[i];
}
}
*y=acc;

## Slide 29: Operators
Operator sizes are defined by the type
  The variable type defines the size of the operator
Vivado HLS will try to minimize the number of operators
  By default Vivado HLS will seek to minimize area after constraints are satisfied
User can set specific limits & targets for the resources used
  Allocation can be controlled
    An upper limit can be set on the number of operators or cores allocated for the design: This can be used to force sharing
    e.g limit the number of multipliers to 1 will force Vivado HLS to share
  Resources can be specified
    The cores used to implement each operator can be specified
    e.g. Implement each multiplier using a 2 stage pipelined core (hardware)
3
2
1
0
Use 1 mult, but take 4 cycle even if it could be done in 1 cycle using 4 mults
3
1
Same 4 mult operations could be done with 2 pipelined mults (with allocation limiting the mults to 2)
2
0

## Slide 30: Outline
Introduction to High-Level Synthesis
High-Level Synthesis with Vivado HLS
Language Support
Validation Flow
Summary

## Slide 31: Comprehensive C Support
A Complete C Validation & Verification Environment
  Vivado HLS supports complete bit-accurate validation of the C model
  Vivado HLS provides a productive C-RTL co-simulation verification solution
Vivado HLS supports C, C++, SystemC and OpenCL API C kernel
  Functions can be written in any version of C
  Wide support for coding constructs in all three variants of C
Modeling with bit-accuracy
  Supports arbitrary precision types for all input languages
  Allowing the exact bit-widths to be modeled and synthesized
Floating point support
  Support for the use of float and double in the code
Support for OpenCV functions
  Enable migration of OpenCV designs into Xilinx FPGA
  Libraries target real-time full HD video processing

## Slide 32: C, C++ and SystemC Support
The vast majority of C, C++ and SystemC is supported
  Provided it is statically defined at compile time
  If it’s not defined until run time, it won’ be synthesizable
Any of the three variants of C can be used
  If C is used, Vivado HLS expects the file extensions to be .c
  For C++ and SystemC it expects file extensions .cpp

## Slide 33: OpenCl
OpenCl is essentially C with three main extensions:
  An implicit set of 6 loops over:
    Work Groups (WGs) in a kernel, over 3 dimensions, whose iterations can be executed in any order
    Work Items (Wis) in a WG, over 3 dimensions, whose iterations can be executed in any order except when required by a barrier
  An explicit definition of memory hierarchy:
    Global data, mapped in slow large external DRAM (typically via pointers or arrays), shared among all WGs
    Local data, mapped to fast but limited-port on-chip BRAM, shared among WIs in a WG
    Private data, mapped to registers, local to each WI
  Image processing-specific data types and functions

## Slide 34: OpenCl support
WG size must be chosen at compile time via __attribute__ ((reqd_work_group_size(X_SIZE, Y_SIZE, Z_SIZE)))
The implicit loops over WGs and WIs are supported like on a GPU, with two very significant differences:
  The loops over WIs are typically pipelined, so they execute in order (very useful for debugging)
  There is no divergence problem: on a GPU threads with different condition values for if-then-else, switch and data-dependent loops are sequentialized, while control on an FPGA does not have this issue
The loop over WIs cannot be unrolled
The best way to improve task parallelism is to instantiate multiple independent WGs

## Slide 35: SDAccel versus Vivado HLS
SDAccel manages the host code compilation, driver creation, and simulation of OpenCl applications
Vivado HLS (called automatically by SDAccel) synthesizes individual kernels
SDAccel works pretty much like a compiler (it requires a lot of experience to understand how to optimize code)
The Vivado HLS GUI provides much more information about how to solve performance bottlenecks

## Slide 36: SDAccel versus Vivado HLS
SDAccel performs, via a TCL script or Makefiles, the following tasks:
  Estimate for each kernel
    cost (FPGA resource utilization, i.e. LUTs, FFs, DSPs, BRAMs)
    performance (clock cycle counts)
      possible only if all loops are bounded,
      use a very approximate model of global memory access
  Simulate the entire application:
    Functionally (“SW emulation”) for debugging via
      gdb, which currently does not work if the application contains more than 1 kernel
      printf, which is useful because WGs and WIs execute in order on the FPGA
    At a cycle-accurate level (“HW emulation”) for precise (slow) performance analysis with data-dependent loops and with the real delays of the global memory interface
  Generate the bitstream, by calling Vivado
    P&R is time consuming but running on the FPGA is much faster than RTL simulation

## Slide 37: SDAccel versus Vivado HLS
Vivado HLS can also directly synthesize OpenCl kernels
Best option when performance bottleneck is unclear
Since 2016.4, optimization directives are supported using both the OpenCl __attribute__ style and the Vivado HLS #pragma style
Note that the Vivado HLS simulator will only call one WG
  The full application simulation must still be done in SDAccel
Typical optimization flow:
  Use SDAccel SW emulation and printfs to trace global memory accesses
  Optimize global-to-local memory burst transfers
  Pipeline the WI loop (via __attribute__((xcl_pipeline_workitems)))
  If performance is still unsatisfactory, use the Vivado HLS GUI
  Go back to SDAccel for final performance analysis

## Slide 38: Outline
Introduction to High-Level Synthesis
High-Level Synthesis with Vivado HLS
Language Support
Validation Flow
Summary

## Slide 39: C Validation and RTL Verification
There are two steps to verifying the design
  Pre-synthesis: C Validation
    Validate the algorithm is correct
  Post-synthesis: RTL Verification
    Verify the RTL is correct
C validation
  A HUGE reason users want to use HLS
    Fast, free verification
  Validate the algorithm is correct before synthesis
    Follow the test bench tips given over
RTL Verification
  Vivado HLS can co-simulate the RTL with the original test bench
Validate C
Verify RTL

## Slide 40: C Function Test Bench
The test bench is the level above the function
  The main() function is above the function to be synthesized
Good Practices
  The test bench should compare the results with golden data
    Automatically confirms any changes to the C are validated and verifies the RTL is correct
  The test bench should return a 0 if the self-checking is correct
    Anything but a 0 (zero) will cause RTL verification to issue a FAIL message
    Function main() should expect an integer return (non-void)
int main () {
int ret=0;
…
ret = system("diff --brief -w output.dat output.golden.dat");
if (ret != 0) {
printf("Test failed !!!\n");
ret=1;
} else {
printf("Test passed !\n");
}
…
return ret;
}

## Slide 41: Determine or Create the Top-level Function
Determine the top-level function for synthesis
If there are Multiple functions, they must be merged
  There can only be 1 top-level function for synthesis
int main () {
  ...
  func_A(a,b,*i1);
  func_B(c,*i1,*i2);
  func_C(*i2,ret)
  return ret;
}
func_A
func_B
func_C
main.c
#include func_AB.h
func_AB(a,b,c, *i1, *i2) {
  ...
  func_A(a,b,*i1);
  func_B(c,*i1,*i2);
  …
}
#include func_AB.h
int main (a,b,c,d) {
  ...
  // func_A(a,b,i1);
  // func_B(c,i1,i2);
  func_AB (a,b,c, *i1, *i2);
  func_C(*i2,ret)
  return ret;
}
func_A
func_B
func_AB
func_C
main.c
func_AB.c
Given a case where functions func_A and func_B are to be implemented in FPGA
Re-partition the design to create a new single top-level function inside main()
Recommendation is to separate test bench and design files

## Slide 42: Outline
Introduction to High-Level Synthesis
High-Level Synthesis with Vivado HLS
Language Support
Validation Flow
Summary

## Slide 43: Summary
In HLS
  C becomes RTL
  Operations in the code map to hardware resources
  Understand how constructs such as functions, loops and arrays are synthesized
HLS design involves
  Synthesize the initial design
  Analyze to see what limits the performance
    User directives to change the default behaviors
    Remove bottlenecks
  Analyze to see what limits the area
    The types used define the size of operators
    This can have an impact on what operations can fit in a clock cycle

## Slide 44: Summary
Use directives to shape the initial design to meet performance
  Increase parallelism to improve performance
  Refine bit sizes and sharing to reduce area
Vivado HLS benefits
  Productivity
  Portability
  Permutability