## Slide 1
Overview on heat loads in the LHC
G. Iadarola
with input many colleagues from the
CERN e-cloud working group
and the Beam Induced Heat Load Task Force
Special thanks to the CERN cryogenics team for the work done to setup and improve the heat load measurements

## Slide 2
Outline
    Introduction and main observations
    Comparison against beam energy loss
    Heat load distribution along the machine
    Effect of shutdown periods
    Inferred SEYmax
    Observed dependence on the beam properties
    Data from special instrumented cells

## Slide 3
The Large Hadron Collider (LHC)
  27-km proton (and ion) collider:
    Energy: injection at 450 GeV  collisions at 7 TeV (6.5 TeV achieved)
    Beam intensity: 2800 bunches (2556 achieved), 1.1e11p/bunch, 25 ns
    Luminosity: L = 1e34 cm-2s-1 (L = 2.0e34 cm-2s-1 achieved)
Beam 1
Beam 2

## Slide 4
The Large Hadron Collider (LHC)
  8-fold symmetric structure:
  8 Long Straight Sections (LSS) to host experiments and other equipment
  8 Arcs (2.45 km each - Periodic magnet lattice, to bend and focus the beams)
  8.33 T dipoles
  223 T/m quadrupoles
  Main magnets
  (superconducting)

## Slide 5
Quad
(3.1 m)
Dipoles (3 x 14.3 m)
Quad
(3.1 m)
Dipoles (3 x 14.3 m)
Quad
(3.1 m)
Dipoles (3 x 14.3 m)
Quad
(3.1 m)
Half-cell (53.4 m)
Half-cell (53.4 m)
Half-cell (53.4 m)
    Superconducting coils (1.9 K)
    Beam screen
    (5 – 20 K)
    Beam screen cooling circuit
    (helium)
  Section of a main dipole
  The beam screen intercepts beam-induced heat loads (RF heating, synch. radiation, e-cloud)
  It is held by low conductivity supports and is actively cooled with a helium flow to operate in the range 5-20 K
  By measuring the thermodynamic properties of helium, it is possible to know the heat load on the screen
  Magnets in each “half-cell” (53.4 m long) share the same cooling circuit
    Heat load is measured per half-cell
The LHC beam screens
  To avoid too high power deposition on the superconducting coils a beam screen is inserted in installed inside the 1.9 K cold bore
  More details in B. Bradu’s talk

## Slide 6
Run 1
LS1
Run 2
LS2
Run 3
Run 1 and Run 2: the two eras of the LHC history
2010
2013
2015
2019
2021
Run 1 - data taking with:
Beam energy: 3.5 - 4 TeV
Bunch spacing: 50 ns
Max. n. of bunches: 1380
Bunch intens.: 1.7e11p
Run 2 - data taking with:
Beam energy: 6.5 TeV
Bunch spacing: 25 ns
Max. n. of bunches: 2556
Bunch intens.: 1.2e11p
Long Shutdown 1:
No beam
Consolidation and maintenance
All arcs were warmed up and vented
Today

## Slide 7
Avg. half-cell load
Run 1 configuration
4 TeV, 50 ns, 1.7e11 p/bunch
Run 2 configuration
6.5 TeV, 25 ns, 1.2e11 p/bunch
Heat loads on beam screens: Run 1 vs Run 2
  In Run 1 heat loads were very modest (~10 W/hcell)
  Compatible with estimated heat from impedance and synchrotron radiation
  Heat loads were extremely similar for the eight arcs
  In Run 2 heat loads became much larger (>100 W/hcell)
    Need for new feed-forward control on the cryo regulations (see B. Bradu’s talk)
  Much larger than estimated loads from impedance and synchrotron radiation
  Very large differences among for the eight arcs (up to a factor of 3). Not at all expected!

## Slide 8
25 ns
50 ns
The key parameter is the bunch spacing
Dedicated tests showed that the change that causes such a radical heat load increase, is the reduction of the bunch spacing
This behavior is not compatible with impedance and synchrotron radiation heating while is expected for e-cloud effects
Test with 50 ns beams in Run 2 (2017)
Avg. half-cell load

## Slide 9
Evolution during Run 2
Short bunch trains
2015
2017
2016
2018
Vented
Heat load evolution has been closely monitored during the entire Run 2
Conditioning observed on all sectors but only until mid-2016
Differences among the eight sectors remained basically unchanged during the entire process!
  Differences are unexpected (the eight arcs are by design identical) and remain unexplained!

## Slide 10
In present configuration: small contributions from impedance and synchrotron radiation  large available margins to cope with e-cloud
When moving to larger beam intensities (and to 7 TeV) the margin reduces strongly
  In the high load sectors margin is not sufficient to stand the intensity increase
Implications for the High-Luminosity upgrade (HL-LHC)
Maximum allowed by cryogenics
Margin
~7 kW
e-cloud S12
(2017)
~6 kW
Margin
~4 kW
2556b
1.1e11 p/bunch
6.5 TeV
2748b
2.2e11 p/bunch
7 TeV
e-cloud S34
(2017)
~2kW
Dedicated Task Force setup at the end of 2017 for in-depth analysis
Considered also heating mechanisms different from e-cloud:
  They were all discarded
  e-cloud heating remains the most solid hypothesis

## Slide 11
Outline
    Introduction and main observations
    Comparison against beam energy loss
    Heat load distribution along the machine
    Effect of shutdown periods
    Inferred SEYmax
    Observed dependence on the beam properties
    Data from special instrumented cells

## Slide 12
Comparison against beam power loss
For details on the RF measurements see: J. Esteban Muller, “Synchronous Phase Shift at LHC”, ECLOUD12
The power deposited in the form of the heat load ultimately comes from the beam
The power lost by the beam can be inferred from RF stable phase measurements
Found to be consistent with heat load measurements from the cryogenics

## Slide 13
Comparison against beam power loss
RF stable phase measurements also provide bunch-by-bunch power loss measurements
  e-cloud pattern is clearly visible
  Heat load is generated mainly by bunches at the tail of the trains
At 6.5 TeV

## Slide 14
Outline
    Introduction and main observations
    Comparison against beam energy loss
    Heat load distribution along the machine
    Effect of shutdown periods
    Inferred SEYmax
    Observed dependence on the beam properties
    Data from special instrumented cells

## Slide 15
Distribution along the ring
S12
S81
S23
S78
S34
S67
S45
S56
The heat loads are distributed very unevenly along the machine
It is possible to identify two families
  A group of high-load sectors (including S12, S23, S78, S81)
  A group of low-load sectors (including S34, S45, S56, S67)
High-load sectors are contiguous
The machine is practically split in a good and a bad part

## Slide 16
Distribution along the machine: cell-by-cell observations
50 ns
25 ns
Sector 12 (high load)
Increase with respect to 50 ns is observed in all cells
Large differences are present from cell to cell

## Slide 17
Sector 23 (high load)
50 ns
25 ns
Distribution along the machine: cell-by-cell observations
Increase with respect to 50 ns is observed in all cells
Large differences are present from cell to cell

## Slide 18
Sector 34 (low load)
50 ns
25 ns
Distribution along the machine: cell-by-cell observations
For low-load sectors, heat load per bunch is much more similar for 50 ns and 25 ns
A few outliers are present

## Slide 19
Sector 45 (low load)
50 ns
25 ns
Distribution along the machine: cell-by-cell observations
For low-load sectors, heat load per bunch is much more similar for 50 ns and 25 ns
A few outliers are present

## Slide 20
Sector 56 (low load)
50 ns
25 ns
Distribution along the machine: cell-by-cell observations
For low-load sectors, heat load per bunch is much more similar for 50 ns and 25 ns
A few outliers are present

## Slide 21
Sector 67 (low load)
50 ns
25 ns
Distribution along the machine: cell-by-cell observations
For low-load sectors, heat load per bunch is much more similar for 50 ns and 25 ns
A few outliers are present

## Slide 22
Sector 78 (high load)
50 ns
25 ns
Distribution along the machine: cell-by-cell observations

## Slide 23
Sector 81 (high load)
50 ns
25 ns
Distribution along the machine: cell-by-cell observations

## Slide 24
Outline
    Introduction and main observations
    Comparison against beam energy loss
    Heat load distribution along the machine
    Effect of shutdown periods
    Inferred SEYmax
    Observed dependence on the beam properties
    Data from special instrumented cells

## Slide 25
Run 1 (50 ns)
LS1
Run 2 (25 ns)
LS2
2010
2013
2015
2019
Today
Test period
with 25 ns beams
Before LS1
After LS1
A test period with 25 ns beams took place in 2012, data can be directly compared against Run 2
Heat load differences appeared only after LS1 (in which all sectors warmed up and vented)!
Differences were not present in 2012!
In the high load sectors, loads are 4 times larger than before LS1
Were the heat load differences always present?

## Slide 26
Can a thermal cycle change the situation?
In the 2016-17 winter shutdown, Sector 12 had to be warmed-up and vented to replace a faulty main magnet
Situation right after the the cool-down, before conditioning:
  Large deconditioning observed in S12 (as expected)
  Conditioning of other sectors (which stayed cold) was basically preserved
2016 (end)
2017 (before scrubbing)
(450 GeV)
Vented

## Slide 27
Nb inj.
72
144
144/288
288
Evident conditioning observed over the first 4 d
On day 4 heat load similar to end-2016 were reached
No evolution observed thereafter (important info for planning future scrubbing runs)
Impossible to get back to 2012 levels
Arc heat loads during the 2017 scrubbing run
Seven days of scrubbing were allocated at the beginning of 2017 re-condition Sector 12
S12-2016
S12-2012

## Slide 28
Cell-by-cell analysis at 450 GeV: S12
End 2016 2017 – beginning of scrubbing
Particularly interesting to look at cell-by-cell behavior
Heat load increase observed on all cells

## Slide 29
Cell-by-cell analysis at 450 GeV: S12
End 2016 2017 – end of scrubbing
Situation at the end of scrubbing run was practically identical to end-2016
   Effect of LS1 is somehow more permanent than effect of 2016-17 venting

## Slide 30
Outline
    Introduction and main observations
    Comparison against beam energy loss
    Heat load distribution along the machine
    Effect of shutdown periods
    Inferred SEYmax
    Observed dependence on the beam properties
    Data from special instrumented cells

## Slide 31
6.5 TeV
Simulations
450 GeV
6.5 TeV
Measurements
High-load
Low-load
A ballpark estimate can be made comparing the average arc loads against simulations
For details on simulation model see talk by P. Dijkstal
Inferred SEYmax range

## Slide 32
450 GeV
Simulations
450 GeV
6.5 TeV
Inferred SEYmax range
Measurements
High-load
Low-load
For details on simulation model see talk by P. Dijkstal
A ballpark estimate can be made comparing the average arc loads against simulations

## Slide 33
Outline
    Introduction and main observations
    Comparison against beam energy loss
    Heat load distribution along the machine
    Effect of shutdown periods
    Inferred SEYmax
    Observed dependence on the beam properties
    Data from special instrumented cells

## Slide 34
Dependence on the bunch spacing
(*) 8b+4e: scheme interleaving 25 ns trains of 8b with empty gaps of 125 ns
Sector 12 (high load)
(*)
(*)
Sector 34 (low load)
Different bunch patterns have been explored:
  Excess w.r.t. impedance and synchrotron radiation and differences among sectors visible only with the 25 ns variants

## Slide 35
Dependence on the bunch intensity
Measurements have been taken with 25 ns beams with different bunch intensity
  Inferred intensity threshold around 0.4e11 p/bunch
  Consistent with e-cloud simulations
e-cloud in quadrupoles
e-cloud in dipoles
e-cloud in drifts
Impedance
Synchrotron radiation
Measurements
Simulations
SEYmax = 1.35

## Slide 36
Dependence on the beam energy
Acceleration
Collisions
Large heat loads and heat load differences are already present at injection energy (450 GeV) and increase only moderately during the energy ramp
   It is unlikely that photoelectrons from synchrotron radiation play a major role

## Slide 37
Outline
    Introduction and main observations
    Comparison against beam energy loss
    Heat load distribution along the machine
    Effect of shutdown periods
    Inferred SEYmax
    Observed dependence on the beam properties
    Data from special instrumented cells

## Slide 38
Special instrumented half-cells
Q1
D2
D3
D4
A small selection of arc half-cells have been equipped with extra thermometers to measure the heat loads magnet by magnet
  3 cells in S45 were instrumented during LS1 (they always showed relatively low heat loads 2016-17)
  1 cell in S12 instrumented during the 2016-17 winter shutdown when one of the magnets had to be exchanged (it shows a large heat load)

## Slide 39
Dipole magnets: scrubbing run data
Nbun inj.
72
144
144/288
288
Low heat load observed in existing instrumented cells in S45
S12
S45
Particularly interesting to look at what happened right after the 2016-17 winner shutdown when S12 vented, 31L2-D4 dipole exchanged

## Slide 40
Nbun inj.
72
144
144/288
288
Newly installed magnet in 31L2 conditioned very rapidly to the level of those in S45
Dipole magnets: scrubbing run data
S12
S45
Particularly interesting to look at what happened right after the 2016-17 winner shutdown when S12 vented, 31L2-D4 dipole exchanged

## Slide 41
Nbun inj.
72
144
144/288
288
Other dipoles at 31L2 show a much larger heat load and very little conditioning
Most likely, also other high-load cells have this kind of behavior in some of their magnets
Dipole magnets: scrubbing run data
S12
S45
Particularly interesting to look at what happened right after the 2016-17 winner shutdown when S12 vented, 31L2-D4 dipole exchanged

## Slide 42
Tests at the interconnection
Efforts are ongoing to further localize the source:
Analysis of heat load transients
Solenoid installed at interconnection between magnets (where Plug-In Modules are installed)
Additional ionization chamber sensors (BLMs) installed to measure beam-gas interactions
Effect of solenoidal field on BLM signal visible but small
Solenoid current
BLM signal
Plug-in module

## Slide 43
Summary
Large heat loads on the arc beam screens are observed only when operating with 25 ns bunch space spacing. Worrisome when scaling to HL-LHC.
Heat loads are very different when moving from arc-to-arc, from cell-to-cell and from magnet-to-magnet, which are identical by design
Large differences appeared only after the 2013-15 shutdown in which the arcs were warmed-up and exposed to air, but no further change was observed when the operation was repeated on one of the sectors in 2016-17
Several observed features are compatible with e-cloud effects, and very difficult to explain with other considered mechanisms (e.g. impedance, synchrotron radiation, beam losses):
  Dependence on the bunch spacing
  Dependence on bunch intensity
  Bunch-by-bunch patter on beam power loss (RF)
  Dependence on energy

## Slide 44
Thanks for your attention!

## Slide 45
What about the dipole that was taken out?
End 2016 2017 – last fill before TS1
No magnet-by-magnet diagnostics in 31L2 before the EYETS but:
  Total cell heat load measured now is extremely similar to end-2016 values
  Other cells show that other magnets have practically recovered the end-2016 conditioning state
  This means that the old magnet was behaving similarly to the newly installed one
  The extracted magnet was a low-load magnet (consistent with the fact that no issue was revealed by the lab analysis by TE-VSC)

## Slide 46: Investigation on possible causes and sources of abnormal beam induced heating (1/2)
Category | Abnormal beam-induced heating cause or source | Credibility
Measurement artefact | Measurement inaccuracy | Low
 | All beam-screens receive the same power but in low-load sectors, part of the beam-induced heating is transferred to the cold-mass. | Low
BS manufacturing and tolerances | Beam-screen manufacturing process | Low
 | Beam-screen angular position | Low
LS1 intervention on beam pipes | Plug-ins module exchange and endoscopic inspection on the beam vacuum | Low
 | RF ball material, air quality during venting or RF ball processing | Low
 | Magnet change and training activities during LS1 | Low
 | Duration of vented and pump-down periods | Low
 | Beam vacuum pressure before cooldown start | Low
 | Effect of venting with beam-screen below room temperature | Low
 | Regenerative heating of beam screens | Low

## Slide 47: Investigation on possible causes and sources of abnormal beam induced heating (2/2)
Category | Abnormal beam-indued heating cause or source | Credibility
Beam operation | Collisions in detectors | Low
 | Bump in S81 to avoid the ULO | Low
 | Degradation of sectors during the Run 2 | Low
Heat load deposition process | Direct loss of proton particle energy in the beam screen wall | Low
 | Image current on beam-screen wall | Low
 | Beam instabilities | Low
 | Degradation by beam losses (SEY,…) | Low
 | Electromagnetic dissipation in new protective half-shells | Low
 | Power loss from impedance | Low
 | Heat deposited in the magnet interconnect | ?
 | Driven by hardware non-conformity | ?
 | Driven by the position in the machine | ?
 | E-cloud deposition | ?

## Slide 48
Intensity ramp-up with 25 ns beams: heat loads
Around ~1450b. (1.5x1014 p) we started approaching the limit of the available cooling capacity on the arc beams screens. Additional margin gained by:
  Increased longitudinal emittance blow-up on the ramp
  optimized filling scheme to gain additional margin
By the end of the proton run reached 2244b. (in trains of 36 b.) with 1.2x1011 ppb
High b*
72 bpi
144 bpi
72g72
72g72
(4x36) bpi
Filling pattern
1.25 ns
1.3 ns
1.35 ns
1.35 ns
Target b. length
100 ns
In the first stages, even with relatively low number of bunches, strong transients of the beam screen temperatures were observed, leading to loss of cryo-conditions :
  Intensity ramp-up performed in “mini-steps” for fine tuning of cryo-regulations
  During the first stages, injection speed often decreased to control beam screen temperatures
  Limitation from transients strongly mitigated over the year by (see talk by K. Brodzinsky):
    Modified Cryo Maintain rules to allow for larger temperature excursion
    Improvement on cryogenic feed-forward control

## Slide 49
Evolution during run 2

## Slide 50
Electron cloud suppression with 50 ns confirmed by heat load measurements on the beams-screens
Consistent with expectations from impedance and synchrotron radiation
Large differences between sectors observed with 25 ns are not visible with 50 ns
25 ns
50 ns
More data on 50 ns test in 2017 can be found here
Heat loads are strongly dependent on bunch spacing

## Slide 51
Arc heat loads - scaling with bunch intensity
  HL-LHC
  8 kW/arc (~160W/hcell)
e-cloud in quadrupoles
e-cloud in dipoles
e-cloud in drifts
Impedance
Synchrotron radiation
  Present situation in the low-load sectors
  HL-LHC
  8 kW/arc (~160W/hcell)
Present state of the low-load sectors
(Sec. 34, 45, 56, 67 - SEY = 1.25)
Present state of the high-load sectors
(Sec. 12, 23, 78, 81, SEY = 1.35)
Heat load [kW/arc]
Bunch intensity [1011 p/bunch]
Heat load [kW/arc]
Bunch intensity [1011 p/bunch]
G. Skripka
  Assuming surface properties are uniform along the arc half-cell (probably optimistic):
  Present conditioning achieved in the low-load sectors is compatible with HL-LHC
  Expected heat load for the high-load sectors is ~10 kW/arc  not acceptable
    Ongoing work to identify and suppress the source of differences among arcs is very important for HL-LHC
    A solid backup plan must be available…