## Slide 1: ECAL Upgrade per HL-LHC Contributo Italiano
Stefano Argirò per ECAL Italia
CMS Italia, Piacenza, 29 Novembre 2017

## Slide 2: ECAL upgrade
What will be upgraded
  EB electronics, from APD (excluded, as MB) to off-detector
    Requires extraction and refurbishment of all Supermodules
  EB cooling to 9±0.02 C to limit noise (1/2 APD dark current)
  Cabling and services (HV,LV,DCS)

## Slide 3: ECAL barrel electronics upgrade
Goals
  Move L1 trigger off-detector for max flexibility
  Cope with increased latency
  Improve timing (30 ps) for vertexing and spike rejection (99.9% L1)
How to meet the goals
  Faster analog response (shaping ~20 ns) -> TIA Asic
  40-> 160 Mhz sampling with 12 bit resolution, 15 bit dynamic range -> LiTE-DTU Asic
  Ship all samples off-detector -> new off-detector electronics

## Slide 4: Since Spoleto …
TDR released
Specifications frozen
Design (almost completely…) frozen
and validated by test beam campaigns (and presented at confs)
  TIA prototype
  FE demonstrator
Schedule is credible
Costs are (almost everywhere …) well defined
ADC IP contract close to signature

## Slide 5: Legacy vs. Upgrade
25x better trigger granularity
Better shape-based spike rejection at trigger
Current
Upgrade

## Slide 6: EB electronics upgrade, overview
Upgrade: L1 trigger formed off-detector.
All samples shipped off-detector @160 Mhz
Torino
Next slide

## Slide 7: Analog set, ADC, LiTE-DTU (Torino)
Compression
LUT or Huffman encoding
Data Transmission Unit
Logic to trasmit N samples in case of gain switch
Compression is necessary to cope 12 bit/160 Mhz with the available optical link (lpGBT) bandwidth.
The basic idea is that large signal are rare, and 6/7 bits are sufficient to code small signals
La parte DTU è pronta
Lisbon-Torino-Ecal

## Slide 8: ADC Specs
Sampling rate : 160 MS/s
Resolution : 12 bits @ 50 MHz
SNDR > 63.2 dB
DNL < 0.9 LSBs, INL<1.5 LSB
Temperature range : ­20 °C ÷ 85 °C
Power consumption <30 mW
TID tolerant up to 20 kGy
SEU tolerant control logic
Designed by S3. Contract should be signed any day

## Slide 9: ASIC workflow and schedule
Wafer Testing
Foundry
ADC IP
DTU
Integration
S3 Inc.
INFN TO
INFN TO
IMEC
EXT.
Packaging
INFN TO
?
Final Test
(2x proto)
ASIC
ADC ­IP core delivery ; May 2018 Prototype 1 submission : Aug 2018 Prototype 1 testing : Q4 2018 Prototype 2 submission : Jun 2019 Prototype 2 testing: Sept 2019 Production ready : Aug 2020 – Engineering Run Chip delivered & tested : Oct 2021
DTU Design and Simulation well advanced

## Slide 10: Demonstrator VFE/FE– Test Beam
Protype TIA Asic 130nm has been submitted in fall 2016
VFE with CATIA ASIC; used in test beam October 2017
Commercial ADC: 14 bits, 160 MHz
Irradiation tests
HF

## Slide 11: FE Design / Demonstrator – Test Beam
Versatile link
GBTx
GBT-SCA
lpGBT
lpGBT
lpGBT
lpGBT
lpGBT
lpGBT
10Gbps
10Gbps
10Gbps
2.5Gbps
lpGBT
lpGBT
10Gbps
lpGBT based FE card
  One control link
    2.56 Gbps, effective 1.6 Gbps
  Four lpGBT data links
    10.24 Gbps up effective 8.96 Gbps
    Requires data compression (baseline), or use two more data links
GBT- based demonstrator
Tested on-beam while waiting for
lpGBT availability

## Slide 12: Mechs, High Voltage, Services
To speed-up installation, a second enforneur will be required.
Enforneur 1 has been refurbished
  Drawings updated
  New alignment system
  Counterweight added
Enforneur 2
  To be built under italian (RM) responsibility
High Voltage (IT, Roma)
Cables USC-CMS (uncable YB0)
[HV boards and crate ] (obsolence)

## Slide 13: Italian Involvement in ECAL upgrade, summary
Roma: nuovo Enforneur, HV system
Torino: LiTE-DTU design, integration with ADC, prototype and testbed. Production and full-scale test.
Mi, To, Ts, Rm : performance studies, simulation, testbeam validation. Installation and integration ( 1 out of 6 integration lines).