## Slide 1
Experimental activity #2: RF pulse compressors
Real objects widely used in electron linac to increase the available peak power;
Also very instructive, suitable for an RF lab experience;
Based on RF response of resonant cavities and other connection devices (hybrid couplers or circulators);
The Problem
High accelerating gradients require very high RF power (). RF peak power available from klystrons is typically limited to . But the duration of the klystron RF pulses () may largely exceed the typical filling time of an accelerating structure ().

## Slide 2
The Idea: SLED (Stanford Linac Energy Doubler)
A factor of 4 in power corresponds to a factor of 2 in accelerating gradient, i.e. In beam energy. Smart idea! But how a large RF power flowing in a waveguide can be manipulated in order to be compressed?
Pulse Compression
This idea has been firstly implemented at SLAC in the 70’s [1]. The compression is obtained by capturing the RF power reflected by high-Q resonant cavities.
Let’s compress the energy of the RF pulse in about 1 filling time to increase the peak power to the maximum!
[1] Farkas et al. - SLED A method of doubling SLAC energy

## Slide 3
The coupling strength of a port can be measured as the amount of power extracted from the cavity through the port itself for a given level of the mode fields inside.
This leads to the definitions of the external-Q () (in analogy with the definition of the resonance quality factor ) and coupling coefficient of a coupler according to :
The extra-power flow through the cavity couplers, in addition to the power loss in the walls, may significantly change the characteristics of the resonance. This effect is known as “cavity loading”. The loaded cavity Q-factor is lowered by the power coupled out through the cavity ports and results to be:
where is the usual quality factor of the resonant mode, related only to the dissipation on the cavity walls.
Coupling coefficients of a resonant cavity
«Real» resonant cavities are NOT perfectly closed volumes, i.e. at least 1 opening (port) must be present to allow the RF power to flow in (and out).

## Slide 4
Wave reflection in guide terminated on a resonant load
A resonant cavity is a non-matched load for a waveguide or a transmission line, and can be modeled as an RLC parallel circuit.
An RF wave travelling from the generator toward the cavity is always partially reflected at the cavity input. The reflected wave can be calculated according to:

## Slide 5
Cavity reflected waves and input coupling coefficient
Lorentzian network transfer function
Depending on the value of the input coupling coefficient , 3 practical situations can occur:
undercoupling
critical coupling
overcoupling
Let’s calculate and plot the wave reflected by a cavity excited by a pulsed source.
In the previous equation, if we substitute the expression for , the reflected wave becomes function of the coupling coefficient:

## Slide 6
Lorentzian network response to RF Pulses
with
The response of a Lorentzian network to an RF step pulse is:

## Slide 7
Lorentzian network response to RF Pulses
The response of a Lorentzian network to an RF rectangular pulse is:
with

## Slide 8
RF step pulse reflected by a resonant cavity
;
Undercoupled,
Critically coupled,
Overcoupled,
In time domain:
The reflected power of a Lorentzian network to an RF step pulse has the following transfer function:

## Slide 9
RF rectangular pulse reflected by an over-coupled resonant cavity
The RFL peak field is maximum at the end of the FWD pulse, and its value exceeds the peak of the FWD itself.
This effect can be enhanced by forcing a 180° phase jump in the driving pulse at a certain time before the end of the pulse. By doing that we induce an equivalent step in the driving signal of double amplitude which adds in phase with the signal originated by the first rising front of the driving RF pulse.
The wave reflected by an over-coupled cavity excited by a rectangular RF pulse is:

## Slide 10
But...

## Slide 11
Circulators are non-reciprocal (typically) 3-ports devices whose scattering matrix is ideally given by:
All this power has to be delivered to the accelerator and not to the power units (e.g. klystrons)
90° hybrids are non-reciprocal (typically) 4-ports devices whose scattering matrix is ideally given by:

## Slide 12: Experimental activity #2
Frequency domain: tuning demonstration
Time domain: set-up of the RF pulse
  CW signal at 2856 MHz
  Pulsed signal at 2856 MHz (5 us length, 100 Hz rep. rate)
Time domain: visualization of SLED output pulse w/o 180° phase jump
  Resonant frequency fine tuning
Frequency domain: realization of the 180° phase jump
  Design of a 180° phase shifting circuit
  Functionality cross-check of the 180° phase shifter provided
  Actual phase shift measurement
  Timing of the trigger signals
Time domain: visualization of SLED output pulse with 180° phase jump
  Eventual optimization of the SLED pulse
  Qualitative measurement of energy/power gain
  Scan Tjump vs energy gain
Input
port
90°
hybrid
High Q
cavities
Output
port