## Slide 1
LASA
Attività gruppo SRF
Paolo Michelato

## Slide 2: Riassunto
Attività relative al contributo LASA per European Spallation Source
E-XFEL: attività in corso, primo fascio FEL nella zona sperimentale
Installazione nella seconda metà anno della meccanica del telescopio STRIP del gruppo Astrofisica di UNIMI, di Marco Bersanelli, per le prove di funzionamento della parte meccanica
Situazione generale lavori di ristrutturazione: tutto fermo.
Possibili solo limitati investimenti per sistemare i punti critici? Antincendio? Infiltrazioni acqua?

## Slide 3: Ongoing activities at LASA for ESS
From the design to the Vertical Test of the cavity prototype integrated in the tank

## Slide 4
LUND (Sweeden)
ESS &
MAX IV

## Slide 5: ESS linac
Acceleration to 2 GeV
Average beam power of 5 MW
Peak beam power of 125 MW
Peak proton beam current of 62.5 mA
Pulse length of 2.86 ms at a rate of 14 Hz (4% duty factor)
96% of acceleration will be provided by superconducting cavities supplied by 150 high power RF sources (one per cavity):
80% of the RF power sources delivering over 1.1 MW of peak RF power
The RF system is the cost driver for the ESS accelerator.
8

## Slide 6: ESS design
High Power Linear Accelerator:
Energy: 2 GeV
Rep. Rate: 14 Hz
Current: 62.5 mA
16 Instruments in Construction budget
Committed to deliver 22 instruments by 2028
Peak flux ~30-100 brighter than the ILL
Target Station:
He-gas cooled rotating W-target (5MW average power)
42 beam ports
Ion Source
Environmental goal (“Sustainability”)
Energy responsible
Renewable energy
Recyclable heat

## Slide 7: Construction plan
4
2009
ESS in Lund
2003
European Design of ESS Completed
2012
ESS Design Update Phase Complete
2019-20
Machine Ready for 1st Beam on Target
2014
Construction Starts
2023
2025
ESS Construction Phase Complete
ESS Starts User Program

## Slide 8
ESS: European Spallation Source
Lund, Sweeden.

## Slide 9
Target
Monolith & Active Cells
36

## Slide 10: Target, monolith, moderators etc.
24
Main components:
Monolith:
  Vessel (6 m diameter x 8 m height)
  Steel shielding (6000 tons)
  Instrumentation plugs
  Proton beam window
  Neutron shutters
  Neutron beam extraction system
Rotating Tungsten target
2.5 m diameter x 10 cm height
7500 Tungsten bricks (3.5 tons)
• 0.39 rev./s
Target He gas-cooling
3 MW capacity
3 kg/s flow rate
Dt = 200 degrees C
High brightness moderators
2 liquid H2 moderators
Water premoderators and moderators
He cryoplant (35 kW – 16 K)
proton beam window
proton beam instrumentation plug
moderator- reflector plug
target wheel
neutron beam extraction port
target diagnostics plug
monolith vessel

## Slide 11: Beam Line Gallery 8,000 m2 base slab – last casting 14/03/2017
37

## Slide 12: ESS linac
Acceleration to 2 GeV
Average beam power of 5 MW
Peak beam power of 125 MW
Peak proton beam current of 62.5 mA
Pulse length of 2.86 ms at a rate of 14 Hz (4% duty factor)
96% of acceleration will be provided by superconducting cavities supplied by 150 high power RF sources (one per cavity):
80% of the RF power sources delivering over 1.1 MW of peak RF power
The RF system is the cost driver for the ESS accelerator.
8
INFN LASA
LNL
LNS

## Slide 13: INFN LASA in-kind contribution: medium beta SC cavities
MB cavity technical requirements | 
Frequency (MHz) | 704.42
Number of cells | 6
Geometric beta | 0.67
Nominal Acc. Gradient (MV/m) | 16.7
Epeak (MV/m) | < 45
RF peak power (kW) | 1100
Q external | 5.9-8 105
Q0 at nominal gradient | > 5 109
INFN In-Kind contribution:
  Niobium procurement for the fabrication of 36 medium beta cavities.
  Cavity fabrication of 36 medium beta cavities in the industry, including treatments, tuning, Helium tank integration. Full treatment at the vendor.
  Ancillaries, certification activities, documentation.
  Cold test in a qualified infrastructure (DESY). Test can be done also LASA, but not with the occurrence needed for the series.
  Transportation in special boxes and delivery at CEA cryomodule assembling facility.
R&D on prototypes (already done):
  Built 2 prototypes of medium beta cavities.
  INFN design, using Large and Fine Grain Nb, plug compatible with ESS cryomodule.
  Full treatment at the industry.
  Final handling and test done in the qualified infrastructure at LASA.

## Slide 14: Cavity Prototype Mechanical Parameters INFN Design
Mechanical parameter | INFN Design
Cavity wall thickness (mm) | 4.5
Stiffening ring radius (mm) | 70
Internal volume (l) | 69
Cavity internal surface (m2) | 1.8
Stiffness (kN/mm) | 1.7
Tuning sensitivity KT (kHz/mm) | 210
Vacuum sensitivity KV for Kext ~ 21 kN/mm (Hz/mbar) | 31
LFD coefficient KL for Kext ~ 21 kN/mm (Hz/(MV/m)2) | -1.7
Pressure test scenario:
Cavity fully constrained
Pressure in the tank
The maximum pressure difference allowable is
2.60 bar for 50 MPa VM (worst scenario)
3.64 bar for 70 MPa VM (best scenario)
Scenario:
Cavity with one free end
Increasing displacement on free end
The maximum displacement allowable is
2.59 mm for 50 MPa VM (worst scenario)
3.60 mm for 70 MPa VM (best scenario)

## Slide 15: From design to prototype test 1/2
F=1742.4 MHz
Max R/Q=23Ohm
Qext=9.6×10^5
LFD from cavity simulator
Cell shape design
HOM analyses
Dynamical analyses: natural modes
Deep Drawn Die
Large Grain Nb
Dumb-Bells
RF measures

## Slide 16: From design to prototype test 2/2
Final Tuning
Surface Treatments
VT installation
Annealing

## Slide 17: ESS cavity qualification at 2.0 K
100 W CW cryo power, i.e. 16,7 MV/m @ Q0 5e9

## Slide 18: LASA Installation of the naked cavity for cold test

## Slide 19: Cavity integration
After successful cold test the cavity was integrated in the He tank
Frequency change: 35 kHz. OK!
Pressure test: done
New Final BCP: 15 min, 20 mm
Successful cold test after integration done. No performance change.
Installation in the medium beta cryomodule demonstrator at CEA near completed

## Slide 20: Cavity with tank cold test preparation at LASA

## Slide 21: ESS cavity box and transportation
Two prototype boxes built
Four soft rubber dampers in place of foam supports
5 shipments made so far and OK
  4 EZ to LASA
  1 LASA to CEA
Data analyses on prototypes:
  g-shock reducing factor > 8
  Residual oscillations < 7 Hz
  Damping t0 about 0.25 s
Series box design under finalization

## Slide 22: Status and perspectives
First LASA prototype cavity outperformed ESS specifications:
  Design Review by ESS successful. Committee and reviewers were “impressed by both the level of detail of the work and the application of LASA’s previous experience in SRF cavity design and production”.
  An additional test on the integrated cavity confirmed no degradation of performances
  Currently at CEA being part of the first medium-beta demonstrator cryomodule that is under assembly

## Slide 23: Series cavities CFTs and more
Nb sheets (RRR 300 and RRR 40) for the cavities, CFT in two lots.
CFT closed. Contract under finalization.
CFT budget:  3.0 M€
Construction and treatment of the full set of medium beta SC cavities:
CFT closed. Bids under evaluation.
Procurement budget: 4.6 M€
Many ancillaries required:
Cryogenic feedthroughs with HiQ antenna and pick-up: 100 k€, started
Vacuum valves: 30 k€, transports, boxes, etc
Agreement with DESY for the vertical tests of series cavity: under finalization
QA/QC strategy fully developed at LASA:
Document management based on INFN ALFRESCO
Inspection template under finalization
Based on E-XFEL experience

## Slide 24: The European XFEL Facility
Experimental Hall
Beam Dumps
Undulators
Collimation
Bunch
Compressors
Linear Accelerator
Injector
Photon Beam Lines
Electron Beam
Distribution

## Slide 25: The European XFEL
Some specifications
Photon energy: 0.3-24 keV
Pulse duration ~ 10-100 fs
Pulse energy: few mJ
Superconducting linac: 17.5 GeV
10 Hz (27 000 b/s)
5 beamlines / 10 instruments
  Start version with 3 beamlines and 6 instruments
Several extensions possible:
  More undulators
  More instruments
  …….
SASE2
(= SASE1)
SASE1, lu= 40 mm
0.2 – 0.05 nm
17.5 GeV
SASE3, lu= 68 mm
1.7 – 0.4 nm

## Slide 26: Italian Contribution (based on INFN LASA know-how)
IN-KIND contribution for 33 M Euro (2005)
400 Bulk Nb 9 cell 1.3 GHz cavities
45 cryomodules
Tuners for SC linac
3.9 GHz Cryomodule with 8 SC Nb cavities (+ spares)
4 WPs co-leaded INFN - DESY
All components produced by Italian Industry

## Slide 27: 800 SC 1.3 GHz Nb cavities (VT): two recipes (BCP & EP), two companies (RI & EZ)
Best Performance Cavities
Both recipes are OK
Final Performances
Emax = 33.0 ±4.8 [MV/m]
Eusable = 29.8 ±5.1 [MV/m]
Q0 (23.6MV/m) = 1.37 ±0.25 [1010 ]
(Egoal = 23.6 [MV/m], Q0 ≥1·1010)
Retreated Cavities (~30%)
Reasons:
Bad performances (15%)
Bad inc. insp. & other (15%)
Kind of retreatment:
HPR (86%)
BCP (9%)
Special recovery (grinding) (4%)

## Slide 28: WP3: accelerating cryomodules

## Slide 29: Injector tunnel
1.3 GHz gun
1.3 GHz cryo module A1 (XM29)
3.9 GHz cryo module AH1
Diagnostic section
Laser heater
Fast kickers and screen stations
Transverse deflecting structure
Spectrometer dipole
Beam dump

## Slide 30: XFEL 3rd Harmonic System (3.9 GHz)
Due to alternating couplers requirement, for coupler kick compensation, and to the position of the 2-phase pipe there are two dressed cavity configurations (left and right)
Blade tuner updated to the “slim” type, concept derived from ILC tuner work by INFN. Lighter, cheaper, motor to the side.
Design of the Module is “Plug compatible” with XFEL modules
String Assembly (DESY)
Blade Tuner

## Slide 31: XFEL 3rd Harmonic System (3.9 GHz): fabrication, treatments and tests at LASA
3 rd Harmonic Module in Operation
Beam image on screen in the spectrometer beamline
← AH1 off
AH1 on →
Weld inspection
Cavity Tests
RF VT (LASA)
VT preparation (LASA)
All cavities above specifications!
XFEL Injector with Beam
X (i.e. E)
y
Time resolved

## Slide 32: E-XFEL: Actual Status
23 June 2017 First XFEL beam in experimental hall (SPB/SFX Experiment)
Ee- = 14 GeV, lph = 1.5 Å

## Slide 33
Photocathodes for High Brightness RF Guns
Transport Box
Preparation Chamber at LASA
The INFN Mo plugs
Cs2Te films
INFN-LASA activities:
Cs2Te photoemissive film deposited on Mo plugs (since ‘90s, > 140 produced photocathodes)
10 % average QE @ λ = 254 nm
> 180 days operative lifetime (24h/24h 7d/7d)
High robustness and QE spatial uniformity
UHV condition (~10-10 mbar range)
The Cs2Te deposition
Characterization of Cs2Te film
Hg lamp
Filter wheel
Shutter
Remote controller
Photocurrent signal
Prep. chamber viewport
Photodiode
Reflected power
Incident power
QE Production Stability

## Slide 34
Photocathodes for High Brightness RF Guns
How it works
RF Gun transfer system in FLASH tunnel
INFN-LASA photocathodes for accelerator facilities:
Collaboration with:
DESY (FLASH and E-XFEL at Hamburg, PITZ at Zeuthen)
FNAL (FAST)
LBNL (APEX)
SLAC (LCLS II)
Collaborazioni Internazionali
Trasferimento
Produzione
RF Gun transfer system for LCLSII
INFN Transport Box
Production & Transfer
Production
Transfer

## Slide 35: Montaggio e test telescopio STRIP @ LASA
Il gruppo di Cosmologia Sperimentale di UniMI di Marco Bersanelli monterà e testerà la meccanica e le movimentazioni del telescopio STRIP nel capannone del LASA.
Verrà agganciato a due grosse travi in acciaio già disponibili nel capannone, e che faranno da robusto e stabile basamento e supporto.
Il telescopio STRIP, come Daniele Mennella ha illustrato nel suo seminario tenutosi al LASA, fa parte di attività relative alla caratterizzazione della polarizzazione della radiazione di fondo a microonde, (Cosmic Microwave Background, CMB) nell’ambito del LSPE, The Large Scale Polarization Explorer.
Il telescopio verrà poi installato a Tenerife

## Slide 36: Observation site
Tenerife, Izana site
2390 m s.l.m.

## Slide 37: STRIP Telescope
Baseline:
Clover telescope offered by M. Jones, Oxford 1.5m aperture (20 arcmin resolution)
Mount:
H/W parts mostly built Develop I/F S/W, Rotary joint

## Slide 38: LSPE in a nutshell
●
●
●
43, (90) GHz
QUIET coherent polarimeters
Dragone side-fed telescope (~ 0.5° - 1° angular res.)
STRIP
Telescope
Mount
Max. height of the telescope + mount: ~ 6 m

## Slide 39: LASA experimental area
Clean room
class 100 & HPR
UPW production
Vertical test area
High field solenoids
Nuclear dosimetry area
He pumping system for subatm ops He Recovery balloons
SC wire testing area
High current PS
Area montaggio telescopio

## Slide 40
Area montaggio e test del telescopio STRIP

## Slide 41: Telescope and mount testing
T/M integr.
In UK
In Italy
T/M testing
Alignment plan
In UK
Telescope test
T/M test in Italy
Shipment UK→I Shipment I→ES
Telescope and mount arrive at LASA
Telescope and mount are tested at LASA

## Slide 42: Personale
Giorgio Fornasier, Tecnologo, art. 36
Saeid Pirani, dottorando Uni LUND
ESS XFEL