## Slide 1
SIDDHARTA - 2
Catalina Curceanu
for the SIDDHARTA-2 Collaboration
CL, 30 Giugno 2017

## Slide 2
SIDDHARTA-2 Collaboration
SIlicon Drift Detector for Hadronic Atom Research by Timing Applications
LNF- INFN, Frascati, Italy
SMI- ÖAW, Vienna, Austria
Politecnico, Milano, Italy
IFIN – HH, Bucharest, Romania
TUM, Munich, Germany, Germany
RIKEN, Japan
Univ. Tokyo, Japan
Victoria Univ., Canada
Univ. Zagreb, Croatia
Helmhotlz Inst. Mainz, Germany
CNRS, Paris, France
Indian Inst. of Science, Bangalore, India
StrangeMatter

## Slide 4
The strong int. width > Radiative trans. width
Kaonic atom formation
K-
e-
Auger Electron
Nucleus
2) Cascade
1) Initial capture
3) Strong interaction
stopped in a target medium
4) Absorption
K-
X-ray
Shift and Width
of last orbit
e.g.
1s for K-p, K-d
2p for K-He
highly-excited state
deexcite
n ~ sqrt(M*/me) n’ ~ 25 (for K-p)
(M* : K-p reduced mass)
K-

## Slide 9
SIDDHARTA-2 apparatus – status with time lines
- Mounting frame
- Beam pipe
- Luminosity monitor
- Kaon trigger
- Cooling system
- Vacuum chamber
- Cryogenic target
- SDD X-ray detector
- Veto system
Overall time schedule

## Slide 10
SIDDHARTA-2 setup
    Mounting frame
    Beam pipe
    Luminosity monitor
    Kaon trigger
        Platform

## Slide 11
mounting frame
Cesidio Capoccia
Giovanni Fuga
shielding
beam pipe
luminosity monitor
kaon trigger
SIDDHARTA-2 apparatus

## Slide 14
SIDDHARTA – beam pipe

## Slide 15
SIDDHARTA-2 beam pipe
design / quotation
  final diameter to be decided – depending
  on new quadrupoles of DAFNE

## Slide 16: SIDDHARTA-2 - Luminosity monitor (measuring kaons)
Size: 8 x 8 cm2 both side of the beam pipe,
made of 2 pieces 8 x 4 cm2, thickness = 2 mm
distance y = ± 4 cm off beam
Coincidence rate:
25.7 % per charged kaon pair
single rate at the boost side: 42.7 %
single rate at the anti-boost side: 32.3 %
With a luminosity L = 1032
 37 Hz (coincidence) / 62 Hz (on boost-side)
in 5 seconds:
185 counts (7%) / 310 counts (5.7%)
prototype under construction,

## Slide 17
SIDDHARTA-2 setup
    Cooling systems
    Vacuum chamber + feedthroughs
    Cryogenic target

## Slide 18
Target + SDD cooling:
1 Leybold MD10 – 16 W @ 20 K
target cell and SDDs will be cooled
via ultra pure aluminum bars
TTC = 30 K
TSDD = 50 K
Line driver boards:
2 CryoTiger – 30 W @ 120 K
copper-band cooling lines
TLD = 120 K
SIDDHARTA-2 cooling
ultra pure
Al bars
copper-band

## Slide 19
SIDDHARTA-2 vacuum chamber

## Slide 20
SIDDHARTA-2 cryogenic target
Working temperature: 30 K
Working pressure : 0.3 MPa
Pressurised for 16 days
with P = 0.3 MPa (overP)
Cooling/pressure test
2.5 weeks 30 K / 0.19 MPa
3.5 days 30 K / 0.31 MPa
Target cell wall is made of a
  2-Kapton layer structure
(25 µm + 25 µm + Araldit < 100 µm)
140 mm

## Slide 21
SIDDHARTA-2 setup
  SDD X-ray detector

## Slide 22
4 x 2 matrix SDD chip - testing
SDD testing facility - Milano

## Slide 23
New SDD technology: CUBE preamplifier BTF test - July 2017
55Fe spectrum
123.0 eV FWHM
SDD characteristics:
area/cell = 64 mm2
total area = 512 mm2
T = - 100°C
drift time < 500 ns

## Slide 24
4x2 SDD arrays around the cryogenic target
In total 48 SDDs
will be used

## Slide 25
SIDDHARTA-2 setup
    the veto system

## Slide 26
SIDDHARTA-2 setup: Veto-1 + Veto-2
Veto-1
Veto-2

## Slide 27
To achieve a good timing resolution, (independent of the “hit” position) < 600 ps (FWHM),the scintillator has to be read out on both side.
Because the available space is limited due to shielding material, the photomultiplier tubes have to be on the same side (a special light-guide mirror design was used).
The veto-1 system

## Slide 28
The veto-2 system
Veto-2 arrangement
SiPM – 4x4 NUV-Trento
BC-408
scintillator tile

## Slide 30
SIDDHARTA-2 setup
    Assembling plan
    Installation at DANE

## Slide 31
 | Q4/2016 |  |  | Q1/2017 |  |  | Q2/2017 |  |  | Q3/2017 |  |  | Q4/2017 |  |  | Q1/2018 |  | 
SIDDHARTA-2 assembling plan |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Cryogenic target cells |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
48 SDDs bonded and mounted SDD final tests (with SFERA + DAQ) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Veto-1 constructed/tested Veto-2 constructed/tested Kaon trigger Luminosity monitor constructed/tested |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SIDDHARTA beam pipe |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
final mounting, debugging and testing |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Gantt chart SIDDHARTA-2:
installation
at DANE

## Slide 32
Installation on DAFNE starting summer 2018
Technical run in 2018
Kaonic deuterium run in 2019:
200 pb-1, to debug and optimize the apparatus
800 pb-1, to perform the first measurement of the strong interaction induced energy shift and width of the konic deuterium ground state (similar precision as K-p) !
SIDDHARTA-2 plan for the K-d measurement
QED
K
K
Khigh
achievable precision:
shift: 30 eV
width: 75 eV
Plans to secure personal for beam time and analysis is under discussion!
Notes: This window of opportunity should be realized.
32

## Slide 33
SIDDHARTA-2 future programme and perspectives
Other light kaonic atoms (K O, K C,…)
Heavier kaonic atoms (K Si, K Pb…)
Kaonic helium transitions to the 1s level
Kaon mass - precision measurement at a level < 7 keV
  Radiative kaon capture – (1405) study
  Investigate the possibility of the measurement of other types of hadronic exotic atoms (sigmonic hydrogen ?)

## Slide 36
Kaonic Deuterium Measurement of SIDDHARTA2: MCurie IF:
I am pleased to inform you that your proposal has been awarded the Marie Sklodowska-Curie Actions Seal of Excellence. This quality label is awarded to all proposals submitted to the MSCA Individual Fellowships Call that scored 85% or more but could not be funded from the call budget.
We will present it to the 2017 call again
ASTRA: Advances and open problems in low-energy nuclear and hadronic STRAngeness physics
ECT*, 23 Oct 2017 to 27 Oct 2017

## Slide 38
1. M. Miliucci 0.8
2. M. Cargnelli 0.5
3. A. Clozza 0.15+0.15
4. C. Curceanu 0.5 + 0.2
5. R. Del Grande 1
6. M. Donari 1
7. C. Guaraldo -
8. P. Levi Sandri 0.2
9. M. Merafina 0.2
10. D. Pietreanu 0.6
11. D. Sirghi 0.8
12. A. Spallone 1
13. O. Vazquez 0.5
14. J. Zmeskal 0.5
15. S. Dabagov 0.2
16. E. Pace 0.8
17. M. Iliescu 1
18. M. Bazzi 0.6
19. M. Skurzok 1
20. D. Hampai 0.2
+ 1 borsista
Richieste ai servizi LNF (supporteria, installazione,…):
SEA: 4 mesi/uomo (alimentazioni, readout veto…)
SPAS: 6 mesi/uomo (luminometro, supporteria, integrazione)
SPCM: 8 mesi/uomo (costruzione supporteria, shielding…)
2 tecnici al 50%
Richieste personale: Assegni, borse (post doc) e contratti
Richieste 2018 (very prelim.)
Missioni | Manut. | Invent. | Altri cons. | Cons. Lab | Totale
15 | 10 (pompe vuoto, criogenia, DAQ…) | 20 (DAQ, veto2 readout, Lumin. Monitor) | 20 (shield., support, gas cryo, ..) | 30 (lumin., cavi e connettori,, SDDs…) | 99

## Slide 39
SDD arrays, delivery and qualification
48 SDDs arrays needed
Delivery status:
52 arrays received
37 bonded (Milano)