## Slide 1
RD_FA Collaboration Meeting
July 3, 2017 – CNAF, Bologna
FCC-ee MDI studies
E.Belli
M.Migliorati, G.Rumolo
Acknowledgments: F. Bedeschi, M. Boscolo

## Slide 2
2
Outline
E. Belli - FCC-ee MDI studies
      The FCC project
      Impedance studies
        Heat load due to resistive wall impedance
        Heat load due to geometric impedance
      Trapped modes
      Electron cloud studies
        EC induced heat load in the IR magnets
      Conclusions

## Slide 3
Beam energy [GeV] | 45.6 | 80 | 120 | 175
Circumference [km] | 97.75 |  |  | 
RF frequency [MHz] | 400 |  |  | 
Arc cell | 60º/60º | 90º/90º |  | 
RF voltage [MV] | 255 | 696 | 2620 | 9500
Momentum compaction [] | 1.479 | 0.731 |  | 
Horizontal tune | 269.14 | 389.08 |  | 
Vertical tune | 267.22 | 389.18 |  | 
Synchrotron tune | 0.0413 | 0.0340 | 0.0499 | 0.0684
SR energy loss/turn [GeV] | 0.036 | 0.34 | 1.72 | 7.8
Longitudinal damping time [ms] | 414 | 7608 | 22.9 | 7.49
Beam current [mA] | 1390 | 147 | 29 | 6.4
Bunches/ring | 70760 | 7280 | 826 | 64
Bunch population [] | 4 | 4.1 | 7.1 | 20.4
Horizontal emittance [nm] | 0.267 | 0.28 | 0.63 | 1.34
Vertical emittance [pm] | 1 | 1 | 1.26 | 2.7
Energy spread SR [%] SR + BS [%] | 0.038 0.073 | 0.066 0.072 | 0.099 0.106 | 0.147 0.193
Bunch length SR [mm] SR + BS [mm] | 2.1 4.1 | 2.1 2.3 | 2.0 2.2 | 2.4 2.9
Beam energy [GeV] | 45.6 | 80 | 120 | 175
 | 97.75 |  |  | 
 | 400 |  |  | 
Arc cell | 60º/60º | 90º/90º |  | 
 | 255 | 696 | 2620 | 9500
 | 1.479 | 0.731 |  | 
 | 269.14 | 389.08 |  | 
 | 267.22 | 389.18 |  | 
 | 0.0413 | 0.0340 | 0.0499 | 0.0684
 | 0.036 | 0.34 | 1.72 | 7.8
 | 414 | 7608 | 22.9 | 7.49
 | 1390 | 147 | 29 | 6.4
Bunches/ring | 70760 | 7280 | 826 | 64
 | 4 | 4.1 | 7.1 | 20.4
 | 0.267 | 0.28 | 0.63 | 1.34
 | 1 | 1 | 1.26 | 2.7
 | 0.038 0.073 | 0.066 0.072 | 0.099 0.106 | 0.147 0.193
 | 2.1 4.1 | 2.1 2.3 | 2.0 2.2 | 2.4 2.9
3
FCC-ee parameters 2017
E. Belli - FCC-ee MDI studies
      Within the Future Circular Collider studies, FCC-ee would be the first step towards the 100 TeV hadron collider FCC-hh
      Motivation: study the physics at the highest energy

## Slide 4
4
Interaction Region
E. Belli - FCC-ee MDI studies
15 mm radius at IP
15 mm radius for pipes through QC1
20 mm radius for pipes in QC2
30 mm radius outside QC2
Be pipe at 80 cm, Cu elsewhere
M. Sullivan

## Slide 5
Wake fields and impedances
E. Belli - FCC-ee MDI studies
Wake fields (time domain): electromagnetic fields generated by the interaction of the beam with the vacuum chamber
Beam coupling impedance (frequency domain):
Perfectly conducting smooth pipe  the witness does not feel any force from the source
Ultrarelativistic limit : no EM field in front of the beam
Discontinuity  the source loses energy and the witness feels a force along the length of the discontinuity
Source
Witness
Finite conductivity  Delayed EM fields due to a delay in the induced currents and the witness feels a force all along the length
5

## Slide 6
Heat load
E. Belli - FCC-ee MDI studies
6
        For an uniformly filled machine () with bunch spacing , the power loss depends only on the real part of the longitudinal impedance
Bunch spectrum
number of bunches
harmonic number
revolution period
average beam current
      The energy loss of a beam can cause the heating of the environment
      FCC-ee beam pipes at room temperature
        No cryogenic systems
        Heat load can still represent an issue
        Possible heat load sources in the IR
          RW impedance
          Geometric impedance
          HOMs
          Electron cloud

## Slide 7
7
Resistive wall
E. Belli - FCC-ee MDI studies
Wake fields induced by the finite resistivity of the beam vacuum chamber
Three layers
  Cu/Be (2/1.2 mm, Ωm)
  Dielectric (6 mm, Ωm)
  Iron (Infinity, Ωm)
Energy [GeV] |  | 45.6 | 80 | 120 | 175
Bunch population [] |  | 4 | 4.1 | 7.1 | 20.4
Bunches/beam |  | 70760 | 7280 | 826 | 64
Bunch length [mm] |  | 2.1 | 2.1 | 2 | 2.4
[mW/m] | Cu | 1.4 | 1.5 | 4.9 | 30.7
 | Be | 2.22 | 2.3 | 7.5 | 47.4
[W/m] | Cu | 102.2 | 11.04 | 4.04 | 2
 | Be | 157.08 | 16.7 | 6.2 | 3.03
Energy [GeV] |  | 45.6 | 80 | 120 | 175
 |  | 4 | 4.1 | 7.1 | 20.4
Bunches/beam |  | 70760 | 7280 | 826 | 64
Bunch length [mm] |  | 2.1 | 2.1 | 2 | 2.4
 | Cu | 1.4 | 1.5 | 4.9 | 30.7
 | Be | 2.22 | 2.3 | 7.5 | 47.4
 | Cu | 102.2 | 11.04 | 4.04 | 2
 | Be | 157.08 | 16.7 | 6.2 | 3.03
IW2D
Analytic formula for a circular beam pipe with radius

## Slide 8
8
SR masks
E. Belli - FCC-ee MDI studies
Energy [GeV] |  | 45.6 | 80 | 120 | 175
Bunch population [] |  | 4 | 4.1 | 7.1 | 20.4
Bunches/beam |  | 70760 | 7280 | 826 | 64
Bunch length [mm] |  | 2.1 | 2.1 | 2 | 2.4
[mW] | Q1 | 19.5 | 20 | 68.2 | 393.5
 | Q2 | 5.6 | 5.9 | 21.5 | 122.4
[W/m] | Q1 | 1379.8 | 145.6 | 56.3 | 25.2
 | Q2 | 396.2 | 42.9 | 17.7 | 7.8
Energy [GeV] |  | 45.6 | 80 | 120 | 175
 |  | 4 | 4.1 | 7.1 | 20.4
Bunches/beam |  | 70760 | 7280 | 826 | 64
Bunch length [mm] |  | 2.1 | 2.1 | 2 | 2.4
 | Q1 | 19.5 | 20 | 68.2 | 393.5
 | Q2 | 5.6 | 5.9 | 21.5 | 122.4
 | Q1 | 1379.8 | 145.6 | 56.3 | 25.2
 | Q2 | 396.2 | 42.9 | 17.7 | 7.8
r
l
ltr
h
ABCI
175 GeV

## Slide 9
9
Trapped modes
E. Belli - FCC-ee MDI studies
Small variations in the geometry of the pipe can generate accidental cavities and produce trapped modes
These modes cannot propagate into the pipe and therefore they remain localized near the discontinuity, producing narrow resonance peaks of the impedance.
Possible source of heating
Model: BB resonator
Worst case scenario when

## Slide 10
10
Trapped modes
E. Belli - FCC-ee MDI studies
Time domain simulations (Gaussian bunch with =5mm) show the existence of a trapped mode at frequency 3.5 GHz
Longitudinal slots perpendicular to the HOM field
Frequency domain simulations confirmed the presence of this mode
CST
CST
Electric field lines perpendicular to the beam trajectory
A. Novokhatsky
Water-cooled absorber on these slots

## Slide 11
emitter
absorber
11
Electron cloud
E. Belli - FCC-ee MDI studies
Lost
t
Bunch spacing
Beam pipe
Bunch
Positively charged bunches passing through a section of an accelerator
Primary or Seed Electrons
  Residual gas ionization
  Photoemission due to synchrotron radiation (photoelectrons)
Primaries attracted and accelerated by the beam to energies up to several hundreds of eV
Emission of secondary electrons (energies up to few tens of eV)
1
Absorbed or reflected (no secondaries generation)
Accelerated by the following bunch (secondaries production)
Avalanche electron multiplication
(multipacting effect)
Property of the surface
emitter
absorber
2
3
4
5

## Slide 12
12
EC build up studies
E. Belli - FCC-ee MDI studies
Energy [GeV] | 45.6 |  | 
Bunch spacing [ns] | 2.5 |  | 
Bunch population [] | 0.4 |  | 
Horizontal emittance [nm] | 0.255 |  | 
Vertical emittance [pm] | 1 |  | 
Bunch length [mm] | 2.1 |  | 
Bunch train patterns | 100b+40e |  | 
IR elements |  | L[m] | G[T/m]
 | QC1L1 | 1.2 | -96.3
 | QC1L2 | 1 | 50.3
 | QC1L3 | 1 | 9.8
 | QC2L1 | 1.25 | 6.7
 | QC2L2 | 1.25 | 3.2
Energy [GeV] | 45.6 |  | 
Bunch spacing [ns] | 2.5 |  | 
 | 0.4 |  | 
Horizontal emittance [nm] | 0.255 |  | 
Vertical emittance [pm] | 1 |  | 
Bunch length [mm] | 2.1 |  | 
Bunch train patterns | 100b+40e |  | 
IR elements |  | L[m] | G[T/m]
 | QC1L1 | 1.2 | -96.3
 | QC1L2 | 1 | 50.3
 | QC1L3 | 1 | 9.8
 | QC2L1 | 1.25 | 6.7
 | QC2L2 | 1.25 | 3.2
Simulation studies
Round chamber of 15mm radius in Q1/ 20mm radius in Q2
Electron cloud build-up for 2.5 ns bunch spacing beam in IR magnets
  Initial uniform distribution electrons
  SEY scan

## Slide 13
13
EC induced heat load
E. Belli - FCC-ee MDI studies
SEY < 1 to run the machine IR without electron cloud

## Slide 14
14
Conclusions
E. Belli - FCC-ee MDI studies
      Heat load due to RW and SR masks impedances estimated
        Higher losses at low energy
          > 1KW/m for Q1 SR masks  to be optimized
      One trapped mode found in the IR at 3.5 GHz
        Insertion of longitudinal slots
        Design of HOM absorbers needed
      Multipacting threshold in IR quadrupoles 1.1
        Low SEY coating needed to keep IR e-cloud free (compatible with impedance requirements!)
        Instability studies needed

## Slide 15
Thanks for your attention