## Slide 1
SMI – STEFAN MEYER INSTITUTE FOR SUBATOMIC PHYSICS
WWW.OEAW.AC.AT/SMI
Overview of kaonic atom research plans
at J-PARC
Johann Zmeskal
SMI, Vienna, Austria
Strange and non-strange mesons induced processes studies at DAFNE, J-PARC and RIKEN:
present and future
LNF-INFN, Frascati
July 10-11, 2017

## Slide 2
SMI – STEFAN MEYER INSTITUTE FOR SUBATOMIC PHYSICS
WWW.OEAW.AC.AT/SMI
Outline

## Slide 3
Kaonic Atom Research @ J-PARC

## Slide 4
20 Institutes / 10 Countries
K-d at J-PARC

## Slide 5
E57 kaonic deuterium
physics goal

## Slide 6
Low-energy KN interaction
non-perturbative
coupled channels
approach based on
chiral SU(3) dynamics
Chiral perturbation theory was developed
for p,  is not applicable for KN systems
Notes: appropriate framework to analyse the anti-kaon-nucleon system at low energy
In light exotic hadronic atoms the Bohr radius is still much larger than the typical range of strong interaction formulated in QCD, and the average momentum of the bound hadron is very small. Chiral perturbation theory (ChPT) [20–22], with symmetries and symmetry breaking patterns of QCD included, is an appropriate framework to analyse the dynamics of hadrons at low energy and to describe the observable effects in the spectrum of exotic hadronic atoms.
There are non-perturbative coupled-channel techniques based on the driving terms of the chiral effective Lagrangian which generate the (1405) dynamically as a Kbar-N quasi-bound state and as a resonance in the pi-Sigma channel. They have proved useful and successful.
High precision K- p threshold data set important constraints for such theoretical approaches.

## Slide 7
Improved constraints on chiral SU(3) dynamics from kaonic hydrogen
Y. Ikeda, T. Hyodo and W. Weise, PLB 706 (2011) 63
Real part (left) and imaginary part (right) of the Kp  K  p forward scattering amplitude extrapolated to the subthreshold region, deduced from the SIDDHARTA kaonic hydrogen measurement.

## Slide 8
W.Weise, LEANNIS meeting July 2011

## Slide 9
Chiral SU(3) coupled channels dynamics
W.Weise
Needed: accurate constrains from antikaon-deuteron threshold measurement

## Slide 10
X-ray transitions to the 1s state
n=1
p
e-
K-
n=1
n=2
n~25
X-ray

## Slide 11
U.-G. Meißner, U.Raha, A.Rusetsky, Eur. phys. J. C35 (2004) 349
next-to-leading order, including isospin breaking
SCATTERING LENGTHS
Deser-type relation connects shift 1s and width 1s to the
real and imaginary part of ɑ K-p
(µC reduced mass of the Kp system,  fine-structure constant)

## Slide 12
E57 kaonic deuterium
cryogenic X-ray detector

## Slide 13
JFET integrated on SDD
lowest total anode capacitance
limited JFET performance
sophisticated SDD+JFET technology
SDD
CUBE
radiation entrance window
cooler
external CUBE preamplifier (MOSFET)
larger total anode capacitance
better FET performances
standard SDD technology
SIDDHARTA
Kd @ J-PARC / DANE
Development of new SDDs

## Slide 14
8 x 8 mm2 single SDD
Array: 9 SDDs (8 x 8 mm2 each)
12 x 12 mm
single SDD
FBK production:
4’’ wafer
6’’ wafer upgrade just finished
New SDDs - present layouts
developed by Politech Milano and FBK-Trento, Italy
26mm

## Slide 15
4x2 and 3x3 SDD arrays
SDD-chip back side with bonding pads
connector
9 holes for bondings
CUBE
preamplifier
SDD-chip glued to ceramic board, bonded to CUBE preamplifier

## Slide 16
4x2 SDD array
single unit
4x2 SDD array:
55 pieces of 4x2 SDD-chips
+ ceramic boards
available
Shipping package

## Slide 17
SDD mounting / bonding
ceramic boards
4x2 SDD chip
device for gluing and bonding
mounting and bonding process under control

## Slide 18
Back Bonding Block
Take the Back bonding block.
8
SDD Back side view
Place the ceramic board with SDD Back side up on the Back bonding block.
9
Ceramic Back side view
Back Bonding Block
10
Perform back bonding.
BACK
BONDING

## Slide 19
5
Ring N and Substrate bonding
SUB
LAST RING

## Slide 20
7
Arrows show directions to mount cubes

## Slide 21
3 cooling cycles
cryostat set to 65 K
ceramic temperature 73 K
no visual damage of SDD/ceramic
4x2 SDD array cooling test

## Slide 22
New SDD technology with CUBE preamplifier
55Fe spectrum
123.0 eV FWHM
SDD characteristics:
area/cell = 64 mm2
total area = 512 mm2
T = - 100°C
drift time < 500 ns

## Slide 23
E57 kaonic deuterium
setup at J-PARC K1.8BR

## Slide 24
J-PARC K1.8BR spectrometer

## Slide 25
K1.8BR experimental area
J-PARC K1.8BR spectrometer
neutron counter
beam dump
beam sweeping
magnet
liquid 3He-target
system
CDS
beam line
spectrometer
K-
γ, n
p
15m

## Slide 28
T1
T0
main degrader
CDC
BLC
CDH
Solenoid
SDD and
deuterium
target
CDH...cylindrical detector hodoscope
CDC...cylindrical drift chamber
T0.......beam line counter
T1.......beam line counter
BLC....beam line chamber
Kd setup within the K1.8BR spectrometer

## Slide 29
K
start counter T0
entrance window 75 µm Kapton
Al reinforced side wall 75 µm Kapton
12 x 4 SDD arrays
SDD cooling and support
target cell: l = 160 mm, d = 65 mm
target pressure max.: 0.35 MPa
target temperature: 23 – 30 K
SDD active area: 246 cm2
density: 4% LHD
at 29K/0.35 MPa
The cryogenic target and SDD design

## Slide 30
4x2 SDD array – layout + arrangement around target
CUBE

## Slide 31
J-PARC E57 K-d cryogenic target
and SDD detector setup
Cryo target + SDD detector
Line driver boards
Ultra-pure aluminium cooling lines
Analogue signal and HV-LV cables
16-channel amplifier boards
2-stage closed cycle cryo-cooler

## Slide 32
K-d apparatus – cryo target + SDDs + line driver boards

## Slide 33
K-d apparatus – vacuum feed-through + amplifier boards
Prototype of the
16-channel amplifier board
37pin D-sub
analogue out
reset
trigger

## Slide 34
E57 kaonic deuterium
cryogenic target cell

## Slide 35
Prototype cryogenic target cell
length: 180 mm
diameter: 65 mm
wall thickness:
one-layer: 75 µm / 100 µm (overlap 10 mm)
  (N-1 and N-2 / N-3 and N-4)
two-layer: < 70 µm (without / with overlap)
  (N-5 / N-8 and N-9 under construction)
three-layer: < 100 µm (with overlap)
  (N-6 and N-7; N-10 and N-11 under construction)

## Slide 36
Tool for the production of the cylinder barrel

## Slide 37
2016-09-06
17:56
2016-09-22
15:15
Cell: #01.V2
Kaonic deuterium target – prototype tests
Pressurised for 16 days
with P = 0.3 MPa (overP)
Cooling/pressure test
2.5 weeks 30 K / 0.19 Mpa
3.5 days 30 K / 0.31 MPa

## Slide 38: Strength test of the target cell at low temperature (< 77K)
Strength test (< 77 K) to confirm safety factor
Operational (maximum) pressure = 0.35 MPa
Procedure :
(1) Cool down the cell (~ 30 K)
(2) Pressurize the cell with He gas
Thermometer
Pressure gauge
Refrigerator
Cell
gas inlet

## Slide 39: Strength test of the target cell ~ cont’d
pressure
> 7 bar
Temperature
~ 50 K
burst
Safety factor confirmed > 2 at cryogenic temperature
snapshot just before burst

## Slide 40
220 mm
Status of the lightweight cryogenic target cell
working temperature: 30 K
working pressure: 0.3 MPa
wall thickness: < 100 µm
Technical safety report was presented at the Facilities Impact and Finance
Committee (FIFC) meeting in December 2016
by Masaharu SATO

## Slide 41
E57 kaonic deuterium
kaon beam tune

## Slide 42
E57 - SDD test setup
pre-amplifier boards
3x3 SDD array
3-stage Peltier-cooler
24 (+2) working channels

## Slide 43
May 25, 2016
16:27

## Slide 44
J-PARC SDD setup, calibration run with Fe-55, June 22, 2016; 14:00
SDD temp. - 40°C

## Slide 45
Setup of E57 and E62 in K1.8BR area
SDD
setup
TESs
Li-
block
Co-57
optimisation of stopped kaons in low mass targets
KLi X-ray intensity to background ratio and range tuning in agreement with MC simulation

## Slide 46
Range curve comparison

## Slide 47: 0.9 GeV/c with Cu degrader

## Slide 48: Kaonic Lithium 32
Sum of all K runs, extracted
KLiL transition:
  15.323 ± 0.008 keV
~ 1200 counts
resolution 160 eV (sigma)
Theory:
    15.330 keV (pure QED)
    J.P.Santos et al.
    Phys. Rev. A 71 (2005) 032501
preliminary
Experiment:
  15.321 ± 0.024 keV
C.J.Batty et al.
Nuclear Physics A282 (1977) 487

## Slide 49
Summary beam tune run
optimisation of stopped kaons in low mass targets
SDDs performing very well, as expected
  energy resolution ~ 200 eV (FWHM) at 6 keV @ T ~ - 40°C
  energy shift dependence of counting rate:
  spill-on / spill-off < 6 eV
KLi X-ray intensity / range tuning in agreement with MC simulation, detailed analysis is ongoing

## Slide 50
E57 kaonic deuterium
theory + MC simulation

## Slide 51
Kd scattering lengths - theory
aKd [fm] | 1s [eV] | 1s [eV] | Reference
-1.55 + i 1.66 | - 969 | 938 | Weise 2015 [2]
-1.58 + i 1.37 | - 887 | 757 | Mizutani 2013 [4]
-1.48 + i 1.22 | - 787 | 1011 | Shevchenko 2012 [5]
-1.46 + i 1.08 | - 779 | 650 | Meißner 2011 [1]
-1.42 + i 1.09 | - 769 | 674 | Gal 2007 [6]
-1.66 + i 1.28 | - 884 | 665 | Meißner 2006 [7]
-1.62 + i 1.91 | - 1080 | 1024 | Oset 2001 [3]
[1] M. Döring, U.-G. Meißner, Phys. Lett. B 704 (2011) 663
[2] W. Weise, arXiv:1412.7838[nucl-theo]2015
[3] S.S. Kamakov, E. Oset, A. Ramos, Nucl. Phys. A 690 (2001) 494
[4] T. Mizutani, C. Fayard, B. Saghai, K. Tsushima, Phys. Rev. C 87, 035201 (2013), arXiv:1211.5824[hep-ph]
[5] N.V. Shevchenko, Nucl. Phys. A 890-891 (2012) 50-61
[6] A. Gal, Int. J. Mod. Phys. A22 (2007) 226
[7] U.-G. Meißner, U. Raha, A. Rusetsky, Eur. phys. J. C47 (2006) 473
1s = (-800 ± 60) eV
1s= (800 ± 140) eV
Notes: Compilation of predicted Kd scattering lengths a K¯d
and corresponding experimental quantities 1s and 1s

## Slide 52
arXiv:1705.06857v1 [nucl-th] 19 May 2017

## Slide 53
X-ray energy [keV]
counts per 80 eV bin
Ka
Kb
Khigh
DAQ WITH HYDROGEN
45 kW proton beam, 3 days
detector area 120 cm2
4% LHD
achievable precision:
sigma(shift) ~ 35 eV
sigma(width) ~ 71 eV
Commissioning of the Kd apparatus
for stage-2 approval (proof of principle using Kp)
ε1s = -283 ± 36(stat) ± 6(syst) eV
Γ1s = 541 ± 89(stat) ± 22(syst) eV
Notes: For 250 K-p K(alpha) events, assuming S/B = 4:1
dE = 280 +- 40 width= 540 +- 110

## Slide 54
QED
K
K
Khigh
Geant4 simulated Kd X-ray spectrum
for 160 kW·weeks
achievable precision:
shift: 60 eV
width: 140 eV
signal: shift - 800 eV
width 800 eV
density: 5% (LDD)
detector area: 246 cm2
K yield: 0.1 %
yield ratio as in Kp
S/B ~ 1 : 3
vertex cut
charged particle veto
asynchronous BG
1s
1s

## Slide 55
SDDs for kaonic helium 1s “search”
T1
T0
main degrader
CDC
BLC
CDH
Solenoid
liquid He target
+ SDDs
kaons produced at 27 kW:
1 GeV/c ~ 4·109 kaons/day
stopping: ~2·10-3
K-He K-yield: ~1·10-4
tagging eff. ~ 0.5
He K events ~ 400 per day

## Slide 56
Kaon atom factory at J-PARC
high resolution X-ray spectroscopy

## Slide 62
kaonic helium 2p

## Slide 68
Sources of experimental data on K-N interaction
68

## Slide 69
Kaon – nucleon scattering database
cross section figure from: Review of particle physics, Phys. Lett. B667 (2008), 1
J-PARC
J-PARC

## Slide 70
Alessandra Filippi, INFN Torino

## Slide 71
T1
T0
main degrader
CDC
BLC
CDH
Solenoid
Scattering setup:
double-side Si-strip detectors
TimePix ?
“active” TPC
Low-energy K-p / K-d scattering
BLC
Cryo-target
double-side
Si-strip
~ 100 µm

## Slide 72
Supported by
Thank you
P24756-N20