## Slide 1
Mattia Parise
TTC Meeting, Milan
6-9 February, 2018
Preparation, processing, assembling and testing of spoke resonators: from SSR1 jacketed cavities to string assembly

## Slide 2: SSR1 cryomodule for PIP-II
SSR1 cryomodule
SSR1 cavity string
PIP-II Linac
SSR1

## Slide 3: SSR1 string overview
Interconnection cavity-cavity
Solenoid-BPM subassembly
Solenoid
BPM
Gate Valve
20
mm
Gate Valve
Movable rail system
Vacuum-end coupler
Type
A
Type
B
Type
A
Type
B
Type
A
Type
B
Type
B
Type
A
Edge-welded bellows

## Slide 4: Preparation of the SSR1 string assembly dry-run
Wheels were found to be inappropriate because of unexpected uneven floor
Wheels lose contact with floor during motion leading to the wobbling of the rail system and excessive cavities displacements

## Slide 5: Preparation of the SSR1 string assembly dry-run
Wheels were found to be inappropriate because of unexpected uneven floor
Wheels lose contact with floor during motion leading to the wobbling of the rail system and excessive cavity displacements
New suspension wheels and stiffer connections were procured
Measurement of the cleanroom floor profile
Wheel spring stiffness is optimized to minimize cavity vertical displacement
Final
position
Initial
position
Cleanroom floor profile
Movement

## Slide 6: Preparation of the SSR1 string assembly dry-run
Link
Rail system with string weight can be successfully moved to the desired location. The process has been repeated 5 times and final position can be achieved with an uncertainty of ~ 5 mm

## Slide 7: Preparation of the SSR1 string assembly dry-run
Dry-run of SSR1 string assembly is carried out on a half cavity string
The goal is to assess the feasibility of a cleanroom-compatible assembly

## Slide 8: Preparation of the SSR1 string assembly dry-run
Solenoid-BPM-Bellows
Cavity connection
Cavity-cavity connection
Dry-run of SSR1 string assembly is carried out on a half cavity string
The goal is to assess the feasibility of a cleanroom-compatible assembly

## Slide 9: Preparation of the SSR1 string assembly dry-run
Bellows cages provides 2 rotational degrees of freedom at the end flange
Can be splitted in 2 halves so that can be removed prior cryomodule assembly

## Slide 10: Preparation of the SSR1 string assembly dry-run
Vertical assembly facilitates handling of components
Sub-assembly can rotate 360 degrees for an easy assembly
The movable cart allows easy handling of the heavy sub-assembly

## Slide 11: Preparation of the SSR1 string assembly dry-run
Link

## Slide 12: Preparation of the SSR1 string assembly dry-run
Link
Sub - millimeter precise and reliable alignment
Easy to use system

## Slide 13: Preparation of the SSR1 string assembly dry-run
Bellows cage is disassembled once the cavity-cavity connection is completed

## Slide 14: Preparation of the SSR1 string assembly dry-run
Edge welded bellows can be successfully assembled and bellows cage can be removed

## Slide 15: Edge welded bellows particle counts
3 cycles compression and extension (10 liters sample) |  |  | 
Time [s] | > 0.3 μm | > 0.5 μm | > 1 μm
7 | 2 | 0 | 0
14 | 2 | 1 | 0
21 | 3 | 1 | 0
28 | 1 | 0 | 0
35 | 3 | 0 | 0
42 | 1 | 0 | 0
49 | 1 | 0 | 0
56 | 1 | 0 | 0
63 | 1 | 0 | 0
70 | 1 | 0 | 0
77 | 1 | 0 | 0
84 | 0 | 0 | 0
91 | 2 | 1 | 0
Edge welded bellows was cleaned and brought inside class 10 cleanroom:
  30 min Liquinox (1%) + DI water ultrasonic cleaning at 50 °F
  30 min Citranox (2%) + DI water ultrasonic cleaning at 50 °F
  30 min DI water ultrasonic cleaning at 50 °F
  Handheld HPR
Particle counts of the nitrogen dried bellows approach 0 particles > 0.3 μm in less than 1 minute
Particle counts during contraction are acceptable

## Slide 16: Gate valves particle counts: all metal vs Viton sealed
Viton sealed
Pneumatic actuation (<1 sec for opening and closing)
Viton may degrade due to radiation
All metal construction
Manual actuation (~ 5 min for opening and for closing)
Radiation resistant
SSR1 Gate Valve
LCLSII All-Metal Gate Valve

## Slide 17: Gate valves particle counts: all metal vs Viton sealed
Chart: Opening - Closing cycles from side 1
| Counts 0.3 μm | Counts 0.5 μm | Counts 1 μm
Opening 1 - Side 1 | 94 | 42 | 8
Closing 1 - Side 1 | 177 | 88 | 19
Opening 2 - Side 1 | 180 | 60 | 8
Closing 2 - Side 1 | 164 | 77 | 24
Opening 3 - Side 1 | 142 | 65 | 17
Average Opening | 138.6667 | 55.6667 | 11
Average Closing | 170.5 | 82.5 | 21.5
Average total | 151.4 | 66.4 | 15.2
Chart: Opening - Closing cycles blowing from side 1 (string side)
| Counts 0.3 μm | Counts 0.5 μm | Counts 1 μm
Opening 1 - Blowing from string side | 803 | 439 | 129
Closing 1 - Blowing from string side | 73 | 27 | 6
Opening 2 - Blowing from string side | 230 | 94 | 30
Closing 2 - Blowing from string side | 211 | 88 | 34
Opening 3 - Blowing from string side | 138 | 43 | 12
Average Opening | 390.3333 | 192 | 57
Average Closing | 142 | 57.5 | 20
Average total | 291 | 138.2 | 42.2
SSR1 Viton sealed pneumatic actuated gate valve performed better than the all-metal gate valve in terms of particle counts
SSR1 cryomodule is located at the early stage of the LINAC
Damaging of the Viton due to beam radiation is limited at this stage
SSR1 Viton sealed gate valve is compact, generate less particulate, reliable (does not depend on the operator to be actuated) and can be opened/closed in <1 sec
SSR1 Gate Valve
LCLSII All-Metal Gate Valve

## Slide 18: Nitrogen purging line
Shut-off valve
Pressure regulator
High pressure gauge
Pressure relief valve
Shut-off valve
Shut-off valve
Metering valve
Low pressure gauge
High purity filter
To vacuum cart
Nitrogen purging line can provide up to 20 SLPM
Filter is located on the cavity as last element to avoid cavity contamination
Can be manually operated
Mass Flow Controller can substitute the metering valve for a reliable soft start

## Slide 19: Nitrogen purging line
No Nitrogen purging applied
Nitrogen purging at 4 SLPD purge flow speed 0.1 m/s

## Slide 20: Nitrogen purging line
No Nitrogen purging applied
Nitrogen purging at 4 SLPD purge flow speed 0.1 m/s
Back flow inside the beam pipe

## Slide 21: Nitrogen purging line
Link

## Slide 22: 48 hours bake @120°C: a new approach
Infrared heater characteristics:
90% energy efficient
5 – 7 min warmup/cooldown time
Elements reach up to 815°C
Output power can be controlled through cavity temperature
Infrared
heaters
to
vacuum
cart
A couple of infrared heaters can bring the cavity up to 120°C in 2 hours
Cavity never leaves the cleanroom
Baking can be performed after the cold test assembly leak check
Quartz fabric Faced Heater

## Slide 23: Thank you for your attention
On behalf of the SSR1 team

## Slide 24: Backup slides

## Slide 25: Gate valves particle counts: all metal vs Viton sealed
Chart: Opening - Closing cycles from side 1
| Counts 0.3 μm | Counts 0.5 μm | Counts 1 μm
Opening 1 - Side 1 | 94 | 42 | 8
Closing 1 - Side 1 | 177 | 88 | 19
Opening 2 - Side 1 | 180 | 60 | 8
Closing 2 - Side 1 | 164 | 77 | 24
Opening 3 - Side 1 | 142 | 65 | 17
Average Opening | 138.6667 | 55.6667 | 11
Average Closing | 170.5 | 82.5 | 21.5
Average total | 151.4 | 66.4 | 15.2
Chart: Opening - Closing cycles from side 2
| Counts 0.3 μm | Counts 0.5 μm | Counts 1 μm
Opening 1 - Side 2 | 52 | 27 | 12
Closing 1 - Side 2 | 57 | 21 | 7
Opening 2 - Side 2 | 52 | 23 | 8
Closing 2 - Side 2 | 34 | 12 | 2
Opening 3 - Side 2 | 62 | 26 | 8
Average Opening | 55.3333 | 25.3333 | 9.3333
Average Closing | 45.5 | 16.5 | 4.5
Average total | 51.4 | 21.8 | 7.4
Chart: Opening - Closing cycles blowing from side 1 (string side)
| Counts 0.3 μm | Counts 0.5 μm | Counts 1 μm
Opening 1 - Blowing from string side | 803 | 439 | 129
Closing 1 - Blowing from string side | 73 | 27 | 6
Opening 2 - Blowing from string side | 230 | 94 | 30
Closing 2 - Blowing from string side | 211 | 88 | 34
Opening 3 - Blowing from string side | 138 | 43 | 12
Average Opening | 390.3333 | 192 | 57
Average Closing | 142 | 57.5 | 20
Average total | 291 | 138.2 | 42.2
Chart: Opening - Closing cycles blowing from side 2
| Counts 0.3 μm | Counts 0.5 μm | Counts 1 μm
Opening 1 - Blowing from non-string side | 503 | 210 | 84
Closing 1 - Blowing from non-string side | 27 | 5 | 0
Opening 2 - Blowing from non-string side | 78 | 30 | 6
Closing 2 - Blowing from non-string side | 14 | 4 | 1
Opening 3 - Blowing from non-string side | 104 | 37 | 9
Average Opening | 228.3333 | 92.3333 | 33
Average Closing | 20.5 | 4.5 | 0.5
Average total | 145.2 | 57.2 | 20
SSR1 Gate Valve (Viton Sealed - Pneumatic actuated)
LCLSII Gate Valve (All-metal - Manually actuated)

## Slide 26: Extra precautions
Cavity beam pipes are protected using cleanroom tape and cleanroom plastic to avoid contamination outside of the cleanroom.
Extra precautions are taken wrapping the hose with foam. Each time the cavity is crated an Engineer is present to check that all the security precautions are followed

## Slide 27: SSR1 vacuum-end couplers
The procurement of coupler antennas presented a series of technical issue that led them to be on the SSR1 CM1 critical path
Vacseal (silicon resin solution) was used on the first 2 antennas on the beam vacuum volume side and it has never been “cured”
The company notified of this unconformity after the 2 antennas were assembled onto 2 different SSR1 cavities
The 2 cavities performed poorly during the cold tests and the RGA scans showed anomalies that can be linked to the Vacseal composition
Vacseal suspected area

## Slide 28: SSR1 vacuum-end couplers
New antenna from current supplier broke during testing at 20 kW, CW full reflection due to high dependence of loss tangent on temperature
Couplers are as important as cavities but in this case, suppliers were not actively followed, leading to several problematics

## Slide 29: Preparation of the SSR1 string assembly dry-run
Cavity to solenoid bellows
Solenoids
BPMs
Cavity to BPM bellows
Cavity to cavity bellows

## Slide 30: Preparation of the SSR1 string assembly dry-run

## Slide 31: Preparation of the SSR1 string assembly dry-run

## Slide 32: Preparation of the SSR1 string assembly dry-run
Diamond aluminum seal

## Slide 33: Preparation of the SSR1 string assembly dry-run
BPM

## Slide 34: Preparation of the SSR1 string assembly dry-run
Cavity to BPM bellows

## Slide 35: Preparation of the SSR1 string assembly dry-run

## Slide 36: Preparation of the SSR1 string assembly dry-run

## Slide 37: Avoid active pumping: burst disk
Connection to the vacuum cart was done in a portable glove box
2 days required
Environment is not ideal for a clean connection
Potential contaminations during the connection and from the vacuum cart are avoided
Installation time into the test cave is substantially reduced
With active pumping:
Without active pumping: Burst Disk

## Slide 38: Right Angle Valve (RAV) to cavity connection
Gravity
RAV was directly sitting on top of the cavity beam volume
Particle may be generated during valve actuation and gravity force or bad venting procedure can move particles inside the cavity beam volume

## Slide 39: Nitrogen purging line

## Slide 40: Preparation of the SSR1 string assembly dry-run
Maximum relative Z displacement is within the bellows specs: ±1.5 mm lateral movement