## Slide 1: C-ADS tuner systems at IMP
Lubei Liu, Ruoxu WANG, Fengfeng Wang, Lei Zhang
Tiancai Jiang, Zheng Gao, Weiming Yue, Shenghu Zhang
SRF Group
On behalf of ADS Linac Team
Institute of Modern Physics, CAS

## Slide 2: Outline
Introduction
Tuner experience on the Helium Pressure Fluctuation
Summary

## Slide 3: The Demo 25 MeV SRF Linac
RFQ
ECRIS
HEBT
162.5 MHz HWR010
162.5 MHz HWR015
MEBT
IHEP
IMP
12 scissor tuner for HWR010
5 scissor tuner for Taper HWR015

## Slide 4: Specifications
Parameters | HWR010 Design | HWR015 Design
Frequency(MHz) | 162.5 | 162.5
Tuning sensitivity(KHz/mm) | 180 | 110
Tuning force(KN/mm) | 2.2 | 1.2
Tuning resolution(Hz) | 9 | 9
Tuning resolution (step/nm) | 44 | 64
Tuning range(KHz) (push condition) | 160 | 110
Fine tuning range(Hz) | 180 | 180
Backlash Tolerance(Hz) | ＜2 | <2
Max. Stress - 330Mpa/mm
Max. Stress - 460Mpa/mm

## Slide 5
stepper motor
Tuner sketch
zero backlash
pivot joints
Beam flange
anti-backlash pivot
Cryomodule flange
Tuner Attachment Points
speed reducer
Tuner Structure
scissor
dual-member lever arms
Material: TC4
condition: pre-pressing
HWR010 Tuner
HWR015 Tuner

## Slide 6: HWR010 Tuner Test Result at Stand
Δf/ ΔL=170KHz/mm
Enhancing the strength of the arm

## Slide 7: Helium Pressure Fluctuation
For the same helium pressure fluctuation, the frequency of the phase loop unlock of HWR015-CM is higher than HWR010-CM.
Varing in one direction, the phase loop can be locked more stable
For fluctuation, phase loop sometimes will be unlocked
Helium Pressure

## Slide 8: Possible Reasons
Qext of the coupler is different, bandwith of HWR015-CM is less than half of HWR010-CM.
Require faster response of HWR015 CM3 tuner
Tuner performance
Return difference
 | Qe | Bandwith
HWR010 CM1 | 5.2E5 | 312
HWR015 CM3 | 1.2E6 | 136

## Slide 9: Return Difference
Possible Reason ?
Chart: HWR010 CM1-3
Chart: HWR015 CM3-3
Flexible joint
Machining and assembly accuracy of the linear motion unit
Control system
...

## Slide 10: Test The Linear Motion Unit
A constant step of motor motion (5000 steps)
Corresponding displacement of movable plate is measured by micrometer gauge
Movable
plate
micrometer gauge

## Slide 11: Linear Part Test Result
Machining and assembly accuracy of the linear motion unit is the problem.
Chart: HWR010 CM1-3
DOWN | -0.003 | -0.016 | -0.021 | -0.023 | -0.027 | -0.032 | -0.037 | -0.042 | -0.047 | -0.051 | -0.057 | -0.062 | -0.067 | -0.072 | -0.077 | -0.082 | -0.088 | -0.094 | -0.101 | -0.107 | -0.114 | -0.121 | -0.126 | -0.132 | -0.138
UP | -0.015 | -0.022 | -0.027 | -0.032 | -0.038 | -0.043 | -0.047 | -0.053 | -0.06 | -0.065 | -0.071 | -0.075 | -0.081 | -0.086 | -0.091 | -0.096 | -0.101 | -0.107 | -0.112 | -0.118 | -0.125 | -0.13 | -0.134 | -0.137 | -0.138
Chart: HWR015 CM3-3
UP | 0.004 | 0.014 | 0.022 | 0.026 | 0.032 | 0.037 | 0.044 | 0.049 | 0.056 | 0.061 | 0.068 | 0.072 | 0.078 | 0.083 | 0.089 | 0.095 | 0.102 | 0.108 | 0.113 | 0.119 | 0.126 | 0.131 | 0.138 | 0.143
DOWN | 0.136 | 0.142 | 0.148 | 0.156 | 0.163 | 0.161 | 0.157 | 0.155 | 0.152 | 0.15 | 0.15 | 0.15 | 0.149 | 0.149 | 0.149 | 0.149 | 0.149 | 0.149 | 0.149 | 0.149 | 0.148 | 0.147 | 0.147 | 0.147

## Slide 12: Improvement
Chart: HWR015 CM3-3
Chart: HWR015 CM3-3
cycle1 | 0.005 | 0.011 | 0.015 | 0.02 | 0.023 | 0.029 | 0.036 | 0.04 | 0.047 | 0.052 | 0.059 | 0.063 | 0.07 | 0.079 | 0.083 | 0.09 | 0.096 | 0.099 | 0.108 | 0.113 | 0.121 | 0.128 | 0.131 | 0.137 | 0.144
cycle2 | -0.016 | -0.012 | -0.005 | 0.002 | 0.008 | 0.013 | 0.019 | 0.026 | 0.032 | 0.038 | 0.044 | 0.049 | 0.056 | 0.063 | 0.07 | 0.075 | 0.082 | 0.088 | 0.096 | 0.103 | 0.11 | 0.117 | 0.127 | 0.135 | 0.144
cycle3 | -0.023 | -0.029 | -0.035 | -0.041 | -0.048 | -0.054 | -0.06 | -0.068 | -0.072 | -0.078 | -0.084 | -0.091 | -0.095 | -0.103 | -0.108 | -0.114 | -0.121 | -0.127 | -0.133 | -0.139 | -0.145 | -0.151 | -0.157 | -0.164 | -0.17
cycle4 | -0.012 | -0.019 | -0.024 | -0.031 | -0.036 | -0.043 | -0.051 | -0.057 | -0.062 | -0.069 | -0.072 | -0.08 | -0.085 | -0.092 | -0.097 | -0.105 | -0.111 | -0.122 | -0.125 | -0.134 | -0.142 | -0.145 | -0.151 | -0.161 | -0.17
Reduce the return difference
Increase the stability of cavity

## Slide 13: Microphonics*
*Zheng GAO, “LLRF commissioning of 25 MeV Proton SC Linac and design for 500 MeV CW Linac”, this meeting.
Vibration source removed
Pick up
25.7dBc
CM2-6 works unstable
The sideband of reflected signal from coupler appeared when the RF drive signal of solide state amplifer set to -30 dBm (0.001 mW).

## Slide 14: Future HWR010 Tuner -- Piezo
PI Corp.：
the length 147mm
PIEZO
In-series piezoelectric actutaor is in the design
Piezo
Stochastic background noise
Microphonics
Electromagnetic-mechanical vibration
Thermal acoustic oscillation

## Slide 15: Summary
HWR010 tuners work for more than four years, they can work out slow helium pressure fluctuation. The speed, force and resolution of the tuner to be fully adequate to the requirements.
HWR015 tuners have return difference due to machining errors.
To compensate the microphonics effect, an in-series piezoelectric actuator is considering to be exploited.

## Slide 16
Thanks for your attention