## Slide 1: Current Understanding of Field Emission in SRF Cavities in CEBAF Linacs
Rong-Li Geng
Jefferson Lab
TTC Meeting in Milano, February 6 - 9, 2018
Root causes: solid particulates input & gas molecules input
Mitigations: helium processing, gradient re-distribution
Counter-measures: controlling source particulates/molecules; blocking particulate/molecule transportation; eliminating resident particulate/molecules

## Slide 2
Outline
CEBAF and its SRF linacs
Field Emission (FE) and its impact
  Machine energy reach
  Machine operation reliability
Current understanding of FE in CEBAF linacs
  Root-causes
  Mitigations
  Counter-measures
Open questions and discussions

## Slide 3
CEBAF: Continuous Electron Beam Accelerator Facility
Basic research of atoms’s nucleus
First large-scale application of SRF linac technology
Construction 1987-1993
Upgrade 2008-2015

## Slide 4
R.L. Geng
2011 – present
12 GeV Upgrade
Two 1.1 GeV linacs
1995 - 2011
6 GeV improvement
Two 0.6 GeV linacs
1987 - 1994
4 GeV, 200 µA CW
Two 0.4 GeV linacs
CHL-2
Upgrade magnets and power supplies
Add arc
Add 5 cryomodules
Add 5 cryomodules
Add beamline
CEBAF Evolution

## Slide 5
Latest News: CEBAF Operation Enabling
Simultaneous Data Collection in 4 Experimental Halls

## Slide 6: CEBAF SRF Cavities
Original CEBAF cavity
CEBAF 12 GeV upgrade cavity
7-cell, Low-Loss Shape
80+8 cavities in 10+1 moduels
Design
  Ea=19.2 MV/m (Epk = 19.2 X 2.17 = 41.7 MV/m)
  Q0=7.2×109 @ 19.2 MV/m
Achieved
  <Ea>=22.2 MV/m
  <Q0 @ 19.2 MV/m>=8.1×109
2x (600 + 500) MV
Add ~5 kW 2K cooling power
Add ~ 5 MW liquefier operation power
5-cell, Cornell-Type
338 cavities in 42-1/4 moduels
Design
  Ea=5 MV/m (Epk = 5 X 2.56 = 12.8 MV/m)
  Q0=2.4×109 @ 5 MV/m
Achieved
  <Ea>=7.5 MV/m, <Q0>=5×109@ 5MV/m
  Helium processing
Acheived
  <Ea>=12.5 MV/m, <Q0>=5×109@ 5MV/m
  Refurbishing
2x 600 MV
5 kW 2K cooling power
5 MW liquefier operation power
Together for 12 GeV nuclear physics run

## Slide 7
R. Bachimanchi, J. Benesch, M. Drury, A. Freyberger, R. Geng, J. Mammosser, “2014 Update: CEBAF Energy Reach and Gradient Maintenance Needs”,
JLAB-TN-14-024
CEBAF “Gradient Degradation” - I
Loss rate: 34 MeV/pass-year.
Cryomodules consisting original 5-cell cavities
based on operations data since 1995.
Mitigation:
helium processing
module refurbishment
(C50 -> C75)
Root cause ???

## Slide 8
Final qualification
individual cavity
Fantastic!
Cryomodule
Linac
Cavities “possess” high gradient capability. Good cryomodule results.
Why can’t cavities run in linacs at gradients as in cryomodules?
Interlock protection – trip rate limit
Root causes being studied: FE a principal issue of interest (also other topics)
CEBAF “Gradient Degradation” - II
New 12 GeV upgrade7-cell Low-Los shape cavities

## Slide 9: Current Understanding of FE in CEBAF Linacs
Root causes
  Solid particulates input
  Direct evidence by identification of particulates collected from cavities extracted from linac following long term beam operation (the 11th refurbishment cryomodule C50-11)
  “Clay” particulates
  Stainless-steel particulates
  Titanium/Tantalum particulates (from beam line ion pump external to cryomodule)
Particulate collection from cavities extracted from linac
SRF2015, MOPB035

## Slide 10: Solid Particulates Input - continued
Beamtubes btw cavities
Cavity 2nd Equators
S0137 – C2-9 – Area 14
Copper
From Franklin cavity #2, cell 2
Further particulate collection and identification from cryomodules (C50-12 and C50-13) as well as from warm girders near them
Large population of metallic particulates:
  copper
  stainless-steel
  aluminium
  titanium…
Species found in cavity match those found in warm girders
A-M Valente-Feliciano et al., Particulate Sampling & Analysis - 2017 Ops StayTreat

## Slide 11: Current Understanding of FE in CEBAF Linacs
Root causes: Gas molecules input
  Molecular species identification with RGA during controlled warm up of CEBAF 12 GeV upgrade cryomodule 2L25
  H2 being the leading species
Chart: 2L25 Warm Up 5/04/16

## Slide 12
Gas Molecules Input - continued
Further analysis of gas loading during unplanned linac warm following 27july17 cryo plant incident
  100 monolayers of H2 equivalent gases frozen onto 7-cell Cavities; 2 monolayers onto 5-cell cavities
  Data being collected to compare FE of Spring17 with Spring16

## Slide 13: Current Understanding of FE in CEBAF Linacs
Mitigations
  Gradient re-distribution: reduce FE induced radiation while preserving integrated accelerating voltage of cryomodule
    Requires dedicated FE instrumentation in accelerator tunnel
    Demonstration at CEBAF injector cryomodule: radiation at its beamline exit reduced by 5 orders w/ total voltage preserved (see IBIC17 talk, TH1AB1)
    Eliminates inter-cryomodule and long-distance propagation of FE electrons
      Effectively reduce radation production (see IBIC17 talk)
  Helium processing
    Successful application of helium processing against 5-cell cavities (C.E. Reece et al, PAC1997)
      Enabled cavities limited to 4–6 MV/m to operate stably at 6–9 MV/m
    Massive effort in helium processing during 2015 summer shut down (A. Drury et al., NAPAC16, THA1IO02)
      Average increase in FE free gradient was 0.93 MV/m

## Slide 14: Current Understanding of FE in CEBAF Linacs
Counter-measures
  Controlling source particulates/molecules
    Improved procedure for cavity-string assembly, cryomodule UHV assembly
    Reduce beamline gate valve actuation
    Outlaw ion pump hi-potting
    Replace ion pump by NEG pump
  Blocking particulate/molecule transportation
    Study of beam-enabled particulate transportation (next slide)
    Electrostatic precipitator (old idea)
  Eliminating resident particulate/molecules
    Cryomodule warmup
    In-situ processing beyond helium processing or plasma processing (TBD)
    Cost-effective refurbishment (TBD)

## Slide 15: Study of Beam Enabled Particulate Transportation in CEBAF
The motion of charged dust particle in accelerators has been studied from 1990 to 1995 by P. Marin, H. Saeki, D. Sagan, F. Zimmermann, et al.
Charged dust particles can be picked up by the field of the electron beam.
  insulating surface (no space charge)
  conducting surface (space charge field)
Dynamic equations of the charged dust particle has been developed.
  Quadrupole or higher order magnetic field and RF field can be ignored.
  Horizontal motion is driven by the electron beam field and the image charge field.
  Vertical motion is driven by the electron beam field, image charge field and gravity.
  Longitudinal motion is driven by collisions with the electron beam and the magnetic dipole field.
  If the transverse size of the electron beam varies, it induces longitudinal force on the dust particle and the coupling of the transverse motion with the longitudinal motion of the dust particle.
Modeling and simulation for charged dust particles in CEBAF is in progress.
He Zhang, CASA

## Slide 16: Open Questions and Discussions
What is the reason for heavy gas loading in C100 cryomopdules as compared to C20/C50?
Is helium processing the right tool for recovering gradient in cavities operated at > 15 MV/m?
How particulates are transported in SRF linac beamline vacuum?
What is needed for dislodging resident particulates and transport them out of cavities in cryomodules installed in accelerators?

## Slide 17: Backup slides

## Slide 18: Low-Loss Shape Cavity Accelerating Beam
CEBAF 12 GeV Upgrade Cavity
1.5 GHz, Low-loss Shape, 53mm bore dia.
C. Reece, TTC Meeting, Feb. 28-Mar.3, 2011
J. Hogan et al., PAC2013, WEZAA2

## Slide 19: Radiation Reduction by Gradient Redistribution
Lower gradient of FE source cavities
Raise gradient of FE free cavities
0L04 at constant gradient
0L03 total gradient maintained at constant
Radiation reduced by 5 order of magnitude
With total accelerating voltage preserved
0L03-3 lowered by 3 MV/m
0L03-7 lowered by 3 MV/m
0L03-5 raised by 3 MV/m
oL03-6 raised by 3 MV/m
IBIC17, TH1AB1

## Slide 20: Observed Radiation Enhancement due to FE Electron Exportation across Cryomodules
0L04 on 0L03 off
Barely any count
0L04 off 0L03 on
Count rate ~ 1E4
0L04 on 0L03 on
Count rate ~ 1E6
IBIC17, TH1AB1