## Slide 1: Performance Recovery at CEBAF
Michael Drury
SRF Operations Support
Jefferson Lab

## Slide 2: Outline
CEBAF Description
Helium Processing
Cryomodule Refurbishment

## Slide 3: Background
5 C100 cryomodules
5 C100 cryomodules
20 C20 / C50 cryomodules
20 C20 / C50 cryomodules
CEBAF Accelerator
First large high-power CW recirculating e-linac based on SRF technology
In operation since 1995
Some of the oldest cryomodules have been in tunnel for ~25 years.
Maintaining performance is constant battle ~ 5 FTE’s / year
30 cryomodules per linac
  2 ¼ cryomodules in the injector
  25 ¼ C20 cryomodules (5 cell cavities)
    20+ years
  12 C50 cryomodules (refurbished C20’s)
    1 – 10 years
  11 C100 cryomodules (7 cell cavities)
    4 – 5 years

## Slide 4: Helium Processing
Proven technique for reducing field emission
There have been three mass He processing runs at JLAB
  1st in late 90’s
    Gauge utility of HeP for reducing arc rates
  2nd after Hurricane Isabel
    Uncontrolled warm up – increased field emission
  3rd summer of 2015 (314 cavities processed over 3 months)
    Increase energy reach for 12 GeV program
Going forward, we intend to process a few likely candidates every summer
Several rounds of mass processing over the years for performance recovery
  Inject 99.9999% pure Helium into the cryomodule beamline
  Partial pressure ~5E-05 torr
  Apply RF to process
    Operate Cavity at highest reasonable gradient
  Cryocycle the module to remove helium
    Cavity temperatures to ~30 K
  Before and after characterization with GM tube array
Note relatively low cost – 4 FTE’s plus ~$50K

## Slide 5: Helium Processing - Benefits
Arc Rate Reduction
Original C20 FPC Design suffers from periodic arcing in vacuum space between RF windows.
  Usable gradient reduction of 20 – 30% to minimize trip rates
C50 and C100 designs corrects this problem
For C50 and especially C100 style cryomodules:
Increased dynamic heat load becomes an issue
  Heat loads increase exponentially
  In C100’s heat loads can reach higher than piping design limits
    Pressure increase -> Temperature approaches lambda
    Cavity can quench at lower gradients than expected
  May drive vacuum degradation
  Can cause hardware failures and material deterioration over time

## Slide 6: Helium Processing - Results
Spring 2015- Estimated Energy Reach ~2.05 GeV / single pass
Needed energy reach of 2200 GeV / single pass
Mass Helium Processing most CEBAF cryomodules during summer 2015
  Total of 314 cavities
~201 MeV / pass gained by fall of 2015 enabling needed energy reach
Raised Field emission onset gradients by 0.9 MV/m on average
Lowered max dose rates by 2- 4 R/hr depending on measurement location

## Slide 7: Cryomodule Refurbishment
C50 Refurbishment Program
includes reprocessing of SRF cavities
  Attempts to eliminate field emission
  increase the nominal gradient from 5 MV/m to 12.5 MV/m.
  New “dogleg” couplers between the cavity and helium vessel flanges eliminate cold window charging and periodic arcing
  Modification of the Qext of the FPC will allow higher gradient operations.
new ceramic warm RF windows
improvements to the mechanical tuners.
Any damaged or worn components replaced.
More recently, the program includes
Investigations into improvement of magnetic hygiene
And particulate hygiene
Currently 13 C50 cryomodules installed with a goal of one per year
Increase in operating voltage 15 - 25 MV / module
Note Costs: ~0.5 – 1 M $ plus labor

## Slide 8: Summary
Addressed to major techniques for recovering gradient in CEBAF cryomodules
Helium Processing is a tool that has been used on several occasions during CEBAF history to recover gradient performance and has some other beneficial side effects.
  Most recent attempt netted 201 MeV per pass in the linacs.
  Another processing run being contemplated for this coming summer using a more targeted method
  Most recent attempt netted 201 MeV per pass in the linacs
Cryomodule refurbishment has been used to improve the design of existing cryomodules along with reprocessing of cavities.
  Gains of 15 - 25 MV per refurbished cryomodule