## Slide 1: Trouble Shorting of CW Operation of Superconducting Linac for Chinese ADS
Yuan He, Yongming Li, Xinmeng Liu, Zheng Gao, Guirong Huang, Weiming Yue, Shenghu Zhang
On behalf of Linear Accelerator Center
Institute of Modern Physics, Chinese Academy of Sciences
Supported by “Strategic Priority Research Program” of the Chinese Academy of Sciences.
TTC meeting, Feb. 6-9, 2018, Milan

## Slide 2: Outlines
Operation status of Chinese ADS front-end Demo Linac
Pickup-drop caused by field emission
Phase-error trips
Summary

## Slide 3: Overview of Chinese ADS Front-end Demo Linac
HEBT
DUMP
Beta=0.1
Injector II
IMP
IHEP
Beta=0.21
Beta=0.15
IMP
162.5 MHz Taper HWR
Goal: to demonstrate the technology of 10 mA CW beam of superconducting front-end Linac for ADS technology.
Design: 25 MeV, 10 mA, CW
IMP collaboration with IHEP 2011 ~ 2017
Supported by “Strategic Priority Research Program” of the Chinese Academy of Sciences.

## Slide 4: Operation of Chinese ADS Front-end Demo Linac
162.5 MHz HWR010
4
Commission Stage | First beam | First CW beam | E Max (MeV) | Beam time (hours) | CW beam time (hours) | Pulse Current Max (mA) | CW Current Max (mA) | CW Power Max (kW)
3
162.5 MHz HWR010
2
162.5 MHz HWR010
1
162.5 MHz RFQ
5
RFQ | Jun. 06, 14 | Jun. 21, 14 | 2.15 | 3007 | 105 | 18 | 11 | 23
TCM1 | Sep. 29, 14 | Nov. 24, 14 | 2.55 | 208 | 22.5 | 11 | 11 | 28
TCM6 | Jun. 06, 15 | Jun. 24, 15 | 5.30 | 438 | 11 | 10 | 4 | 21
Injector II | Sep. 09, 16 | Sep. 24, 16 | 10.2 | 735 | 30 | 10.6 | 2.7 | 26
Demo front-end Linac | May 23, 16 | Jun. 06, 17 | 26.2 | 355 | 27 | 12.6 | 0.3 | 5.4

## Slide 5: Cavities configuration of first CW operation
23 low beta cavities
AMPs for CM1 and CM2 are 12 kW
AMPs for CM3 and CM4 are 24 kW
RF power ranges from 1 kW to 6 kW due to different coupling Coef. and Epk.
Epk ranges from 18 MV/m to 38 MV/m
Qe of CM2-3 is far from designed value. It makes troubles.

## Slide 6: SRF specifications in the first commission
Chart: 
| 耦合器与腔真空 | 腔体温度 | 耦合器夹层真空 | Pt闪断 | 相位不稳脱环
CM1-CM3 脱环原因 | 28 | 2 | 8 | 28 | 419
Chart: 
| 耦合器与腔真空 | 腔体ARC | 腔体温度 | 耦合器夹层真空 | T型盒温度 | 失超快保护 | 氦压波动 | Pt闪断 | 相位不稳脱环
CM1-CM3 脱环原因 | 29 | 5 | 2 | 10 | 1 | 11 | 30 | 5 | 85
Trips during conditioning
Trips during beam commission

## Slide 7: Outlines
Operation status of Chinese ADS front-end Demo Linac
Pickup-drop caused by field emission
Phase-error trips
Summary

## Slide 8: Typical signals of pickup-drop
Pickup from
cavity
Forward
RF signal
Reflected
RF signal
250 us
Amplitude, phase, frequency loops activated, SEL

## Slide 9: Signals of pickup-drop
Generator-Drive Resonator
Self-Excited loop
Pt
LLRF output
Power forward
Pt
LLRF output
Power forward
Pt detection

## Slide 10: Experimental setup
Agilent Technologies DSO-X 3034A oscilloscope
350MHz, 4GSa/s, input impedance 50Ω
Vertical scale: 50 mV
Horizontal scale: 500 ns
CM1-2
CM1-1
CM1-3
CM1-4
CM1-5
CM1-6
CM1-2：Epk= 20.53 MV/m Gam：751 uSv/h
CM1-1：Epk= 18.94 MV/m Gam：355 uSv/h
CM1-3 : Epk= 21.82 MV/m Gam : 236 uSv/h
CM1-4 : Epk= 27.36 MV/m Gam : 364 uSv/h
CM1-5 : Epk= 23.27 MV/m Gam : 394 uSv/h
CM1-6 : Epk= 24.52 MV/m Gam : 132 uSv/h

## Slide 11: Pickup-drops Relative to FE
Monitor 12 hours for each point

## Slide 12: Reason of pickup-drop
Pt port
FPC port
Trajectory of FE electrons
beam port
beam port
The coupler and Pt ports are located at the strong electric area of coaxial structure.
Highest surface field areas were designed not to face the pickup ports.
FE electrons can see the windows of FPC and Pt.
Electrons on ceramic discharge when accumulating to a certain value
L
H
0
E

## Slide 13: Outlines
Operation status of Chinese ADS front-end Demo Linac
Pickup-drop caused by field emission
Phase-error trips
Summary

## Slide 14: Operation Reliability Test
13
ECR
HV
RFQ AMP
PS
Diagnostics
test
Cryo-plant
Mag-quench
2017-12-19-00：00 ~ 2017-12-22-00：00；72 hours operation test
CW RF and Pulse beam (w/o MPS)
18MeV@1mA@1Hz@10uS & 18MeV@10mA@1Hz@10uS

## Slide 15: Preliminary RAMI analysis
Operation time | Beam time | Down time | Availability
4050 min | 3566 min | 484 min | 0.88
 | ECR HV | RFQ AMP | SRF (incl. LLRF) | Cryo-plant | Power supply
Beam trips | 6 | 2 | 21 | 1 | 1
Down time | 53 min | 77 min | 78 min | 183 min | 100 min
Beam trip required by ADS demo facility | 
Beam trips（10s-5min） | 2500/year
Beam trips（>5min） | 300/year
Availability | 80%
Mean time between failure MTBF (min) | Mean time to repair MTTR (min) | Beam trips (10s-5min) | Beam trips (>5min)
111.4 | 16.1 | 20 | 10
Some long time repair failures (> 5 min), such as HV, AMP, Cryo-plant, PS, have very clear reason, can be avoided in the nest stage.
10s-5min-trip number is less than the requirement. Root cause of trips of SRF are still under investigation.

## Slide 16: MPS Trigs of phase-error during CW Beam
Statistics of MPS trig numbers
phase error trips（） beam: 0.2mA CW Operation time: 22 h
Chart: 
| cm1-1 | cm1-2 | cm1-3 | cm1-4 | cm1-5 | cm1-6 | cm2-1 | cm2-2 | cm2-3 | cm2-4 | cm2-5 | cm2-6 | cm3-1 | cm3-2 | cm3-3 | cm3-4 | cm3-5 | cm4
Phase Trips | 1 | 11 | 1 | 2 | 0 | 2 | 0 | 0 | 30 | 1 | 9 | 1 | 0 | 0 | 1 | 0 | 0 | 13
Ep(MV/m) | 18 | 18 | 20.09 | 27 | 22.44 | 24.74 | 29.94 | 28.64 | 30 | 30 | 22.14 | 18 | 12 | 12 | 20 | 20.07 | 13.95 | 23
Weakness FPC coupling of CM2-3, at least 1/3 of the others, means narrow bandwidth, might be the reason.

## Slide 17: Trips with phase vibrate w/o open loop
Phase vibrate with loop-close

## Slide 18: Outlines
Operation status of Chinese ADS front-end Demo Linac
Pickup-drop caused by field emission
Phase-error trips
Summary

## Slide 19: Summary
Multipacting and Field emission
  Fundamental Power Couplers （coupler operation and activity at IMP, Tiancai Jiang）
    Multipacting? -> contamination -> FE -> ceramic window broken -> worse case
  Pickup couplers
    FE -> discharging -> LLRF instability
Phase-error trips
  Tuner Hysteresis (C-ADS tuner system, Tiancai Jiang)
  Microphonic and Vibration (electromagnetic-mechanical vibration , Zheng Gao)

## Slide 20: Thanks for your attention
Acknowledgement:
ADS accelerator team at IMP and IHEP
Helps from PKU, SINAP, LBL, JLab, and Review experts