## Slide 1: Power Coupler in Pulsed Operation ~higher peak power & longer RF pulse~
Kirk
Special thanks to Matsumoto-san, C. Arcambal, E. Cenni, W.D. Möller, W. Kaabi

## Slide 2: Outline
Motivation
Specification for each power coupler in pulsed operation
Necessary RF power at 35 MV/m operation in ILC
Issues for higher peak power and longer RF pulse
Necessary ceramic property for longer RF pulse
Summary

## Slide 3: Motivation
Higher peak power
  Maybe necessary at 35 MV/m operation by N-infusion in ILC
Longer RF pulse
  Quasi-CW operation
P
t
P
t
P
t
P
t
Higher peak power
Longer RF pulse

## Slide 4: Specification of power coupler in each project
Project | ESS | E-XFEL | STF-2 | ILC
Type | Coaxial structure |  |  | 
# of RF windows | 1 | 2 | 2 | 2
# of couplers | 120 | 808 | 12 | ~16,000
RF frequency | 704.42 MHz | 1.3 GHz | 1.3 GHz | 1.3 GHz
RF power in beam operation | 1.1 MW | 120 kW (195 kW at max.) | ? | 189 kW
RF pulse width | 3.6 msec | 1.40 msec | 1.65 msec | 1.65 msec
RF repetition rate | 14 Hz | 10 Hz | 5 Hz | 5/10 Hz
RF duty | 5 % | 1.4 % | 0.8 % | 0.8/1.6 %
Set position of Qext | 7.6 x 105 | 4.6 x 106 | 5 x 106 | 5.5 x 106
Range of Qext | fixed | 106 ~ 107 | 3~7 x 106 | 106 ~ 107
Cooling for inner conductor | Water |  |  | 
※ C. Arcambal, E Cenni
※ W.D. Möller, W. Kaabi

## Slide 5: Power couplers in pulsed operation
ESS Coupler
E-XFEL Coupler
STF-2 Coupler
ILC/TDR

## Slide 6: Necessary RF power at 35 MV/m operation in ILC
Matsumoto-san estimated necessary RF power for CM operation at 35 MV/m
 | 31.5 MV/m | 35.0 MV/m
RF power / coupler | 189 kW | 210 kW
QL | 5.46 x 106 | 6.07 x 106
Filling time | 927 μsec | 1030 μsec
RF pulse width | 1.65 msec | 1.76 msec

## Slide 7: Klystron, modulator, circulator…
Multi beam klystron
Circulator
10 MW  11 MW (10% higher)
1.65 msec  1.76 msec (7% longer)
Discharge issue
(SF6 with higher pressure?)
Marx modulator
We have to think about not only power coupler, but also klystron and waveguide/circulator systems!

## Slide 8: Issues to be considered
Higher peak power
  Discharge in waveguide/circulator systems
Longer RF pulse
  Thicker copper plating (30μm  50μm?)
  Lower tanδ ceramic

## Slide 9: Necessary ceramic property
Longer RF pulse operation needs ceramic with lower dielectric loss tangent.
RF duty | ~1% | ~10%
Percent of Al2O3 | > 95% | > 99%
Surface resistivity | 1014~15 Ω/□ @25℃ | 1014~15 Ω/□ @25℃
Relative permittivity | 9~10 @1GHz | 9~10 @1GHz
Dielectric loss tangent | ~10-4 @1GHz | ~10-5 @1GHz
Secondary electron emission coefficient | ~2 (5 as production) | <2 (5 as production)
Specification for secondary electron emission coefficient is not clear.

## Slide 10: SEM for ceramic study
SEM
19mm (dia.) ceramic samples
Many ceramic samples were fabricated to measure the secondary electron emission coefficient.
We are preparing the “improved” scanning electron microscope (SEM) in KEK.
Vendor A
(sample #1)
Vendor B
(sample #2)
Vendor C
(sample #4)
Vendor C
(sample #5)
We can start the measurement from March!

## Slide 11: Summary
Higher peak power operation
  Should pay attention for discharge in waveguide/circulator systems
  Should upgrade klystron/modulator systems
Longer RF pulse operation
  Thicker copper plating
  Lower loss tangent ceramic

## Slide 12: Thank you very much for your attention
Special thanks to Matsumoto-san, C. Arcambal, E. Cenni, W.D. Möller, W. Kaabi

## Slide 13: ILC-TDR (for Power coupler specification)
These figures are shown on Page 35 in ILC-TDR Vol.3 Part-II.