## Slide 1: High-Resolution Heterogeneous Digital PET Brain Phantom based on the BigBrain Atlas
M. A. Belzunce and A. J. Reader
School of Biomedical Engineering and Imaging Sciences
Faculty of Life Sciences & Medicine
PSMR 2018, 23rd May 2018

## Slide 2: Outline
  Motivation
  Problems in available digital brain phantoms
  The BigBrain dataset
  A method for the creation of radiotracer dependent digital brain phantoms
  A high-resolution heterogeneous digital brain phantom for [18F]FDG
  Simulation and reconstruction results for the [18F]FDG phantom
  How to get and use the phantoms
  Conclusion

## Slide 3: Motivation
Scan Simulation
  The evaluation of image reconstruction algorithms needs realistic simulated data sets where the ground truth is known
  Brain phantoms that emulate a radiotracer distribution are then needed to assess the accuracy of image reconstruction and post-processing algorithms in specific tasks
  MR-guided reconstruction methods have attracted new attention since the introduction of clinical simultaneous PET-MR scanners, however the evaluation of MR-guided reconstruction methods is not completely satisfactory
Image Reconstruction
MLEM
Method 1
Method 2
Problem 1
Realistic ground truth?
Problem 2
Is this metric important in clinical applications?
Problem 3
PET-MR simulated data sets are too optimistic

## Slide 4: Problems of Available Digital Brain Phantoms
  Most of the available digital brain phantoms are usually of limited spatial resolution making them not ideal to evaluate quantification errors due to partial volume effects (PVE)
  They are piece-wise constant and usually generated from segmented MRI images of the brain
    There is a controversy about the truthfulness of MR-guided reconstructions and using PET phantoms created from segmented MRI images is not beneficial to improve confidence in this methods
T1-weighted image
Brainweb phantom (Collins et al, IEEE TMI 1998 )
Example of a simulated PET-MR data set for [18F]FDG:
PET phantom
The MRI image is segmented in tissue types and activity values are set to have a contrast of 4:1 between GM and WM
Piece-wise constant
(GM uniform)
Perfect match between PET and MR boundaries

## Slide 5: A New high-resolution heterogeneous digital brain phantom
We propose a new PET digital brain phantoms that overcomes most of the problems mentioned previously by using the BigBrain data set:
The PET phantom is created from ultra high-resolution histology images (100 to 400 μm) and not from an MRI image
The activity values in the phantom are region-dependent in order to match the particular distribution of a given radiotracer
A real MRI image that corresponds to the brain of the histology images is available
Heterogeneous
High-resolution
Realistic radiotracer distribution
Boundaries of PET and MRI phantoms do not match perfectly
Biological
information
MRI Phantom
PET Phantom
MRI scan
Emulation of a radiotracer distribution

## Slide 6: The BigBrain Dataset
The BigBrain dataset is a free accessible high-resolution 3D digital atlas of the human brain created by teams in Montreal Neurological Institute and Forschungszentrum Jülich (https://bigbrain.loris.ca/) (K. Amunts et al. Science 2013)
Katrin Amunts et al. Science 2013;340:1472-1475
The brain model was created by slicing a paraffin-embedded brain (65 years old man with no neurological or psychiatric diseases in clinical records at time of death) and acquiring 7400 sections at 20-μm thickness stained for cell bodies
MR imaging (MPRAGE sequence, 0.4 x 0.4 x 0.8 mm3 resolution) was formed prior to histological processing to obtain an undistorted reference for further 3D reconstruction of histological sections
The resampled 3D stack of BigBrain sections at resolutions of 100 μm, 200 μm and 400 μm isotropic were normalized to MNI space.
stained histological volume
(MNI space)
tissue classified volume
(MNI space)
MRI
(histology space)

## Slide 7: Estimation of a Radiotracer Specific Phantom
In order to create a realistic PET phantom, the voxel values in the phantom should match the distribution and contrast of the radiotracer to be simulated
Depending on the biological target of the radiotracer, the uptake in different regions of the brain would be different
We propose a method to estimate uptake values in the phantom that matches real data from an specific radiotracer, based on cell-body densities, tissue types and standard regions of the brain
[18F]FDG
Phantom
PET Scan
low resolution, noise
Cell-body Density
Tissue Type
Brain Atlas

## Slide 8: Estimation of a Radiotracer Specific Phantom (II)
The tracer uptake in each voxel of the phantom is obtained by maximizing a similarity metric between a single scan (i.e. [18F]FDG) and the estimated phantom:
Model proposed for the estimation of the phantom from parameters θ :
The objective function was optimized with the EM algorithm
-Kullback-Leibler distance
θ : vector with the relative uptake value for every atlas region in the brain and for a specific tissue type
m: scan image
T: matrix that models tissue class for each voxel
H: Gaussian filter that models the resolution of the PET scan or template
A: is a matrix that has as many rows as voxels in the phantom and as many columns as uptake parameters to be estimated.
C: cell-body density
(diagonal matrix)

## Slide 9: Implementation
All the data set used were registered to the BigBrain volumes and normalized into MNI space
To define the regions within the brain we used the probability maps of the Hammersmith Atlas (n30r95)
An uptake value was estimated for each tissue type (8 types) and region (95 regions + 11 ad hoc small regions) -> 848 parameters in total

## Slide 10: Results
High intensity values in small regions
(ill-posed problem)
Artificial small regions due to misregistration

## Slide 11: Penalized Estimation of the Parameters
Objective function
Quadratic regularization to penalize large intensity differences between close ROIs, OSL MAP-EM optimization
Penalty term
ξ: inverse of the distance between the centroids of ROI j and k

## Slide 12: Post-processing and PET-MR Dataset Generation
The skull was added to the PET phantom after the estimation of the activity distribution
The MR T1-weighted image was registered to MNI space using the SyN algorithm (BB Avants et al, Med Image Anal 2008)
A pseudo CT was created from the T1-weighted image using the UCL method (N Burgos et al, TMI 2014)
An attenuation map for 511 keV was generated from the pseudo CT
CT
μMap
convert into attenuation map
Notes: SyN algorithm (symmetric diffeomorphic image registration)

## Slide 13: MRI Image Registration
MRI
PET Phantom
Fused Images

## Slide 14
[18F]-FDG Full Data Set

## Slide 15: Example of Simulated and Reconstructed Data
The original patient data was compared with simulated data of the proposed phantom and a Brainweb based phantom
A dataset was simulated using the following model:
Image reconstruction with MLEM and MR-guided MAP (Lange prior, Bowsher similarity weights and two different regularization hyperparameters)
f: phantom image
H: scanner resolution (Gaussian kernel)
X: geometrical projection (Siddon)
A: attenuation factors
N: normalization factors
s: scatter
r: randoms

## Slide 16: Example of Simulated and Reconstructed Data

## Slide 17: How to Get the [18F]FDG Dataset
Dataset available in zenodo: 10.5281/zenodo.1190598
Links and information on the full dataset will be found at https://pet-mr.github.io/
The dataset is available at 400 μm isotropic voxel sizes
Formats: NIfTI, binary and MATLAB .mat
In the future:
      Simulated dataset for the Siemens
      mMR scanner
      MLEM reconstructed images
      A set of functions to evaluate
      quantitatively reconstruction methods
      Datasets for other radiotracers

## Slide 18: Conclusions and Discussion
A method to create high-resolution heterogeneous digital brain phantoms was presented
Using this method a realistic [18F]FDG PET-MR dataset was created and is publicly available
A limitation of this phantom is that the histology images used contain the cell-body density in the brain, which is not directly related to glucose metabolism
This limitation, only in effect at a very low scale, is compensated for by using an atlas and a scan data of the radiotracer of interest to estimate the uptake in different regions of the brain
The MR image boundaries does not match perfectly the histology images, however there are two possible source of errors: limitations of the MRI scan and misregistration

## Slide 19: Acknowledgements
This work was supported by the Engineering and Physical Sciences Research Council [EP/M020142/1]; and by the Wellcome/EPSRC Centre for Medical Engineering [WT
203148/Z/16/Z].

## Slide 20: THANKS FOR YOUR ATTENTION