## Slide 1: Task 2.4 Status of Luminosity Monitor
Philip Bambade
LAL-Orsay
JENNIFER general meeting KEK 6 October 2017
LAL group:
Cécile Rimbault, Didier Jehanno (elec. engineer), Yann Peinaud (mech. engineer)
Dima El Khechen (PhD student  CERN/FCC-ee), Pang Chengguo (PhD student)
Viacheslav Kubytskyi (postdoc), Salvatore di Carlo (postdoc), P. B.
KEK group:
Sadaharu Uehara (Belle II, ZDLM), Yoshihiro Funakoshi, Takashi Kawamoto, Mika Masuzawa, Toshiyuki Oki + several other experts from SuperKEKB

## Slide 2
Task 2.4 Deliverables
Release optimized sensor configuration and readout for accelerator feedback (month 36)
 Due in March 2018 (during Phase 2 Commissioning)
Two intermediate steps:
Deploy first diamond sensor prototype for synchronization test during 2015 single beam commissioning with nuclear bremsstrahlung background (month 6)
Deploy full set of diamond sensors for luminosity measurements during first commissioning and tuning of colliding beams in 2016 (month 18)
 Both done during Phase 1 commissioning in 2016
Task 2.4 Secondments
15 person-months  already used 92.2%
 Remaining 7.8% (16 + 19 days) will be used in 2018

## Slide 3
Main goals of luminosity monitor
Input to horizontal IP orbit feedback  Train Integrated Luminosity (TIL)
Integrated bunch-by-bunch luminosities  Bunch Integrated Luminosity (BIL)
Comparison with absolute Belle II luminosity to probe QED screening effects in radiative Bhabha process at vanishing angle (from the nm level vertical beam size)
Specifications
TIL  10-3  10-2 @ 1 kHz 2500  BIL  10-2 @ few Hz
Method
-  0.2 barn cross section of radiative Bhabha process at vanishing scattering angle
- e+ detection  10 meters after IP in LER
-  detection  30 meters after IP in HER
- 140 m and 500 m sCVD diamonds with fast charge and current amplifiers
- ZDLM (based on Cherenkov + scintillator)
- 1 GHz ADC + FPGA readout to compute TIL and 2500  BIL on-line
- DAC to output TIL to SuperKEKB lock-in amplifier for feedback control (initially…)
- EPICS and GUI for convenient TIL and 2500  BIL transfer, display and “on-line” analysis
- Data storage and archiving for off-line analyses

## Slide 4
New specially built 45 “window shape” beam pipe to be installed in LER in January 2018 (Kanazawa-san, SuperKEKB)
Yann Peinaud
Chengguo Pang
Window + tungsten radiator boosts detected Bhabha e+ fraction up to 2%
 100  rate with normal beam pipe
Optimization with GEANT4

## Slide 5
Photon tracking in HER
Original library developed for photons tracking
A photon coming out with zero angle from the IP hits the beam-pipe at s=28.01 m
The majority of the photons hit the antechamber
Exit point
Salvatore di Carlo

## Slide 6: GEANT4 description of HER antechamber
The geometry of the beam-pipe has been reconstructed in GEANT4.
The sensors are located on the side and on the top and bottom of the antechamber
The number of photons tracked in this simulation is 500,000
x
y
TOP
SIDE
Salvatore di Carlo
BOTTOM
Notes: Sigma1=sigma2 e dare la definizione di probability distribution
𝑓=250 𝑀ℎ𝑧 collision frequency
𝑇=1/𝑓=4𝑛𝑠 interval between to bunches

## Slide 7: Preliminary results for phase 2.2
SIDE
TOP
About 1% of the photons are detected with cut at 0.1 MeV
The mean deposited energy per detected photon is about 0.4-0.5 MeV on the top-side sensors
The photons deposit more energy on the top sensor by a factor 1.2
Expected precision for phase 2.2 is 5% in 10 ms
Expected precisions for phases 2.3-2.4 and 3 being computed  should be much better due to larger beam angular divergence at the IP
RATIO
Salvatore di Carlo
Notes: Sigma1=sigma2 e dare la definizione di probability distribution
𝑓=250 𝑀ℎ𝑧 collision frequency
𝑇=1/𝑓=4𝑛𝑠 interval between to bunches

## Slide 8
detectors
DAQ STATUS & PROGRESS
LER+HER
CVD 140µm : OK
Amplifier : OK
Remote Control : OK
Mechanics : in progress
cables
DAQ
ADC 1GSPS : OK
FPGA : firmware OK, tested 50%
DAC : 8-channels (preliminary)
EPICS Client
b2epics
bdaq
Template GUI for EPICS Client with
to be developped
DAQ rack: in progress
ADC
x4
FPGA
firmware
TIL
BIL
SERVER (Linux)
DAC
x8
analog
Server : in progress
● Deliver Train and Bunch Integrated Luminosities : TILx2 (LER, HER), BILx5120x2 (LER, HER)
TIL
LER (1) and HER (1)
Integration period : 1ms-3600s
ZDLM-like counting included
Resolution : 1 train, 10µs
BIL
LER (1) and HER (1)
Resolution : bucket (2ns)
Integration period : 1ms-3600s
5120 values : 5000 bunches (max) + 120 (Space Charge Reset)
● TIL and BIL are derived from CVD signal AMPLITUDE acquisition at BUCKET (2ns) resolution
● The DAQ is configured by the SERVER (Linux) which includes the protocol
● Provide EPICS GUI for KEK Clients : TIL, BIL configuration + data Display/Archive
● Provide 8x Analog Outputs for : debug, feedback use, …
EPICS : OK in LAL domain
Estimated Time of Development : end of 2017/11
network
Roll-In position
Network is used to :
SEND Luminosity EPICS PVs (TIL, BIL,…)
RECEIVE SuperKEKB/BELLE2 PV (Current,
Pressure, Fill Pattern, …)
(example next slide)
Since 04/11
2017.06.16
LAL Monitor digital DAQ for Phase 2/3
Didier Jehanno

## Slide 10: Relative precision can be achieved in LER
“Realistic” Monte Carlo Signal sequence and DAQ sampling
not so sensitive to phase
When integrating in every 1ms
6.2
7
Chengguo Pang

## Slide 11
Summary status and further prospects
ZDLM and LAL luminosity monitors will be ready to measure first luminosities (integrated and bunch-by-bunch) during Phase 2
Horizontal feedback is only expected to be needed during Phase 3
Precision sufficient ( 1-2% @ 1kHz) from LER to stabilize the horizontal orbit at the IP from initial to ultimate luminosities
Initial specs of 0.1% @ 1 kHz will cause radiation damage on sCVD diamond sensors in the current design with a fully digital DAQ
HER Bhabha signal efficiency estimate now in good progress
Simulation of feedback controller to re-evaluate specs under way
LER and HER Phase 2/3 single backgrounds investigated in detail  coupling with BEAST effort, also in longer term ?
Simulation of ZDLM ?
Discuss IP ground motion monitoring in operation with SuperKEKB
Upgrade to fully digital dithering feedback ( LAL FPGA) ?
LAL (4+ people) will support Phase-2 commissioning at KEK

## Slide 12
Further topics

## Slide 13: Potential radiation damage
Phase-3
Phase-2
To reduce the dose rate:
Reduce relative precision
Use thicker diamond DS
Use charge amplifier with lower noise
Chengguo Pang

## Slide 14: Analysis of relative luminosity precision needed for dithering based orbit feedback
Goal of lock-in amplifier :
Minimize Fourier component in luminosity at dithering frequency
Maximize it at twice the dithering frequency
Dithering frequency: 77Hz
Luminosity loss

## Slide 15
Use toy Monte Carlo to compute probabilities of fake orbit offset detection as function of correct detection (from statistical errors)
Chengguo Pang
2% relative luminosity measurement @ 1 kHz
 1 % confusion probability for > 90% efficient detection

## Slide 16: Single beam backgrounds during Phase2 (preliminary)
Bremsstrahlung
Touschek
Phase2.2: 0.64mA, 1576 bunches, y/x coupling = 5%, =
Detected Bhabha rate in diamond (140 DS):
Background rate in diamond(140 DS):
S/N 600
Phase2.3: smaller beam size  S/N 1000
Almost no observed losses from Coulomb scattering
Chengguo Pang

## Slide 17
Backup slides

## Slide 19
ZDLM / LAL Monitors
 Same Location in LER and HER, downstream (after IP)
Sharing same mechanical pillars
Distance from IP : LER / 13 m HER / 30 m
 Same positionning along beam pipe, H plan, few mm away
 Different detector types
ZDLM
LAL-M
Čerenkov, Scintillator
Diamond sCVD

## Slide 20
508.887 MHz
1.965 ns
RF
t
t
BUCKET
 For all couples Sample (peak) and Sample (baseline) :
Calculate the DIFFERENCE = Amplitude of the pulse
Make AMPLITUDE = 0 if < THRESHOLD (typ. 10mV)
5120 AMPLITUDES
THRESHOLD
peak
t
SAMPLING
1017.774 MHz
baseline
COUNT +1 if AMPLITUDE > THRESHOLD
5120 COUNTS
 For ONE train (round-trip 10.06 µs), we obtain
x2
DIAMOND
signal
LAL Monitor digital DAQ
Didier Jehanno

## Slide 21
LAL Luminosity monitor : test setup for Phase 1 commissioning
HER ~ 30 m  photon
LER ~ 11.9 m  positron
500 mm diamond sensors

## Slide 22
Data acquisition for Phase 1 commissioning
beam background measurement  validation
Data processing
→ Define waveforms and save them
→ Extract maximum of signal (total
integrated charge)
→ Position in time
→ FWHM
→ Save in .mat files
→ Merge them to EPICS

## Slide 23
Beam gas Bremsstrahlung
→ Inelastic Coulomb scattering
→ Beam particles pass by EM of nucleus of molecules of residual gas
→ Emission of photon → particle loses energy
→ Particle is lost downstream of emission point
Loss vs (current x pressure)
→ Scattering and loss rates are proportional to beam current and vacuum pressure

## Slide 24
Touschek scattering
→ Scattering of beam particles upon each other
→In CM; pinit1, 2 = (±px,0,0)
pscat1, 2 = (±px sinχ cosφ, ±pxcosχ, ±px sinχ sinφ)
→ In Lab frame: maximum momentum transfer : DE= g x px
→ One particle loses energy and the other gain energy
→ Scattering and loss rates are proportional to I2 and inversely proportional to the beam size
Energy vs emission position
3.7%
analytic calculation

## Slide 25
Physical processes interfaced in SAD tracking code by Y. Ohnishi to simulate overall beam loss in SuperKEKB rings
Simulation improvement: scattering resolution
Scattering @ quad
Scattering @ all elements
Slicing drifts (10 cm) and bends (15 cm)
Default code
Energy
vs emission point

## Slide 26
→ Vacuum bumps were performed upstream of the IP
→ Fraction of losses in the sCVD from scattering regions were calculated and compared to data
→
4-12 m
17-35 m
4-12 m
17-35 m
Vacuum bumps in LER
Pressure profile
Loss profile
total loss simulated in the sCVD, when pressure everywhere in the
ring is equal to that of the maximum of the bump at the given section
is the loss in the sCVD at the maximum of the bump
4~12 m
17~35 m

## Slide 27
→ The vertical beam size sy was varied adjusting
the x-y coupling (“Emittance Control Knob”)
→ Losses in the sCVD were fitted as a function of
the inverse vertical beam size (sy-1)
→ Loss = Bremsstrahlung + Touschek  s-1y
Vertical beam size scans
720 mA
540 mA
180 mA
360 mA
900 mA
1000 mA
(constant term) (slope)

## Slide 28
→ Data is larger than simulation by factor about 3
Bremsstrahlung losses (from constant terms of vertical beam size scans)
simulation
data
→ Factor 3 ± 1.5 was estimated by simulation for KEKB
by vacuum group
→ The pressure measured at Gauges should be multiplied
by  3 to represent the pressure at center of beam pipes

## Slide 29
Touschek losses (from slopes of vertical beam size scans)
Measured slopes combined after quadratic extrapolation to I = 1 A to compare with simulation
→ simulation / data = 1.7 ± 0.74
(preliminary)
Uncertainties
(for future improved comparison)
Statistics (both data and simulation)
Beam size measurement considered reliable in vertical but not in horizontal
Emittance growth with beam current due to intra-beam scattering was neglected

## Slide 30
Conclusions from Phase 1
Successful real-scale test of LAL and KEK fast luminosity monitor hardware during 2016 single beam commissioning
Measured single beam backgrounds at LER luminosity monitor location; validated simulation to extrapolate to Phase 2 & 3 :
- LER Bremstrahlung rates consistent with modeling after taking
into account a factor x 3 for the pressure (based on KEKB…)
- LER Bremstrahlung >> LER Touschek
- LER Touschek rates have 1.7 +/- 0.7 discrepancy with modeling
Single beam background rates in HER (Bhabha photons) << in LER (Bhabha positrons), due to absence of final focus to create sizeable divergence
Detailed understanding of data/simulation comparison requires careful handling of SAD-interface to track scattered particles (photons  geometry, apertures ; positrons  optical transport) and constant communication with machine group

## Slide 31: 140 diamond test for Phase 2/3
Landau distribution of energy deposited and signal amplitude- 140 DS
G4 simulation: 58.2KeV
Experiment: 3.35mV
G4 simulation
Test with Sr-90
May lead to pile up
scintillator
diamond

## Slide 32
Coulomb scattering
→ Elastic scattering of particle beams on the nucleus of residual gas molecules
→ Particle receives a transverse kick and is lost downstream the emission point
→ Transverse offset of particle lost at position B and emitted at A depends on

## Slide 33
simulation
data
Calibration
→ Maximum of signal of Data were fit by “Landau”
→ A cut at 6 mV separates signal from noise
→ In simulation: minimum of 50 KeV ( > 3s of noise )
→ MPV= 11.6 mV in data
→ MPV= 9.2 mV in simulations
→ 11.6/9.2 = 1.3  threshold is at ~ 4.7 mV for simulations
11.6 mV
9.2 mV

## Slide 37: Luminosity monitoring with nano-beam concept Fast & slow variations at IP require feedback corrections
Beam-beam deflection (SLC, KEKB,…) for fast vertical motion
Luminosity feedback by “dithering” (PEP-II) for slower horiz. correction
Luminosity tuning with optical knobs (SLC, FFTB, ATF2) to maintain small spot sizes ( time scales of  hours ? )
Dy at IP=
 5nm  1/10sy*
BPM
IP
BPM
Dy at BPM=  1.3mm
x
Luminosity
Vertical vibration  25-100 Hz
Sampling (BPMs)  32 kHz
Horizontal motion  1 Hz
Modulation freq. f0  77 Hz
Sampling (lumi. meas.)  1 kHz
 minimize f0 output component


2f0
f0

## Slide 38
Radiative Bhabha at vanishing scattering angle
luminosity monitoring
major background source from induced particle losses after IP
  250 mbarn (E > 1% Ebeam )
Luminosity monitoring specs
Relative measurements
10-3 in 1 ms over all bunches (“dithering”)
10-3 in  1 s for each 2500 bunch  4ns
(for nominal luminosity)
Non luminosity scaling contamination < 1% (e.g. beam gas bremstrahlung and Touschek losses)
Should also work for low initial luminosity
Positron
energy
LAL & KEK
re-evaluate

## Slide 39
ZDLM
LAL Monitor
LER
2015.12.20
PMT
Det.
Amp.
Diamond
Beam pipe
ZDLM / LAL Monitors
PHASE-1

## Slide 40
ZDLM
Beam pipe
ZDLM / LAL Monitors in Phase 2
IP
LAL Monitor
radiator
to E-HUT
F-8
Window design : KANAZAWA-san
LER
45°
54.2 cm
x00V
12V
HV
LV
CH 2
CH 1
CH3
H-scan
ČERENKOV
Čerenkov
PMT
S
-xkV
HV
SCINTILLATOR
passive
Scint.
to E-HUT
F-9
C
few mm

## Slide 41
Diamond
Amplifier
Charge or Current
140-500µm
CH 2
CH 1
ZDLM
LAL Monitor
to E-HUT
F-8
few mm
IP
HER
Beam pipe
CH3
x00V
12V
HV
LV
PMT
S
C
-xkV
HV
SCINTILLATOR
passive
Scint.
to E-HUT
F-9
Čerenkov
ČERENKOV
H-scan
ZDLM / LAL Monitors in Phase 2

## Slide 42
508.887 MHz
1.965 ns
RF
t
t
DIAMOND
signal
BUCKET
THRESHOLD
Must adjust the SAMPLING ruler to the EVENT=RF ruler
RF (bucket) ruler
REFERENCE
SAMPLING ruler
RF ruler
peak
t
SAMPLING
1017.774 MHz
baseline
LAL Monitor digital DAQ
x2

## Slide 46
Tolerance to x depends on crossing angle and βy (IP), not on x
L = 1 x 1034 cm-2 s-1
L = 1 x 1035 cm-2 s-1
L = 8 x 1035 cm-2 s-1
K. Ohmi : “nano-beam scheme”
M. Masuzawa :
recent vibration measurements
for x  10 m
tolerance for Lnominal
frequency  0.1Hz
 10 x slower dithering specs
For x  100 m tolerance for LPhase 2 frequency << 0.1Hz
 even looser dithering specs
preliminary

## Slide 47: Relative precision needed
After the lock-in amplifier, we want to :
Minimize the amplitude of base frequency
Maximize the amplitude of double frequency
Dithering frequency: 77Hz
Dithering amplitude/
Luminosity loss
Well collimated
With a small offset
0.4% luminosity lost !
For base frequency case:
when ratio is larger than 1, which means we can observe the amplitude change due to offset.
In this case, a relative precision better than 1.3% in 1ms is sufficient for luminosity monitoring.
R|x=0.1, p=0.1

## Slide 48: Back-up