## Slide 1: Muon colliders

## Slide 2: Outline
Muons case
Muon accelerators challenges:
  muon production
  emittance reduction via cooling
  high-gradient acceleration
Conclusions
Ancora in fase di R&D o idee, ancora molto lontani rispetto al Linear Collider o Circular collider

## Slide 3: Muons: a long history of development
Rob
Ryne
C.Rubbia
proposal
2015

## Slide 4: Muon based colliders great potential
  IF THE MUON BEAM NOVEL TECHNOLOGY
  CAN BE DEMONSTRATED TO BE FEASIBLE
As with an e+e− collider, a m+m− collider offers a precision probe of fundamental interactions without energy limitations
By synchrotron radiation (limit of e+e− circular colliders)
By beam-strahlung (limit of e+e− linear colliders)
Muon Collider is the ideal technology
to extend lepton high energy frontier in the multi-TeV range
with reasonable dimension, cost and power consumption
Muon based Higgs factory takes advantage of
a strong coupling to Higgs mechanism by s resonance

## Slide 5: Muons: Issues & Challenges
Limited lifetime: 2.2 ms (at rest)
    Race against death: generation, acceleration & collision before decay
    Muons decay in accelerator and detector
      Shielding of detector and facility irradiation
      Collider and Physics feasibility with large background environment?
        Not by beamshtrahlung as with e+/e- but by muon decay (e, n)
        Reduced background at high energy due to increased muon lifetime
    Decays in neutrinos:
      Ideal source of well defined electron & muon neutrinos in equal quantities whereas Superbeams by pion decay only provide muon n:
      The neutrino factory
      concept
Generated as tertiary particles in large emittances
    powerful MW(s) proton driver and pion decay
    novel (fast) cooling and acceleration methods
  Development of novel technologies
  with key accelerator and detector challenges



p +  m + + nm
p -  m - + nm

## Slide 6: Muon beams specific properties
Muons are leptons like electrons & positrons
but with a mass (105.7 MeV/c2) 207 times larger
Negligible synchrotron radiation emission (a m-2)
  Multi-pass collisions (1000 turns) in collider ring
    High luminosity with reasonable beam power and wall plug power consumption
      relaxed beam emittances & sizes, alignment & stability
    Multi-detectors supporting broad physics communities
    Large time (15 ms) between bunch crossings
  No beam-strahlung at collision:
    narrow luminosity spectrum
  Multi-pass acceleration in rings or RLA:
    Compact acceleration system and collider
    Cost effective construction & operation
  No cooling by synchrotron radiation in
  standard damping rings
    Requires development of novel cooling method



3 TeV


## Slide 7: Synchrotron radiation
electrons Uo (GeV) = 9 10-5 E4(GeV)/r(m)
muons Uo (GeV) = 5 10-14 E4(GeV)/r(m)
protons Uo (GeV) = 7 10-18 E4(GeV)/r(m)
Uo = 5.5 x 10-18 g4/r
r =3000 m (LEP/LHC tunnel)
@ Uo/Eb ~ 10% electrons are limited to ~ 150 GeV (Uo = 15 GeV)
@ Uo/Eb ~ 10% muons can go up 200 TeV (Uo = 20 TeV)

## Slide 8: Multipass
B= 16 T
E ≈ P(GeV) = 0.3 B(T) r (m)
Lacc = 2p r 3/2(dipole filling factor)
Lacc (m) = 3 p E/[0.3 B(T)] ≈ 30/B(T)
decay length = gbc tm = 6000 E
tm = 2.2 ms
3000 turns
Lifetime (machine turns) = decay length / Lacc = 200 B(T)
Luminosity and RF acceleration can benefit of this factor !

## Slide 9: Luminosity
N(p)= s(p) N(e+) r(e-) L
N(e+) number of e+
r(e-) target electron density
L target length
N(p)= s(p) N(e+)N(e-)/A
N(e+) number of e+
N(e-) number of e-
A area of intersection
dN(p)/dt= s(p) N(e+) N(e-) /A f
f intersection frequency
L=N(e+) N(e-) /A f
Notes: efficienza massima che si puo’ avere: processo che domina e’ il radiative Bhabha (e+ su e-, senza nuclei)
sigma*L*rho
radiative Coulomb scattering (brems) e’ sui nuclei
mettendoli insime il processo va come 10^-25 cm-2 *Z^2

## Slide 10: Muon Colliders potential of extending leptons high energy frontier with high performance
Muons
Muons
Linear
Linear
Circular
Circular
C.Rubbia
C.Rubbia

## Slide 11: Muon Colliders extending leptons high energy frontier with potential of considerable power savings
Muons
Muons
Circular
Linear

## Slide 12: Muon Source
Goals
Neutrino Factories: O(1021) m/yr within the acceptance of a m ring
Muon Collider: luminosities >1034/cm-2s-1 at TeV-scale (~Nm2)
Options
  Conventional: Tertiary production through proton on target (and then cool), baseline for Fermilab design study
    Rate > 1013m/sec Nm = 2×1012 /bunch
  e+e- annihilation: positron beam on target (very low emittance and no cooling needed), baseline for our proposal here Rate ~ 1011 m/sec Nm~ 5x107 /bunch
  by Gammas: GeV-scale Compton gs
  Rate ~ 5×1010 m/sec Nm ~ 106 (Pulsed Linac )
  Rate > 1013 m/sec Nm ~ few×104 (High Current ERL)
  Unconventional:
see also: W. Barletta and A. M. Sessler NIM A 350 (1994) 36-44
[V. Yakimenko (SLAC)]
not discussed here

## Slide 13: Proton-Based Source

## Slide 14: Muon Accelerator Program (MAP) Muon based facilities and synergies
~1013-1014 m / se
Tertiary prby MW p+
od.: pgpgFast m: cosund
(1kHz0
Key Challenges
~1013-1014 m / sec
Tertiary particle pgpgm:
Fast cooling
(t=2ms)
by 106 (6D)
Fast acceleration
mitigating m decay
Background
by m decay
Key R&D
MW proton driver
MW class target
NCRF in magnetic field
Ionization cooling
High field solenoids (30T)
High Temp Superconductor
Cost eff. low RF SC Fast pulsed magnet
(1kHz)
Detector/machine
interface
Mark
Palmer

## Slide 15: Key Feasibility Issues
Proton Driver
Target
Front End
Cooling
Acceleration
Collider Ring
Collider MDI
Collider Detector
High Power Target Station
Capture Solenoid
Energy Deposition
RF in Magnetic Fields
Magnet Needs (Nb3Sn vs HTS)
Performance
Acceptance (NF)
>400 Hz AC Magnets (MC)
IR Magnet Strengths/Apertures
SC Magnet Heat Loads (m decay)
Backgrounds (m decay)
M. Palmer

## Slide 16: High Power Target
Compact Taper Design
C Target Option
1 cm
MERIT @CERN
MERIT Expt:
  LHg Jet in 15T
  Capability: 8MW @70Hz
MAP Staging aims at 1-2 MW a C Target
Improved Compact Taper Design
  Performance & Cost

## Slide 17: MAP muon generation by Proton driver
MW-Class proton driver at ~5-10 GeV
Capture solenoid system (m+ & m-)
  15 T outsert, 5 T insert
  ~3GJ stored energy
Initial operation with 1MW carbon target
Upgrade to multi-MW with Liquid Metal Jet Technology (demonstrated in MERIT Experim.)
H.Kirk
(BNL)
H.K.Sayed
(BNL)
Muon per proton production at Front End exit

## Slide 18: Ionization Cooling
No damping from SR ->Ionization ‘dE/dx’ cooling:
  Helical 6D Cooling
  PIC
  …
D. Neuffer

## Slide 19: SR and damping in m collider
Beam energy(TeV)
Damping time (turns)
Muon lifetime (turns)
B=16 T
Beam energy(TeV)
U0 (GeV)
B=16 T

## Slide 20: SR and damping in m collider
Beam energy(GeV)
Damping time (turns)
Muon lifetime (turns)
B=20 T
Beam energy(GeV)
U0 (GeV)
B=20 T

## Slide 21: Damping time & muon lifetime
Dipole field (Tesla)
turns
Muon lifetime
Damping time in LHC tunnel
Damping time in FCC tunnel
Uo = 5.5 x 10-18 g4/r

## Slide 22: Ionization Cooling-general principle
Transverse Cooling:
Particle loses momentum in material
Particle gains only p|| in RF
This method, called “dE/dx cooling" closely resembles to the synchrotron compression of relativistic electrons - with the multiple energy losses in a thin, low Z absorber substituting the synchrotron radiated light.
On the other hand,
Multiple scattering in material increases rms emittance

## Slide 23
D. Neuffer
small beam size and large divergence
then damped by absorber + RF

## Slide 24: Cooling Methods
The particular challenge of muon cooling is its short lifetime
  Cooling must take place very quickly
  More quickly than any of the cooling methods presently in use
  a Utilize energy loss in materials with RF re-acceleration
Muon Ionization Cooling
Kaplan
M. Palmer

## Slide 25: MAP Cooling scheme overview
P.Snopok
(IIT)
Ionization cooling
Two
methods
Vacuum Cooling Channel (VCC)
Helical Cooling Channel (HCC)
Major
challenges
Accelerating field limitation
by magnetic field (10 T)
High pressure (160atm)
Gas (GH2) filled RF cavities

## Slide 26: RF cavities in strong magnetic field
RF cavity in vacuum:
RF cavity filled with gas
25 MV/m at 3 T
Pure GH2
1% Dry Air (0.2% O2) in GH2
E0 = 25 MV/m
~50X reduction in
RF power dissipation
1% Dry Air
(0.2 % O2)
in GH2 at
B = 3T
D.Li
(LBNL)
Breakdown by field emission
New cavity design
very encouraging !
New cavity by LBNL/SLAC
for tests in FNAL/MTA
Magnetic field (T)
Accelerating field (MV/m)
No accelerating field degradation up to 3 T
Operation with beam under heavy beam loading

## Slide 27: Muon Ionization Cooling
Advanced techniques a Improved HF Luminosity Simplified Final Cooling requirements
MAP Higgs Factory Target
PIC assumed in Carlo Rubbia’s Proposal
M. Palmer

## Slide 28: 3.-PIC, the Parametric Resonance Cooling of muons
Combining ionization cooling with parametric resonances is expected to lead to muon with much smaller transv. sizes.
A linear magnetic transport channel has been designed by Ya.S. Derbenev et al where a half integer resonance is induced such that the normal elliptical motion of particles in x-x' phase space becomes hyperbolic, with particles moving to smaller x and larger x' at the channel focal points.
Thin absorbers placed at the focal points of the channel then cool the angular divergence by the usual ionization cooling.
LEFT ordinary oscillations
RIGHT hyperbolic motion
induced by perturbations near an (one half integer) resonance of the betatron frequency.
x x’ = const
V. S. Morozov et al, AIP 1507, 843 (2012);
C. Rubbia

## Slide 29: Details of PIC
Without damping, the beam dynamics is not stable because the beam envelope grows with every period. Energy absorbers at the focal points stabilizes the beam through the ionization cooling.
The longitudinal emittance is maintained constant tapering the absorbers and placing them at points of appropriate dispersion, vertical b and two horizontal b.
. Comparison of cooling factors (ratio of initial to final 6D emittance) with and without the PIC condition vs number of cells: more than 10x gain
C. Rubbia

## Slide 30: Parametric Resonance Cooling
The first muon cooling ring should present no unexpected behaviour and good agreement between calculations and experiment is expected both transversely and longitudinally
The novel Parametric Resonance Cooling (PIC) involves instead the balance between a strong resonance growth and ionization cooling and it may involve significant and unexpected conditions which are hard to predict.
Therefore the experimental demonstration of the cooling must be concentrated on such a resonant behaviour.
On the other hand the success of the novel Parametric Resonance Cooling is a necessary premise for a viable luminosity of the initial proton parameters of the future CERN accelerators since the expected Higgs luminosity is proportional to the inverse of the transverse emittance, hence about one order of magnitude of increment is expected from PIC.
Carlo Rubbia – FNAL May 2015

## Slide 31: Acceleration Requirements
Key Issues:
  Muon lifetime a ultrafast acceleration chain
  NF with modest cooling a accelerator acceptance
  Total charge a cavity beam-loading (stored energy)
  TeV-scale acceleration focuses on hybrid Rapid Cycling Synchrotron a requires rapid cycling magnets Bpeak ~ 2T f > 400Hz
M. Palmer

## Slide 32
Acceleration
Technologies include:
EMMA – FFAG
  Superconducting Linacs (NuMAX choice)
  Recirculating Linear Accelerators (RLAs)
  Fixed-Field Alternating-Gradient (FFAG) Rings
  (Hybrid) Rapid Cycling Synchrotrons (RCS) for TeV energies
  RCS requires
  2 T p-p magnets
  at f > 400 Hz
  (U Miss & FNAL)
Hybrid RCS
Design concepts in hand
Magnet R&D indicates parameters achievable
M. Palmer

## Slide 33: CMC
CERN
Muon
Collider
14 TeV cme
LHC tunnel
SPS tunnel and mb PS
~7GeV SRF
Cost ~LHC
SRF
SRF
SRF
SRF

## Slide 34: Assume RCS Acceleration
Bmax : DC
Bmin : pulsed from –Bmin to + Bmin
Packing factor П<1
B
<B>C= 2π Ebeam /0.3, e.g. 146 Tkm
for 7 TeV and 26.7 km

## Slide 35: (Simple math)
Acceleration range:
f
If the ratio of fields :
then :
and equation for the required fields reads :

## Slide 36: Example: 7 TeV, 26.7 km tunnel, 16T max
then :
146 T×km 26.7km 16T 0.85 0.4=1/2.5
4.2 | 16 | 3.8T | 0.45TeV
4.5 | 7 | 3.5T | 1TeV
5 | 4 | 3.2T | 4TeV
8 | 1.75 | 2.0T | 9.1TeV
f

## Slide 37: Example 2: 1 TeV, 6.9km tunnel, 16T max
then :
20.9 T×km 6.9km 16T 0.9 0.21=1/5
10 | 9 | 1.6T | 110 GeV
9.5 | 17 | 1.7T | 60 GeV
f

## Slide 38
Collider Rings
Detailed optics studies for Higgs, 1.5 TeV, 3 TeV and now 6 TeV CoM
  With supporting magnet designs and background studies
Higgs, 1.5 TeV CoM and 3 TeV CoM Designs
  With magnet concepts
  Achieve target parameters
Preliminary 6 TeV CoM design
  Key issue is IR design and impact on luminosity
  Utilizes lower power on target
Higgs
1.5 TeV
3 TeV
Higgs Ring (single IR)
M. Palmer

## Slide 39
Muon Collider Parameters
Success of advanced cooling concepts a several × 1032 [Rubbia proposal: 5×1032]
Exquisite Energy Resolution Allows Direct Measurement
of Higgs Width
M. Palmer

## Slide 40: Annual dose
muon rate: p on target option 3 1013 m/s
Straight section
arc

## Slide 41: Backup Slides

## Slide 42
Conclusion
NF a precision n microscopes
Multi-TeV MC a potentially only cost-effective route to lepton collider capabilities with ECM > 5 TeV
Key technical hurdles have been addressed:
  High power target demo (MERIT)
  Realizable cooling channel designs with acceptable performance
  Breakthroughs in cooling channel technology
  Significant progress in collider & detector design concepts
Muon accelerator capabilities offer unique potential for the future of high energy physics research
M. Palmer

## Slide 43: Future accelerators programs at CERN
A new LHC injector complex to increase the collider luminosity 10x with the High Luminosity LHC (HL-LHC)).
Two accelerators (the LP-SPL and a new 50 GeV synchrotron, PS2) would replace the three existing ones (Linac2, the PSB, and the PS), with the injection of the SPS at 50 GeV,
C. Rubbia

## Slide 44: CERN-SPL parameters
Layout of superconducting SPL with intermediate extractions.
SPL design is very flexible and it can be adapted to the needs of many high-power proton beam applications.
50 Hz
4 MWatt
CERN 14-07
Venice,March.2015
C. Rubbia

## Slide 45: A muon based Higgs factory at CERN
A muon cooled Higgs factory can be easily housed within CERN
The new 5 GeV Linac will provide at 50 c/s a multi MWatt H- beam with enough pions/muons to supply the muon factory.
The basic additional accelerator structure will be the following:
  Two additional small storage rings with R ≈ 50 m will strip H- to a tight p bunch and compress the LP-SPL beam to a few ns.
  Muons of both signs are focused in a axially symmetric B = 20 T field, reducing progressively pt with a horn and B = 2 T
  A buncher and a rotator compresses muons to ≈ 250 MeV/c
  Muon Cooling in 3D compresses emittances by a factor 106.
  Bunches of about 2x1012 m± are accelerated to 62.5 GeV
  Muons are colliding in a SC storage ring of R ≈ 60 m (about one half of the CERN-PS ,1/100 of LHC) where about 104 Higgs events/y are recorded for each of the experiments.
Venice,March.2015
C. Rubbia

## Slide 46: Staged Neutrino Factory and Muon Colliders
Neutrino Factory at intensity frontier
Muon Collider at the energy frontier
Cooling 6D no final Full 6D
main parameters

## Slide 47: Muon generation by GeV-scale Compton gs
Brightness 103 larger than with proton driver
103 too low with pulsed linac
102 flux increase with high current ERL
Approaching intensities desired for NF (but train structure not favorable for collider luminosity, N2 issue)
V.Yakimenko
(SLAC)