## Slide 1
MEASUREMENT OF THE DIFFERENTIAL CROSS SECTION OF NEUTRON SCATTERING ON DEUTERIUM IN THE NEUTRON ENERGY RANGE FROM 400 keV TO 2.5 MeV
Elisa Pirovano (a), Luciano Canton (b), Ralf Nolte (a), Markus Nyman (c), Arjan Plompen (c)
(a) Physikalisch-Technische Bundesanstalt
(b) Istituto Nazionale di Fisica Nucleare, Sezione di Padova
(c) European Commission, Joint Research Centre - Geel
EuNPC
Bologna, 2-7 September 2018

## Slide 2: n-d scattering differential cross section
in research:
to study the effect of introducing three-body forces in the nuclear potential models
for applications:
fast-neutron detectors, metrology, energy production
issues with the data below 3 MeV
experimental database:
angular distribution measurements scarce and partially inconsistent
especially at backward angles
evaluated libraries
proved to cause inconsistencies in criticality benchmarks

## Slide 3: experimental setup
setup
monoenergetic neutron beam
proportional counter filled with deuterated gases
measurement
deuteron recoil energy distribution
proportional to the neutron scattering angular distribution
objective
measurement of the differential cross section at given neutron incident energies, below the break-up threshold

## Slide 4: experimental setup
measurement at the PTB VdG
quasi-monoenergetic neutrons via 7Li(p,n) or 3H(p,n)
energy range 400 keV – 2.5 MeV
different gas mixtures/pressures to limit the escape of recoil deuterons
D2/CD4 C3D8 600 hPa C3D8 1000 hPa | neutron energy: | 400 – 625 keV 625 keV – 1.25 MeV 1.25 – 2.5 MeV
400 – 875 keV
875 – 2500 keV

## Slide 5: background components
photon background → rise-time discrimination
neutron room-return background → shadow-cone technique

## Slide 6: analysis of the recoil energy distributions
fit of the model to the data
(iterative procedure):
→ determination of the coefficients
of the Legendre expansion of dσ/dΩ
analysis:
first guess of the differential cross section
dedicated Monte Carlo model:
  → n & d transport inside the detector
simulation of the deposited energy distribution
ENDF/B VII.1

## Slide 7: analysis of the recoil energy distributions

## Slide 8: results
En ≤ 750 keV
results based on the ENDF/B VII.1 library compatible with the measurements

## Slide 9: results

## Slide 10: results

## Slide 11: comparison with other measurements

## Slide 12: conclusions
experimental results
differential cross sections over a large angular range
for neutron incident energies from 400 keV to 2.5 MeV
limitation: modelling the energy deposition process in the counting gas, especially propane
analysis of the uncertainties ongoing…
preliminary results:
below 750 keV: ENDF/B VII.1 evaluation reproduces the measurements
above: forward/backward asymmetry still not properly described