## Slide 2
3.
L’imaging NMR convenzionale
Struttura di un tomografo NMR: schema a blocchi.
MRI apparato sperimentale

## Slide 3
3.
Relazione fondamentale dell’NMR:
0 =  H0.
In questo caso, lo spettro che fornisce l’intensità del segnale in funzione della frequenza non permette di distinguere il contributo di spin che appartengono ad un certo volume piuttosto che ad un altro. Per discriminare spazialmente questi contributi bisogna sovrapporre un gradiente di campo magnetico, G, al campo statico H0. Tale gradiente introduce una dipendenza spaziale nel campo magnetico totale, che si ripercuote sulla frequenza di risonanza degli spin:
(r) =  (H0 + Gr)
La frequenza di precessione diventa così funzione delle coordinate spaziali r ed è quindi in grado di fornire informazioni sulla distribuzione degli spin nello spazio.
L’imaging NMR convenzionale

## Slide 4
3.
Imaging monodimensionale
Supponiamo ad esempio che il sistema di spin sia posto in un campo magnetico uniforme H0 diretto lungo l’asse z, ; applichiamo quindi un gradiente diretto anch’esso lungo lo stesso asse, Gz. Il campo magnetico complessivo sperimentato da uno spin diventa:
H(z) = (H0 + Gzz) .
Se il gradiente è lineare, tutti gli spin che si trovano su di un piano ortogonale all’asse precederanno con la stessa velocità angolare:
(z) =  H(z)
(z) = (H0 + Gzz).
L’introduzione di Gz, detto gradiente di selezione, determina quindi la dipendenza dalla coordinata z della frequenza di risonanza degli spin.
L’imaging NMR convenzionale

## Slide 5
3.
L’imaging NMR convenzionale

## Slide 6
3.
0 =  H0.
(r) =  (H0 + Gr).
r
G
L’imaging NMR convenzionale

## Slide 7
3.
L’imaging NMR convenzionale

## Slide 8
3.
IMAGING NMR convenzionale
Purche’:
LG è la massima estensione del campione nella direzione individuata da G
LG /N risoluzione dell’immagine
Lorenziane:
Proiezioni monodimensionali prelevate a diverse orientazioni del gradiente
con:
Inviando la combinazione corretta delle correnti di gradiente x e y attraverso le bobine, il gradiente ruota

## Slide 9
3.
IMAGING NMR convenzionale

## Slide 10
3.
Slice selection
IMAGING NMR convenzionale
Selezione della “fetta” o strato
Utilizziamo ora un grad. lungo (ad esempio) la direzione z (ma potrebbe essere una direzione qualsiasi. In tal caso: (z) = (H0 + Gzz).
L’introduzione di Gz, detto gradiente di selezione, determina quindi la dipendenza dalla coordinata z della frequenza di risonanza degli spin. Questo rende possibile selezionare un determinato strato (slice) del campione del quale si vuole ottenere l’immagine, mediante un procedimento noto come eccitazione selettiva.
L’eccitazione selettiva coinvolge l’applicazione di un impulso a radiofrequenza (r.f.), H1(t) il quale deve agire solo in una specifica regione dello spettro in frequenza NMR, corrispondente all’allargamento delle frequenze di Larmor (dovuto alla presenza del gradiente di selezione) degli spin appartenenti allo strato z che si vuole eccitare.
Quindi, questi impulsi r.f. andranno ad eccitare in modo risonante solo una determinata “fetta” del campione lungo , quella contenente spin con frequenze di precessione il cui range sia rappresentato dallo spettro dell’impulso. Un’ efficiente e precisa eccitazione selettiva è una componente importante delle tecniche di imaging NMR. Risulta quindi fondamentale modulare opportunamente l’impulso r.f. in modo tale che il suo spettro in frequenza abbia una forma corrispondente al profilo dello strato z che si vuole selezionare.
3D 2D

## Slide 11
3.
Slice selection: Impulso “soft” selettivo
IMAGING NMR convenzionale

## Slide 12
3.
Slice selection: Impulso “soft” selettivo
IMAGING NMR convenzionale

## Slide 13
Il segnale proveniente da ogni slice è infatti determinato in questo caso dalla media dei contributi di tutti gli spin che ad essa appartengono. Si può infatti dimostrare che, trascurando i tempi di rilassamento, detta la densità degli spin e G un gradiente di campo magnetico qualunque agente sul sistema, il segnale MRI può essere così espresso:
Posto:
abbiamo che, nel formalismo dello spazio k ed usando il concetto della trasformata di Fourier e della sua inversa:
(1)
(2)
Le (1) e (2) sono relazioni fondamentali dell’imaging NMR ed affermano che il segnale NMR , e la densità degli spin, sono variabili mutuamente coniugate.
6.
IMAGING NMR
3.
Trasformata di Fourier 2D
IMAGING NMR convenzionale

## Slide 14
Se, ad esempio, G rappresenta il gradiente di selezione Gz , che seleziona la fetta, si ottiene:
da cui:
Quindi, la trasformata di Fourier del segnale FID consente di ottenere la proiezione della densità degli spin lungo l’asse definito dalla direzione del gradiente di selezione.
3.
IMAGING NMR convenzionale

## Slide 15
Ricostruzione di immagini in due dimensioni
3.
IMAGING NMR convenzionale
Una volta selezionata la fetta….ad esempio con un gradiente lungo z… Consideriamo quindi la slice selezionata, di spessore z, sulla quale sta agendo il gradiente di campo magnetico G(Gx,Gy,0): possiamo infatti considerare nullo il gradiente di selezione Gz al suo interno.
read gradient ( frequency encoding):
phase encoding:
definendo le frequenze spaziali:
Si ottiene:
La trasformata di Fourier rispetto a kx e ky del segnale fornisce l’immagine 2D di
In generale:
FT
Fourier imaging (FI) o tecnica della trasformata bidimensionale di Fourier (2D-FT).

## Slide 16
3.
IMAGING NMR convenzionale
Campionamento di S(Kx,Ky) con sequenza spin-echo (TR=tempo di ripetizione della sequenza; TE=tempo d’eco; tx=intervallo di tempo in cui agisce il gradiente Gx; ty=intervallo di tempo in cui agisce il gradiente Gy).
Ricostruzione di una slice tramite la trasformata inversa di Fourier del segnale campionato S(Kx,Ky).

## Slide 17
3.
IMAGING NMR convenzionale
Diversa fase
Gradiente di fase e gradiente di lettura

## Slide 18
3.
IMAGING NMR convenzionale

## Slide 19
Per la ricostruzione di una immagine è necessario quindi il campionamento del segnale MR nello spazio k, l’acquisizione cioè di per un numero finito di punti (kx, ky).
3.
IMAGING NMR convenzionale
Spin warp imaging
Il reticolo dello spazio k (sinistra) rappresenta le combinazioni dei punti Kx Ky di cui è necessario conoscere il valore S per ricostruire l’immagine nel piano xy.
Campionamento di una riga nello spazio k con una sequenza spin-echo.
Lo spostamento obliquo che porta sul primo punto campionato è dovuto all’applicazione simultanea dei due gradienti di codifica, Gx e Gy, durante ty. La seguente applicazione del gradiente di lettura Gx consente il campionamento, nell’intervallo di tempo tx , di tutti i punti della riga precedentemente selezionata.
L’intercetta di questa riga sull’asse ky viene cambiata ad ogni sequenza, prima che inizi il campionamento, variando l’intensità del gradiente di codifica di fase Gy, ma mantenendo costante l’intervallo temporale . Questo tipo di approccio (non è l’unico possibile, potendosi ottenere lo stesso risultato tenendo costante Gy e variando ) è noto come spin warp imaging. Con N sequenze di questo tipo verrebbero acquisiti N2 valori di (es.: 2562) necessari per il calcolo di e per la ricostruzione dell’immagine.

## Slide 20
Sequenza EPI
Veloce. Con una acquisizione si ottiene tutta l’immagine.
Pesa il segnale in T2*
IMAGING NMR convenzionale
3.
Imaging veloce

## Slide 21
Passa alto
Passa basso
3.
IMAGING NMR convenzionale
Notes: The low pass filter cuts out all the high spatial frequency data from the periphery of k-space (it allows low spatial frequencies to pass). This results in a lack of detail on the image, although the coarse contrast of the image remains.
The high pass filter removes the low spatial frequencies from k-space. When the fast Fourier transform is performed, the image shown is produced. It can be seen that there is little contrast in this image, yet edge definition remains. This is because the fine details of the image (edges etc.) are contained in the high spatial frequencies which are in the peripheries of k-space.

## Slide 22
3.
Rapporto segnale rumore
IMAGING NMR convenzionale
Il rapporto segnale-rumore (SNR) di un tessuto in un'immagine è il rapporto tra il valor medio del segnale del tessuto e la deviazione standard del rumore nello sfondo dell'immagine

## Slide 23
Cryoprobes differ from conventional NMR probes in that the rf circuits and preamplifiers are cooled with cold helium gas while the sample is maintained at ambient temperature. The benefit of cryogenically cooled electronics compared to room temperature electronics is that the thermal noise in the system is reduced at cryogenic temperatures while the NMR signal remains constant for the sample at ambient temperature. The signal-to-noise ratio in an NMR spectrum acquired in a cryoprobe is therefore increased dramatically compared to a conventional probe, typically by a factor of 4. This allows for data collection times on the order of 16 times shorter than those using conventional probes as well as lower detection limits.
3.
IMAGING NMR convenzionale

## Slide 24
3.
IMAGING NMR convenzionale

## Slide 25
3.
IMAGING NMR convenzionale

## Slide 26
S/N (N)1/2
! TR> (3-5) T1 per mediare segnali identici
3.
IMAGING NMR convenzionale

## Slide 27
La risoluzione dello spettro è legata all’intensità del campo magnetico statico
La risoluzione dell’immagine è legata all’intensità dei gradienti di campo magnetico
Partial volume averaging PVA
Field of view FOV
Matrix
3.
Risoluzione spaziale
IMAGING NMR convenzionale

## Slide 28
3.
IMAGING NMR convenzionale

## Slide 29: MR Imaging Spatial encoding
1e dimension: selective excitation
2e dimension: phase encoding
3e dimension: frequency encoding
Spatial encoding is achieved by
applying gradients in 3 dimensions
3.
IMAGING NMR convenzionale

## Slide 30: Slice selection
selection
gradient
f ~ B
Transmitted
RF pulse
position
3.
IMAGING NMR convenzionale

## Slide 31: Slice position
selection
gradient
f1
position
f ~ B
Transmitted
RF pulse
f2
fo
3.
IMAGING NMR convenzionale

## Slide 32: Slice orientation
No
RF pulse
no selection
gradient
position
f ~ B
3.
IMAGING NMR convenzionale

## Slide 33: Slice orientation
position
f ~ B
Transmitted
RF pulse
fo
z selection
gradient
3.
IMAGING NMR convenzionale

## Slide 34: Slice orientation
No
RF pulse
no selection
gradient
position
f ~ B
3.
IMAGING NMR convenzionale

## Slide 35: Slice orientation
position
f ~ B
Transmitted
RF pulse
fo
y selection
gradient
3.
IMAGING NMR convenzionale

## Slide 36: Slice orientation
No
RF pulse
no selection
gradient
position
f ~ B
3.
IMAGING NMR convenzionale

## Slide 37: Slice orientation
position
f ~ B
Transmitted
RF pulse
fo
x selection
gradient
3.
IMAGING NMR convenzionale

## Slide 38: Slice thickness
position
Transmitted
RF pulse
fo
fo
f ~ B
weak
selection
gradient
3.
IMAGING NMR convenzionale

## Slide 39: Slice thickness
position
Transmitted
RF pulse
fo
fo
f ~ B
strong
selection
gradient
3.
IMAGING NMR convenzionale

## Slide 40: Phase encoding
Phase encoding
direction
Phase encoding steps:
3.
IMAGING NMR convenzionale

## Slide 41: Phase encoding
Phase encoding
direction
Phase encoding steps:
3.
IMAGING NMR convenzionale

## Slide 42: Phase encoding
Phase encoding steps:
Phase encoding direction
3.
IMAGING NMR convenzionale

## Slide 43: Frequency (read) encoding
Frequency encoding direction
Bo
MR response
Frequency
encoding
gradient
3.
IMAGING NMR convenzionale

## Slide 44: Frequency encoding
Frequency encoding direction
Bo
MR response
Frequency
encoding
gradient
3.
IMAGING NMR convenzionale

## Slide 45: Frequency encoding
Frequency encoding direction
Phase encoding direction
3.
IMAGING NMR convenzionale

## Slide 46: In plane encoding
Frequency encoding
Phase encoding
Frequency encoding
Phase encoding
3.
IMAGING NMR convenzionale

## Slide 47: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
90°
180°
Spin echo
3.
IMAGING NMR convenzionale

## Slide 48: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
3.
IMAGING NMR convenzionale

## Slide 49: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
90°
180°
3.
IMAGING NMR convenzionale

## Slide 50: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
3.
IMAGING NMR convenzionale

## Slide 51: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
90°
180°
3.
IMAGING NMR convenzionale

## Slide 52: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
3.
IMAGING NMR convenzionale

## Slide 53: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
90°
180°
3.
IMAGING NMR convenzionale

## Slide 54: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
3.
IMAGING NMR convenzionale

## Slide 55: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
90°
180°
3.
IMAGING NMR convenzionale

## Slide 56: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
3.
IMAGING NMR convenzionale

## Slide 57: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
90°
180°
3.
IMAGING NMR convenzionale

## Slide 58: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
3.
IMAGING NMR convenzionale

## Slide 59: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
90°
180°
3.
IMAGING NMR convenzionale

## Slide 60: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
3.
IMAGING NMR convenzionale

## Slide 61: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
90°
180°
3.
IMAGING NMR convenzionale

## Slide 62: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
3.
IMAGING NMR convenzionale

## Slide 63: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
90°
180°
3.
IMAGING NMR convenzionale

## Slide 64: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
3.
IMAGING NMR convenzionale

## Slide 65: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
90°
180°
3.
IMAGING NMR convenzionale

## Slide 66: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
3.
IMAGING NMR convenzionale

## Slide 67: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
90°
180°
3.
IMAGING NMR convenzionale

## Slide 68: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
3.
IMAGING NMR convenzionale

## Slide 69: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
90°
180°
3.
IMAGING NMR convenzionale

## Slide 70: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
3.
IMAGING NMR convenzionale

## Slide 71: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
180°
90°
3.
IMAGING NMR convenzionale

## Slide 72: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
3.
IMAGING NMR convenzionale

## Slide 73: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
90°
180°
3.
IMAGING NMR convenzionale

## Slide 74: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
3.
IMAGING NMR convenzionale

## Slide 75: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
90°
180°
3.
IMAGING NMR convenzionale

## Slide 76: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
3.
IMAGING NMR convenzionale

## Slide 77: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
90°
180°
3.
IMAGING NMR convenzionale

## Slide 78: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
3.
IMAGING NMR convenzionale

## Slide 79: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
90°
180°
3.
IMAGING NMR convenzionale

## Slide 80: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
3.
IMAGING NMR convenzionale

## Slide 81: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
90°
180°
3.
IMAGING NMR convenzionale

## Slide 82: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
3.
IMAGING NMR convenzionale

## Slide 83: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
90°
180°
3.
IMAGING NMR convenzionale

## Slide 84: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
3.
IMAGING NMR convenzionale

## Slide 85: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
90°
180°
silvia.capuani@roma1.infn.it
3.
IMAGING NMR convenzionale

## Slide 86: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
3.
IMAGING NMR convenzionale

## Slide 87: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
90°
180°
3.
IMAGING NMR convenzionale

## Slide 88: Pulse sequence
RF
MR response
G
phase enc.
G
frequency enc.
G
slice selection
90°
180°
3.
IMAGING NMR convenzionale

## Slide 89
3.
IMAGING NMR convenzionale

## Slide 90
sequenza
3.
L’imaging NMR convenzionale: il contrasto

## Slide 91: Contrast in Spin Echo
Tissue Voxel
Proton density
Relaxation time T1
Relaxation time T2
Magnetic Field
Pulse sequence
Spin Echo
MR Response
PD-W
T1-W
T2-W
Contrast
3.
L’imaging NMR convenzionale: il contrasto

## Slide 92
Spin Echo (SE)
90°
T2
T2
*
90°
180°
TR
TE/2
TE/2
spin echo
Rephasing
Pulse
180°
3.
L’imaging NMR convenzionale: il contrasto

## Slide 93
Proton density
T2-weigthed
T1-weigthed
3.
L’imaging NMR convenzionale: il contrasto

## Slide 94: Spin Echo Long TR, Short TE/Long TE
M
z
M
xy
TE/ms
TR/s
TR
TE1
TE2
3.
L’imaging NMR convenzionale: il contrasto

## Slide 95
3.
L’imaging NMR convenzionale: il contrasto
Affinché una patologia o un qualsiasi tessuto di interesse in un'immagine di risonanza magnetica risulti visibile è necessario che ci sia contrasto,
ovvero, una differenza di intensità di segnale tra la struttura di interesse ed i tessuti adiacenti.

## Slide 96
3.
L’imaging NMR convenzionale: La mappa NMR
FIT intensità con funzione teorica in ogni voxel
S(TE) = M0 exp(-TE/T2)
Color coded T2 map

## Slide 97: Contrast in IR
Tissue Voxel
Proton density
Relaxation time T1
Relaxation time T2
Magnetic Field
Pulse sequence
IR
MR Response
Real T1
Fat suppr.
Flair
Grey matter
only
Contrast
3.
IMAGING NMR convenzionale

## Slide 98: Inversion Recovery (= SE with prepulse)
TI
180°
Inversion
pulse
90°
TE
TR
3.
IMAGING NMR convenzionale

## Slide 99: Inversion recovery T1 relaxation after 180° pulse
1.00
0
-Mz
+Mz
-1.00
MAGNETIZATION ALONG Z AXIS
time
3.
IMAGING NMR convenzionale

## Slide 100: Inversion recovery T1 relaxation after 180° pulse
1.00
0
-Mz
+Mz
-1.00
MAGNETIZATION ALONG Z AXIS
time
3.
IMAGING NMR convenzionale

## Slide 101: Inversion recovery T1 relaxation after 180° pulse
1
2
3
4
T1 TIME
0.26
0.73
0.90
1.00
0
-Mz
+Mz
0.5
-0.21
-1.00
MAGNETIZATION ALONG Z AXIS
silvia.capuani@roma1.infn.it
3.
IMAGING NMR convenzionale

## Slide 102: Inversion recovery T1 relaxation after 180° pulse
1
2
3
4
T1 TIME
0.26
0.73
0.90
1.00
0
-Mz
+Mz
0.5
-0.21
-1.00
0.69 T1
MAGNETIZATION ALONG Z AXIS
3.
IMAGING NMR convenzionale

## Slide 103: Inversion Recovery Phase sensitive detection
+M(t)
B0
3.
IMAGING NMR convenzionale

## Slide 104: Inversion Recovery Phase sensitive detection
-M(t)
180° pulse
B0
3.
IMAGING NMR convenzionale

## Slide 105: Inversion Recovery Phase sensitive detection
-M(t)
B0
3.
IMAGING NMR convenzionale

## Slide 106: Inversion Recovery Phase sensitive detection
-M(t)
B0
3.
IMAGING NMR convenzionale

## Slide 107: Inversion Recovery Phase sensitive detection
-M(t)
B0
silvia.capuani@roma1.infn.it
3.
IMAGING NMR convenzionale

## Slide 108: Inversion Recovery Phase sensitive detection
-M(t)
B0
silvia.capuani@roma1.infn.it
3.
IMAGING NMR convenzionale

## Slide 109: Inversion Recovery Phase sensitive detection
-M(t)
B0
+M(t)
silvia.capuani@roma1.infn.it
3.
IMAGING NMR convenzionale

## Slide 110: Inversion Recovery Phase sensitive detection
B0
90° pulse
-M(t)
+M(t)
Larmor
Precession
Receive
Coil
+M(t):
-M(t):
silvia.capuani@roma1.infn.it
3.
IMAGING NMR convenzionale

## Slide 111: Fat Suppression: STIR
Time/ms
0
-Mz
+Mz
MAGNETIZATION ALONG Z AXIS
+100%
-100%
100
200
300
400
Fat (T1= 200ms)
Brain (T1= 500ms)
90° pulse
real
modulus
3.
IMAGING NMR convenzionale

## Slide 112: Fluid Attenuation IR (FLAIR)
TIME/ms
0
-Mz
+Mz
MAGNETIZATION ALONG Z AXIS
+100%
-100%
1000
2000
3000
4000
Fat (T1=200 ms)
CSF (T1 = 3000 ms)
90° pulse
silvia.capuani@roma1.infn.it
3.
IMAGING NMR convenzionale

## Slide 113: Dual Inversion Recovery
TIME/ms
0
-Mz
+Mz
+100%
-100%
1000
2000
3000
4000
white matter
T1=790 ms
CSF
T1=3000 ms
180° pulse
Application:
Grey matter only
90° pulse
180° pulse
3.
IMAGING NMR convenzionale

## Slide 114: Grey matter only
3.
IMAGING NMR convenzionale

## Slide 115: White matter only
3.
IMAGING NMR convenzionale

## Slide 116: Fat Suppression (SPIR)
180°
90°
TR
TE
Frequency selective
Fat saturating
pulse
3.
IMAGING NMR convenzionale

## Slide 117: Spectral fat suppression
VOXEL
(water and fat)
f
CH2
f0
f1
H2O
Water Fat Shift
3.3 ppm
FWHM B
f
automatic
shimming
f  3.3 ppm
CH2
H2O
t
f1
spectral
presaturation
pulse
3.
IMAGING NMR convenzionale

## Slide 118
3.
L’imaging NMR convenzionale: imaging spettroscopico

## Slide 119
NMR Laboratory
NMR laboratory staff
Biomedicine:
Maria Giovanna Di Trani
(PhD student)
Michele Guerreri
(PhD student)
Riccardo De Feo
(rare disease project)
Clinical collaborators:
Neuroimaging Laboratory,
Fondazione Santa Lucia IRCCS, Rome, Italy.
Radiology Dpt., Policlinico Umberto I Sapienza Rome, Italy
Department of Diagnostic and Interventional Radiology, Molecular Imaging and Radiotherapy & Orthopedic and Traumatology Dip. PTV Foundation,”Tor Vergata” University of Rome,
Edificio Fermi stanza 319,
Edificio Segre’ Laboratorio 5
Silvia.Capuani@roma1.infn.it
Alessandra Caporale
Penn University (USA)
Marco Palombo
UCL (UK)
Cultural heritage
Sveva Longo
(PhD student 50%UNIMe)