## Slide 2
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 3
Diffusione
solvente
soluto
Il fenomeno della diffusione è molto comune nella nostra esperienza quotidiana.
Un esempio può essere quello di versare del vino in un bicchiere d’acqua...
La diffusion tensor imaging e la diffusione non gaussiana
4.
Notes: what we observe macroscopically in everiday experience

## Slide 4
Diffusione
IMPORTANTE: è un processo irreversibile
si tratta di un fenomeno macroscopico
può essere descritto da equazioni continue
La diffusion tensor imaging e la diffusione non gaussiana
4.
Notes: what we observe macroscopically in everiday experience

## Slide 5
J = -D c
Diffusione
Legge di Fick
c/  t = - J
Legge di conservazione della massa
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 6
Diffusione
c/  t =  (Dc)
Equazione della diffusione
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 7
A solution of diffusion equation is a Gaussian function centered in r=0 whose width is proportional to (4Dt)d/2 , where d=spatial dimension
In a isotropic and homogeneous fluid….
Notes: It is easy to show that solutions of this partial differential equation are the concentration profiles resulting from diffusion.
The solution is given by:
C(t) = 1/4πDt1/2 exp(−x2/4Dt)
which is a Gaussian centered in r = 0 whose width is proportional to √4Dt, i.e. it
increases with increasing t.

## Slide 8
Diffusione
ad una analisi microscopica….
La diffusion tensor imaging e la diffusione non gaussiana
4.
Notes: The nature of diffusion is linked to a random process of motion, the brownian motion, it showed that in nature very little invisible particles exist (motion of dust)

## Slide 9
Diffusione
Einstein, 1905
effetto fotoelettrico
teoria della relatività
speciale
moto browniano
(analisi quantitativa)
La diffusion tensor imaging e la diffusione non gaussiana
4.
Notes: Experimental observation confirmed the numerical accuracy of Einstein's theory. This means that we understand Brownian motion is just a
consequence of the same thermal motion that causes a gas to exert a pressure on the container that confines it. We understand diffusion in terms of
the movements of the individual particles, and can calculate the diffusion coefficient of a molecule if we know its size (or more commonly calculate
the size of the molecule after experimental determination of the diffusion coefficient). Thus, Einstein connected the macroscopic process of diffusion
with the microscopic concept of thermal motion of individual molecules.
Often we are not interested in the motion of individual particles, but rather in changes in a concentration profile with time. The two differential
equations that describe bulk diffusion were known well before Einstein. The 1st law is essentially the definition of the diffusion coefficient. The 1st
law plus conservation of mass gives the 2nd law, and solutions of this partial differential equation are the concentration profiles resulting from
diffusion.

## Slide 10
Diffusione
Mostrò che:
Einstein, 1905
La diffusion tensor imaging e la diffusione non gaussiana
4.
Notes: Experimental observation confirmed the numerical accuracy of Einstein's theory. This means that we understand Brownian motion is just a
consequence of the same thermal motion that causes a gas to exert a pressure on the container that confines it. We understand diffusion in terms of
the movements of the individual particles, and can calculate the diffusion coefficient of a molecule if we know its size (or more commonly calculate
the size of the molecule after experimental determination of the diffusion coefficient). Thus, Einstein connected the macroscopic process of diffusion
with the microscopic concept of thermal motion of individual molecules.
Often we are not interested in the motion of individual particles, but rather in changes in a concentration profile with time. The two differential
equations that describe bulk diffusion were known well before Einstein. The 1st law is essentially the definition of the diffusion coefficient. The 1st
law plus conservation of mass gives the 2nd law, and solutions of this partial differential equation are the concentration profiles resulting from
diffusion.

## Slide 11
Diffusione
Einstein, 1905
Il moto browniano di particelle è essenzialmente lo stesso fenomeno della diffusione.
La diffusion tensor imaging e la diffusione non gaussiana
4.
Notes: Experimental observation confirmed the numerical accuracy of Einstein's theory. This means that we understand Brownian motion is just a
consequence of the same thermal motion that causes a gas to exert a pressure on the container that confines it. We understand diffusion in terms of
the movements of the individual particles, and can calculate the diffusion coefficient of a molecule if we know its size (or more commonly calculate
the size of the molecule after experimental determination of the diffusion coefficient). Thus, Einstein connected the macroscopic process of diffusion
with the microscopic concept of thermal motion of individual molecules.
Often we are not interested in the motion of individual particles, but rather in changes in a concentration profile with time. The two differential
equations that describe bulk diffusion were known well before Einstein. The 1st law is essentially the definition of the diffusion coefficient. The 1st
law plus conservation of mass gives the 2nd law, and solutions of this partial differential equation are the concentration profiles resulting from
diffusion.

## Slide 12
Diffusione
Einstein, 1905
< r 2 > = 6 D t
< r 2 > il valore aspettato del quadrato della distanza percorsa in un tempo t, e
D è il coefficiente di diffusione
La diffusion tensor imaging e la diffusione non gaussiana
4.
Notes: Experimental observation confirmed the numerical accuracy of Einstein's theory. This means that we understand Brownian motion is just a
consequence of the same thermal motion that causes a gas to exert a pressure on the container that confines it. We understand diffusion in terms of
the movements of the individual particles, and can calculate the diffusion coefficient of a molecule if we know its size (or more commonly calculate
the size of the molecule after experimental determination of the diffusion coefficient). Thus, Einstein connected the macroscopic process of diffusion
with the microscopic concept of thermal motion of individual molecules.
Often we are not interested in the motion of individual particles, but rather in changes in a concentration profile with time. The two differential
equations that describe bulk diffusion were known well before Einstein. The 1st law is essentially the definition of the diffusion coefficient. The 1st
law plus conservation of mass gives the 2nd law, and solutions of this partial differential equation are the concentration profiles resulting from
diffusion.

## Slide 13
Diffusione
D
misurato in mm2/s
< r 2 > = 6 D t
D = KB T / 6   
KB costante di Boltzman
T temperatura assoluta
 viscosità del solvente
 raggio della particella o molecola
Einstein, 1905
La diffusion tensor imaging e la diffusione non gaussiana
4.
Notes: entrambe possono essere prese come definizione di D
ci da informazioni sulla dinamica delle molecole sospese in un fluido
è in relazioni alle altre grandezze fisiche del fluido e molecole

## Slide 14: When dealing with a large population of particles:
We need to talk about distributions, rather than about what happens to a single particle.
The distribution function that describes
the process above is the
probability density function (pdf).
Each point in this distribution describes
the probability of particle to migrate a
distance dR in a given time
(diffusion time) t=Δ:
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 15
Brownian motion
t = waiting time
r = displacement length
Gaussian pdf
In a isotropic and homogeneous fluid….
mean square displacement
t = 1 ms
t = 2 ms
t = 4 ms
t = 10 ms
La diffusion tensor imaging e la diffusione non gaussiana
4.
[P.T. Callaghan,”Principles of Nuclear Magnetic Resonance Microscopy”,Oxford Science Publications (1995)]
Notes: Taking into account the Brownian diffusion each molecular displacement can be characterized by two parameters: the waiting time t between two consecutive steps, and the variable displacement length r
Here you can see a schematic simulation of a molecule diffusing according to Gaussian diffusion. It is characterized by jumps with finite lengths over a finite time.
The probability of finding a particle in a position r at time t, is proportional to the motion propagator
If a random walk scheme is considered, it is possible to obtain again the diffusion equation. The solution of the diffusion equation is a Gaussian function or Gaussian distribution of water molecules centered at R=0, where Big R is the relative position between initial and final displacement and its width is proportional to diffusion coefficient and the time t.
In particular in the case of Gaussian or Browian diffusion the mean square displacement depends on t linearly
Under the condition that the first two moments of the pdf, describing
the appropriately normalised distance covered in a jump event and the variance,
X =
P
i Xi and X2, as well as the mean time span t between any two individual
jump events, exist, the central limit theorem assures that the random walk process
is characterised by a mean velocity V = X/t and a diffusion coefficient D =
(2t)−1[X2 − X
2]. Furthermore, for long times, i.e., a large enough number of
steps, the pdf of being at a certain position x at time t, is governed by the diffusion
equation 2.19, and it is given by the Gaussian shape, as seen in the previous section.

## Slide 16: L’NMR è l’unica tecnica non ionizzante, non invasiva e non distruttiva che consente di misurare il coefficiente di diffusione delle molecole di acqua nei tessuti o in materiali porosi
Tissue Voxel
Molecular
diffusion
Magnetic Field
Pulse sequence
PGSE
MR Response
Contrast
DWI
ADC maps
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 17
=γδ
P(
S( ,t=)  , ) d
The diffusion weighted signal is proportional to the characteristic function of the diffusion propagator in time 
La diffusion tensor imaging e la diffusione non gaussiana
4.
MSD= 2Dt lD 
Diffusion Lenght

## Slide 18: Why would we want to evaluate the Diffusion parameters of water in materials and biological Tissue?
Because Diffusion parameters and
diffusion-weighted NMR signal
reflect the micro-structural rearrangement of porous materials and tissues
La diffusion tensor imaging e la diffusione non gaussiana
4.
Notes: You can see an example of brain tissue and a schematic representation of water molecules (the blue balls) diffusing in it
Before moving on I would like to underline:

## Slide 19
Diffusion MR images can measure water proton displacements at the cellular level
Probing motion at microscopic scale (10-20 m), orders of magnitude smaller than macroscopic MR resolution (mm)
This has found numerous research and clinical applications
Voxel zoom
NMR diffusion
La diffusion tensor imaging e la diffusione non gaussiana
4.
lD 
Notes: You can see an example of brain tissue and a schematic representation of water molecules (the blue balls) diffusing in it
Before moving on I would like to underline:

## Slide 20
D0
D0=2.3·10-9 m2/s
D1=1.4·10-9 m2/s
D2=3·10-10 m2/s
D=D(r)
D0=2.3·10-9 m2/s
D1=2.0·10-9 m2/s
D2=9·10-11 m2/s
D=D(r,t)
D0
Hindered diffusion
Restricted diffusion
ADC
Apparent diffusion coefficient
Anisotropy and heterogeneity
La diffusion tensor imaging e la diffusione non gaussiana
4.
Notes: It is important to underline the hypotheses of isotropy and homogeneity of the
fluid, which lead to the Fick’s laws. If the isotropy hypothesis is violated, i.e. we are dealing with
heterogeneous environments, then the diffusion behaviour will be direction-dependent and a
single diffusion coefficient will not be able to characterize the diffusion. If instead
the homogeneity hypothesis is violated, then the diffusion coefficient will vary as a function
of spatial and temporal coordinates.

## Slide 21
Short diffusion times:
Long diffusion times:
La diffusion tensor imaging e la diffusione non gaussiana
4.
Notes: As an example you can see here a schematic rapresentation of an heterogeneous system composed of interconnected pores. Depending on pore sizes, only using long diffusion times water molecules can well probe the structural characteristic of the system. Using short diffusion time I can obtain the ADC value of the bulk non interacting water. Conversely by using long diffusion times I can measure an ADC values lower than that of free bulk water and as a consequence I can indirectly obtain structural information about pores dimensions.

## Slide 22
Axon mean diameter ≈7µm
Microtubulus ≈20nm
< r2 > = 6 D
< r2 > = 40μm
Where: D=2.3x10-9 m2/s; Δ=80ms
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 23: In the more general case:
In living tissue, diffusion generally occurs in a rather complex medium, where the mobility of water molecules may seem unobstructed when t=Δ is small with respect to the distance traveled, but becomes obstructed when t=Δ becomes larger:
In that case the displacement distribution function is not Gaussian any longer, at least in the direction perpendicular to the “restrictive walls”.
If the barrier structure is anisotropic, then diffusion becomes anisotropic as well.
t=0
t=t2
t=t1
t=t3
t=t4
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 24
In this case, D(parallel) is more representative of the actual diffusion coefficient, whereas D(perp.) is more defined by the geometric barrier, as t=Δ becomes longer:
√Δ
RMSD.
0 0.05 0.01 0.15 0.2 0.25 0.3
30
25
20
15
10
5.0
0
(m)
lD  RMSD = (2D)1/2
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 25
Conventional Diffusion NMR: Gaussian diffusion
NMR diffusion
Gaussian Motion Propagator

## Slide 26
The effect of barriers to the free diffusion
of water molecules is to modify their
probability distribution.
P(r)
Diffusion
coefficient
decreases
with increasing
diffusion time
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 27
How can we measures the (mean)
displacement of water molecules using NMR?
g(z) is a
magnetic field gradient
added to B0 that
varies with position.
(z) =  (B0 + g(z)z)
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 28
How can we measures MSD
of water molecules using NMR?
Applying g(z) for a time 
results in a phase shift
that depends
upon location
in z
z
z = 0
Tagging the initial position
using phase
of M
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 29
Now, after waiting a time t=∆ we apply
an equal gradient, but with the opposite sign
Apply -g(z) for a time 
if no diffusion:
signal = M0
z
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 30
But, in reality, there is always diffusion so
we find that:
Apply -g(z) for a time 
if diffusion:
signal = M0e(-q2Dt)
(t = ∆ - /3)
q =g
z
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 31
Pulse Gradient Spin Echo (PGSE)
DW Spin Echo
/2



= gradient duration
 = separation of gradient leading edges
[E.O.Stejskal and J.E. Tanner, J. Chem. Phys., 42:288-292, 1965 ]
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 32
90 °
180°
TE
ECHO
G
G
d
D
Diffusion weighted: PGSE
Diffusion measurements by NMR
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 33: Measuring diffusion properties with the Stejskal-Tanner experiment
The DW pulse sequence:
In the absence of gradients (or diffusion):
In the presence of diffusion and gradients:
Dephasing gradient
Rephasing gradient
Diffusion time Δ
Gradient duration δ
Grad strength g
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 34
b factor
(s/mm2)
Signal
(a.u.)
Diffusion weighted imaging:
DWI
S(0)
S(b)
Diffusion measurements by NMR
Gaussian MP !
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 35
b value selects different diffusion (fast, slow)
How select b-value: exp(-bD) bD 1
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 36
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 37
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 38
La diffusion tensor imaging e la diffusione non gaussiana
4.
DWI:Transient Ischaemic Attack

## Slide 39
T2W or S(0)
DW or S(b)
ADC = -(1/b) ln (S1/S0)
ADC
DWI
T2 effect
Diffusion Weighted Imaging
ADC
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 40
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 41
DWI to detect Tumor
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 42
ADC = -(1/b) ln (S(b)/S0)
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 43
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 44
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 45
Diffusion Weighted Image
X direction
Artifact or Abnormality
Higher diffusion in X direction  lower signal
With diffusion weighting applied in a single direction, a bright region may be due either to a focal abnormality or to the particular alignment of tissue structure
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 46
Diffusion anisotropy may result in difficulties when interpreting of changes in diffusivity.
With diffusion weighting applied in a single direction, a bright region may be due either to a focal abnormality or to the particular alignment of tissue structure.
Anisotropic diffusion
DWI
Diffusion Weighted Imaging
The ADC is
greatest along
White Matter
fiber tracts.
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 47
J(r) = -D c(r)
J(r) = -D(r) c(r)
J(r) = -D c(r)
homogeneous and isotropic medium
Heterogeneous medium
Anisotropic medium
Diffusion Tensor Imaging
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 48
Diffusion Tensor Imaging
At least six independent parameters are required.
At least six no-complanar DWI + one T2w
Gx Gy Gz Gxz Gxy Gyz
DWIx DWIy DWIz DWIxz DWIxy DWIyz
Basser et al., JMR, 1994 (103) 247
λ3
λ3
λ1
λ2
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 49
Mean Diffusivity MD
High diffusion  large suppression of signal  dark pixel in DWI, bright in MD map.
Low diffusion  little suppression of signal  bright in DWI, dark in MD map.
Fractional Anisotropy FA
FA range: 0~1, FA=0, perfect isotropic diffusion;
FA=1, an infinite cylinder, maximum anisotropic diffusion
Diffusion Tensor Imaging
Eigenvalues:
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 50
MD map
FA map
Diffusion Tensor Imaging
MD and FA maps
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 51: Water diffusion as a probe for tissue microstructure
Mobility of water molecules in tissue has been used extensively to indirectly probe tissue microstructure via diffusion-weighted MRI.
In particular, the diffusion tensor obtained for each pixel from six (or more) independent diffusion-weighted measurements is an ellipsoid-shaped entity that describes the spatial distribution of diffusion coefficients in the pixel.
The diffusion tensor give us information about:
three diffusion coefficients i in three perpendicular directions i. The average of the three is the mean diffusivity (MD)
the degree of diffusion anisotropy, called fractional anisotropy (FA).
“typical” white matter pixel:
λ1
λ2
λ3
Gray matter pixel:
λ1
λ2
λ3
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 52
Diffusion in the CSF is similar to the diffusion of water at the same temperature.
In gray and white matter MD is about 3 times lower than in pure water at the same temperature.
MD in brain tissues: 2*10-9 -
Diffusion Tensor Imaging
0.8*10-10
In white matter FA : 0.7-0.45
In gray matter FA : 0.2-0.3
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 53
mean diffusivity
anisotropy
WM
GM
CSF
Diffusion Tensor Imaging
MD and FA
Quantitative images
anisotropy
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 54: FA + color (largest diffusion direction)
red = right – left
green = anterior – posterior
blue = superior - inferior
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 55: DTI-based images and maps
FA map
MD Map
FA = 0
FA = 1
LD
RD
MD
La diffusion tensor imaging e la diffusione non gaussiana
4.
Axial view
Sagittal View
Preferred Direction of Diffusion
Vector field map

## Slide 56
NMR: diffusione tensoriale
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 57
NMR: diffusione tensoriale
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 58
NMR: diffusione tensoriale
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 59
NMR: diffusione tensoriale
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 60
Principal directions of diffusion
fiber orientation
Diffusion Tensor Imaging
Eigenvectors
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 61
From the eigenvectors to white matter tracts:
Fibers tractography
Modified from: Mori S, et al., Ann. Neurol. 45: 265-269 (1999)
seedpoint
Diffusion Tensor Imaging
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 63
Tractography
Derek Jones, Cardiff (UK)
Diffusion Tensor Imaging
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 64
PROJECTION
COMMISSURAL
ASSOCIATION
Corona radiata
Fornix
Corpus callosum
Anterior commissure
Cingulum
Inferior longitudinal
Arcuate
Uncinate
Inferior fronto-occipital
Marco Catani

## Slide 65
Axial T2w
Axial T1w
Axial FA map
Axial FA colour coded map
DTI tractography coregistred with T2w image
f) DTI tractography coregistred with T1w image
blue=genu and splenium, green=sensorimotor tracts
In utero tractography of fetal white matter development
Neuroimage 2008
Diffusion Tensor Imaging
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 66
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 67
La diffusion tensor imaging e la diffusione non gaussiana
4.
Diffusion parameters depend on S/N !

## Slide 68
MR scanner
Lesions
Volumetrics
Macroscopic information
Microscopic information
Diffusion-map
Fibre orientation
Fibre
reconstruction
Neuroimaging
Brain connections
Brain pathologies:
Alzheimer
Multiple Sclerosis
Brain structures:
Anatomical regions
Normal Aging
Diffusion Neuroimaging
Diffusion Tensor Imaging
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 69
Can probe diffusion for time scales:
1 ms to seconds
length scales of displacements:
100 nm to 100 m
Porous Media
• Intrinsically multiphase materials
• Pore fluids for NMR detection
• Biological tissues
Microstructure is important
– Rocks, oil and water reservoirs
– Soils, unconsolidated formation
– Cement and concrete, catalysts
– Food stuff, paper, fabric
– Plant and animal tissues, bone
– Human tissues
– Brain
Conventional diffusion = Gaussian diffusion
Multiscale
Complex systems
Anomalous diffusion
system constituted by structures at very different levels of hierarchical organization
More sensitivity
and specificity
Non Gaussian diffusion
e.g. Kurtosis
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 70
S( ,t=)  , ) d
Models
La diffusion tensor imaging e la diffusione non gaussiana
4.
At least 15 DWI + SE
Diffusion Kurtosis imaging

## Slide 71
DKI acqua maggiormente interagente con microstrutture
Dinamiche piu’ lente b values piu’ alti di 1000 s/mm2
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 72
La diffusion tensor imaging e la diffusione non gaussiana
4.

## Slide 73
NMR Laboratory
NMR laboratory staff
Biomedicine:
Maria Giovanna Di Trani
(PhD student)
Michele Guerreri
(PhD student)
Riccardo De Feo
(rare disease project)
Clinical collaborators:
Neuroimaging Laboratory,
Fondazione Santa Lucia IRCCS, Rome, Italy.
Radiology Dpt., Policlinico Umberto I Sapienza Rome, Italy
Department of Diagnostic and Interventional Radiology, Molecular Imaging and Radiotherapy & Orthopedic and Traumatology Dip. PTV Foundation,”Tor Vergata” University of Rome,
Edificio Fermi stanza 319,
Edificio Segre’ Laboratorio 5
Silvia.Capuani@roma1.infn.it
Alessandra Caporale
Penn University (USA)
Marco Palombo
UCL (UK)
Cultural Heritage
Sveva Longo
(PhD student 50%UNIMe)