## Slide 1: Accelerator Summary
Yunlong Chi
Workshop on the Circular Electron-Positron Collider - EU edition
26/05/2018

## Slide 2: 25 Talks (3 plenary + 22 parallel )

## Slide 3
Two Circular Collider
Two Linear Collider

## Slide 4: CEPC CDR Parameters
 | Higgs | W | Z
Number of IPs | 2 |  | 
Energy (GeV) | 120 | 80 | 45.5
Circumference (km) | 100 |  | 
SR loss/turn (GeV) | 1.73 | 0.34 | 0.036
Half crossing angle (mrad) | 16.5 |  | 
Piwinski angle | 2.58 | 4.29 | 16.4
Ne/bunch (1010) | 15 | 5.4 | 4.0
Bunch number (bunch spacing) | 242 (0.68us) | 3390 (98ns) | 8332 (40ns)
Beam current (mA) | 17.4 | 88.0 | 160
SR power /beam (MW) | 30 | 30 | 5.73
Bending radius (km) | 10.6 |  | 
Momentum compaction (10-5) | 1.11 |  | 
IP x/y (m) | 0.36/0.0015 | 0.36/0.0015 | 0.2/0.0015
Emittance x/y (nm) | 1.21/0.0031 | 0.54/0.0016 | 0.17/0.004
Transverse IP (um) | 20.9/0.068 | 13.9/0.049 | 5.9/0.078
x/y/IP | 0.031/0.109 | 0.0148/0.076 | 0.0043/0.04
VRF (GV) | 2.17 | 0.47 | 0.054
f RF (MHz) (harmonic) | 650 (216816) |  | 
Nature bunch length z (mm) | 2.72 | 2.98 | 3.67
Bunch length z (mm) | 3.26 | 3.62 | 6.0
HOM power/cavity (kw) | 0.54 (2cell) | 0.47(2cell) | 0.49(2cell)
Energy spread (%) | 0.1 | 0.066 | 0.038
Energy acceptance requirement (%) | 1.52 |  | 
Energy acceptance by RF (%) | 2.06 | 1.47 | 0.76
Photon number due to beamstrahlung | 0.29 | 0.16 | 0.28
Lifetime due to beamstrahlung (hour) | 1.0 |  | 
Lifetime (hour) | 0.67 (40 min) | 2 | 4
F (hour glass) | 0.89 | 0.94 | 0.99
Lmax/IP (1034cm-2s-1) | 2.93 | 7.31 | 4.1

## Slide 5
parameter | Z | WW | H (ZH) | ttbar
beam energy [GeV] | 45 | 80 | 120 | 182.5
beam current [mA] | 1390 | 147 | 29 | 5.4
no. bunches/beam | 16640 | 2000 | 393 | 48
bunch intensity [1011] | 1.7 | 1.5 | 1.5 | 2.3
SR energy loss / turn [GeV] | 0.036 | 0.34 | 1.72 | 9.21
total RF voltage [GV] | 0.1 | 0.44 | 2.0 | 10.9
long. damping time [turns] | 1281 | 235 | 70 | 20
horizontal beta* [m] | 0.15 | 0.2 | 0.3 | 1
vertical beta* [mm] | 0.8 | 1 | 1 | 1.6
horiz. geometric emittance [nm] | 0.27 | 0.28 | 0.63 | 1.46
vert. geom. emittance [pm] | 1.0 | 1.7 | 1.3 | 2.9
bunch length with SR / BS [mm] | 3.5 / 12.1 | 3.0 / 6.0 | 3.3 / 5.3 | 2.0 / 2.5
luminosity per IP [1034 cm-2s-1] | >200 | >25 | >7 | >1.4
beam lifetime rad Bhabha / BS [min] | 68 / >200 | 49 / >1000 | 38 / 18 | 40 / 18
FCC-ee collider parameters

## Slide 6: LC design parameters

## Slide 7: Time schedule

## Slide 8: http://cepc.ihep.ac.cn
March 2015
April 2017
CEPC-SppC from Pre-CDR towards CDR
CEPCSppC baseline and alternative
decision processe recorded
Nov 2017
CEPC-SppC CDR
Preliminary Draft during
CEPC-SppC Mini review
CEPC-SppC CDR will be printed before May 2018

## Slide 9
CEPC Tunnel General Layout
IP1
IP3
IP2
IP4
LSS1
LSS2
LSS3
LSS4
LINAC
BTL
L=99.67km
3.32km
3.32km
3.24km
3.24km
1.20km
1.20km
1.20km
1.20km
10.2km
Yu Xiao

## Slide 10
主环隧道典型剖面
Typical cross section of collider tunnel
Collider ring tunnel and short auxiliary tunnel
Yu Xiao

## Slide 11
Main detector
主探测器
IP1 / IP3
3.32km
6.0~11.4x4.5
3.02km
3.5x3.5
Yu Xiao

## Slide 12: CEPC-SppC Tunnel Cross Sections
Tunnel cross section at arc-section
  Width: 6,000 mm. Height: 4,800 mm.
Tunnel cross section at RF-section
Width: 8,000 mm. Height: 5,500 mm.
Jianli Wang

## Slide 13
FCC – tunnel integration in arcs
  FCC-ee FCC-hh
  5.5 m inner diameter

## Slide 14
Catia Milardi

## Slide 15
Catia Milardi

## Slide 16: Effect of energy spread increase on polarization
Equilibrium polarization degree in region of Z-pole vs spin tune in two cases of wiggler mode
B+=0.5 T
energy spread =9.9e-4
spin tune spread =0.103
B+=0.6 T
energy spread =1.25e-3
spin tune spread =0.128
|wk|=10-3
Sergei A. Nikitin

## Slide 17: Tracking-based method to calculate F
Attention!
z stands for y!
S.A. Nikitin. Talk at 20th Intern. Spin Physics Symposium (SPIN 2012), 17-22 Sept. 2012, Dubna, Russia
Compare these two graphs!
Cross-checking OK!
Sergei A. Nikitin

## Slide 18
Depolarization effect of quantum fluctuations in presence of vertical closed orbit distortions
at CEPC has been estimated taking into account modulation of spin frequency by
synchrotron oscillations. Resonance harmonic amplitude is input parameter
Spin harmonic amplitude of vertical closed orbit distortion sources at Z-pole should be corrected to level £ 10-3 to ensure 50% equilibrium polarization degree
If this is done, it is possible to reach polarization in range (6-10)% in 45 GeV CEPC in time of (2-4) hours using, for instance, ten shifter magnets with moderate characteristics
Sensitivity of spin motion disturbances to transverse field imperfections is determined through Spin Response Function which has been calculated in two ways
At 45 GeV, expected harmonic amplitude of closest integer spin resonance calculated at typical magnitudes of misalignment (50 m, 310-4rad) is about 3 times larger than desirable one. Correction of resonance harmonics (k= 103 and k= 104) is needed. Similar problem was successfully solved at LEP
CEPC Z-pole polarization Summary
Sergei A. Nikitin

## Slide 19
Project | Beam charge | Normalized Injector emittans | Energy spread
SuperKEKB | 5 nC | ~20 mm mrad | 1%
C-τ Factory | 3 nC | ~10 mm mrad | 0.1%
FCC | 6.5 nC | ~6 mm mrad | 0.08%
Electron sources for FCC-ee
1. Beam charge, normalized beam emittance and energy spread are depended on the electron gun design.
2. High beam charge is needed => large area of the photocathode => beam emittance increasing
3. Ultra low energy spread is necessary => short beam longitudinal size
4. Normalized emittance of the injector is not too low, but taking into account the lengths of the linacs and possible errors of the real devices, low beam emittance of the e-gun can be useful.
The new ideas of the e-gun design and the cathodes material are required
A. Levichev, A.E.Levichev@inp.nsk.su 2018 Workshop on the Circular Electron-Positron Collider 2
A.E. Levichev

## Slide 20
Parallel RF power feeding.
Cavities are not connected with each other by RF power: process in one cavity doesn’t influence on every cavities
Organization of the free electric field distribution along the structure can be obtained by changing the individual coupling slot
In order to develop accelerating structure only one accelerating cells have to be calculated due to absence of the cavities connection by electromagnetic field
Aperture of the structure is defined by only beam motion and can be considerably reduced
Design of the structure allows using internal permanent focusing magnets.
Features:
RF gun based on the parallel coupled accelerating structure (PCAS)
Suggestion
A. Levichev, A.E.Levichev@inp.nsk.su 2018 Workshop on the Circular Electron-Positron Collider 6
A.E. Levichev

## Slide 21
The design of parallel coupled accelerating structure allows using the permanent focusing magnets and create the strong magnetic field along the cavities and save the beam size.
The travelling tube aperture can be decreased as significantly as it allows the beam dynamics.
This design of the RF gun allows us to consider the cavities as independent. The length and field amplitude can be tuned separately for every cavity.
Preliminarily results of beam dynamic simulations gave reason to hope that this construction is acceptable solution for high charge generation.
The prototype of the accelerating structure based on new design with parallel coupling between the cavities have been produced in BINP with operating frequency of 2450 MHz and successfully tested.
It is currently planned to perform tests the new parallel coupled accelerating structure with 2856 MHz .
Ir5Ce cathode is developed
The work function of the cathode is measured. According to this measurements (2.4 eV), the green laser can be used for tests with the cathode
Conclusion
In plan
Stress tests with the cathode
Measuring of the quantum efficiency of the cathode
RF gun production
A. Levichev, A.E.Levichev@inp.nsk.su 2018 Workshop on the Circular Electron-Positron Collider 20
A.E. Levichev

## Slide 22: High Energy CEPC Injector Based on Plasma Wakefield Accelerator
Presenter Chih-Hao Pai
Tsinghua University
Workshop on the Circular Electron-Positron Collider
May 25, 2018
Rome, Italy
Notes: I am here to present

## Slide 23
High Energy CEPC Injector Based on Plasma Wakefield Accelerator
Huge gradient (~100GV/m) + Tiny structures (~10-100um)
T. Tajima and J. M. Dawson PRL (1979) LWFA
P. Chen, J. M. Dawson et.al. PRL (1983) PWFA
Laser or beam Pulse
Wake
Trailing beam
Chih-Hao Pai
Notes: Intense laser or particle beam
2 special features: H+T

## Slide 24: Overall Concept Design CEPC injector
1.3GeV
3.4GeV
Chih-Hao Pai

## Slide 25: PWA Summary
e-/e+ acceleration to 45 GeV in HTR PWFA with single stage TR=3.5 is possible (10GeV electron beam driver)
e-/e+ acceleration to 100 GeV level in Cascaded HTR PWFA with TR=10 is possible (10GeV electron beam driver with higher charge)
Energy spread of 0.2% could be achieved by post processing using a plasma dechirper
Preliminary experimental tests could be performed in near future at FACETII of SLAC
Chih-Hao Pai

## Slide 26: CEPC Collider Ring SRF System
Collider parameters: 20180330 | H | W | Z
SR power / beam [MW] | 30 | 30 | 16.5
RF voltage [GV] | 2.17 | 0.47 | 0.1
Beam current / beam [mA] | 17.4 | 87.7 | 460
Bunch charge [nC] | 24 | 19.2 | 12.8
Bunch number / beam | 242 | 1524 | 12000
Bunch length [mm] | 3.26 | 5.9 | 8.5
Cavity number (650 MHz 2-cell) | 240 | 2 x 108 | 2 x 60
Idle cavities on line / ring | 0 | 12 | 60
Cavity gradient [MV/m] | 19.7 | 9.5 | 3.6
Q0 for long term operation | 1.5E10 | 1.5E10 | 1.5E10
Input power / cavity [kW] | 250 | 278 | 275
Klystron power [kW] (2 cavities / klystron) | 800 | 800 | 800
HOM power / cavity [kW] | 0.57 | 0.75 | 1.94
Optimal QL | 1.5E6 | 3.2E5 | 4.7E4
Optimal detuning [kHz] | 0.2 | 1.0 | 17.8
FM and HOM impedance and power, heat load
Gradient (stored energy) as high as possible
Input coupler power limit 300 kW (high risk)
Keep power level and RF distribution
HOM power per cavity limit 2 kW
Input coupler variable
Revolution frequency: 3 kHz (FM CBI)
SRF parameters and layout established in view of high Higgs priority, low construction cost and upgradability.
Beam cavity interaction issues are challenging but manageable:
FM and HOM CBI, parking cavities
HOM power of different fill patterns, parasitic loss
Gap RF transient, issues for Higgs on-axis injection
Jiyuan Zhai

## Slide 27: CEPC Booster SRF System
10 GeV injection | H | W | Z
Extraction beam energy [GeV] | 120 | 80 | 45.5
Bunch number | 242 | 1524 | 6000
Bunch charge [nC] | 0.72 | 0.576 | 0.384
Beam current [mA] | 0.52 | 2.63 | 6.91
Extraction RF voltage [GV] | 1.97 | 0.585 | 0.287
Extraction bunch length [mm] | 2.7 | 2.4 | 1.3
Cavity number in use (1.3 GHz TESLA 9-cell) | 96 | 64 | 32
Gradient [MV/m] | 19.8 | 8.8 | 8.6
QL | 1E7 | 6.5E6 | 1E7
Cavity bandwidth [Hz] | 130 | 200 | 130
Beam peak power / cavity [kW] | 8.3 | 12.3 | 6.9
Input peak power per cavity [kW] (with detuning) | 18.2 | 12.4 | 7.1
Input average power per cavity [kW] (with detuning) | 0.7 | 0.3 | 0.5
SSA peak power [kW] (one cavity per SSA) | 25 | 25 | 25
HOM average power per cavity [W] | 0.2 | 0.7 | 4.1
Q0 @ 2 K at operating gradient (long term) | 1E10 | 1E10 | 1E10
Total average cavity wall loss @ 2 K eq. [kW] | 0.2 | 0.01 | 0.02
Jiyuan Zhai

## Slide 28: N-doping research
After N-doping, Q0 increased obviously at low field for both 650MHz 1-cell cavities.
650S1: Q0=7e10@Eacc=10MV/m. But Q0 decreased quickly at high field (>10 MV/m) because of no BCP/EP after N-doping.
650S2: Quench at Q0=6.9e10@Eacc=8.8MV/m.
Vertical test results of 650 MHz 1-cell cavities
Vacuum and temperature curve during N-doping
N-doping of 650MHz 1-cell cavities
Vertical test of 650MHz 1-cell cavity
Peng Sha

## Slide 29: Vertical test of CEPC 650 MHz 2-cell Cavity
Vertical test result: Q0=4.0E10@19.2MV/m，which is close to the CEPC target (Q0=4.0E10@22.0MV/m).
Next, the CEPC target will be achieved by N-doping and EP, etc.
Vertical test of CEPC 650MHz 2-cell cavity
Peng Sha

## Slide 30: Test Crymodule of CEPC 650 MHz SRF
Test of HOM coupler
Design of main coupler is finished
Design of the test cryomodule is underway, which consist of two 650MHz 2-cell cavities and other components.
The assembly will be finished in the middle of 2019.
Peng Sha

## Slide 31: 650MHz High Efficiency Klystron R&D plan
FY 2016: done
  Finalize the gun and the collector design of the 1st conventional klystron prototype (UHFKP8001, Ultra High Frequency band Klystron Prototype with 800kW output power)
  Initialize the dynamics design of the UHFKP8001
FY 2017: done
  Finalize the interaction section and coil design of the UHFKP8001
  Preliminary mechanical design of the UHFKP8001
FY 2018: being carried out
  Finalize the mechanical design and fabrication of the UHFKP8001
  Infrastructure construction for the klystron brazing, baking and testing
  Finalize the interaction section design of the 2nd high efficiency klystron prototype (UHFKP8002)
  Design of the new gun and the new collector for the UHFKP8002
Zusheng Zhou

## Slide 32: 650MHz HEK R&D plan
FY 2019
  High power test of the UHFKP8001
  Finalize the mechanical design and fabrication of the UHFKP8002
  Finalize the interaction section design of the 3rd high efficiency klystron prototype (UHFKP8003), reuse the gun and the collector design for the UHFKP8002
FY 2020
  High power test of the UHFKP8002 (>75% efficiency to be expected)
  Finalize the mechanical design and fabrication of the UHFKP8003
FY 2021
  High power test of the UHFKP8003 (>80% efficiency to be expected)
  More klystron prototypes or klystron industrialization
Zusheng Zhou

## Slide 33: Mechanical design for 1st Prototype
Mechanical design achieved (L×W×H: 5.12m×0.87m×1.56m)
The manufacture of the UHFKP8001 will be completed this year and then the high power test will be started at the beginning of next year.
Zusheng Zhou
Main parameters | Goal
Frequency (MHz) | 650
Vk (kV) | 81.5
Ik (A) | 15.1
Perveance (µP) | 0.65
Efficiency (%) | >60
Saturated gain (dB) | >45
Output power (kW) | 800
1dB bandwidth (MHz) | ±0.5
Brillouin magnetic field (Gs) | 106.7
Reduced plasma wavelength(m) | 3.47
N cavities | 6
Normalized drift tube radius | 0.63
Normalized beam radius | 0.41
Filling factor | 0.65

## Slide 34: Design of the Collider magnets
Dual dipole magnet
  1 turn two turns.
Dual quadruple magnet
  large cross section to reduce power consumption
Single aperture sextuple magnets
Mei Yang

## Slide 35: Design of the Booster magnets
Booster Low field dipole magnet (31Gauss ~ 390Gauss )
  Iron dominated frame
    Core is diluted in two directions.
    Laminations with iron and Aluminum.
  Hollow coil frame
    Cosθ type coils with iron shielding.
    Flat top and bottom: adjust the field quality.
Mei Yang

## Slide 36
Low-power low-cost design for FCC-ee magnets
Twin-dipole design with 2× power saving
16 MW (at 175 GeV), with Al busbars
first 1 m prototype
twin F/D quad design with 2× power saving
25 MW (at 175 GeV), with Cu conductor
first 1 m prototype

## Slide 37: CEPC Vacuum chamber and RF bellow for storage ring
Aluminum vacuum chamber (Drawing)
(elliptic 7556, thickness 3, length 6000)
Copper vacuum chamber (Drawing)
(elliptic 7556, thickness 3, length 6000)
Electron ring
Positron ring
Function of the bellows module : allow thermal expansion of the chambers and for lateral, longitudinal and angular offsets due to tolerances and alignment,
Providing a uniform chamber cross section to reduce the impedance seen by beam.
A vacuum in the lower than 310-9 Torr for ring
Yongsheng Ma

## Slide 38: NEG coating of the inside chamber
NEG coating suppresses electron multipacting and beam-induced pressure rises, as well as provides extra linear pumping. Direct Current Magnetron Sputtering systems for NEG coating was chosen.
Ion sputtering pump
NEG coating pump
Vacuum Distribution
Oleg. B. Malyshev
Coating Facility DCMS
NEG coating for HEPSTF has reached the project`s aim
The film lifetimes with a thickness of 100 nm will be experimented.
The NEG coating is Ti, Zr, V, Hf alloy, deposited on the inner surface of the chamber through sputtering.
Yongsheng Ma

## Slide 39
FCC-ee arc vacuum prototyping & integration
The chambers feature lumped SR absorbers with NEG-pumps placed next to them.
Construction of chamber prototypes in coming months and integration with twin magnets
Vacuum chamber cross section: 70 mm ID with ”winglets” in the plane of the orbit (SuperKEKB-like);

## Slide 40
Heating
Discharges
Instabilities
High intensity particle beams are source of:
Pulsed (RF) currents on the pipe surfaces
Wakefields (beam-accelerator components interaction)
synchrotron radiation
Electron clouds (from positive charges)
Accelerator components for high current operation
high beam current EFFECTS
Degradation of beam quality
Iwall
Sasha Novokhatski, Mini Workshop, Diamond, January 30, 2013
Iwall
Egap
y
z
David Alesini

## Slide 41
1- The present generation of lepton factories has been very successful achieving or even exceeding their design luminosities. One of the main important ingredients to reach this results was the stable collision of very intense multibunch beams.
2- This has become possible due to careful design of the low impedance vacuum chambers components and devices to cope with beam instabilities.
3- The proper design of all these machine components is one of the key issue for the success of future particle colliders.
CONCLUSIONS
David Alesini

## Slide 42: Consideration of CEPC Cryogenics
Booster ring:
1.3 GHz 9-cell cavities, 96 cavities
12 cryomodules
3 cryomodules/each station
Temperature: 2K/31mbar
  Collider ring:
650MHz 2-cell cavities, 240 cavities
40 cryomodules
10 cryomodules/each station
Temperature: 2K/31mbar
Shaopeng Li

## Slide 43
CEPC Power Consumption – CDR
Table A3.9:
Wall plug efficiency = 23%
Weiren Zhou

## Slide 44
FCC-ee
FCC-ee
Weiren Zhou

## Slide 45
Power Summary
Future colliders, either circular or linear, require hundreds MW of power.
Circular ones more so because of synchrotron radiation.
But circular ones provide higher luminosity and more IPs, so the power per unit luminosity is actually lower.
The power suckers are RF and magnet.
Klystron efficiency is the key to reduce RF power.
2-in-1 design reduces magnet power by half
Quadrupole is the main consumer of power. Optimization between construction cost and operation cost has been carried out, but may have room for further improvement.
To make CEPC greener, permanent magnets will be employed in the two linac-booster transfer lines (similar to the Fermilab MI-8 line).
The required wall plug efficiency (23%) for CEPC is a tall order.
Innovative thinking and ideas are welcome.
Weiren Zhou

## Slide 46
Goal：
1) To increase the Jc of iron-based superconductor (IBS) by 10 times, reduce the cost to 20 Rmb/kAm @ 12T & 4.2K, and realize the industrialization of the conductor;
2) To reduce the cost of ReBCO and Bi-2212 conductors to 20 Rmb/kAm @ 12T & 4.2K;
3) Realization and Industrialization of IBS magnets and SRF cavities.
Working groups：1) Fundamental sciences study; 2) IBS conductor R&D; 3) ReBCO conductor R&D; 4) Bi-2212 conductor R&D; 5) Performance evaluation; 6) Magnet and SRF technology.
HTS R&D for SppC
“Applied High Temperature Superconductor Collaboration (AHTSC)” formed in Oct. 2016. Including 18 institutions and companies in China. Regular meeting every 3 months.
Proposal for
Strategic Priority Research Program
of Chinese Academy of Sciences (CAS)
Science and Technology Frontier Research
for High Field Applications of High Temperature Superconductors
Ranked No. 1 in 7 candidates
by Academic Committee of CAS !
Qingjin Xu

## Slide 47
10.2 T @ 4.2 K dipole field
in two apertures
(Performance limited by NbTi coils)
1st test result of the 1st high-field dipole magnet in China Feb. 2018
Magnet under test @ Hefei
Magnet fabrication @ Beijing
Test system setup @ Hefei
R&D of 12T Twin-aperture Dipole Magnet
Qingjin Xu

## Slide 48
Next step：Replace NbTi coils with new Nb3Sn coils to further increase the field，and insert the IBS coil to test its high field performance.
R&D of 12T Twin-aperture Dipole Magnet
IBS coil
2nd model dipole magnet(Nb3Sn+IBS)
2*100m IBS tapes
IEECAS
Qingjin Xu

## Slide 49
Worldwide FCC Nb3Sn program
Main development goal is wire performance increase:
Jc (16T, 4.2K) > 1500 A/mm2 50% increase wrt HL-LHC wire
Reduction of coil & magnet cross-section
3150 mm2
~1.7 times less SC
~10% margin
HL-LHC
~10% margin
FCC ultimate
5400 mm2
After only one year development, prototype Nb3Sn wires from several new industrial FCC partners already achieve HL-LHC performance
Conductor activities for FCC started in 2017:
Bochvar Institute (production at TVEL), Russia
KEK (Jastec and Furukawa), Japan
KAT, Korea
Columbus, Italy
University of Geneva, Switzerland
Technical University of Vienna, Austria
SPIN, Italy
University of Freiberg, Germany
  In addition, agreements under preparation:
  Bruker, Germany
  Luvata Pori, Finland
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 50
16 T dipole design activities and options
Cos-theta
Blocks
Common coils
Short model magnets (1.5 m lengths) will be built from 2018 – 2022
Russian 16 T magnet program launched by BINP recently.
Swiss contribution
Canted
Cos-theta
H2020
INFN
CEA
CIEMAT
PSI
LBNL
FNAL

## Slide 51
15 T dipole demonstrator (US-MDP)
All coil parts, structural components and tooling are available at FNAL
Coil fabrication and the work with mechanical structure are in progress
First magnet test in September 2018
Iron Laminations
AL I-Clamps
Fillers
Axial Rods
End Plates
StSt Skin

## Slide 52
16 T ERMC construction at CERN
First ERMC coil winding
Coil Reaction Tool
Coil Impregnation Tool
Aluminum shell
Magnet yoke
Axial rods
Dummy coils
Coil fabrication
  Winding of the first coil has been completed
  Preparation for reaction on-going
  All tooling for coil production ready
Magnet assembly
  components and tooling ready
  Dummy assembly to characterize the structure behavior on-going.

## Slide 53
Thank you all speakers & Thank you for your attention.