## Slide 1
Stefano Corradetti
INFN – Laboratori di Legnaro

## Slide 2
Stefano Corradetti
LNL January 2018
Status of the Project
Experimental activities

## Slide 3
First experimental activities
Choice of a suitable material for ion beams collection and production of the secondary targets;
Beam simulation with the SPES Front End;
Quantification of the ions on the secondary targets;
Purification processes development.
Objective:
prove the possibility of producing a radionuclide for radiopharmaceutical applications with the ISOL technique in Legnaro
Stefano Corradetti
LNL January 2018

## Slide 4
Test with the Front-End
accelerator at LNL
Stefano Corradetti
LNL January 2018

## Slide 5
The proton driver
Commissioning concluded
Stefano Corradetti
LNL January 2018

## Slide 6
The production targets
 | Standard (graphite) | Low density (MWCNTs)
Density (g/cm³) | 4.25 | 2.59
Diameter (mm) | 12.50 | 13.07
Thickness (g/cm²) | 0.41 | 0.41
Calculated porosity (%) | 58 | 75
UCx target already developed and tested on-line!
Other targets under development for specific radionuclides production
UCx target prototype
Porous titanium carbide (TiC)
Stefano Corradetti
LNL January 2018

## Slide 7
The ionization source
Ionized element | Desired radionuclide | Ionization source | Efficiency
Sr | 89Sr, 90Sr/90Y | SIS | ~ 20 %
Y | 90Y | PIS | ~ 1 %
I | 125I, 126I and 131I | PIS | ~ 20 %
Cu | 64Cu, 67Cu | PIS | ~ 10 %
Ag | 111Ag | PIS | ~ 6 %
Surface Ion Source (SIS)
Plasma Ion Source (PIS)
Copper Mass Scan (PIS)
63Cu (~70%)
65Cu (~30%)
Strontium Mass Scan (SIS)
Stefano Corradetti
LNL January 2018

## Slide 8
Beam acceleration and transport
Strontium and yttrium beams focalization
Electrostatic Triplets Quadrupoles and steereers system
Diagnostic boxes 1 and 2
(2 Faraday Cups and 2 Beam profilers)
Extraction -> 25 - 40 kV
Beam Transmission ~ 100%
Stefano Corradetti
LNL January 2018

## Slide 9
Isotope mass separator
Wien Filter
Natural Copper : Mass Scan
63Cu (~70%)
65Cu (~30%)
Stefano Corradetti
LNL January 2018

## Slide 10
Substrates for isotopes collection
For Sr, Y and Cu
Boiling point at 10-6 mbar
Sr ~ 500 °C
Y ~ 1500 °C
Cu ~ 1200 °C
1) Sodium Chloride
Sr1+ spot on the substrate
Cu1+ spot on the substrate
For I2
At 10-6 mbar I2 -> gas
2) Activated Carbon
40 mm
Polyvinyl Alcohol (PVA) as a binder
Stefano Corradetti
LNL January 2018

## Slide 11
Isotopes purification
2) Development of purification processes
Example: Separation of 90Sr from 90Y for 90Y purification
-> synthesis of an ion exchange inorganic material: sodium nonatitanate
1) Irradiated substrates dissolution and quantification of the deposed atoms
HNO3 0.1 M
Sr2+, Y3+ or Cu2+ quantification
via GF-AAS or ICP-AES
Iodine titration
Ongoing collaboration with UniPD-DSF and UniPD-DSC
Development of Seraparation Column for Y vs. Sr
Stefano Corradetti
LNL January 2018

## Slide 12
In vitro developments
2) Development of new targeting agents
1) Development of novel chelators for Ag+
Ongoing collaboration with:
TIFPA (Trento Institute for Fundamental Physics and Applications
DiSC (Department of Chemistry) UniPD
Ongoing collaboration with:
DSF (Department of Pharmaceutical and Pharmacological Sciences)
Nuclear Medicine Unit Advanced Technology Department (Santa Maria Nuova Hospital Reggio Emilia – IRCCS)
Radiolabeled molecule
Cancer cells
Novel molecules radiolabeled with innovative radionuclides as 111Ag
Stefano Corradetti
LNL January 2018

## Slide 13
First new project derived from ISOLPHARM in collaboration with PSI
ISOLPHARM_AG
Stefano Corradetti
LNL January 2018

## Slide 14
ISOLPHARM_AG

## Slide 15: ISOLPHARM_Ag Goals & organization
111Ag
Promising radionuclide for therapy:
b- emitter (average energy 360 keV)
Low percentage of associated g-emission
Good decay properties!
Development of Ag-based radiopharmaceuticals
Task 1: physics and computing
Task 2: production of Ag+, purification and chelators development
Task 3: cellular targets studies and radiopharmaceutical development
Stefano Corradetti
LNL January 2018

## Slide 16: Task 1 Physics and computing
The computing task can be divided into two different case studies, where cloud computing can be an extremely useful tool to perform fast and efficient simulations, related to both the target production and release of radionuclides of interest
Activities of this task:
1. Simulation of radionuclides production in the Isolpharm target
2. Simulation of radionuclides release from the Isolpharm target
μ
Stefano Corradetti
LNL January 2018

## Slide 17: Task 2: activities at LNL, DSF and DSC
1) Ionization and acceleration of Ag+ using the SPES Front End in off-line modality, the production of the secondary targets for Ag+ deposition and the deposition studies
2) Synthesis of a resin for 111Ag+ purification from 111Cd2+
3) Development of chelators for Ag+ (collaboration with Proff. Pastore and Di Marco (DSC))
Stefano Corradetti
LNL January 2018

## Slide 18: Task 3: activities at DSF
Targeting Agent
Linker
Radionuclide
Cellular receptor
Chelator
2) Calreticulin (CRT): a potential target for proton therapy combined with targeted radionuclide therapy
DSF objective: development of a targeting agent for CRT
1) Cholecystokinin receptor (CCK2R and CCK2i4svR)
DSF objective: development of small molecule-based ligands.
Targeting agent: synthesis ongoing
Linker moiety (collaboration with Dr. Francesca Mastrotto)
Chelator
Stefano Corradetti
LNL January 2018

## Slide 19: Cholecystokin receptor 2: CCK2R
Membrane G protein coupled receptor
Physiological ligand: gastrin and cholecistokin
Physiological distribution: cerebral cortex, hypotalamus, stomach mucosa
Overexpressed as it is and its spliced variant (CCK2i4svR) in cancers of the pancreas, medullary thyroid, lung, breast and ovarian, GI tract and colon
Attractive candidate for targeted imaging and therapy of malignant disease
Z-360: small molecule with high binding affinity for CCK2-R and CCK2i4svR (Kd ~ nM, depending on the substituents)
Stefano Corradetti
LNL January 2018

## Slide 20: Targeting CCK2R
Choice of the best linker moieties:
- optimizing length
- optimizing hydrophilicity
Targeting Agent
Linker
CCK2R
Radiolabeling and in vitro studies -> collaboration with Reggio Emilia Hospital (IRCCS)
Stefano Corradetti
LNL January 2018

## Slide 21: Calreticulin: a biological target
Increase the amount of surface exposed CRT depending on the dose and on the radiation type (photon and or particles)
Ionizing radiation
CRT lighthouse that could be used for targeting specific drugs and/or radionuclides.
Delivery of radionuclides in situ could help to overcome resistance problem or to target the high resistant cancer stem cells
Targeting Agent
Strategies:
Small molecules chemical library screening
Design of oligosaccharidic molecules
Other strategies?
Stefano Corradetti
LNL January 2018

## Slide 22: Collaboration with POLATOM and NCSR-DEMOKRITOS
Stefano Corradetti
LNL January 2018

## Slide 23: FETOPEN-RIA Call
Stefano Corradetti
LNL January 2018
HORIZON 2020
FETOPEN-RIA 2016/17
FET: Future and Emerging Technologies
FETOPEN: Novel ideas for radically new technologies
High risk, long-term, multidisciplinary, collaborative research
Novel and visionary thinking to open paths to new technologies
Early stage joint science & technology research
Totally non prescriptive
FETOPEN-RIA: Research and innovation actions
Expected impact: initiating a new line of technology or kick-starting an emerging innovation eco-system

## Slide 24: FETOPEN-RIA Call
Stefano Corradetti
LNL January 2018
High specific activity radiopharmaceuticals production using ISOL beams
Proposed work packages:
WP1 – Management: Organization and dissemination of the results (INFN)
WP2 – Study for radioisotopes production: target, ion source and beam transport development (INFN)
WP3 – Pharmaceutical form development (UNIPD)
WP4 – Radiochemistry (POLATOM)
WP5 – Radiopharmacy (NCSR)
FETOPEN-RIA requires the presence of at least three legal entities, situated in different countries (European or associated to Horizon 2020) and independent from one another. In case of more than three, there can be entities belonging to the same country.