## Slide 1
INFN Roma Tre Group
Stefano Mari, Andrea Fabbri, Paolo Branchini, Domenico Riondino, Cristina Martellini
RMU
Status

## Slide 2
CD trigger block schematic
Data for DAQ without trigger > 2 TByte/sec

## Slide 3
K7 Board
K7 Board
K7 Board
Supply, slow control
Supply, slow control
Supply, slow control
100 pin connector
100 pin connector
100 pin connector
100 pin connector
100 pin connector
100 pin connector
slow control
ethernet link
supply
supply
supply
RMU Reorganize & Multiplexing Unit
Specification:
125 input link from BEC organized in 7 RM Unit:
18x 1 Gb/s input link each
3x 6.25 Gb/s output link each
Each RMU has 3 separate FPGA board with 7x input link and 1x output link
Fanout can be improved with passive 2x or 4x splitter. Dedicated test can will be performed before next general meeting.
Splitters with calibrated propagation delay will be needed to ensure isosynchronous transmission.
RMU board
WR Node
(TTIM from Tsinghua)

## Slide 4
RMU status

## Slide 5
RMU status
Mother Board v1.0
  Mainly works as docking for K7, Power and USOP boards.
  Fit commercial 2U case for 19’’ racks.
  Supplies and control signals routing between different boards.
  I2C bus allows USOP slow control of the system
  A v2.0 is in design phase to implement WR functionality, especially reference clock distribution.
  V1.0 is equipped with clock fan-out from USOP to allow clock distribution test.

## Slide 6
RMU status
Power Board v1.0
  Four DCDC modules for FPGA supplies. Each one is followed by a power monitor (I/V measurement).
  Minor issue with capacitor footprint will be corrected on the v2.
+5V In
Control signals
Output Voltages
1.2V
3.3V
1.0V
1.8V
Power board block schematics

## Slide 7
RMU status
USOP v2.0
Developed by INFN Roma Tre and INFN Napoli for Belle II experiment.
Ten boards on-line at KEKB since 2016 without any failures.
Redundant ethernet link for remote control/diagnostic.
Development of FW for RMU slow control is started:
  Power supply monitor
  Transciever monitor
  Temperature monitor
  ….

## Slide 8
RMU status
K7 Board v1.0
  First prototype debug started on July 2017:
  FPGA ok
  Measured BER (with Xilinx IBERT) on each link is less than 10-13 @ 6.25 Gbit/s (no bit error when 1013 is trasmitted)
  No measurable cross talk
  FW development for isosyncrhonous is ongoing
  v2.0 gerber file is ready to be realized with fixes:
  Supply routing fix
  Added bulk capacitors for FPGA
  Minor footprint correction (thermal pad on clock IC…)

## Slide 9
Ongoing test
Up to 8 Gbps rate with no error
With a 8 Gbps output link data reduction
on the RMU will be
Different speed is possibile only for different quad
with Xilinx IBER Tool. A custom FW is under development
to test the final setup (7x 1.25 Gbps, 1x 6.25 Gbps)

## Slide 10
- Standard Via
- No Shield
- Blind Via
- No shield
- Standard Via
- Shielded
Simulation for differential line improvement

## Slide 11
FPGA Resources
FPGA Resources
Total = 2,501 W
A lot of resources are available for preliminary trigger analysis …
Power consumption estimation for an RMU ≈ 30 W

## Slide 12
Schedule
    Performances of the system will be evaluated in the next three months as function of specification.
    Open point:
          Optical link fanout (how many CTU?)
          Slow control protocol
          AC supply in the experimental hall
          All RMUs in a single rack / RMUs distributed in the experimental hall
Needed for AC/DC supply modules develpoment and WR switches provision

## Slide 13
Thank you!