## Slide 1: ATLAS Forward Proton (AFP) time-of-flight (ToF) detector: construction & existing experiences
WORKSHOP ON PICO-SECOND TIMING DETECTORS FOR PHYSICS AND MEDICAL APPLICATIONS
Tomáš Sýkora
on behalf of the ATLAS collaboration
Institute of Particle and Nuclear Physics
Faculty Mathematics and Physics
Charles University
16-18 May 2018, Turin
Notes: Good evening ladies s and gentlemen, it is my pleasure to be here with you in Valparaiso and to have an opportunity to show you several new results on behalf of the ATLAS collaboration.

## Slide 2: outline
ATLAS-AFP Collaboration: Technical Design Report for the ATLAS Forward Proton Detector, CERN-LHCC-2015-009; ATLAS-TDR-024-2015
ATLAS IBL Collaboration, Prototype ATLAS IBL modules using the FE-I4A front-end readout chip, JINST 7 (2012) P11010
J. Lange et al., 3D silicon pixel detectors for the ATLAS Forward Physics experiment, JINST 10 (2015) C03031
LANGE, J. et al., Beam tests of an integrated prototype of the ATLAS Forward Proton detector, JINST 11 (2016), no. 09, P09005
NOZKA, L. et al., Design of Cherenkov bars for the optical part of the time-of-flight detector in Geant4, Optics Express, 2014, vol 22(23), pp 28984-28996
NOZKA, L. et al., Construction of the optical part of a time-of-light detector prototype for the AFP detector, Optics Express, 2016, vol 24(24), pp 27951- 27960
CHYTKA, L. et al., Timing resolution studies of the optical part of the AFP time-of-flight detector, Optics Express, 2018, vol. 26, Issue 7, pp. 8028-8039
CHYTKA, L. et al., Time resolutions of FBK NUV3S and STMicroelectronics SiPMs, to be submitted
KOMAREK, T., AFP Time-of-Flight detector, Challenges in Photon Induced Interactions, 5-8 September 2017
motivation
AFP ToF detector
  principle
  schema & construction
beam & lab tests
  raw data results
  RCE data results
installation & commissioning
  low trigger efficiency
summary

## Slide 3: motivation

## Slide 4: ToF & Higgs particle
originally pp -> p + H + p, Forward Proton 420 (FP420), arXiv:0806.0302 [hep-ex]
beamline
beamline
ATLAS
p
Interaction Point
p
H0
p – forward proton

## Slide 5: cross section -> pile-up
pile-up is inevitable consequence of needed luminosity increase
arXiv:1310.5189v1 [hep-ph]
~ 0.05 nb ATLAS 2017 ~ 50 fb-1

## Slide 6: AFP ToF detector

## Slide 7
ctA
tC
ctC
tA
δ
A-side
C-side
ToF – principle (z-smearing only)

## Slide 8
long term goal 10 ps resolution, 30 ps at the beginning (10 ps corresponds to the spatial resolution of 2.12mm; see the next slide)
radiation hardness (forward region, very close to the beam)
full overlap with the AFP tracker detector
segmentation (multi-proton capability), rate 5 MHz per channel
usability as L1 trigger
ToF – requirements (original)

## Slide 9
need to effectively select correct event -> need to select correct vertex N vertices in Δ mm -> (assuming flat distribution & only z smearing) δ=Δ/(N-1) per vertex
-> needed time resolution
z & t smearing
(conditions close to HL-LHC!)
ToF – vertex, z & t smearing, time resolution estimate

## Slide 10: ToF & diffraction
Roman Pots at ~ 205 & 217 m; at both sides of the IP
AFP 217
AFP 205
AFP 205
AFP 217
beamline
beamline
ATLAS
p
p
Interaction Point
A-side
C-side
exclusive processes
low x-sections -> high μ
central diffraction, DPE
high backgrounds -> low μ
ToF is crucial
ToF is NOT needed
but good for additional cross checks
ToF is crucial for purity and background rejection
ToF future…?

## Slide 11: AFP ToF construction – schematic view
A-side
C-side
reference clock

## Slide 12
AFP – detector
p
ToF
tracker
ToF = 4 “trains”
1 train = 4 bars
flange prototype
flange

## Slide 13: ToF construction – opto-electronic part
Photonis miniPlanacon XPM85112 MCP-PMT, one inch, 16 channels
4x4 matrix of fused silica bars (Suprasil), L-shaped
bars are rotated 48◦ w.r.t. the LHC beam by Cherenkov angle θ in Suprasil
each bar glued from two parts using Epotek 305
typically ∼ 100 photons reach the PMT per bar
⇒ ∼ 30 photoelectrons
particle passes through a train (= 4 bars)
→ 4 “independent” measurements
→ 1/√4 σsingle measurement
for train made of n bars -> 1/√n
θ
https://www.photonis.com/uploads/datasheet/pd/Mini-PLANACON-4x4-datasheet.pdf
join
edge

## Slide 14: AFP ToF detector beam tests

## Slide 15
Beam tests performed at the H6 beamline, CERN SPS North Area (120 GeV pion/muon beam)
2014 (Photonis PMTs)
  November – integration with tracker and readout test
2015 (Photonis PMTs)
  September – 2 bars per train resolution and basic crosstalk studies
2016 (Photonis PMTs)
  July – two ToF detectors, several full trains measurement, cross talk, LGADs measurement
  September – ﬁnal integration test, full 4x4 ToF, irradiated LGADs measurement
  October – interference related measurement
2017 (Photonis PMTs)
  June/July – ALD coated MCP- PMTs tested, vacuum test, crosstalk, analog-digital trigger module test
  September – re-measurement of new PMTs, test of digital trigger module
2018 (Photonis & Hamamatsu PMTs)
  May/June – measurement of new ALD coated PMT (Photonis), of Hamamastu PMTs, of 3rd stage of PA, interference reduction & shielding, irradiated PMTs, irradiated bars, rad hard TDC (see J. Pinfold talk) & integration test,
  July/August – measurement of glue-less bars, Hamamatsu PMT tests, new ToF signal path test
  September – new (3ps) TDC tests, digital trigger tests

## Slide 16: beam tests 2016
June/July 2016 - box
September 2016, 2017 flange & RP

## Slide 17: beam & lab tests – raw data results (2016 June-July data)
PMT’ = PMT + PAa + PAb + scope + trigger (SiPM*) – lab measurements (Olomouc) – σPMT’ < 20 ps/channel laser signal, directly into a PMT channel, signal amplitude to correspond to a minimally ionizing particle
*STMicroelectronics NRD09 1
PMT’ + 1 train
PMT’ + 1 bar
trigger subtracted
PMT’ + 2 bars
uncertainty ± 1 ps in σfit, ± 2 ps in FWHM

## Slide 18: resolution vs distance from the edge (2016 June-July data)
the position of edge is different on the A & C sides

## Slide 19: beam & lab tests – raw data results (2017 vs 2016) I
new PMTs – ALD coated, coax cable removed & resistors removed, sapphire window, vacuum tight sealing
Serge Duarte Pinto, Photonis
observed effects: 1) ringing
2) (much) higher cross talk between channels
3) worse time resolution per bar, comparable per train
original
modified

## Slide 20: beam & lab tests – raw data results (2017 vs 2016) II
cross talk 2017 (UTA)
signal train
> 50% of signal!
another comparison
cross talk 2016
cross talk 2017
cross talk does represent a problem if
time resolution is affected (next slide)
there is channel rate limitation, e.g. 8 MHz due to TDC; at μ = 50 we expect 32 MHz across the detector but now signal is NOT spread across, rather goes everywhere -> rate will be exceeded

## Slide 21: beam & lab tests – raw data results (2017 vs 2016 September) III
note worse resolutions
w.r.t. slide 13 RP & flange! ->
resolution deterioration
both RP+flange

## Slide 22: beam & lab tests – RCE data results, flange & RP (2016)
] σHPTDC = 17 ps & σMCP’ = 17 ps -> expected value ~ 24 ps; consistent
20.6 ps

## Slide 23: contributions to ToF detector resolution
PA a & b: 3 − 4 ps (each)
CFD: 5 ps
HPTDC: 15 − 17 ps
reference clock: 6 ps (conservative)
SiPM resolution (for beam test): 11-13 ps
for full system we expect(ed) resolution better than 25 ps

## Slide 24: scaling √N & cross talks
train 6
√N
optical “cross talk”
PMT charge sharing
anode 2
photons
anode 1
electrical
crosstalk
(charge
sharing)
pe rebound
optical crosstalk
+
e-
+
+
both processes – optical cross talk & charge
sharing, by their natures, cannot spoil √N scaling
it is electrical coupling of channels, what causes violation of √N scaling
based on slide 16
RCE, train 2, slide 21,
single bar (av.) 33 ps, full train 21 ps, ratio ¼=1.57
ratio ¼=1.43

## Slide 25: scaling √N & electronics
no signal
signal
background
signal
not optimized signal path
optimized signal path
TDC
  cross talk presented when channels on the same TDC chip -> cure = mapping channels from the same train to different chips
  still, a signal in one channel influences another channel -> software corrections of data
  final cure (hope) – new “pico” TDC
PAb
  crosstalk between channels; minimized by improvement of grounding of powering part
cables & connectors
  part of the signal path not optimized for transport of an analog -> reflections, cross talk (c.f. plots)

## Slide 26: interference I
moving ToF into a RP lead to deterioration of time resolution
we tried to find source, one of them was interference coming from the (LHC safety) TETRA system (429.6 MHz) [different frequencies on surface and in the tunnel] the estimate, made based on real data noise shape + real signal -> worsening by < 1 ps
will be tested
attempts to shield it; additional aluminum sheet, ferrites on cables

## Slide 27: installation & commissioning

## Slide 28
EYETS: 12 Dec 2016 – 30 Apr 2017
complete AFP

## Slide 29: MCP-PMT and vacuum
in the AFP ToF detector construction a MCP-PMT is placed in vacuum; it is not LHC vacuum, but rather rough vacuum (10-40 mbar), which puts us in worse location of Paschen’s curve
PMT HV connections were tested to be safe in vacuum (Olomouc & CERN)
during one of the tests, just before the installation, one of the tested PMT tripped and it was not possible to operate it under vacuum anymore; Photonis provided us a solution
new, fully (under vacuum) sealed PMTs were produced by Photonis for our experiment
1.33
0.13
13.33
133.32
1333.22
pd [mbar cm]
https://en.wikipedia.org/wiki/Paschen's_law

## Slide 30: SiT – ToF correlation
beam test

## Slide 31: SiT trigger efficiency – beam test (2016)
beam test September 2016, CFD threshold dependence, similar values during October 2017 BT single bar for the threshold 250 mV (max in tunnel) > ~60 % -> minimal expected efficiency of the trigger 2/4 (tunnel) 80%

## Slide 32: ToF bar efficiency (trigger by SiT)

## Slide 33: SiT – ToF trigger efficiency

## Slide 34: possible reasons (as considered historically)
rate vs PMT
glue/bars deterioration due to irradiation
voltage
PMT lifetime (cumulated charge)

## Slide 35
tests at UTA
all except for Photonis *97 performed at 20p.e.,
Photonis *97 at 10 p.e.
35

## Slide 36
36
LED test Photonis 2097
3 x PA
HV & rate scans
Photonis
PMT behavior different, as expected (R is different)

## Slide 37
PMT behavior very similar, as expected (R is the same)
37
3 x PA
HV & rate scans
Hamamatsu

## Slide 38
to be able to operate we need to go with gain/HV lower
we have to use 3rd stage of PA
we need to reduce noise & interference
ad 3) so far the campaign in Pilsen was successful, reduction of interference by 15 dB, noise to 5mV (P2P)
conclusion high rate measurements

## Slide 39: glue & bar irradiation
in 2017 we got ~ 50 fb-1
measured (irradiated) bar transmissivity at λ = 280 nm showed drop to 62% it corresponds to less than 20 kGy
at 20 kGy, estimate is we should not loose more than 1/5 of light;
absorption length should not play a significant role
-> the trigger efficiency was not caused by irradiated optical detector parts

## Slide 40: PMT voltage
  PMTs gain goal was 5×104: actual gain was 1×104  CFD threshold inefficiency …
 |  | gain vs HV from spec. sheets |  | required gain - extrapolated HV |  |  | 
Ser No. | RMCP [MW] | 1.00E+05 | 1.00E+06 | 7.00E+03 | 1.00E+04 | 5.00E+04 | Comment
2069 | 17 | 2320 | 2650 | 1939 | 1990 | 2221 | A/C-Far 2017
2086 | 48 | 2230 | 2530 | 1884 | 1930 | 2140 | A/C-Far 2017
2090 | 33 | 2290 | 2630 | 1897 | 1950 | 2188 | 
2097 | 29 | 1920 | 2165 | 1637 | 1675 | 1846 | ALD PMT 2017
2096 | 36 | 2005 | 2310 | 1653 | 1700 | 1913 | ALD PMT 2017
2110 | 40 | 2065 | 2365 | 1719 | 1765 | 1975 | New ALD PMT 2018

## Slide 41: PMT lifetime
  PMT life time (~1 C/cm2) was exceeded: ~3 C/cm2 -> gain deterioration
AFP, CERN, 10.5.2018
-> ALD needed

## Slide 42: summary
AFP ToF detector installed at the beginning of 2017
its time resolution, based on results of several beam & lab tests, expected to be better than 25 ps
very low trigger efficiency observed in 2017
several possible sources considered and studied, it led to addition of another stage of PA (requesting noise & interference suppression)
AFP ToF should be re-installed (after May/June beam test) during TS1 period (June 21-24 2018)
we expect improvement in future – pico TDC (<=3 ps), glue-less bars, improvement in signal path