## Slide 1: Computing and Software
Emanuele Leonardi
on behalf of the Computing Working Group
PADME General Meeting - LNF March 8th-9th, 2018

## Slide 2: Summary
On-line Computing
  DAQ Hardware
    Crates, Servers, Network
  DAQ Software
    Data flow, zero suppression, data formats
  DCS → Georgi’s talk
Off-line Computing
  GRID resources
  Off-line software services
Simulation and Reconstruction → my talk tomorrow

## Slide 3: Crates and Boards
2 VME crates CAEN 8100
  21 slots, 15/14 used by V1742, 6/7 available (2 trigger boards, etc.)
1 VME mini-crate CAEN 8004 (for Target)
  Currently in use for crystal tests
V1742: 30 mounted in crates (15+14+1) and 3 spares
  1 spare has ch0-3 with 2Vpp dynamics and is «in visione» from CAEN
  1 spare (first board acquired by PADME) is a VX1742
  1 spare is in use for crystal tests

## Slide 4: Optical fibers
Short (30 cm) single optical fibers (daisy chain within crate)
  23 (12+11) needed, only 14 available
  20 additional ordered from CAEN
Long dual optical fibers (crate to server connection)
  7 (3+3+1) needed, 14 available
  Length is 5m: not enough for the new BTF area layout!
  8 new 20m dual fibers ordered from CAEN

## Slide 5: Other cables
Clock short cables: 28 available, all used, no spares
  Order 3 spares from CAEN
LVDS cables for DAQ control signals distribution
  S-in, Run start/stop, Busy, …
  Still to define what is exactly needed

## Slide 6
Current crate status
15/14 boards per crate: 5+5+(5/4) dist to 3 ports of A3818
1 board on VME mini-crate for Target to 1 port of A3818

## Slide 7
Server Rack
VME Rack
VME Rack
VME Rack
HV
HV
HV

## Slide 8
2 x Dell PowerEdge R730xd
2 ports 10Gbps fiber SR
4 ports 1Gbps copper
2 x Dell PowerEdge R630
4 ports 1Gbps copper
Free PCI slot for 10Gbps
3 x Cisco 2960x
Stackable
2 ports 10Gbps fiber LR
4 ports 10Gbps fiber SR
144 ports 1Gbps copper
2 x Huawei FusionServer RH1288 v3
2 ports 1Gbps copper
Slot for 4 ports 1Gbps copper
L1 + data buffer
DAQ + L0
RC, DCS, services
On-line Servers
1 Dell PowerEdge moved to Tier2 as off-line manager. 10Gbps board added.
First server already in use, second server available at Tier2: to be added next week.

## Slide 9
RC, DB, DCS server
L1 and disk storage servers
DAQ node (l0padme4)
Trigger system
DAQ VME crates
PADME central switch
Online Monitor server
This setup will be moved to BTF as soon as the new experimental hall is ready

## Slide 10
L1_2
L1_1
LNF Net
Online VLAN
DCS VLAN
HV
CTRL
Probe
RC+DB+DCS
Tier2
Display
Control Room
LNF IT Building
Experimental Area
OM
Trigger
L0_1
L0_2
IPMI VLAN
…
Experimental data
IT
CNAF
KLOE2
TimePix
Mimosa
1 Gbps
10 Gbps
Networking

## Slide 11: Optical link between IT and BTF
IT
T2
LAT
BTF
CR
Available now
To be installed
1 Gbps
10 Gbps

## Slide 12: Data Flow
L0/L1 modules based on existing software
  L0: PadmeDAQ (read data from V1742, apply 0-suppression)
  L1: PadmeLevel1 (merge data from all sources, write ROOT file)
Modifications needed:
  PadmeDAQ: split data reading from 0-suppression to optimize CPU usage efficiency
  PadmeLevel1: include data from Trigger and Control system
    later also from TimePix

## Slide 13: I/O Infrastructure
New I/O infrastructure (in GO language)
  DARC: Data Acquisition Resource Controller
  Start/Stop of module
  Module control
  Connects to standard ports of module and handles passage of data from one module to another
  Can send data from one module to multiple modules
    E.g. Output of L0 can be sent to L1 and to Online Monitor
(Almost) no modifications needed to current programs
  The new infrastructure is seen as standard I/O to file
See Franz’s presentation of last December for details.

## Slide 14
PadmeDAQ
Padme0Supp
Online Monitor
PadmeLevel1
…
DARC wrapper
DARC wrapper
DARC wrapper

## Slide 15: 0 Suppression
Need 0 suppression to reduce data from 100MB/s to O(10MB/s)
Can take advantage of multiple CPU cores in L0 servers
  For each board: DAQ on one core, 0 suppression on another
Can implement several different 0sup algorithms
  Optimized for specific detectors (ECal, SAC, Veto, Target)
PadmeDAQ
Padme0Supp
Core 1
Core 2
2.6MiB/s
3.5MiB/s
× 30 = 78MiB/s
× 30 = 105MiB/s
(32ch + 4trg) × 1024smpl × 12bit × 50Hz = 22.1184 Mbps = 2.6MiB/s
O(10MB/s)
PadmeLevel1

## Slide 16
DAQ data format
Added board serial number to file header
Enlarged event status bit pattern
Added code of 0-suppression algorithm used
  Status pattern
  b0: [0=event is empty|1=event has data]
  b1: [DRS4 corrections 0=not applied|1=applied]
  (b2,b3): [0-suppression 00=off, 01=flagging, 10=rejection, 11=reserved])
  b4: board fail (BF) flag
(b5-b9): reserved

## Slide 17
TRawEvent | 
UInt_t | fRunNumber
UInt_t | fEventNumber
TTimeStamp | fEventAbsTime
UInt_t | fEventRunTime
UInt_t | fEventTrigMask
UInt_t | fEventStatus
UChar_t | fNADCBoards
TClonesArray* | fADCBoards
TADCBoard | 
UChar_t | fBoardId
UInt_t | fBoardSN
UShort_t | fLVDSPattern
UInt_t | fBoardStatus
UChar_t | fGroupMask
UInt_t | fEventCounter
UInt_t | fEventTimeTag
UChar_t | f0SuppAlgrtm
UInt_t | fActiveChannelMask
UInt_t | fAcceptedChannelMask
UChar_t | fNADCChannels
TClonesArray* | fADCChannels
UChar_t | fNADCTriggers
TClonesArray* | fADCTriggers
TADCChannel | 
UChar_t | fChannelNumber
Short_t | fSamples[1024]
TADCTrigger | 
UChar_t | fGroupNumber
UShort_t | fStartIndexCell
UChar_t | fFrequency
Bool_t | fTriggerSignal
UInt_t | fTriggerTimeTag
Short_t | fSamples[1024]
RAW data format
fBoardSN, fBoardStatus, and f0SuppAlgrtm are copyed from the DAQ data format
As the new format is a superset of the previous format and the old class interfaces are respected, all code currently in use for analysis should in principle work with files in the new format (need to recompile using the new libraries, of course).
I am now studying how to create code that can use both old and new format (possible according to ROOT).
fEventAbsTime is the global UTC time on the L1 server when the event is merged. Servers use NTP so timing should be good down to the ms level.
fEventRunTime is the time from the start of the run. It is computed taking into account the timing information of all the boards (which should in principle be well synchronized).
fEventTrigMask and fEventStatus are 32 bits patterns reserved for future use.

## Slide 18: GRID Resources
CPU: 4000 HEPSpec financed by INFN (2017+2018)
  2500 HS at LNF Tier2 (1000 HS available)
  1500 HS at CNAF Tier1
Disk: 90 TB net disk storage financed by INFN (2017)
  80 TB at LNF Tier2 (available)
  10 TB at CNAF Tier1 (available)
Tapes: 500 TB at the CNAF Tier1 tape library
  300 TB at the KLOE2 tape library in LNF for the emergency backup of experimental data

## Slide 19: Off-line setup
PADME DAQ
PADME
Offline Manager
KLOE2
Tape Library
LNF Tier2
Disk System
CNAF Tier1
Tape Library
CNAF Tier1
Cluster
LNF Tier2
Cluster
LNF
CNAF
GARR Backbone

## Slide 20: Data Acquisition
PADME DAQ
KLOE2
Tape Library
LNF Tier2
Disk System
CNAF Tier1
Tape Library
CNAF Tier1
Cluster
LNF Tier2
Cluster
LNF
CNAF
GARR Backbone
1
2
3
PADME
Offline Manager

## Slide 21: Simulation
PADME
Offline Manager
PADME DAQ
KLOE2
Tape Library
LNF Tier2
Disk System
CNAF Tier1
Tape Library
CNAF Tier1
Cluster
LNF Tier2
Cluster
LNF
CNAF
GARR Backbone
Job submission and control
1
2
3

## Slide 22: Reconstruction
PADME
Offline Manager
PADME DAQ
KLOE2
Tape Library
LNF Tier2
Disk System
CNAF Tier1
Tape Library
CNAF Tier1
Cluster
LNF Tier2
Cluster
LNF
CNAF
GARR Backbone
Job submission and control
1
2
3
4
5

## Slide 23: Off-line Software
Data mover already available
  Used to automatically backup all test beam data
  Some adjustments needed after water flood at CNAF last October
  Some data were lost but full dataset still on disk system at LNF
Job submission system at (working) prototype level
Some basic services still under development
  File Library, Calibration DB, etc.