## Slide 1: Beam for PADME run 2018
PADME collaboration meeting
9 marzo 2018
BTF + LINAC team

## Slide 2: Sparse thougths on setup and diagnostics
No action on LINAC and DANE complex in general until March, 30
  LINAC maintenance will follow, for 2 or 3 weeks
This brings us to the beginning of April, at the start of BTF upgraded beam line AND of the PADME setup installation
  This implies no beam in BTF before the setup is ready
  Some work on the LINAC optimization can be done, with transport dipole off
    But this implies very limited diagnostics
Most probably, no MIMOSA will be available, at least until summer, so no tracking in vacuum
  Some information on beam spot, at lower resolution, from PADME active target
  Beam imaging by FitPIX Silicon pixel detectors downstream the PADME vessel can be provided (PADME dipole dispersion + multiple scattering on windows and air)
Timing information with quick feedback can come from PbF2 small angle calorimeter

## Slide 3: Things to do: high priority
  Configuration 1
  LINAC electron mode, maximum possible energy: >600 MeV
  BTF target in, 2 x0
  Energy selection: >500 MeV
  Configuration 2
  LINAC positron mode, maximum possible energy: >500 MeV
  BTF target out
  Energy selection = E LINAC
Prepare beam with minimal requirements for PADME in at least 2 configurations
  In both configurations:
  Long pulse: 150 ns or longer
  Beam spot at target 1 mm
  SLTTB02 aperture < 1 mm, SLTTB04 aperture < few mm
  SLTTB01, SLTTB03 and LINAC current tuned to get required intensity:
    102 positrons* /pulse

## Slide 4: Things to do: lower priority
  Tune selected energy with similar positron beam pulse length, spot size and intensity at different values, at least:
    300 MeV
    250 MeV
Prepare beam with minimal requirements for PADME in at least one of the 2 main configurations, and in addition:
Prepare electron beam configurations, with as much as possible same parameters of positron beam

## Slide 5: Some considerations: running mode
Configuration 2 (positrons produced at positron converter and accelerated by the LINAC to required energy, no BTF target) should be better from the point of view of:
  Lower background (beam-related), due low energy photons in the BTF hall, coming from the production target
  Allows running the LINAC at lower current for getting the required intensity:
    Maybe even to loo: need to cut the beam with collimators anyhow (again background…) and stability issues
  Allow running at much higher positron intensity (for “special runs” aimed at checking pile-up or dump mode)

## Slide 6: Some considerations: beam-setup
Need one or more configurations for setting up the beam?
  PADME target in, PADME dipole on (i.e. normal configuration):
    Can monitor the spot with limited resolution on the target, and monitor the spot after magnet dispersion with a FitPIX in the beam path at the exit of the vacuum vessel
  PADME target out, PADME dipole off:
    Beam on SAC. Can provide beam timing but not the spot and the intensity
    Add a FitPIX in front of SAC?
    Leave now some more space (at least 10 cm) in the design stage

## Slide 7: Some considerations: operations
Changing and optimizing the beam in different configurations requires TIME and can spoil stability
Not enough experience for having an estimate of needed time for setup
Basic beam requirements should be clearly stated and monitored
Adequate feedback to machine staff has to be provided