## Slide 1: Status of Simulation and Physics Performances Studies
G. Battistoni
On behalf of many others

## Slide 2: Simulation Update: V14
Geometry of Electronic Setup fully handled by the SHOE software: (S. Valle + M. Franchini)
in /Simulation/foot_geo.h → constants, positions, distances, etc
in /libs/src/TADETbase/TADETparGeo.cxx and .h → methods to write geometry for each detector (both root and FLUKA geo)
/Simulation/MakeGeo.cxx → main code that produces FLUKA geo (recalls methods described in the libraries).
In this way the reconstruction software is ready to reconstruct the events with the same geo used to produce simulations
Of course from now on the management of simulation geometry is less immediate and some dedicated training is necessary

## Slide 3: Studies in view of magnet definition
- Single magnes length 7 cm
- Center-to-center distance of magnetes: 12 cm
Single magnet length 10 cm
Center-to-center distance of magnets: 12 cm (gap btw magnets ~2cm, not realistic)
V14.1
V14.0

## Slide 4: Importance of B•dl: improvement in p resolution with 10 cm magnet (M. Franchini et al.)

## Slide 5: Momentum resolution for higher energies

## Slide 7
Impact of detector resolution

## Slide 8
Impact of detector resolution

## Slide 9: New BGO Crystals (truncated pyramid)
2.2 x 2.2 cm2
3.0 x 3.0 cm2
24 cm
The most simple Calorimeter Design:
19x19 crystal matrix
Some specific simulation study is in progress in view of next test beam activity to be performed at CNAO
Initial guess: to be modified!!!
(see yesterdays’s talk about calo)

## Slide 10: V14.1.2: very first implementation of new calorimeter design in FLUKA geometry
On TIER3:
/gpfs_data/local/foot/Simulation/V14.1.2
16O_C2H4_200_1.root (107 primaries)
More difficult job: it’s not a simple body in FLUKA, it has
to be built using planes in space.
Mechanical boxes to be considered.
See yesterday’ talk about calo
Classes for SHOE not yet implemented!
Aachen prototype @HIT (145 crystals)

## Slide 11: Analysis of Aachen prototype results (as presented on May 8, M.Emde & R. Hetzel)

## Slide 12: Some issues recently emerged which could affect the expected performance:
Magnetic deflection and possible loss of detector acceptance in the downstream region
Longer magnets: how to recover angular acceptance
Effect of uncertainties in the knowledge of magnetic map (position, alignement,…)
Stability of B field of permanent magnets and radiation damage
Actual resolution along z coordinate of Intermediate Tracker

## Slide 13: Deflection in the case of 2 magnets with aligned B: possible loss of efficiency (R. Spighi)
Calo: Shift -5.1 cm
MSD: Shift -0.7 cm

## Slide 14: Possible alternatives for the field orientation of the two magnets
2nd magnet with opposite magnetic field orientation with respect to 1st magnet
On TIER3:
/gpfs_data/local/foot/Simulation/V14.2
16O_C2H4_200_1.root (107 primaries)
2nd magnet with same magnetic field orientation as 1st magnet
On TIER3:
/gpfs_data/local/foot/Simulation/V14.2inv
16O_C2H4_200_1.root (107 primaries)
Under investigation

## Slide 15: V14.2
- Single magnet length 10 cm
- Center-to-center distance of magnetes: 15 cm, gap ~5 cm, as recommended after FOOT Mech Meeting
- ITR and MSD shifted downstream
Suddenly we realize a problem…

## Slide 16: Angular acceptance vs Magnetic Lenght vs Tracking Detector Size
L ~31 cm
d ~7 cm
Having kept constant to r~3.5 cm the radius of the magnet bore reduces semi-aperture of the cone to ~ 6.4°
In order to recover 10°
semi-aperture we would need r~ 5.5 cm
But this would be useless with MSD size of 9x9 cm2

## Slide 17: A possible suggestions for MSD in case of larger diameter of magnet bore:
Increase number of detector layers from 3 to 4, alternating the following 45° rotation (L. Servoli):
The mimimum diameter of the circle covering at least 2 points is ~10.6 cm
4 point coverage
2 point coverage

## Slide 18: Alternative magnet design:
Two different magnets
MSD can be placed as close as possible to the exit of magnets
L ~25 cm
d ~8.8 cm
Here the gap can be even made smaller!
Reduced material and cost
Reduced extension of fringe field
Warning:
maybe we loose something in B•dl

## Slide 19: Initial studies on the uncertainties on mag field (Mi+Bo)
500 µm uncertainty on Intermediate Tracker long coordinate: no significant effect on resolution. A small bias in momentum reconstruction
1 degree disalignment between the two magnets: no significant effect
Alternate alignement of magnets
Systematic error in magnetic map coordinates
Different studies still in progress

## Slide 20: Smearing tests (M. Franchini)
Gaussian random smearing on the magnetic field components read from the magnetic map
Position not smeared

## Slide 21: Radiaton Damage in Permanent Magnets
We have been recently made aware that permanent magnet may suffer magnetization variations under irradiation (For ex.: M. Schanz et al «High energy proton induced radiation damage of rare earth permanent magnet quadrupoles», Rev. Sci. Instr. 88 (2017) 125103)
Some literature available: mostly related to e.m. radiation but also to neutrons and in few cases to protons
Apparently the damage is ~independent from the nature of radiation. It is of course related to dose/fluence in the magnet
Mainly two different materials: Nd-Fe-B and Sm-Co. The latter (our initial choice) is reported to be much more radiation resistant
For a review: A.J. Samin «A review of radiation induced demagnetization of permanent magnets», Journal of Nuclear Materials 503 (2018) 42-55
Specific paper on 200 MeV protons: Ito et al, NIM B183 (2001) 323)

## Slide 22
SmCo magnet
Neutron fluence:
it seems that SmCo magnets can tolerate up to 1020 n/cm2
NdFeB magnets
A more careful study is however recommended
Should we organize an irradiation test on a sample?

## Slide 23: Dose in the magnets. Preliminary simulation study
Dose maps in cylindrical coordinates (integrated in Phi)
16O beam @ 200 MeV/u, (SmCo magnets)
However: not fully realistic environment, no beam halo has been considered!
Neutron contribution
All hadrons
Scale is in GeV/g/primary. To get Gy multiply by 1.602 10-7 The integral is 8.8 10-11 Gy/primary in the first magnet and 1.2 10-10 Gy/primary in the second. Neutron contribution is ~4% Considering runs with 107 - 108 primaries we shoul be on the safe side…

## Slide 24: Fluence in the magnets. Preliminary simulation study
Neutron contribution
All hadrons
Scale is in particles/cm2/primary.

## Slide 25: Study of Fragmentation in Scintillator (A. Kraan)
Fragmentation grows with thickness
Z=6, A=12
Z=8, A=16
Z=7, A=14
Plane 1 or 2
Plane 2
Plane 1
Z=5, A=10
Small thickness (3 mm):
+ less fragmentation
Landau shape for Z=1, 2, 3 at all energies (not shown)
Large thickness (6 mm):
More fragmentation
More expensive
+ More gaussian shape: Z=4 already ok
Fragmentation vs bar thickness

## Slide 26
Z=8, A=16, E=200 MeV/n, d=6 mm
Compare energy deposition in scintillator for events with and without primary fragmentation
Events with no primary fragmentation
Events with primary fragmentation
Fragmentation vs bar thickness
Deposits are much more variable, can be up to 250 MeV (but rare)

## Slide 27
Fragmentation vs energy
Z=6, A=12
Plane 1 or 2
Plane 2
Plane 1
Z=5, A=10
Z=8, A=16
Z=7, A=14

## Slide 28: Simulation of the optical transport in the scintillator bars (E. Ciarrocchi)
Comparison with experimental data:
● Optical attenuation with proton interaction position along the bar
● Absolute number of detected photons
● Exp data for two scintillator bars and for two types of SiPMs
● Comparison only for protons

## Slide 29: Optical attenuation: Hamamatsu
R = bar reflection coefficient

## Slide 30: Absolute number of photons (Hamamatsu)
Only Hamamatsu
Simulation does not account for noise factors
High uncertainty on gain used to determine exp nr of photons

## Slide 31: Summary of Studies of FOOT Performance on charge reconstruction and Fragment Identification (R. Spighi et al.)
INPUT DATA
  4x107 primaries
  Projectile: 16O (200 MeV/u)
  Target: C2H4 (2mm)
  Selected tracks that pass all the subdetectors
INPUT RESOLUTIONS:
  Momentum (tracking)  4.5%
  Kinetic Energy (Calo)  1.5%
  Tof : [70:100] ps depending on Z
  ΔE (scint): [3:10]% depending on energy released
ΔE
Tof

## Slide 32
energy deposited in SCN
reconstructed Z
Z Resolution: [2-6%] << minimum distance between charges (~10% between 7 and 8)
Resol: 6% 3% 2.0%
1H | 4He | 7Li | 9Be | 11B | 12C | 14N | 16O
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
1.01±0.06 | 2.01±0.06 | 3.02±0.07 | 4.05±0.09 | 5.06±0.10 | 6.09±0.12 | 7.11±0.14 | 8.15±0.16
Z Resolution
Charge completely identified (wrong assignment < %), possible to improve with MSD
SCN
TOF
Z reconstruction

## Slide 33
A Identification
TOF
TRACKER
TOF
CALO
TRACKER
CALO
RECO
FITS
Standard χ2
Augmented Lagrangian Method
 | 1H | 4He | 7Li | 9Be | 11B | 12C | 14N | 16O
Z | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
A | 1 | 4 | 7 | 9 | 11 | 12 | 14 | 16
Studied fragments, one per charge

## Slide 34
Example: A of 12C
A2
Tof + Calo
11.93 ± 0.42
A3
Tracker + Calo
12.5 ± 1.3
Reconstruction methods
A1
Tof + Tracker:
12.15 ± 0.59
Fit methods
ALM fit
11.97 ± 0.39
Χ2 fit
11.97 ± 0.39
Cal: Tail due to energy taken away off the calo in nuclear interactins
Χ2
Possibility to eliminate the tail with a χ2 cut

## Slide 35
Systematic on A resolution (example 12C)
σA (%) vs Tof precision
σA (%) vs p precision
Tof precision (ps)
p precision (%)
Ekin precision (%)
σA (%) vs Ekin precision
Resolutions
p = 5%
Ekin = 1.5%
Resolutions
Tof = 100 ps
Ekin = 1.5%
Resolutions
Tof = 100 ps
p = 5%
A Resolution
  Large dependence on the Tof Resolution
  Week dependence on the p and Ekin resolution

## Slide 36
ALM fit (χ2<5)
11.98 ± 0.39
Χ2 fit (χ2<5)
11.97 ± 0.39
A identification: example on Carbon (cut on χ2 )
With these resolution we begin to disentangle the various isotopes

## Slide 37
A Resolution (%)
Tracker + Calo (high  square terms in p and T)
Tof + Tracker
Tof + Calo
Fit methods superimposed
Reconstruction  best performance from Tof + Calo
Fit  slightly improvement of the performances, remove tails
Generated A
Mass Number (A) resolution with Fit methods at level of 3%
 | 1H | 4He | 7Li | 9Be | 11B | 12C | 14N | 16O
Z | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
A | 1 | 4 | 7 | 9 | 11 | 12 | 14 | 16
Resolution (%)
Studied fragments

## Slide 38: Elastic scattering in the target
In CnHm targets the primary nucleus can undergo elastic scattering on H (reversed kinematics of p-C or p-O elastic scattering)
This results in the following pattern:
  The primary undergoes a small deflection
  The recoiling proton has very low energy and is generally absorbed in the target
Can be easily confused with a reaction like, for instance, 12C ➞11C + n
A preliminary study yields ~1.3 10-3 elastic ev/primary in C2H4 against ~10-2 ev/primary inelastic interactions
Not an issue in pure C targets

## Slide 39: Elastic scattering in the target
Event example (notice that this view is the non bending one):

## Slide 40: A lot of work has been done but there is a lot more still to do…
Different distances, materials and parameters for Intermediate Tracker (see talk by E. Spiriti)
Gap between scintillator bars (see talk by M. Morrocchi)
New geometry of calorimeter, plastic boxes,… (see talk by P. Cerello)
Different thickness of MSD, spacing, layout… (see talk by L. Servoli)
Soon we shall hopefully have a new magnetic system layout
…
Man power with the proper training is unsufficient. This is now a bottleneck
Tutorial about basic handling of simulation of FOOT: 13-14 June in Milano (two days are not enough anyway). Only 2 people are surely coming…