## Slide 1
Emulsion Cloud Chamber Status
A. Alexandrov, G. De Lellis, A. Di Crescenzo, G. Galati, A. Lauria, M.C. Montesi, A. Pastore, V. Tioukov
Napoli University and INFN
FOOT General Meeting
Isola d’Elba, 4-5 June 2018

## Slide 2
Outline
Test beam at LNS in July 2017
Test beam at Trento in December 2017
Refreshing procedure for charge separation
P measurement and isotopic identification
1) Test beams results
4He (700 MeV/u) beam on emulsion chamber
Energy and angle distribution of fragments by Fluka simulation
2) Preliminary simulation results for GSI exposure

## Slide 3
Detector structure
The Emulsion Cloud Chamber detector is made of three sections:
SECTION 1: alternated layers of emulsion films and target (C/C2H4)
          Vertex detector
          Tracking of all charged particles
    SECTION 2: emulsion films only
          Charge identification for low Z fragments
SECTION 3: alternated layers of emulsion films and passive material (Plastic/Steel/Lead)
          Momentum measurement by range and Multiple Coulomb Scattering (MCS)
          Isotopic identification

## Slide 4
Emulsion Test Beam
Why:
New nuclear emulsions (Nagoya production) will be used in the FOOT experiment, never used for particle identification
Exposure of nuclear emulsion to calibrate the response at different ioninizing beams (charge identification)
Exposure of two ECC for isotopic identification
What:
1)LNS: Incident beam: P, D, He and C @80 MeV
2)Trento: Incident beam: P @50, 80, 200 MeV
Exposure:
Surface of exposed emulsion samples: 5x4 cm2 (1/6 of emulsion film surface)
Beam particles orthogonal to emulsion surface
Five exposures per beam, each treated with different refreshing procedure
One sample made of 2 consecutive emulsions enveloped in laminated tissue under vacuum

## Slide 5
Emulsions characteristics
Emulsion films produced in Nagoya University in May 2017
Film dimensions:
    Surface: 125 mm x 100 mm
    Total thickness: 380 μm
          Emulsion Layers: 2x100 μm
          Plastic Base: polystyrene: 180 μm
sensitivity: 50 grains/100 μm
100
100
180

## Slide 6
Test beam @LNS: charge separation
Beam Monitor by the Perugia group: silicon microstrip detector (strip pitch 250 μm, thickness 350 μm, total area 8x8cm2)
Main difficulties coped with:
Make the beam uniform over the emulsion surface
Reduce the beam intensity down to 10 particles/mm2
No online monitoring, needed for normalization
Incident beam: P, D, He and C @80 MeV
Emulsion doublet
Si Microstrip
CMOS
Counter by the Perugia group: beam intensity registered by a CMOS detector (up to 3 MHz)

## Slide 7
Test beam @Trento: charge separation
Incident beam: P@50 (same ionization as He@250 MeV), 80 , 200 MeV
Detector by the Perugia group: beam intensity registered by a CMOS detector
Beam Monitor by the Trento group: scintillator counter
Emulsion doublet

## Slide 8
Exposed emulsions
 | H (80 MeV/u) | D (80 MeV/u) | He (80 MeV/u) | C (80 MeV/u) | H (50 MeV/u) | H (80 MeV/u) | H (200 MeV/u)
EQUIVALENT TO |  |  | Li (200 MeV/u) |  | He (250 MeV/u) |  | 
NOT REFRESHED R0 | D1 | D16 | D6 | D11 | D21 | D25 | D29
28°C R1 | D2 | D17 | D7 | D12 | D22 | D26 | D30
34°C R2 | D3 | D18 | D8 | D13 | D23 | D27 | D31
36°C R3 | D4 | D19 | D9 | D14 | D24 | D28 | D32
38°C R4 | D5 | D20 | D10 | D15 |  |  | 
NOT REFRESHED | ECC1 | ECC2 |  |  |  |  | 
D = doublet of emulsions
ECC = 21 emulsions
LNS
TRENTO
74 emulsions (5x4) cm2 scanned and analysed
total scanned area: 1480 cm2

## Slide 9
Emulsion Films: thermal treatment
Refreshing and chemical treatment @LNGS
Treatments performed in the Emulsion Facility in Underground Gran Sasso Laboratories
Climatic chamber GENVIRO 120L used for refreshing procedure
Refreshing conditions used:
            Temperatures ranges from 28°C to 38°C
            Relative humidity: 98%
            Refreshing time: 24h
VR0
100 um
Volume of the track
Sum of the number of pixels associated with each recognised tracks

## Slide 10
New Neapolitan laboratory
New development laboratory (>40m2) in our Physics Department
It will be equipped with:
Dark room for emulsion development
Assembly and development of the film will be done in near future in Naples

## Slide 11
Emulsion Films: Data acquisition
Scanning with optical microscope @Napoli
Data acquisition performed with fully automated optical microscopes
SCANNING SYSTEM CHARACTERISTICS
New reconstruction software to extend track recognition angular acceptance from θ = 30° to θ = 72°
Software: LASSO in Continuous Motion mode [1]
Development a new generation Scanning System with new hardware. Extension of the scanning speed from 20 cm2/h to 190 cm2/h [2]
[1] A. Alexandrov et al., JINST 10 (2015) no.11 P1100
[2] A. Alexandrov et al., Nature Scientific Reports 7 (2017) 7310
Notes: Nuclear emulsions are made by silver bromine crystals immersed in organic gelatine. The passage of a charged particle ionizes the crystal along its path, after the development treatment they will appear as aligned black clusters in a transparent medium. We have about

## Slide 12
beam spatial distribution (LNS)
x (μm)
x (μm)
x (μm)
x (μm)
Films without any thermal treatment

## Slide 13
beam spatial distribution (Trento)
x (μm)
x (μm)
x (μm)
Films without any thermal treatment

## Slide 14
Emulsion films integrates cosmic rays passing through them from production to development (~2 and ~6 months, respectively, for emulsions exposed to CT e TR)
Signal tracks perpendicular to emulsion films (tgθ<0.2)
Cosmic rays tracks: tgθ>0.2
Angular acceptance in the reconstruction after the scanning processes: tgθ<1
Emulsion Analysis: Signal selection
Cosmic rays
Beam

## Slide 15
Not Refreshed emulsions from LNS
Signal
Cosmic rays
signal ionisation response is less than that of cosmic rays
Data taking soon after the test beam

## Slide 17
Tracks in emulsion

## Slide 18
Convolution filter
Image processing based on a 5x5 convolution filter
For carbon: needed to change convolution filter size because of carbon ions produce a lot of ionisation

## Slide 19
Convolution filter

## Slide 20
Not Refreshed emulsions from LNS
Signal
Cosmic rays
filter
9x9
Signal
Cosmic rays
New data taking: saturation

## Slide 21
Refreshing@lns
No refreshing
Refreshing 28°C
Refreshing 34°C
ERASED
Refreshing 36°C
ERASED
ERASED
ERASED
ERASED
ERASED
filter
9x9

## Slide 22
Refreshing@lns
Refreshing 28°C
Refreshing 36°C
Refreshing 34°C
filter
5x5

## Slide 23
Refreshing@tn
Refreshing 28°C
Refreshing 34°C
ERASED
ERASED
ERASED
ERASED
Signal
Cosmic rays
filter
5x5
No refreshing
ERASED

## Slide 24
Charge separation at 80 MeV/n
C
He
He
C
VR0: volume with no refreshing
VR1: volume with refreshing at 28°C
VR2: volume with refreshing a 34°C
to be
published

## Slide 25
Test beam @LNS: isotopic identification
H
(80 MeV/u)
D
(80 MeV/u)
ECC2
21 nuclear emulsion films
20 stainless steel planes 0.5 mm-thick (X0 = 1.76 cm)
Surface: 5x4 cm2
ECC1 exposed to H (80 MeV/u)
ECC2 exposed to He (80 MeV/u)
Motivation:
Develop and test with data an algorithm for isotopic identification
Exposure of two ECC chambers to H and D at the same energy (80 MeV)
ECC1

## Slide 26
Emulsion analysis: P measurement
Angular deflections in passive layers due to Multiple Coulomb Scattering show a gaussian distribution centered in zero with a sigma
Proportional to 1/pβ
H
(80 MeV/u)
D
(80 MeV/u)

## Slide 27
Preliminary estimation of pβ from “standard” OPERA algorithm [1] that assumes the fitted track not to lose energy during its path
[1] N. Agafonova et al. Momentum measurement by the Multiple Coulomb Scattering method in the OPERA lead emulsion target. New J. Phys., 14:013026, 2012
Expected 1/pβ: 0.0068 MeV-1
Measured 1/pβ: 0.008±0.003 MeV-1
Expected 1/pβ: 0.0034 MeV-1
Measured 1/pβ: 0.004±0.002 MeV-1
Combination of momentum measurement by range and MCS (both dependent on the mass of the particle) could provide isotope identification
Emulsion analysis: P measurement
risultato sul fascio, non sulle particelle(DA FARE)

## Slide 28
Next step: Exposure@GSI
He Beam
sliding up to touch the beam monitor
When: November 2018
Beam: He @700 MeV/u
Exposure:
ECC with stacks 1, 2 and 3
Surface of exposed emulsion samples: 12x10 cm2
Shift along x and y axes to have the beam uniformity distributed on the ECC surface (particle density < 1000 particles/cm2)
Beam particles orthogonal to emulsion surface
front view

## Slide 29
Exposure@GSI: movement
Exposure Movement:
The emulsion set up will be XY remotely controlled to avoid pile-up
The emulsion movement must be tuned according to the beam parameters (impact point, rate, beam width) measured by the start counter and the beam monitor
The distance ∆y between two raws, covered during the inter-spill time, must be 3 times the size of the beam spot
moving pattern in the xy plane
t
vx
tearly start
tspill start
tspill stop
tstop
ramp
up
ramp
down
spill
stage speed along the x axis
y
x
∆y=3 σbeam spot

## Slide 30
Simulation: beam and detector set-up
optimization of the number of films in each section/stack of the ECC
Exposure@GSI: simulation studies
He
Start Counter
Beam Monitor
ECC detector

## Slide 31
Stack 1: 30 emulsion films interleaved with 29 carbon layers 1 mm thick
Stack 2: 27 emulsion films
Stack 3: 30 emulsion films interleaved with 29 lead layers 1 mm thick
Simulation: tentative ECC detector set-up
SECTION 1
SECTION 3
SECTION 2
He
to be optimised
Fluka driven
4He, 700 MeV/u, 2000 events
Start Counter and Beam Monitor as for FOOT “standard” set-up

## Slide 32
  N° 4He absorbed before ECC=0.2%
N° 4He absorbed in stack1=15.2%
N° 4He absorbed in stack2=2.3%
N° 4He absorbed in stack3=18.9%
Simulation: beam particle characterisation
stack 1
stack 2
stack 3

## Slide 33
  N° protons = 81%
N° 3He = 4%
N° 3H = 4%
N° 2H = 2%
𝝅+ ,𝝅— = 9%
Simulation: particle fragmentation

## Slide 34
Energy distribution and angular distribution of secondary particles from He beam (contained inside ECC)
Simulation: secondary from He
nuclear evaporation

## Slide 35
Simulation: proton component
nuclear evaporation
from beam fragmentation

## Slide 36
Materials
          Carbon 1 mm thick
            25 foils
            Other to buy
          2) Poliethilene
            50 foils
            Bent: maybe 2 mm thick?

## Slide 37
Conclusions
          Results from test beam exposures
            Test beam @LNS in July 2017
            Test beam @Trento in December 2017
                Saturation effects established thanks to a new filter
                Charges separation
                Momentum measurement by MCS compatible with expectations
          Simulation
            Preliminary analysis for exposure at He beam (700 MeV/u @GSI)
          Next step
            Detector optimisation for exposure at He beam (700 MeV/u @GSI)
            New algorithms for isotope identification to be developed

## Slide 38
Simulation: proton characterisation
proton x-y position in S3

## Slide 39
VISIBLE
VISIBLE
partial degradation
NOT VISIBLE
Definition of working point for R1:
  28°C,
  98% relative humidity,
  24 h
Definition of working point for R2:
  34°C,
  98% relative humidity,
  24 h
Refreshing effects: summary
DELIVERED | H (80 MeV/u) | D (80 MeV/u) | He (80 MeV/u) | C (80 MeV/u) |  | H (50 MeV/u) | H (80 MeV/u) | H (200 MeV/u)
EQUIVALENT TO |  |  | Li (200 MeV/u) |  |  | He (200 MeV/u) |  | 
R0 |  |  |  |  |  |  |  | 
R1 28°C |  |  |  |  |  |  |  | 
R2 34°C |  |  |  |  |  |  |  | 
LNS
TN