## Slide 1
The LARAMED project at LNL: a new facility for the Production of Radionuclides for Medicine
J. ESPOSITO, ON BEHALF OF LARAMED COLLABORATION gropu
juan.esposito@lnl.infn.it
Laboratori Nazionali di Legnaro (LNL)

## Slide 2: The LARAMED project mission: 4 basic items….
To setup a new nuclear science & technology research center at LNL;
(dedicated to both nuclear medicine and applied nuclear physics R&D activities)
To stimulate technology transfer of relevant scientific results; ( Novel/unprecedented radionuclides to the healthcare system, thus favoring the development of useful radiopharmaceutical products)
To provide additional funding routes for INFN (and LNL);
(External funds from radioisotopes research/production are a must to guarantee the future running of LARAMED facility)
To grow up a research community interested in radioisotopes (both for Medicne&Physics); (Proposal of research project to INFN National Scientific Committees to be funded )
The big Challenge: INFN ready for partnership with private enterprises in the field?
Waiting for the new research infrastructure (now under construction), LARAMED may currently be seen as a research environment for some running experimental projects
To establish a LAboratory of RAdionuclides for MEDicine granted as “competitive project” at national level:

## Slide 3: How LARAMED infrastructure is setup
LAboratory of RAdionuclides for MEDicine, includes:
A research laboratory (RILAB)
Jointly owned by INFN and CNR for:
High-precision determination of nuclear excitation functions
Low-activity-production of Radio-isotopes/Radio-pharmeceutical for research purposes
A proving ground for new/advanced technologies developed to test high power targets
A production facility (RIFAC)
operated by INFN and a private partner:
Production of 82Sr/82Rb and 68Ga/68Ge radionuclides for generator systems to meet market demands

## Slide 4: The New SPES/LARAMED Building/infrastructure
2015 2014
2012 2013
4 years to complete the work
No additional costs respect to the initial budget
It was a success of public tender management
12
50 x 60 m2
-7 to +11 m height
24.000 m3 of concrete
1.150 tons iron
3-4 m thick shielding walls
Plants
Plants
Control room
Power Supply room

## Slide 5: Final Configuration of Cyclotron and Beamlines (-1 floor)
Up to 9 irradiation target points
2 ISOL target stations (A6, A4)
3 Shielded bunkers (RI
#1,#2,#3) for High Intensity irradiation
4 medium and low intensity target areas (A8, A9, A15)
8
SPES/LARAMED building -1 level

## Slide 6: The new 70 MeV, 750µA proton driver
Main Parameters | 
Accelerator type | Cyclotron AVF with 4 sectors, Resistive Magnet
Particle | Protons (H- accelerated)
Energy range | 35-70 MeV
Max Current Intensity | 700 µA (variable within the range 1µA-700µA)
Extraction | Dual stripping extraction
Max Magnetic Field | 1.6 T (Bo = 1 T)
RF System | nr. 2 delta cavities; harmonic mode=4; f RF =56 MHz; 70 kV peak voltage; 50 kW RF power (2 RF amplifiers)
Ion Source | Multi-cusp volume H- source; Iext =8mA; Vext=40 kV; axial injection
Dimensions | Φ=4.5 m, h=2 m, W=190 tons

## Slide 7
Hot cells
Target process. lab
Radionuclide
Purification lab
Spectrometry
lab
Target processing/ radiochemistry lab
LARAMED Infrastractures (+ 2 floor)
Start of installation schedule: 2017/2018
Future GMP-compliant
production
Target production
cold chemistry lab

## Slide 8: LARAMED program overall funding (as of April 2018)
The project is currently supported by public fundraising coming from: a) MIUR-approved projects - INFN/CNR/SZN collab. (infrastructure)
b) INFN CSN-funded experiments (research)
Project title | MIUR Funds (k€) | INFN funds allocated (k€) | LNL funds used/reserved (k€)
LARAMED (Premiale 2012) | 6 808 | 6 408 | ~5 250
TERABIO (Premiale 2014) | 4 413 | 3 458 | ~1 400
TOTAL | 11 221 | 9 866 | ~6 650
APOTEMA (CSN 5 - 2012-2014) |  | 172 | 172
TECHN-OSP (CSN 5 – 2015-2017) |  | 271 | 271
COME (CSN 3 - 2016) |  | 27 | 27
PASTA (CSN 5- grant – 2017-2018) |  | 66.5 | 56
E-PLATE (CSN 5- grant – 2018-2019) |  | 32 (2018) | 10.5
METRICS (CSN 5 - 2018-2020) |  | 55 (2018) | 2.5
TOTAL |  | 623.5 | 539
Atti parlamentari FOE anno 2012
Atti parlamentari FOE anno 2014
Full LARAMED facility cost - instrum. Included - (2015 estimation): ~ 13 M€

## Slide 9: past/running R&D activities within LARAMED framework
Radioisotope | Half-life
Tc99m | 6.01 h
Cu-64 | 12.7 h
Cu-67 | 2.58 d
Sc47 | 3.35 d
Mn-52 | 5.59 d
LARAMED first radionuclides list of interest
INFN already funded/running projects | Project name
Accelerator-Tc-99m alternative (direct) production route through hospital cyclotrons | APOTEMA (2012-2014) TECHNOSP (2015-2017)
“Coordinated Research Project ' (CRP) on“Alternative, non HEU-based, Tc-99m /Mo99 supply” | IAEA CRP (2011-2015)
Alternative Cu-64/Cu-67 production for theranostic application | COME (2016)
Alternative Sc-47 production for theranostic application | PASTA (2017-2018)
CRP on “Radiopharmaceuticals Labelled with New Emerging Radionuclides” Cu-67, Re-186, Sc-47” | IAEA CRP (2016-2019)
High Power Target concepts R&D (64/67Cu) | TERABIO comp. project (2016-2019)
High intensity vibrational powder plating | E_PLATE (2018-2019)
Multimodal pET/mRi Imaging with Cyclotron-produced Mn-52/51 and stable paramagnetic Mn iSotopes | METRICS (2018-2020)
Il progetto LARAMED ha come scopo l’R&D per la produzione da ciclotrone di radioisotopi metallici convenzionali, come il Tc-99m (progetto TECHN-OSP), ed emergenti, come il Cu-67 (progetto COME), per uso medicale

## Slide 10: LARAMED External Collaboration Network
ARRONAX facility (Nantes, France), 70 MeV multi-particle cyclotron
St. Orsola Hospital (Bologna, Italy). 16 MeV cyclotron
Sacro Cuore Don Calabria Hospital (Negrar, VR, Italy). 19 MeV cyclotron
Ferrara University (Italy), YAP-(S)PET-CT small-animal imaging system
National Research Council (CNR) in Milan (Italy), Facility for cellular and pre-clinical studies
LNL-INFN
S.C. Don Calabria Hospital
(Negrar)
St. Orsola Hospital
(Bologna)
CNR
Milan
ARRONAX
(Nantes)
University of Ferrara
Waiting for dedicated beam-lines and available laboratories, we are collaborating with:

## Slide 11
APOTEMA - CSN5 - 2012/2014
TECHN_OSP - CSN5 - 2015/2017
Laboratori Nazionali di Legnaro (LNL)

## Slide 12: Tc99m supply World crisis: seeking for alternative routes
Published online 15 July 2009 | Nature 460, 312-313 (2009) | doi:10.1038/460312a
Published online 23 October 2008 | Nature | doi:10.1038/news.2008.1186
Published online 12 February 2010 | Nature | doi:10.1038/news.2010.70
Published online 12 December 2013 | Nature doi:10.1038/504202a
Published online 12 September 2016 | Nature ! doi:10.1038/nature.2016.20577

## Slide 13: The Canada's NRU reactor: the largest HEU-based 99Mo world-supplier (2/3 demand)
March 31, 2018: the world's oldest operating nuclear reactor in the world (first criticality, Nov. 1957) has been permanently shut down
As of July 2017, almost all Mo-99 for medical use was being produced by irradiating solid uranium targets in the six research reactors listed below (available production capacity of the reactors is shown in parentheses)
BR-2, Belgium (7,800 six-day Ci/week)
HFR, Netherlands (6,200 six-day Ci/week)
LVR-15, Czech Republic (3,000 six-day Ci/week)
Maria, Poland (2,700 six-day Ci/week)
OPAL, Australia (2,150 six-day Ci/week)
SAFARI-I, South Africa (3,000 six-day Ci/week)
End of operation
2026
2024
2028
2030
2057
2030
What will happen in the mid term: another shortage ?

## Slide 14: The most promising alternative route for 99mTc supply
APOTEMA (2010-2014)
Feasibility studies aimed at investigating, possible alternative Tc99m production routes, from the nuclear physics (both theoretical and experimental) point of view.
TECHNOSP (2015-2017)
R&D of a technology aimed at having an, as easy as possible, and cheap accelerator-Tc99m in-house production.
Basically make available, to an already existing 16-20 MeV class medical cyclotrons network in a country (e.g. Italian situation) the possibility of a routine accelerator-Tc99m local supply.
INFN studies started in 2010. Two CSN5- funded research projects approved in last 6 years:
Main conclusion:
Direct production of 99mTc is by far the best route

## Slide 15
Target
production
Cyclotron
irradiation
Extraction separation purification
Radio-pharmaceuticals,
QC, imaging
100Mo recovery techniques
100Mo(p,2n)99mTc
Direct 99mTc Cyclotron Production
Closed-loop technology developed at LNL: recovery of costly target material

## Slide 16
First successful test to deposit multiple layers (0.5 m each) up to 300 m on a copper backing using the Physical Vapor Deposition (PVD) technique under UHV at LNL. No stress at micro-structure level has been observed.
Direct 99mTc Cyclotron Production
New solid target technology R&D
Isotopic composition (%) |  |  |  |  |  | 
Mo-100 | Mo-98 | Mo-97 | Mo-96 | Mo-95 | Mo-94 | Mo-92
99,05 | 0,54 | 0,07 | 0,11 | 0,10 | 0,05 | 0,08

## Slide 17: Target Irradiation tests at S. Orsola Hospital (Bologna)
110 μm Mo-nat directly sputtered onto Cu backing (first time ever)
70µA, 15.6 MeV (1hr irradiation) -> ~1.1 kW/cm2 achieved!!
Contact between sputtered Mo film, and Cu-backing remains excellent
6hrs irr/day -> ~2.0 Ci daily needs S. Orsola Hospital could be fulfilled
Before
After
Additional ~1.5 kW/cm2, no-direct cooling target concept under study
GE PetTRACE -16
Protons: 16 MeV, up to 75 A (1.2 kW)
Deuterons:8.4 MeV, 50 A deuterons
MaX available
PetTRACE beam current

## Slide 18
First automatic Prototype
(Unife/S. Orsola OspBO)
Direct 99mTc Cyclotron Production
Extraction Separation Purification
Second automatic Prototype
(Unife/S. Orsola OspBO)
Recovery Yield | >93%
Time | 60 min
Target mass | Up to 500 mg

## Slide 19: Target dissolution/Purification of 99mTc
MEK-based (Methyl-Ethyl-Ketone) Solvent Extraction method:
Process time: 60-70 min
99mTc Recovery Yield (efficiency) : > 93%
Radiochemical Purity: > 99% 99mTcO4 (ref. Eu-Pharm >95%)
Trace analysis: < 5 ppm Al3+ (ref. Eu-Pharm <5 ppm)
non-Tc impurities < MDA
P. Martini, et al. ARI, 118, (2016) 302-307
M. Gumiela, Separation methods of
cyclotron-produced 99mTc, Nuclear Medicine and Biology (2017), doi:
10.1016/j.nucmedbio.2017.11.001
“…It is worth to emphasize that this solvent-extraction fully automated module results among the discussed methods in the highest recovery yield of 99mTc…”.
The fully-automated, PLC-operated, remote-controlled chemical separation module prototype Developed: Ferrara Univ. and S. Orsola Hospital (Bologna) working groups.

## Slide 20
 | Generator-99mTc | Cyclotron-99mTc
99mTc-Myoview SPECT-CT Immages |  | 
Tomographic images of the Jaszczak phantom |  | 
Planar image of the grid phantom |  | 
Direct 99mTc Cyclotron Production
Radio-pharmaceuticals, QC, imaging
CHEMICAL PURITY | pH | 4.5-5
 | Mo | <5ppm
 | Al3+ | <5ppm
 | MEK | <0.0004% (v/v)
SEPARATION YIELD | % | 9xTc | 99Mo | 9xNb
 | Final solution | 93 ± 3 | ND | ND
 | Aqu. phase | 5 ± 1 | 96 ± 2 | 97 ± 2
 | Waste | 0.03 ± 0.02 | ND | ND
 | Washing | 0.5 ± 0. 1 | 3 ± 1 | 2 ± 1
 | Silica column | 0.2 ± 0.1 | ND | ND
 | Alumina col. | 0.2 ± 0.1 | ND | ND
RN/ ISOTOPIC PURITY | Radionuclide | T1/2 | % Activity
 | Tc-93g | 2.8 h | 0.012%
 | Tc-94g | 4.9 h | 0.094%
 | Tc-95g | 20 h | 0.110%
 | Tc-95m | 61 d | 0.001%
 | Tc-96g | 4.3 d | 0.031%
 | Tc-99m | 6.01 h | 99.758%
RADIOCHEM. PURITY | 99mTc-NaTcO4 | >99%
 | 99mTc-HMPAO | 83%
 | 99mTc-Myoview | >99%
(ref. Eu-Pharm >95%)
(ref. Eu-Pharm
<5 ppm)
Eu-Parmacopoeia approved Oct 2016

## Slide 21
Direct 99mTc Cyclotron Production
100Mo Recovery Techniques
Yield >95% Mo
450°C-750°C
750°C-950°C
MoO3(s) +H2(g) = MoO2(s)+H2O(g)
MoO2(s) +2H2(g) = Mo(s)+2H2O(g)
Yield >90% MoO3
Na2MoO4  MoO3
100Mo/99mTc separation module “waste”:
Na2MoO4 (H2O)x + NaOH
Stage 1 : Na2MoO4(H2O)x  MoOx
Stage 2 : MoOx  Mo
Notes: Na2MoO4 + HNO3(excess) (80⁰C, reflux)= NaNO3 + H2MoO4
ΔT  MoO3 + H2O
Washing with EtOH+H2O solutions, centrifugation, drying
Riduzione in 780 minuti

## Slide 22: The daily need of 99mTc in Italy: Some facts and starting numbers....
Based on meetings had with the medical physics head of the St. Orsola Hospital (Bologna)-Nuclear Medicine Dept., and with people involved in Ferarra hospital we have been aware that:
99mTc needs for S. Orsola Hospital only for routine diagnostic procedures : 12 Ci/day
99mTc daily need for the whole country be about S. Orsola Hospital x 150  150-300 Ci
Is this range likely?
-------------------------------------------------------------------
Former information we had for Veneto region in past years: ~7 Ci/day
Rough extrapolation: 7x 20 Italian regions =140 Ci
Former information we had for Ferrara Hospital in past years: ~1 Ci/day
Emilia Romagna region estimated ~ 10 times Ferrara needs = 10 Ci/day x 20 = 200 Ci/day
Average 99mTc daily need may thus be supposed ~150-200 Ci in the whole country

## Slide 23
By using high-performance cyclotrons (i.e. 300-500 µA current intensity and energies up to 20 MeV) the daily needs of the entire Veneto region (273 GBq/day = ~ 7 Ci/day) may be supplied.
By using medical cyclotron commonly installed in Nuclear Medicine Dep. (16-19MeV), 100Mo-enriched targets up to 99.86% (thickness 260 and mass 450 mg) irradiated at 80 µA, 15.0 MeV, over a period of 120 min. Under these conditions, the expected yield of Tc-99m is approximately 30-36 GBq ~ 0.7-1 Ci/day.
Direct 99mTc Cyclotron Production
How much 99mTc may we produce?
The generator-produced Tc-99m price is expected to further increase with NRU reactor permanent shutdown in 2018.
Chart: Mo99/Tc99m generators market price hystory (Italy)
| 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
MCD23Y-12.5GBQ 12,5 GBq | 956.48 | 956.48 | 956.48 | 1243.42 | 2060 | 2060 | 2060 | 2060 | 2060 | 2060 | 2060 | 2060
MCD23Y-25GBQ 25 GBq | 1523.55 | 1523.55 | 1523.55 | 1980.62 | 2884 | 2884 | 2884 | 2884 | 2884 | 2884 | 2884 | 2884
Source: GE-Healthcare
0.63€/mCi
0.36€/mCi
Tc99m cyclotron production (15 MeV, 100 A ) | 
2 hrs irr | 6 hrs irr
~80 €/dose (2.02€/mCi) | ~60 €/dose (1.51€/mCi)
Generator 99mTc cost ~25 €/dose (0.63€/mCi) | 
Injected dose: 20 mCi; (preparation dose is 40 mCi)

## Slide 24
COME - COpper Measurements
2016
Laboratori Nazionali di Legnaro (LNL)

## Slide 25: 67Cu and 64Cu: new emerging radionuclides couples
Mean β energy: 141 keV
Mean Auger e energy: 28 keV
Mean β energy: 190 keV
Mean Auger e energy: 2 keV
64Cu
67Cu
SPECT
PET
Cu-67 very attractive because of physical-chemical properties (T1/2 2.58 d). Suitable for Theranostic (Therapy + Diagnostic ) applications, as single isotope, or in pair with 64Cu (β-emitter, half-life 12.7 h).
64Cu is ALREADY used in nuclear medicine for PET (diagnostic proc.)
64Cu seems to provide excellent results also in THERAPY (under simple 64CuCl2)
After
Before
Malignant melanoma images (left leg) before and after 100 mCi 64CuCl2 injection
*Peng F et al., J Nucl Med (2006)47:1649-1652 ; **H Cai et al. , J Nucl Med (2014) 55:622-628.
What will it happen by using 67Cu ?
  67Cu is a promising nuclide in RAdio Immuno Therapy (RAIT)
  67Cu‘s limiting factor: LOW availability
  Worldwide Production per month : only (100 mCi ≈ 3.7 GBq); 1 patient dose
   67Cu production: Goal for both LARAMED and ARRONAX !
Notes: Intro sui rami :
2 - spiegazione TERANOSTICA sia come isotopi singoli sia come miscela dei due

## Slide 26: 67Cu current production route
In order to have a pure 67Cu (RNP>99%) it is necessary to wait that 64Cu decays  lose ≈ 80% of 67Cu activity
68Zn(p,2p) reaction, already used but…not efficient
IAEA Technical Report Series No. 473 (2011)
67Cu monthly production: 100 mCi (@ BNL)
Only ONE
therapeutic dose !
In order to have a pure 67Cu (RNP>99%) it is necessary to wait that 64Cu decays  lose ≈ 80% of 67Cu activity
IAEA Technical Report Series No. 473 (2011)
New reaction route under exam.: 70Zn(p,α)67Cu
No experimental data available for EP > 35 MeV
COME (COpper xs MEasurement) exp.: INFN funded (2016)
CoMe project:
70Zn(p,x)67,64Cu
xs measurements

## Slide 27
Ongoing and just started projects
Laboratori Nazionali di Legnaro (LNL)

## Slide 28
PASTA –Production with Accelerator of Sc-47 for Theranostic Applications
2017/2018
CONCORSO PER GIOVANI RICERCATORI
PI: Gaia Pupillo
Laboratori Nazionali di Legnaro (LNL)

## Slide 29: PASTA project : 47Sc cyclotron production@LNL
Scientific Motivation: Why 47Sc?
47Sc (3.35 d, γ SPECT, β- terapy) is a promising radionuclide in Radio Immuno Therapy (RIT).
Suitable half-life to follow the slow bio distribution of monoclonal antibodies (mAbs)
Low energy β-emitter suitable to treat small-sized tumors
47Sc current production methods through neutron induced nuclear reactions at reactor sites: 47TiO2(n,p)47Sc or 46Ca(n,γ)47Ca ->47Sc
Contaminants co-production: 44mSc (58.61 h, β+), 44Sc (3.97 h, β+), 46Sc (83.79 d, β- )
Main goal: find-out 47Sc alternative cyclotron-driven production routes, with as low as possible contaminant nuclides
PASTA: Production with Accelerator of Sc-47 for Theranostic Applications
Overall proton-induced reactions for 47Sc production (NNDC, 2016)
J. Esposito, 9ICI 2017, Doha (Qatar), 12-16 Nov. 2017
The trend of these nuclear cross sections has to be confirmed..

## Slide 30
E-PLATE Electrostatic Powder pLating for Accelerator TargEts
CONCORSO PER GIOVANI RICERCATORI
PI: Hanna Skliarova
Laboratori Nazionali di Legnaro (LNL)

## Slide 31
High intensity vibrational powder plating - HiViPP
This deposition technique exploits the phenomenon of vibrational motion of metallic particles in a static electric field [1].
[1] An application of a new type deposition method to nuclear target preparation, Isao Sugai
Experimental set up
E-PLATE
natTi metal on Al foil
for PASTA project
Ti per Pasta
Cr per METRICS
Mo per E-PLATE
Te per I production
Gd per ARRONAX
Sn su Carbon foil NUMEN
1 – backing (upper electrode, anode)
2 – backing (lower electrode, cathode)
3 – quartz or glass cylinder
4 – pressing plate
5 – spring
6 – insulator holder
Process is realized in vacuum
Advantages:
Two targets are deposited simultaneously
High Efficiency: 95-98%!
High uniformity
Notes: Technique is very interesting, but has a lot of not clear aspects

## Slide 32
METRICS Multimodal pET/mRi Imaging with Cyclotron-produced 52/51Mn and stable paramagnetic Mn iSotopes
Laboratori Nazionali di Legnaro (LNL)

## Slide 33: METRICS- Mn-52
Multi Modality Imaging MMI | 
PET/SPECT | CT/MR
functional imaging | anatomical imaging
radiolabeled tracer | contrast agent
e.g. 18F-FDG for PET | e.g. Ba and I for CT
or 99mTc-HMPAO for SPECT | or Gd-OMNISCAN for MRI
Diagnostic imaging mismatch because of the chemical diversity between the contrast and radioactive agents.
To achieve a genuine fusion between PET and MRI, the contrast and radioactive agents should be chemically identical
Mn is the only element having both:
isotopes with positron-emitting nuclear properties (i.e. 52Mn average Eβ+ ~ 250 keV; 51Mn average Eβ+ ~ 960 keV) that could be conveniently employed as PET tracer
and useful paramagnetic properties to be used as MRI contrast agents (Mn2+)
Aiming at new dual-modality PET/MRI investigations using the same injected radionuclide/contrast agent
Project Goals:
Develop/optimize the proper separation and purification method to minimize chemical reagents
Establish stable Mn(II)-complexes

## Slide 35
The research on COPPER does not end with CoMe project
This is just the beginning
On the basis of CoMe results we have big project in mind for Cu-64/67
More Copper-64/67 @ LNL

## Slide 36
S. Todde (MI)
A. Duatti (UNIFE)
M. Marengo e G. Cicoria (BO)
C. Rossi Alvarez (INFN-LNL)
THANK YOU
J. Esposito
(INFN-LNL)
F. Haddad
(Director)
H. Skliarova
S. Cisternino
G. Keppel (INFN-LNL)
L. Uccelli
P. Martini
A. Boschi
M. Pasquali
L. Mou
G. Pupillo
G. Gorgoni e
E. Cazzola (VR)
Collaborators
G. Sciacca (LNL)
A. Duatti
G. Di Domenico
LARAMED
Family
G. Fiorentini (INFN/UNIFE)
L. Uccelli