## Slide 1: Gravitational tests using atom interferometers
Gabriele Rosi
CDS seminar
07/03/2018

## Slide 2: Outline
Introduction to atom interferometry
MAGIA experiment
MAGIA ADV: 2017 results and 2018 on going activities
Long term prospects
G. Rosi CDS 2018

## Slide 3: Atom Interferometry for gravity measurement
Ingredients:
A source of Cold Atoms (~ μ K or less)
(the sample must be slowly expanding and weakly interacting )
A laser system to cool the sample and to manipulate
the wavepacket
Atom Interferometry can measure accelerations
We use Cold Atoms as free falling microscopic masses
Quantum features of matter allow to improve the sensitivity
(not just a time-of-flight measurement in the “classical way”)
G. Rosi CDS 2018

## Slide 4: Atom / light Interferometry: the analogy
Once you have an atomic two level system you can make the analogy with light looking at the Rabi’s population oscillations scheme
Interaction time τ [1/Ω]
P1-2
π
π/2
|1 ›
|2 ›
π /2 pulse works like a beamsplitter
momentum transfer
π pulse works like mirror;
momentum transfer
state |2>
state |1>
Mirror
beamsplitter
interference
fringe
Optical interferometer
Atom interferometer
SPLIT
RECOMBINE
REFLECT
G. Rosi CDS 2018

## Slide 5: Atom Interferometry: theory
Wave function PHASE evolution
|1>
|2>
If
Population on final State depends
On the interferometer phase
GRAVITY BREAKS
THE SIMMETRY
fringes
varying RAMAN laser’s phase
z
t
totally symmetric
evolution
G. Rosi CDS 2018

## Slide 6: MAGIA
Misura Accurata di G mediante Interferometria Atomica

## Slide 7: MAGIA - the procedure
G
SOURCE MASSES
Well-characterized tungsten cylinders
PROBE MASSES
Cold, freely falling 87Rb atoms
MEASUREMENT METHOD
Raman atom interferometry (local acc.)
Spatial & temporal differential scheme
CALCULATION of gravitational attraction
G. Rosi CDS 2018

## Slide 8: The G measurement
Features:
Source masses modulation time: 30 mins
Integration time:
more than 100 hours over 2 weeks (July 2013)
Sensitivity: 3x10-9 g/Hz1/2
Final sensitivity: ~ 10-11 g
G = 6.67191(77)stat(62)sys× 10-11 m3 Kg-1 s-2
G. Rosi CDS 2018

## Slide 9: MAGIA ADV: 2017 Results

## Slide 10: Quantum formulation of the EEP
The Einstein Equivalence Principle plays a crucial role in our understanding of gravity.
It can be organized into three conditions:
Equivalence between the system’s inertia and weight (WEP)
Independence of local non-gravitational experiments from the velocity of the free falling reference frame (LLI)
Independence of local non-gravitational experiments of their location (LPI)
How to implement EEP in a non-relativistic quantum theory?*
*Zych et al. “Quantum formulation of the Einstein Equivalence Principle”, arXiv:1502.00971 (2015)
Non-relativistic Hamiltonian with classical potential
Developing to the first order:
Relativistic time dilation term
Gravitational time dilation term
G. Rosi CDS 2018

## Slide 11: Quantum formulation of the WEP
The acceleration operator in the Heisenberg picture is:
If internal and external degrees of freedom can be entangled!
where
*Zych et al. “Quantum formulation of the Einstein Equivalence Principle”, arXiv:1502.00971 (2015)
and
G. Rosi CDS 2018

## Slide 12
A quantum WEP test
Quantum formulation of WEP requires
In QM a state of internal energy can involve superpositions of states → for
the validity of the quantum WEP we need equivalence between the off-diagonal elements of the operators.
Classical WEP is valid if r1 = r2 =1
Quantum WEP holds if r = 0
r1 and r2 are real numbers
r is a complex number r=|r|eiφ
Let us consider a two level systems (in our case F=1 and F=2 hyperfine ground state of 87Rb:
G. Rosi CDS 2018

## Slide 13
A quantum WEP test
A classical WEP violation (introduced by diagonal elements r1,2) emerges as a differential acceleration proportional to r1 – r2.
A quantum WEP violation would produce an excess phase noise on the acceleration measurements due to γ (random phase >> 2π).
Instrument is sensitive to*:
*G. Rosi et al. Nature Communications 8, 15529 (2017)
(|s> = (|1> + eiγ |2>)/√2)
G. Rosi CDS 2018

## Slide 14
A quantum WEP test
*G. Rosi et al. Nature Communications 8, 15529 (2017)
With the Bragg gradiometer we compare the free fall accelerations for atoms prepared in pure hyperfine states (F = 1, F = 2) and atoms prepared in a coherent superposition of two different hyperfine states.
Superposition state is prepared with RF pulse
s = (|1> + |2> eiγ)/√2
γ: random phase introduced with RF pulse
G. Rosi CDS 2018

## Slide 15
A quantum WEP test
Quantum WEP test → Attributing all observed phase noise on 1-s ellipse to a WEP violation we estimate an upper limit for |r| → r ≤ 5 ∙ 10-8.
Black ellipse: 1 – 1 gradiometer
Blue ellipse: 1 – s gradiometer
Black ellipse: 1 – 1 gradiometer
Blue ellipse: 1 – 2 gradiometer
We realize three possible gradiometric configurations → Φ1-1, Φ1-2, Φ1-s
Classical WEP test → δg1-2 ~ (Φ1-1 - Φ1-2) → η1-2 = (1,4 ± 2,8) x 10-9
G. Rosi CDS 2018

## Slide 16
A quantum WEP test: prospects
Energy difference between hyperfine state very tiny! (28 μeV)
Likely, the commutator is proportional to the typical magnitude of H and therefore large ΔE yields to larger effects!
Next step: Sr interferometer on clock transition!* ΔE= 1.8 eV!
Next next step: entangled states between different isotopes**?
*L.Hu et al., PRL (2017)
**Geiger et al. PRL (2018)
G. Rosi CDS 2018

## Slide 17
Cancelling gravity gradients
The tidal forces on the atoms in a uniform gravity field and gradient modify the wavepacket trajectories. The gravimetric phase shift is
φ = keffgT2 + keffΓzz(z0 + v0T)T2
z0, v0 initial atomic position and velocity.
The error on z0 and v0 is one of the major sources of noise and systematics:
For WEP tests at 10-15 level is required a control on z0 and v0 of 1 nm and 0,3 nm/s.
In the AI determination of G[1] one of the major sources of systematic error arises from the limited control on the thermal cloud degrees of freedom.
[1] G. Rosi, F. Sorrentino, L. Cacciapuoti, M. Prevedelli & G. M. Tino, “Precision measurement of the Newtonian gravitational constant using cold atoms”, Nature 510, 518-521 (2014).
G. Rosi CDS 2018

## Slide 18
Cancelling gravity gradients
Readapting the effective wave vector keff of the π pulse it is possible to compensate the effect of Γzz[1]
Δkeff = (ΓzzT2/2)keff
φ no longer depends on z0 and v0.
This procedure simulates the effect of a gravity gradient on the atomic trajectories. We implement it to measure gravity gradients, gravity curvature
[1] A. Roura, Phys. Rev. Lett. 118, 160401 (2017).
G. Rosi CDS 2018

## Slide 19
For the three gravity gradiometers (1-2, 2-3, 1-3) we measure the linear dependence Φ(Δν) vs Δν (Φ gradiometric phase)
We simultaneously interrogate three clouds with the Raman interferometer for two source masses configurations. During the π pulse the frequency of the Raman lasers is changed by Δν*.
Gravity gradient is traslated into a frequency!*
Cancelling gravity gradients
G. Rosi CDS 2018

## Slide 20
Final results*:
 | Γ23 [10-6 s-2] | Γ12 [10-6 s-2] | Γ13 [10-6 s-2]
Far | -3,32 ± 0,02 | -3,48 ± 0,01 | -3,40 ± 0,01
Close | 0,497 ± 0,006 | -4,87 ± 0,01 | -2,193 ± 0,006
Measurements also provide gravity gradient sign.
As expected Γ13 = (Γ12 + Γ23)/2.
Measured cloud distances and gravity curvature in close configuration:
d23 = (307,2 ± 0,3)mm d12 = (308,6 ± 0,4)mm
ξclose = (Γ23 - Γ12)/d = (1,743 ± 0,004) x 10-5 m-1s-2
Far configuration
Close configuration
*D’amico et al. PRL(2017)
Cancelling gravity gradients
G. Rosi CDS 2018

## Slide 21
Prospects
In presence of a linear gravity gradient the zero crossing frequency is independent by clouds positions and velocities
The main systematic effect in G determination with cold atoms arises from the required knowledge of atomic distribution
Can we fabricate a source mass in order to produce an almost linear acceleration profile? Yes
Determination of G at 10 ppm possible with thermal clouds!*
Recipe: double differential zero-crossing frequency determination
*G. Rosi, Metrologia (2018)
G. Rosi CDS 2018

## Slide 22
Clock Interferometer 698 nm*
Phase shift gradiometro
Isotopo 88Sr
Campo statico B=300 G -> Dn=20 mHz
Frequenza di Rabi W~1kHz
*Hu et al PRL (2017)
G. Rosi CDS 2018
Activities 2017 (Sr)

## Slide 23
Sr squeezing on momentum states
G. Rosi CDS 2018
Salvi et al PRL (2017)
Activities 2017 (Sr)

## Slide 24
  Rb
  Implementazione e test di fasci non gaussiani sul campione atomico;
  Studio e implementazione di sistemi di raffreddamento con dark mot;
  Test di schemi interferometrici a più impulsi;
  Studio di sistemi di raffreddamento evaporativo;
  Sr
  Update sistema Sr (fontana da 1 m)
  Completamento sistema laser a 461 nm con sistema laser di raffreddamento 2D;
  Costruzione sistema laser di ripompa a 497 nm;
  Completamento sistema laser a 689 nm con tapered amplifier;!
  Caratterizzazione e test della cavità ottica in aria;
  Costruzione apparato da vuoto con produzione di campione di atomi freddi;
  Integrazione dell’apparato con la cavità ottica.
G. Rosi CDS 2018
Activities 2018

## Slide 25
G. Rosi CDS 2018
Long term developments
EP Tests, Dark matter detection
Miniera di SOS ENATTOS