## Slide 1: Endcap Description
Peter Sutcliffe
5th April 2018
INFN - Laboratori Nazionali di Frascati
IT-UK Pixel Endcap Meeting

## Slide 2: Endcap pixel layout TDR 9-8-10 Layout
Pixel Support Tube
Outer Pixel Layers
3 Layers
Heavyweight Pixel Endcap support flanges
Lightweight Pixel Endcap Support Flanges
Inner Support Tube
Beam Pipe
1975mm
Half rings
9 outer half rings R275
8 middle half rings R212.5
10 inner half rings R150
  Incorrect radii
Z=3120
1st half rings Z=1200
Last half rings Z=3000

## Slide 3
Pixel Endcap originally concepted as a modular structure.
Populated Half Rings
  Bare Half Ring + Modules – Populated Half Ring
Populated Half Cylinder
  Bare Half cylinder, with glued in attachments
  Cooling and cabling services
  Z=3000 End Bulkhead
  Populated Half Rings
Fully Assembled Endcap
  6 Half Cylinders
  Z=1200 Support Structure
  Services Support Structure

## Slide 4: Middle Half ring Description
Nominal Radius 212.5
Section 44mm x 5mm

## Slide 5: Half cylinder manufacture
Half cylinders layed up on carbon steel cylinders.
Oven cured (not autoclave due to size)

## Slide 6: Bare cylinder preparation
Trim and dress half cylinders, add holes etc.
Mount CFRP end-flanges on jig and attach inserts (2x)
Spread adhesive on outer rims of end-flanges, mount two ½-cylinders and allow to cure
Cut end-flanges at top and bottom to split assembly into two parts
Add link pieces

## Slide 7: Completed middle half cylinder
Discrete components added, ready for services to be added….see Freds talk
At this stage tube and cable clips can also be added
Heavy Z=3000 will need to be added.

## Slide 8: Half Cylinder and Services (Fred)

## Slide 9: Half Cylinder with Half Rings Attached

## Slide 10: Assembly of half cylinders
Half cylinders will be assembled in the following order:
  Fix the lightweight Z=1200 end flange in position
  Inner left and right hand
  Middle left and right hand assembled around the Inner layers
  Outer left and right hand will be assembled around the Inner and Middle layers
  Half cylinders connected with connection pieces and captive dowel screws

## Slide 11: Cylinder Prototyping – what we intend to do
Middle Layer
  L1400mm
  D527mm
Start with one ½-cylinder and learn …
  How to position shell on end-flanges
  How to position ½-ring mechanical interfaces
  How to verify the placement accuracy
  Very Important – to determine the accuracy a half cylinder can be made in order to stay within our envelope.
1400mm
Dia. 527mm

## Slide 12: What we have done…
60 cm long half cylinders, with end flanges and connecting pieces.

## Slide 13: Note on the Design
Currently trying to ‘fix’ the design
  Well defined half ring, module and bus tape concept
  Half ring radii fixed
  Outer cylinder envelope
  Overall endcap length