## Slide 1: Endcap Integration and Tooling
Peter Sutcliffe
5th April 2018
INFN - Laboratori Nazionali di Frascati
IT-UK Pixel Endcap Meeting

## Slide 2: Integration and tooling overview
Clean room layout
Tooling x 3
  Cylinder manufacturing, trim jigs, end flanges
  Bare cylinder preparation and component gluing
  Services preparation
  Half ring insertion
  Transport around the assembly room?
  Systems testing-endcap frame
  Half cylinder into full cylinder assembly
  Dispatch to CERN-see Helens talk

## Slide 3: Clean room layout
First thing you notice is we still can’t afford chairs
Quite a minimalistic layout
Environmental Chamber
Services and welding bay
Endcap assembly
Half cylinder pre-production.
Half ring attachment
(on CMM)

## Slide 4: Endcap pixel layout TDR 9-8-10 Layout
Pixel Support Tube
Outer Pixel Layers
3 Layers
Heavyweight Pixel Endcap support flanges
Lightweight Pixel Endcap Support Flanges
Inner Support Tube
Beam Pipe
1975mm
Half rings
9 outer half rings R275
8 middle half rings R212.5
10 inner half rings R150
Z=3120
1st half rings Z=1200
Last half rings Z=3000

## Slide 5: Bare cylinder preparation
Trim and dress half cylinders, add holes etc.
Mount CFRP end-flanges on jig and attach inserts (2x)
Spread adhesive on outer rims of end-flanges, mount two ½-cylinders and allow to cure
Cut end-flanges at top and bottom to split assembly into two parts
Add link pieces
Currently this is mounted on aluminium tooling plate on the CMM, but will be considering using a 2.2m long optical table instead
CMM 2.7m long

## Slide 6: Completed middle half cylinder
Discrete components added, ready for services to be added….see Freds talk
At this stage tube and cable clips can also be added
Heavy Z=3000 will need to be added.

## Slide 7: Half ring insertion Liam Cunningham
Fully populated ring in handling frame ready for insertion into the half cylinder
Attach T-piece to the handling frame
Remove the outer half of the handling frame, now ready to load into insertion jig

## Slide 8: Half ring insertion… Liam
Unloaded jig, vertical edge mates with back of the T-piece
Close up of linear slides for two axis movement
Ring in frame loaded into insertion jig ready for installing to half cylinder

## Slide 9: Half ring insertion…. Liam
Insertion tooling in retracted position with ring loaded ready for insertion
Insertion tooling in loaded position ring mounting tabs located at the correct position to be attached

## Slide 10: Assembly of half cylinders
Half cylinders will be assembled in the following order:
  Fix the lightweight Z=1200 end flange in position
  Inner left and right hand
  Middle left and right hand assembled around the Inner layers
  Outer left and right hand will be assembled around the Inner and Middle layers
  Half cylinders connected with connection pieces and captive dowel screws

## Slide 11: Endcap envelopes – 5th April 2018
Envelope max R327
Outer cylinder I/R324.5
Middle cylinder I/R264.15
50mm
7mm tape
Nominal Module R295
8mm outer services
1.75mm clearance
Inner cylinder I/R203.8
50mm
7mm tape
Nominal Module R234.65
8mm middle services
1.75mm clearance
cylinder thickness 0.6mm
cylinder thickness 0.6mm
cylinder thickness 0.6mm
IST O/R144
50mm
7mm tape
Nominal Module R174.3
8mm inner services
1.8mm clearance
Endcap I/R145.8
R316.5
R266.5
R256.15
R206.15
R195.8
R145.8
1.9mm clearance
41.1
41.1
41.1
Preliminary
For
Discussion