## Slide 1
Title
Design of the Diagnostic Stations for the ELI-NP Compton Gamma Source
Supervisor: L. Palumbo Co-Supervisor: A. Mostacci
M. Marongiu Accelerator Physics Doctorate

## Slide 2
Outline
Optical Transition Radiation properties
GBS main parameters
OTR Screens
  Thermal issues
  Fatigue Stress
  Photons Evaluation
Beam Imaging
  Magnification
  Resolution
Energy Measurements
  Angular Distribution
  Data Analysis
  Simulation

## Slide 3
OTR Properties
Optical Transition Radiation (OTR) screens are widely used for profile measurements
The radiation is emitted when a charged particle beam crosses the boundary between two media with different optical properties
The visible part of the radiation is used and an observation geometry in backward direction is mainly chosen
Advantages
  Instantaneous emission process  Single shot measurements
  Good linearity
Disadvantages
  The process of radiation generation is invasive
  The radiation intensity is lower in comparison to scintillation screens

## Slide 4
Electron Beam Parameters @ IP
Electron Beam Specifications | 
Max. Energy at IP [MeV] | 280 – 720
Macro Pulse rep. Rate [Hz] | 100
Number of bunches | up to 32
Bunch spacing [ns] | 16.1
Bunch length [ps] | 0.91
Bunch charge [pC] | 25-250
εn_x,y [mm·mrad] | 0.2-0.6
Bunch Energy Spread | < 0.1%

## Slide 5
Linac diagnostics
Non-intercepting diagnostics:
Charge measurements:
4 Integrating Current Transformers (bunch by bunch)
Position measurements:
29 stripline BPMs (Macro pulse)
4 cavity BPMs (bunch by bunch)
Beam Loss Monitor System
Intercepting diagnostics:
Phase-Space measurements:
23 Beam Screens (YAG and OTR)

## Slide 6
Beam envelope along the Linac
A. Bacci, A. Giribono, C. Vaccarezza
From Gun to S-Band (80MeV)
C-Band (280MeV)

## Slide 7
Thermal Analysis OTR
32 bunches, 250pC each
M. Marongiu, et al., https://doi.org/10.1016/j.nima.2016.07.040

## Slide 8
Fatigue Stress
6 seconds
F. Cioeta, et al., ISBN 978-3-95450-182-3, pag. 246-249
Equivalent Von Mises Stress (Pa)

## Slide 9: Photons Evaluation
(400-700 nm) continuous lines
(515-585 nm) dashed lines
M. Marongiu, et al., Proceedings of IBIC 2017
x104

## Slide 10
Gated intensified camera
Measurements @ DAFNE
@ SPARC
82%@550nm
46% for Basler scA640-70gm
A. Stella, G. Franzini

## Slide 11
Camera lens layout
Camera Lens 180mm w/o teleconverter (2x)
Camera Lens 105mm w/o teleconverter (2x)
The resolution is 1/x (mm).
The sizes of each horizontal line are 2,5/x for the length and 1/(2x) for the width (mm) and vice versa for the vertical lines.
180mm lens with teleconverter (2x)
180mm lens
F. Cioeta, D. Cortis
180mm lens with teleconverter (1.4x)

## Slide 12
Camera lens test-bench
Camera Lens 180mm w/o teleconverter (2x)
Camera Lens 105mm w/o teleconverter (2x)
The resolution is 1/x (mm).
The sizes of each horizontal line are 2,5/x for the length and 1/(2x) for the width (mm) and vice versa for the vertical lines.
180mm lens with teleconverter (2x)
180mm lens
M. Marongiu et al., ISBN 978-3-95450-182-3, pag. 238-241
180mm lens with teleconverter (1.4x)

## Slide 13
Camera lens Results
Camera Lens 180mm w/o teleconverter (2x)
Camera Lens 105mm w/o teleconverter (2x)
M. Marongiu et al., ISBN 978-3-95450-182-3, pag. 238-241
105mm
105mm with teleconverter (2x)
180mm
180mm with teleconverter (2x)
180mm with teleconverter (1.4x)
1:8
1:2
Screen (3 cm)
Beam (1 mm)
100µm

## Slide 14
Gaussian Reconstruction
8 Samples
Error ~4%
If Resolution=30µm and σ>30µm
If σ=10µm and Resolution<10µm
20 Samples
Error <<0,01%
If Resolution=30µm and σ>75µm
If σ=10µm and Resolution<4µm
5 Samples
Error ~7%
If Resolution=30µm and σ>19µm
If σ=10µm and Resolution<16µm
M. Marongiu et al., ISBN 978-3-95450-182-3, pag. 238-241

## Slide 15
Energy Measurements
@ SPARC
SPF
~ 120 MeV
~ 120 pC

## Slide 16
Data Analysis
M. Marongiu, et al., https://doi.org/10.1016/j.nima.2018.02.093
Data Set 1
Data Set 2
Notes: Carica 100pC e 120pC e enrgy spread 0.1% nei 2 casi

## Slide 17
Zemax Simulation
F. Bisesto, A. Giribono, M. Croia
M. Marongiu, et al, WEPAL013, Proceedings of IPAC2018, Vancouver, BC, Canada
Simulation
Theory
Data

## Slide 18
Further Development
Distributed energy measurement
  Define layouts
Bunch to bunch measurements
  Gating System Characterization
  Intensifier Characterization
Zemax Programming Language (ZPL) Macro
  Full Spectrum OTR Beam
  Longitudinal Information
IP Diagnostics
  Measurements @ LAL -> YAG limits

## Slide 19
Thank you for your attention!