## Slide 1
Advances in Time Division Multiplexing for X-ray TES arrays
40 row TDM X-IFU demo (NASA LPA 2.5a TES array)
Co Kα (6.9 keV)
1 column X 40-row TDM
combined, ~190 k counts
ΔEFWHM = 2.40 ± 0.02 eV
Malcolm Durkin, on behalf of US Athena Collaboration.
NASA LPA 2.5a TES array
University of Colorado, Boulder: Malcolm.Durkin@NIST.gov
New flux locked loop Controller Algorithm Simulations
Highest energy pulse that the controller can handle.
Old Algorithm
New Algorithm
48 row TDM for X-IFU?

## Slide 2
DC Voltage Biased TESs
Time Division Multiplexing
Row 0
(on)
Row 1
(off)
TES bias
Notes: Fix 2 and 3 to be more similar in transition

## Slide 3
DC Voltage Biased TESs
Time Division Multiplexing
Row 0
(on)
Each TES read out by a first stage SQUID ammeter (SQ1).
Row 1
(off)
TES bias
Notes: Fix 2 and 3 to be more similar in transition

## Slide 4
DC Voltage Biased TESs
Time Division Multiplexing
Row 0
(on)
Each TES read out by a first stage SQUID ammeter (SQ1).
Row 1
(off)
SQ1 is activated opening SC switch (TESs read out one at a time)
TES bias
Notes: Fix 2 and 3 to be more similar in transition

## Slide 5
DC Voltage Biased TESs
Time Division Multiplexing
Row 0
(on)
Each TES read out by a first stage SQUID ammeter (SQ1).
Row 1
(off)
SQ1 is activated opening SC switch (TESs read out one at a time)
Signal further amplified by SQUID series array amplifier on 1K stage.
TES bias
Notes: Fix 2 and 3 to be more similar in transition

## Slide 6: Time Division Multiplexing
TES bias
Row 0
(on)
Row 1
(off)
Column 1
Column 0
We can read out many columns in parallel
8 column x 32 row systems routinely deployed.
(capable of reading out 250 pixel scale TES arrays)
TES bias

## Slide 7: LPA 2.5a 40 row demo for Athena X-IFU
X-Ray Integral Field Unit
3,168 pixel TES array
FDM is primary readout option
TDM is backup readout option
~ 40 rows being considered for TDM
“40 row” Demonstration of LPA2.5a with 8 x 32 system
160 ns row times allow readout of 12 keV pulses.
S. J. Smith et al. Poster Session
NASA LPA 2.5a TES array
Notes: Ref. Steve Smith

## Slide 8: 40 Row Demo for X-IFU
40 timing rows( 32 unique physical rows and 8 repeat rows)
Replicates noise and dynamic range of 40 row TDM
Individual Pixel Spectra

## Slide 9: 40 Row Demo for X-IFU
40 timing rows( 32 unique physical rows and 8 repeat rows)
Replicates noise and dynamic range of 40 row TDM
Individual Pixel Spectra
Coadded Spectrum

## Slide 10: 40 Row Demo for X-IFU
X-IFU Requirements
TDM 1x40: Achieved
Non-multiplexed: estimated
M. Durkin et al. IEEE Trans. Appl. Supercond. 29, 25000305 (2019).
TDM 3x40: Achieved
Future testing will occur on 960 pixel (40 row x 24 column ) TDM systems under construction.
See W. B. Doriese et al. Poster Session.

## Slide 11: TDM Beyond 40 rows
TDM is a credible readout option for X-IFU and meets its specifications.
Further improvements are desirable to save spacecraft resources and/or offer expanded capabilities.
A new flux locked loop controller could allow significant increases in row count.

## Slide 12: The Digital Flux Locked Loop
Lock Point
We linearize our SQUID amplifiers using a Flux locked loop.
Row 0
(on)
Row 1
(off)
Verr
VSQ1B
A TDM column has one flux feedback line.
The active SQ1 is locked.

## Slide 13: The Digital Flux Locked Loop
Lock Point
We linearize our SQUID amplifiers using a Flux locked loop.
Row 0
(on)
Row 1
(off)
Verr
VSQ1B
A TDM column has one flux feedback line.
SSA readout used as error signal.
Feedback updated next frame
Each SQ1 FLL is updated once a frame
using an integral controller:
The active SQ1 is locked.

## Slide 14: The Digital Flux Locked Loop
Lock Point
We linearize our SQUID amplifiers using a Flux locked loop.
Row 0
(on)
Row 1
(off)
Verr
VSQ1B
A TDM column has one flux feedback line.
SSA readout used as error signal.
Feedback updated next frame
Each SQ1 FLL is updated once a frame
using an integral controller:
The active SQ1 is locked.
Controller is a frame behind
(ΦFB1, n+1 corrects for ITES, n, not ITES, n+1)

## Slide 15: The Digital Flux Locked Loop
Lock Point
We linearize our SQUID amplifiers using a Flux locked loop.
Consequence: Verr is roughly proportional to dITES/dt.
(Higher energy X-rays greater Verr)

## Slide 16: The Digital Flux Locked Loop
Lock Point
We linearize our SQUID amplifiers using a Flux locked loop.
Consequence: Verr is roughly proportional to dITES/dt.
(Higher energy X-rays greater Verr)
We do correct for this controller error,
However, this assumes linearity and fails at higher energies, setting limits on max energy.

## Slide 17: Identifying Controller Failure Modes
We test effects of nonlinearity by moving the lock point.
Controller becomes trapped in nonlinear regime (41%), resolution degrades significantly
Controller becomes unlocked (43%), pulses no longer measurable
Failure Modes
We propose a new controller to address these issues.

## Slide 18
A New Controller Algorithm
Tracks slope of smooth part of pulse
Makes Rapid adjustment at start of pulse
(applied once during a pulse)
Integral Term
Predictive term anticipates changes in Φin

## Slide 19: Simulation Results: Faster Convergence
Error Signal near old algorithm unlock point
Measurement Error
Old Controller
New Controller
Old Controller
New Controller
pulse max slew rate
0.24 Φ0 / frame
pulse max slew rate
0.24 Φ0 / frame
Typical TDM corrections
(i.e. applying mix terms)

## Slide 20: Simulation Results
New controller algorithm allows 1.35 x higher TES current slew rates without unlocking.
Simulated pulse tracking of highest energy pulse possible without readout failure.
Old Algorithm
New Algorithm
Our 40 row demo’s max measurable energy would increase from 13 KeV to > 17.5 KeV.
Row count could be increased by a factor of (1.35)2/3 at constant SQUID noise.
48 row TDM possible (reduces multiplexer per TES by factor of 0.83).

## Slide 21: Recent Reductions in TDM Crosstalk

## Slide 22: A High Energy Tail at High count rates
MUX 18B, LPA 2.5a @21.2 cps / pixel input count rate
High Energy Tail
Events affected by PNN and TNN crosstalk have large spread in energies (High Energy tail)
Event cuts find:
2/3 of Tail due to PNN crosstalk
1/3 of Tail due to TNN crosstalk
Excluding PNN and TNN events:
Maximum output count rate per pixel ¼ that of nonmultiplexed TES
We can do better than this.

## Slide 23: The Flux Focusing Washer/ TES readout coil
To SQ1
ITES
Coil Orientation
(simplified)

## Slide 24: Implementation of Flux Focusing Washer and TES readout coil
-
+
+
-
-
+
+
-
-
+
+
-
-
+
+
-
Row 1
Row 2
Old Design:
Rows Packed together closely
-
+
+
-
-
+
+
-
-
+
+
-
-
+
+
-
New Design:
Coil windings encoded to reject signals from adjacent rows
Row 1 (pattern 1)
Row 2 (pattern 2)
Level of Nearest Neighbor Crosstalk = 3.4 ppt
Level of Nearest Neighbor Crosstalk < 0.1 ppt

## Slide 25: Conclusions
Our 40 row performance satisfies the requirements of X-IFU.
We have a credible path towards higher multiplexing factors (~48 row TDM).
We continue to reduce crosstalk to improve high photon count rate performance.
Grant Acknowledgements
The authors gratefully acknowledge funding from the NASA SAT program “Providing Enabling & Enhancing Technologies for a Demonstration Model of the Athena X-IFU.”