## Slide 1
WG2-ET General –Erice –October 15th 2009
SuspensionThermal noise limit
on the ET sensitivity curve
Outline
The last stage suspension of the ET interferometer;
The model for the thermal noise;
Parameters for the LSS in ET;
Numerical evaluations and comparison with the ET goal curve
Conclusions.
P. Puppo INFN Roma, Italy paola.puppo@roma1.infn.it

## Slide 2
Cryogenic 3° Generation GW detector
---MirrorsThermal(Low T)
Suspensions Thermal (Low T, monolithic)
---Readout (High P, Bigmasses)
---Newtonian (go underground)
big massmirrors,
monolithicsuspensions
low T
High Pcavity(>1MW)
From S. Hild et al. http://arxiv.org/abs/0810.0604
Suspension Thermal Noise
WG2-ET General –Erice –October 15th 2009

## Slide 3
The mirror last stage suspension
The role of the Last Stage Suspension is to compensate the residual seismic noise and to steer the optical components maintaining the relative position of the interferometer mirrors.
Components and roles:
      Marionette: Mirror control with actuators (coil-magnets, electrostatic) between the upper suspension stage and marionette;
      Reaction Mass (RM): Mirror steering with (coil-magnets, electrostatic) actuator between RM and mirror; Mirror protection;
      Mirror: monolithic silicon suspension.
Requirements:
Materials:
    UHV compatible;
    Amagnetic;
    No electrostatic charges;
    Internal Frequencies above the antenna bandwidth;
    Low frequencies of the system below control bandwidth;
Compatibility with SuperAttenuator and lower part of the tower:
    Weights
    Shape
WG2-ET General –Erice –October 15th 2009

## Slide 4
Mirror and its suspension wires:
  wires and mirror materials compatible with good mechanical and thermal properties;
    High thermal conductivities materials;
    Low mechanical and optical losses;
a promising material both as mirror substrate and wire is silicon having
high thermal conductivity
very low thermal expansion (zero below 17K)
The ET mirror last stage suspension (Cryogenic)
WG2-ET General –Erice –October 15th 2009

## Slide 5
Q from laser beam
Q from refrigerator
Mirror Reaction Mass:
Thermal Shield
Marionetta Reaction Mass:
Thermal Shield
High Efficiency Soft Thermal Links
(e.g. pure Al, copper)
Vacuum Chamber and Cryostat Thermal Shields
Silicon Monolithic Suspension
Conceptual scheme
WG2-ET General –Erice –October 15th 2009

## Slide 6
Big Masses: Mmirror= 150 kg,
Mrm = 150 kg(to have a proper recoil mass action)
Mmario= 400 kg (to reduce the marionette recoil)
High Power on the mirror: Plaser= 500 W
Arm Power: PFP = 3 MW
Power on coating and substrate Pabs = 3 W
Going at cryogenic temperature: thermal noises reduced
Thermal lensing negligible
T? 20K is OK for silicon
can we do better? do we need that?
Refrigeration system: noiseless, reliable
a. PT coolers
b. cryogenic fluids
WG2-ET General –Erice –October 15th 2009

## Slide 7: We can look some experimental facts The “cryo last stage”
Set-up:
Silicon mirror suspended by using two Be-Cu wires loops (1.25mmX2.5mm section);
Marionette with copper clamps,connected to the cooler by copper heat links, suspended with a titanium alloy cable;
Reaction mass of the mirror and marionette position monitored with fiber bundle sensors to measure the system modes (suspended with copper wires);
Reaction mass of the marionette holding the Virgo-like electromagnetic actuators (macor support, copper wire kapton insulated);
MRM suspended with three titanium wires;
WG2-ET General –Erice –October 15th 2009

## Slide 8: First Payload Cooling run (January 5th 2009)
During the cooling several times the PT cryo-coolers were stoppes, because of failure in the water refrigeration system of the compressors.
Helium gas filling
Helium gas pumped out
The final mirror temperature results to be 30 K while the cold head is at 15 K.

## Slide 9: Thermal inputs Estimations
Mirror: 1.9 mW (CoBe3 wires)
Recoil Mass: 1 mW (Steel c70 wires)
Marionette: 6 mW (Ti6Al4 wires)
If there is a thermal input, in the steady state, the temperature is not homogenous
30 K
27 K
23 K
29.5 K
15 K
WG2-ET General –Erice –October 15th 2009

## Slide 10: FEM thermal simulation
draw the expected equilibrium temperature when there is a laser light on the mirror
Boundary Conditions
Cryocooler Second stage link to the marionetta
Laser power on the mirror
Gaussian beam
Pabs= 1W
Pabs = 100 mW by the mirror bulk
The power absorbed by the coating is dominant
Starting point:
termalised system at 10 K
laser power on
surrounding system at 10K
The reaction masses are not present in the simulation;
Their screen effect is simulated by the surround system at 10K;
The marionetta arms are not present.
Copper and silicon thermal properties vs temperature are included in the simulation.
The mirror and marionette reaction mass will lengten the overall cooling time;
The model
Pcooler depends on the temperature (Cryomec PT curve used)
with 2 coolers the extracted power at 5 K is 1 W

## Slide 11: FEM thermalsimulation
For a wire diameter of 1.0 mm.
The transient depend on the masses
involved
Thermal flux in the steady state
Steady state Mirror temperature
5K
9 K

## Slide 12
With liquid Helium
With PT cooler
Thermal steady state
To reach a temperature of 20K with a power of 3W on the mirror we need a silicon suspension wire with a diameter of 4.5 mm;
The temperature of the marionette stage can be 5 K or 2K depending on which kind of refrigeration system is used

## Slide 13
Example: branched pendulum Virgo-like:
Upper pendulum 110 kg (Q=50) Recoil mass 50 kg (Q=105) Mirror 21 kg (very low losses monolithic suspensions)
LLS pendulum model
In presence of low dissipative mirror suspensions, the contributions of the other last stage suspension elements to thermal noise of the mirror cannot be neglected.
A new thermal noise estimation must be done by including the viscous and internal dissipations of the marionette and recoil mass pendulum.
It turns out that the marionetta’s mechanical pendulum losses give a non negligible effect via its recoil, in the off-resonance high-freq. range.
[*] VIR-015C-09, F. Piergiovanni, M. Punturo and P. Puppo, The thermal noise of the Virgo+ and Virgo Advanced Last Stage Suspension (The PPP effect).
Simple pendulum
The suspension Thermal noise

## Slide 14
q3
q2
q1
M3
M2
M1
A Virgo-like last stage suspension is a cascade of three pendula. To the first pendulum (the marionette) the mirror and the recoil mass are hung as branches.
Equivalent to a branched combination of three harmonic oscillators [*]. This is true for
horizontal and vertical degrees of freedom.
M1marionette
M2mirror
M3recoil mass
The mirror last stage suspension as a branched system
[*] Bernardini A., Majorana E. ,Puppo P. ,Rapagnani P. , Ricci F., Testi G. "Suspension last stages for the mirrors of the Virgo interferometric gravitational wave antenna." Rev. Sci. Instr. 70, no. 8 (1999): 3463.
M1
M2
M3

## Slide 15: Lagrangian of the branched system
Pendulum frequencies
Vertical frequencies
Wire radius
Wire length
Young’s modulus
Wire load
Number of
suspension wires

## Slide 16: How dissipation is introduced
Wires loss angle:
Qvhi, Qvvi viscous quality factors Di pendulum dilution factors
Fi(w), Fiv(w) loss angles describing the structural losses of the suspension wires.
Dissipation function
Intrinsic, thermoelastic and eccess losses

## Slide 17
Thermal Noise models (PPP):
1. FDT model
Lagrange Equations
Generalized forces related to the uncoupled stochastic thermal forces
Equations of motion with thermal stochastic forces
Thermal noise of an element of the branched system via the FDT theorem
The impendance matrix Z(w) contains the whole system mechanical behavior
The system is at temperature T
The thermal noise of each mass is influenced by the presence of the other masses

## Slide 18
Thermal Noise models (PPP):
2. The normal modes treatment
Normal Modes,Normal Frequencies
and normal masses
Independent thermal noise generators
Lagrange Equations

## Slide 19
ET suspensions parameters
Marionette: (Ti6Al4V wire)
d = 3 mm, Mass: 400 kg, L=2 m T=2 K
Mirror (silicon wire)
d = 5 mm, Mass: 150 kg, L=2 m T=20 K
Recoil Mass (silicon wire)
d = 3 mm, Mass: 150 kg L=2 m T=20 K
Modes: pendulum 0.28 Hz, 0.36 Hz, 0.60Hz
vertical 0.4 Hz (blades), 19 Hz, 36 Hz
violins 25 Hz, 52 Hz, 82 Hz, 120 Hz, 160 Hz, 207 Hz
Some Issues on:
Big Masses:
    reduces the recoils (good for suspension thermal noise )
    increases the violin modes (good for control)
    BUT
    reduces the vertical modes (not good for control)
    look at the overall weight!!
Wires Length Increment
    reduces the pendulum frequencies (good for suspension thermal noise )
    BUT
    reduces the violin modes (not good for control)
    reduces the vertical modes (not good for control)
Wires Diameter Increment:
    increment of the wire sections (good for cooling)
    BUT
    reduces the violin modes (not good for control)
    reduces the dilution factor (not good for suspension thermal noise )

## Slide 20
ET suspensions Materials
Ti6Al4V
Si

## Slide 21: SuspensionThermal Noise
P. Puppo. Suspension Thermal Noise for ET. (ET – 023 – 09)

## Slide 22: Suspension Thermal: comparison with FDT @ 20K + violin modes

## Slide 23: Conclusions
The suspension thermal noise affects the sensitivity in the frequency range below 10 Hz;
Importance of the different temperatures of the pendulum stages in the computation of the thermal noise
The marionette stage thermal effect is very important
The thermal noise of violin modes is negligible (but look at the frequencies)
The presence of the Marionette RM is crucial
      It acts as intermediate mass
      The marionette suspension cable must be at 2 K, Marionette RM cooled
The modal expansion model is ready and can be included in the matlab gwinc program.

## Slide 24: Materials Database
Definition of a standard data format
  data format has been defined over the “Parameters and Constants used in the Advanced and Third Generations Interferometers noise calculations” document
DB is a common container that permits:
  Simple query, looking for a specific material, e.g. on the base on the name
  More complex query, aggregating materials following user search criteria and particular parameters requirements or constrains
  It uses a standard query language: SQL (Simple Query Language)
Flexibility on output data organization and presentation
The system can be attached to a web frontend and interrogated remotely
The system is based on MySQL DBMS, Apache server and php

## Slide 25: Materials Database http://virgo.pg.infn.it/MaterialDB/v1
Properties
Type of property
Table data type
Operations
Insertion

## Slide 26: Materials Database
Some characteristics:
  Materials properties can be expanded without limitations
  During the insertion of material a sub set of properties can be used
  Properties are automatically classified and visualized by typology
  The data type can be also extended (In the current versionwe have implemented:value@300K, 2 table data, completeness, References and note)
For more information, the document about materials and DB is under develop and will be released soon.