## Slide 1: A primary electron beam facility at CERN
ICHEP 2018 Seoul July 7th, 2018
Y. Dutheil (CERN), T. Åkesson (Lund University), L. Evans (CERN), Y.Papaphilippou (CERN), S. Stapnes (CERN)*, A. Grudiev (CERN) on behalf of the working group PBC-acc-e-beams** (email: PBC-acc-e-beams@cern.ch) CERN, Switzerland
*Presenter today
** PBC: Physics Beyond Colliders (Annual workshop 2017: https://indico.cern.ch/event/644287/)

## Slide 2: Motivations
Next step for X-band technology: Any next machine at CERN is beyond LHC, i.e. 15+ years away
  We have looked carefully at what we could do with CLIC beam and/or drive-beam at a small scale – scaling the industry experience
Physics: Large increasing interest in Light Dark Matter – using e-beams, the key to this ”proposal”
Future accelerator R&D: Accelerator R&D and project opportunities with e-beams as source - many of great interest for CERN
Primary electron beam facility at CERN
2

## Slide 3: Physics with e-beams, LDMX
[1]Talk by P. Schuster Exploring Hidden Sector Physics with an electron beam facility Physics beyond collider annual workshop
November 21 2017, CERN
indico.cern.ch/event/644287/contributions/2762531/
[2] See more about the physics and project in recent talk: T. Åkesson https://indico.lal.in2p3.fr/event/4884/
Primary electron beam facility at CERN
3

## Slide 4: Electrons at CERN - overview
Accelerator implementation at CERN of LDMX type of beam
X-band based 70m LINAC to ~3.5 GeV in TT4-5
Fill the SPS in 1-2s (bunches 5ns apart) via TT60
Accelerate to ~16 GeV in the SPS
Slow extraction to experiment in 10s as part of the SPS super-cycle
Experiment(s) considered by bringing beam back on Meyrin site using TT10
Beyond LDMX type of beam, other physics experiments considered (for example heavy photon searches)
Acc. R&D interests: Overlaps with CLIC next phase (klystron based), FEL linac modules, e-beams for plasma, medical/irradiation/detector-tests/training, impedance measurements, instrumentation. positrons and damping ring R&D
Primary electron beam facility at CERN
4

## Slide 5: The flow
3.5GeV Linac
Acceleration to in SPS
Extraction
Primary electron beam facility at CERN
5
Transfer to SPS

## Slide 6: Linac parameters
0.1GeV S-band injector
3.4GeV X-band linac
  High gradient CLIC technology
  13 RF units to get 3.4 GeV in ~70 m
2 x 50MW
c
p
kl
kl
~5.3m
e-
modulator
Possible parameters | 
Energy spread (uncorrelated*) | <1MeV
Bunch charge | 52 pC
Bunch length | ~5ps
Norm. trans emittance | ~10um
N bunches in one train | 40
Train length | 200 ns
Rep. rate | 50/100 Hz
RF design of the X-BAND linac for the EUPRAXIA@SPARC_LAB project M. Diomede Et al., IPAC18
Primary electron beam facility at CERN
6
Notes: 52pC is 3E8 electrons

## Slide 7: Linac components available
Examples
One RF unit accelerates 200ns bunch train up to 264 MeV
+
Accelerating structure
Pulse compressor
c
p
kl
kl
~5.3m
e-
modulator
Klystron
Modulator
Primary electron beam facility at CERN
7

## Slide 8: Linac in TT5/TT4
Flexible bunch pattern provided by photo-injector 5ns, 10ns, … 40ns bunch spacing
High repetition rate
  200 ns trains at 100 Hz
To be installed in the available transfer tunnels TT4, in line with the SPS
Room for accelerator R&D activities at end of linac (duty cycle in many cases low for SPS filling so important potential)
Primary electron beam facility at CERN
8

## Slide 9: Transfer tunnel, TT60, from the Linac into the SPS
Bunch to bucket injection in the 200MHz SPS longitudinal RF structure.
Total of 75 trains of 40 bunches
3000 bunches
1012 electrons in the ring
Injection into the SPS
Primary electron beam facility at CERN
9
Notes: Up to 1.5E12
Discuss injection gap

## Slide 10: SPS RF system
Acceleration to 16 GeV can safely be achieved
Existing 200 MHz cavities from LEP era to be re-installed
  Need 10MV for 16GeV electrons
  (12 + 1) 200 MHz Standing Wave Cavities [1 MV per cavity] available
Space is available to install them
5ns, 10ns, … 40 ns longitudinal structure is imposed by the available cavities
Trains of 200ns (linac) separated by 100ns gaps (injections kicker)
Voltage for 5min quantum lifetime
Energy loss per turn (MeV)
Courtesy J. Jowett
Primary electron beam facility at CERN
10

## Slide 11: Slow extraction to experiments
Extraction
Primary electron beam facility at CERN
11

## Slide 12: Slow extraction principle, in frequency space
Spread in oscillation frequency within the beam follows
  Transverse distribution
  Longitudinal distribution in presence of chromatic lattice
Position of the resonant condition is set by the machine
Synchrotron radiation constantly diffuse the particles to fill the tail in the distribution
The extraction rate can be controlled by changing the position of the resonant condition
Extraction rate
Resonant condition extraction
Tune (frequency)
diffusion
Electrostatic Septum
Primary electron beam facility at CERN
12

## Slide 13: Structure of extracted beam
Flexibility
  Bunch spacing 5ns, 10ns, … 40ns
  Average electrons per bunch can be chosen from <1 to anything
  Transverse beam spot on target from very small up to hundred cm2
This flexibility can deliver the needs of LDMX
  Phase 1 : 1014 electrons
  Phase 2 : 1016 electrons
up to 40 bunches with 5ns spacing
200 ns
100 ns
Gap of 100ns with 0.5m injection kicker
0s
10s
20s
30s
Beam in the SPS
Energy
Beam on target
~1s
Primary electron beam facility at CERN
13

## Slide 14: Beamdump experiments possible
After this beam has been delivered there is still a lot of electrons in the SPS
These can quickly be dumped into a separate beam line
  1012 electrons within 23μs, possibly up to 4 times more
If there would be a high priority the dump can be repeated every 2 s
0s
10s
20s
30s
Beam in the SPS
Energy
Beam on target
~1s
Beam dumped
…
Primary electron beam facility at CERN
14

## Slide 15: An Electron Beam Facility at CERN
Primary electron beam facility at CERN
15

## Slide 16: Electron beam transfer line from the SPS to experiments
Uses existing TT10 line, designed to transport 10/20 GeV beams
Collimation in the line for control of beam distribution and intensity
  ~ Gaussian beam can be made almost flat by careful collimation
Beam size might be increased greatly at the target
  Size of beam-spot chosen to deliver number of electrons/cm2/bunch-crossing on target
  For instance a 2cm vertical and 20cm horizontal beam is feasible
  There is flexibility on the choice of both horizontal and vertical beam sizes
Primary electron beam facility at CERN
16
Notes: TT10 was designed for 10 to 20 GeV

## Slide 17: Extracted beam and experimental area
In total ~50 m new tunnel
Primary electron beam facility at CERN
18

## Slide 18: Extracted beam and experimental area
Experiment hall
Primary electron beam facility at CERN
19

## Slide 19: Extracted beam and experimental area
Location of the experiment hall
Primary electron beam facility at CERN
20

## Slide 20: Instrumentation
Linac:
Position
  Re-use of CTF3 inductive pick-ups
  Simple button BPMs would also do the job
Beam Size
  OTR screens (can also be combined with streak camera for bunch length)
Intensity
  Re-use of CTF3 inductive pick-up or standard beam current transformers
[1] R. Jones, Instrumentation challenges, March 1st 2018, indico.cern.ch/event/703049/
SPS:
Position
  Standard orbit system (consolidated in LS2)
  Should be able to measure to 1e9 (limit ~5e8)
Beam Size
  Wirescanners
  Possible use of synchrotron radiation
Intensity
  DC Transformer OK for total current
  Fast BCT does not distinguish 5ns spaced bunches
  Could do batch by batch but at limit of resolution (tbc)
The challenge of measuring very low intensity beam can be circumvented using a higher intensity for beam setup
Extracted beam:
Position & Intensity
  Use of fibre monitors.
    Developed for new EHN1 (neutrino platform) secondary lines
    Scintillating (or Cherenkov) fibres
    Low material budget
    > 90% efficiency for single particles demonstrated
  R&D required to make them UHV compatible
Primary electron beam facility at CERN
17

## Slide 21: Potential use of such a facility
Physics
LDMX
Other hidden sector experiments, incl. dump-type experiments using the available higher intensity
Nuclear physics
Accelerator physics
CLIC: Linac goes a long way towards a natural next step for use of technology (collaborate with INFN and others also using technology for X-band linacs in coming years)
  Possibly relevant also for other potential future facilities using electrons (rings) considered at CERN
Plasma studies with electrons
  Use electron (3.5 GeV) beam as driver and/or probe – study by AWAKE WG
Positron production (interesting for LC and plasma) and studies with positrons for plasma and LEMMA concept for muon collider
General acc. R&D as in CLEAR – existing ~200 MeV linac - today (https://clear.web.cern.ch)
  Plasma-lenses, impedance, high grad studies, medical (electron irradiation), training, instrumentation, THz, ESA irradiation
  Recent results: https://acceleratingnews.web.cern.ch/article/first-experimental-results-clear-facility-cern
General Linear Collider related studies
  Example: damped beam for final focus studies (beyond ATF2)
Primary electron beam facility at CERN
21

## Slide 22: Concluding remarks
Important physics opportunities with e-beams at CERN
Based on previous usage of the CERN accelerator complex, and building on the accelerator R&D for CLIC an electron beam facility would be a natural next step
  No show-stoppers have been found when exploring this option
  LDMX interest in pursuing this option as beam close to ideal (LDMX beam: https://arxiv.org/abs/1805.12379)
Will also provide many opportunities for important and strategic accelerator R&D at CERN
Work well underway to write this up and conclude on outstanding points, including a cost estimate – within next ~4 months
  Some user cases will need further studies
Working group meets ~monthly
Representation across user groups, machines, technical systems and CE/infrastructure
- Thank you -
Primary electron beam facility at CERN
22