## Slide 1: MUonE Muon Electron Elastic Scattering
U. Marconi
INFN Bologna
On behalf of the proponents
“When all else fails, you can always tell the truth.” A. Salam

## Slide 2: Content
Introduction
Test beam 2018 results
  Implications on the detector design
Plans for 2019
Measurement technique
Progresses with the theory

## Slide 3: Test beam 2018
The setup has been located downstream COMPASS, behind the Tungsten hadrons filter.
  Aim of the measurement campaign: ese muons, mainly from pion decays, to study the muon – electron elastic scattering.
    Estimated beam momentum p = (187±7) GeV
    Correlation between the scattering angles: muon angle vs the electron angle;
    Electron energy vs the electron angle correlation and PID.
The detector consists of:
  Tracking system: stations equipped with the AGILE silicon strip sensors: 400 micron thick, single sided, ~40 micron intrinsic hit resolution.
  Electromagnetic calorimeter: 3x3 cell matrix.

## Slide 4: Test beam 2018
beam

## Slide 5: Test beam 2018: arrangements
beam
Tracking station positioning
Δz ~ 1mm

## Slide 6: Simulation: Test beam 2018, GEANT4
Tracking algorithm applied.
Configuration: without T2, using the downstream boxes 2, 4 and 5
Box 3 removed since it was not working properly
150 million incoming muons → 5742 reconstructed events
angle_µ vs angle_e
40µm hit resolution
angular ~ 0.1 mrad
Elasticity curve: beam momentum at 187 GeV
5 mrad
50 mrad

## Slide 7
Signal
Background
angle_µ vs angle_e
Pair production
Simulation: Test beam 2018, GEANT4

## Slide 8
Pair production
Signal
Background
Simulation: Test beam 2018, GEANT4
Electron candidate: Ee > 1 GeV

## Slide 9
Energy_e vs angle_e
Simulation: Test beam 2018, GEANT4
Electron energy angle correlation

## Slide 10: Data: using the Calorimeter
angle_μ vs angle_e
Elasticity curve: beam momentum (187 ± 7) GeV
Data with E > 1 GeV
ECAL

## Slide 11: Data: using the Calorimeter
angle_μ vs angle_e
Elasticity curve: beam momentum (187 ± 7) GeV
Data with E > 0.5 GeV
ECAL

## Slide 12: Ongoing studies
Efficiency of the selection
  χ2 of the tracks
  Coplanarity of the three direction vectors.
  Elasticity: d= d(P,γ) of the angles from the elasticit curve. Not used yet.
  Common vertex constraint at the target of the tracks (muon in, muon out, electron candidate)
  Energy

## Slide 13: Effects of the selection cuts
Signal candidates

## Slide 14: How relevant is the hit resolution?

## Slide 15: Effect of the resolution: GEANT4 UA9 resolution 7μm
angle_µ vs angle_e
angle_µ vs angle_e

## Slide 16: Effect of the resolution: GEANT4 UA9 resolution 7μm
Signal
Background

## Slide 17: Effect of the resolution: GEANT4 UA9 resolution 7μm Ee > 1 GeV
Signal
Background
Who are them?
Notes: Che cosa sono I punti blue sotto la curva di elasticità?
Dunque, cosa sono quelli verdi?

## Slide 18: Sensors comparison
Electron energy (GeV)
Angular resolution
10 μm hit resolution
20 μm hit resolution

## Slide 19: Sensors
Requirements:
  Dimensions: 10 cm × 10 cm
  Single hit resolution: r ≤ 10 μm
  Clock rate: 40 MHz
  Minimal thickness: d ≤ 300 μm
Possible implementation:
  strip pitch p ≤ 50μm and floating electrodes charge sharing to get a resolution better than the geometrical σ=p/sqrt(12), depending on S/N
  1028 channel hybrid per sensor single sided

## Slide 20: Requests for funding
Sensor: 3 kE each, if to be built on purpose.
Hybrid circuit, to host the ASICs: 1 kE each.
DAQ system: 10 kE
Mechanics: 2 kE
To build 8 detector planes (XY coordinates): 8 × 4 + 10 + 2 = 44 kE
We assumed the cost would be order ~50 kE , sub-judice:
  Do ASICs providing the required features exist?

## Slide 21: Plans for 2019
Sensors and ASIC:
  Surface: 10 cm x 10 cm
  Rate: 40 MHz
  Hit resolution: 5 - 10 μm Sensors’s thickness ≤ 300 μm
  Charge division, i.e. floating strip technology
Mechanics support to get ~10 μm z precision
Test beam: DESY, MAINZ and Fermilab.
Measure the energy or the momentum of the electron candidates
  In order to reject the background due to muon pair production and to get rid of low energy MSC electrons

## Slide 22: Plans for 2019 (2)
Detailed MC description of the detector:
  Needed to perform detailed feasibility studies.
  Correct for MSC effects, account for detector’s efficiency and selection cuts.
Measuring the running of α = α (q2) with simulated data
  LO based feasibility studies ongoing
  NLO We can’t rely on a mathematical function expression for the cross-section: It might turn to be rather an involved procedure.

## Slide 23: Possible location at CERN M2
Between BSM and COMPASS
A. Magnon & C. Valle document

## Slide 24: Measuring the momentum
C dipole magnet
B

## Slide 25: Measuring the momentum (2)

## Slide 27: Spare slides

## Slide 28: Signature: elastic scattering in the (θe , θμ) plane
e-out
μ-out
μ-in
θe
θμ
θe  Ee  t = q2 = 2me2 - 2meEe

## Slide 29: Cross section and the signal
To reach a precision on aμHLO as with time-like data (4 × 10-10):
2 years of data taking, with a muon beam of intensity of 1.3 × 107 s-1 60 cm of low Z material segmented in thin layers, each of 10mm

## Slide 30: Tracking efficiency