## Slide 1
Terahertz Driven
Particle Acceleration of relativistic beams
S.P Jamison
Department of Physics, Lancaster University, U.K.
Cockcroft Institute for Accelerator Science, Daresbury, U.K.
S.P. Jamison, EAAC 2019, September 2019

## Slide 2
Dr. David Walsh
Dr. Edward Snedden
Terahertz acceleration group
The Cockcroft Institute: Terahertz acceleration group
Vasileios Georgiadis
Elliott Smith
Dr. Morgan Hibberd
Dr. Robert Appleby
Dr. Darren Graham
Dr. Daniel Lake
Oliver Finlay
Prof. Steven Jamison
Alisa Healy
Prof. Graeme Burt
S.P. Jamison, EAAC 2019, September 2019
Dr Yuri Saveliev
Dr James Jones
Tom Pacey

## Slide 3: Why THz radiation for particle acceleration?
Oscillation period short, and well matched to the bunch duration
High field strengths possible.
Wavelength allows for easy fabrication of structures.
THz advantages:
Obtaining sub-luminal phase velocities
Broadband pulses – controlling dispersion
High field THz sources still challenging
THz challenges:
Radio frequencies
Frequency 3 GHz period  300 ps,
l  10 cm Cavity aperture ~ 2 cm
Eacc ~ 10 - 100 MV m-1
Pulse length: 5 ms (superconducting) 5 ms (normal conducting)
THz frequencies
Frequency 1 THz period  1 ps,
l  300 mm – 1 mm Cavity aperture  1 mm
Eacc  100 MV/m to > GV/m
Pulse length 1-5 ps
Optical frequencies
Frequency 300 THz period  3 fs,
l  0.8 – 1 mm Cavity aperture  1 mm
Eacc  100 MV m-1 to >> GV/m
Pulse length 20 fs – 1 ps
50um silica
[2] E.A Peralta et al., Nature, 503.7474 (2013): 91-94
S.P. Jamison, EAAC 2019, September 2019
Notes: There are several points to consider; (1) phase matching of electrons and THz pulse over a wide bandwidth,
(2) accelerating gradient, (3) shunt impedance, and (4) ease of fabrication.
(5) Other issues include charging of the dielectric and electron bunch injection into a small aperture.
waveguide dispersion typically results in an unmatched group velocity and so the pulse envelope of a short THz pulse changes along the length of the structure. This reduces field amplitude and therefore accelerating gradient as the envelope propagates at a different velocity to the electron

## Slide 4
Terahertz-driven interactions: Relativistic electrons
E. C. Snively et al. arXiv:1906.03358 (2019)
THz-driven compression
2.5 MeV electron beam
x3 compression
x2 timing jitter reduction
THz-driven streaking
THz-driven streaking
R. K. Li et al. Phys. Rev. Accel. Beams 22, 012803 (2019)
Streaking of a 3.1 MeV electron beam using a parallel-plate waveguide
L. Zhao et al. Phys. Rev. Lett. 122, 144801 (2019)
Dielectric tube, helical deflection for 50-fold longitudinal compression
of 3.4 MeV beam
M.T. Hibberd et al, arXiv 1908.04055 (2019)
Dielectric lined waveguide
Quasi-monochromatic THz
Energy modulation &
acceleration on 35MeV beam
THz-driven acceleration

## Slide 5
Dielectric lined waveguides for particle beam acceleration
Mode patterns in waveguide can support longitudinal electric field
Dielectric layers enable velocity matching of carrier-frequency to particle beam
Longitudinal Cross-section field pattern
propagation
LSE11 mode
Phase-velocity matching
vg ~ 0.6c
S.P. Jamison, EAAC 2019, September 2019

## Slide 6
Dielectric lined waveguides for relativistic particle beam acceleration
Phase velocity matching, vf = b c
Group velocity vg << vf
Single-cycle THz input
Field in frame of 50MeV electron beam (v = 0.9995 c)
few-cycle THz input (quasi-monochromatic)
Particle trajectory
Particle see constant electric field phase (accelerator or decelerating)
Particle trajectory
S.P. Jamison, EAAC 2019, September 2019

## Slide 7
Dielectric lining results in:
Longitudinal Section Magnetic modes
LSM11 for acceleration
Designed for velocity-matching to the 35 MeV electron beam
Our approach: Rectangular dielectric-lined waveguide
DLW side
1200 μm
575 μm
DLW exit
695 μm
Mirror side
DLW assembly
3.18 mm
3.25 mm
Coupler entrance
S.P. Jamison, EAAC 2019, September 2019

## Slide 8
THz network analyser for waveguides
structure characterization with electro-optic time-domain sampling
Power spectra
plus phase
spectra
S.P. Jamison, EAAC 2019, September 2019

## Slide 9
The Wigner-Ville Distribution (WVD) of signal S(t) is
Fourier transformation of autocorrelation.
WVD describes how the spectral density changes over time.
THz network analyser for waveguides
structure characterization with electro-optic time-domain sampling
S.P. Jamison, EAAC 2019, September 2019
Notes: Having now the corrected, free of reflections waveforms, we proceed with time-frequency analysis. We can see how the frequency content changes over time.
although this model did not consider the influence the effect of the coupler.

## Slide 10
First demonstrated using a Michelson interferometer with a photoconductive antenna
Narrowband terahertz source
Tilted-pulse-front pumping in LiNbO3
H. Hirori et al. Appl. Phys. Lett. 98, 091106 (2011)
Chirped-pulse beating for narrowband THz generation
Our tilted-pulse-front setup
A.S. Weling & D.H. Auston, J. Opt. Soc. Am. B 13, 2783 (1996)
J. Hebling et al. Opt. Express 10, 1161-1166 (2002)
Diagram from:
S.P. Jamison, EAAC 2019, September 2019

## Slide 11
Polarisation of the terahertz beam
To excite the accelerating mode of the DLW
 THz beam with a TEM01 mode is required
quasi-TEM01
TEM00
PTFE
phase-shifter plate
THz beam
TEM01 mode
Previously demonstrated using the interferometric recombination of two polarity-inverted, linearly polarised THz beams
M. Cliffe et al. Appl. Phys. Lett. 108, 221102 (2016)
Phase-shifter plate
Achieve effective polarity inversion by using a phase delay
Half-cycle phase delay difference between top and bottom halves of the THz pulse
S.P. Jamison, EAAC 2019, September 2019

## Slide 12
35 MeV
CLARA electron beam
Experimental approach
Dipole
magnet
PTFE
phase-shifter
plate
THz
beam
Dielectric-lined
waveguide
YAG screen
quasi-TEM01
mode
Mirror with
400 µm aperture
Quadrupole
magnet (triplet)
Off-axis parabolic mirror
x3
x3
TEM00
mode
S.P. Jamison, EAAC 2019, September 2019

## Slide 13
Daresbury Laboratory: CLARA test facility
CLARA
Compact Linear Accelerator for Research and Applications
≈ 50 MeV
≈ 5 MeV
Bunch parameters
Energy: ≈ 50 MeV
Charge: 20 – 100 pC
Duration: 0.3 – 6 ps
Spot size: 100 µm
Rep. rate: 10 Hz
S.P. Jamison, EAAC 2019, September 2019

## Slide 14
Experimental user area
Electron beam
Quadrupole magnets
Interaction chamber
Dipole magnet
to YAG screen
Electron beam
Flexible end-station for rapid
reconfiguration of experiments on an
optical breadboard inside vacuum chamber
Optical breadboard
S.P. Jamison, EAAC 2019, September 2019

## Slide 15
Experimental setup
S.P. Jamison, EAAC 2019, September 2019

## Slide 16
Experimental setup
S.P. Jamison, EAAC 2019, September 2019

## Slide 17
Results: Chirped electron bunch
CLARA operated in a long electron bunch configuration
Bunch duration of 6 ps FWHM
Linear (approx.) chirp of 53 keV/ps
Estimated from beam dynamics simulations
THz pulse
Electron bunch
6 ps
2.5 ps
Energy
Time
Energy
Time
THz off
THz on
Intensity (arb. units)
Image on electron energy spectrometer
f = 0.4 THz
Δf = 100 GHz
Longitudinal phase space
S.P. Jamison, EAAC 2019, September 2019
High-charge: 60pC through structure

## Slide 18
Results: Chirped electron bunch
CLARA operated in a long electron bunch configuration
Bunch duration of 6 ps FWHM
Linear (approx.) chirp of 53 keV/ps
THz pulse
Electron bunch
6 ps
2.5 ps
Energy
Time
Energy
Time
THz off
THz on
f = 0.4 THz
Δf = 100 GHz
Longitudinal phase space
Determining the peak terahertz-driven acceleration
Calculation imposing a sinusoidal THz-driven modulation on to a model electron bunch, including:
 Bunch emittance, energy spread and chirp
Estimated from beam dynamics simulations
δETHz = 8.8 keV
Linear chirp = 47.3 keV/ps
S.P. Jamison, EAAC 2019, September 2019

## Slide 19
Results: Chirped electron bunch
CLARA operated in a long electron bunch configuration
Bunch duration of 6 ps FWHM
Linear (approx.) chirp of 53 keV/ps
Measured longitudinal phase-space distribution
Obtained from 100 single-shot spectra with varying THz-electron bunch timing, using:
The measured energy modulation period δE(E)
The known THz period τ = 2.5 ps (0.4 THz)
Estimated from beam dynamics simulations
2.5 ps
2.5 ps
Determining the peak terahertz-driven acceleration
Calculation imposing a sinusoidal THz-driven modulation on to a model electron bunch, including:
 Bunch emittance, energy spread and chirp
δETHz = 8.8 keV
Linear chirp = 47.3 keV/ps
100 shots
Linear chirp 47.5 keV/ps
S.P. Jamison, EAAC 2019, September 2019

## Slide 20
Results: Chirped electron bunch
CLARA operated in a long electron bunch configuration
Bunch duration of 6 ps FWHM
Linear (approx.) chirp of 53 keV/ps
Waveguide resonance and velocity-matching
Estimated from beam dynamics simulations
Determining the peak terahertz-driven acceleration
Calculation imposing a sinusoidal THz-driven modulation on to a model electron bunch, including:
 Bunch emittance, energy spread and chirp
δETHz = 8.8 keV
Linear chirp = 47.3 keV/ps
Terahertz frequency varied from 0.32 – 0.55 THz
 Peak in modulation strength at 0.40 THz
Constant modulation period observed
 Interaction dominated by velocity-matched frequency
S.P. Jamison, EAAC 2019, September 2019

## Slide 21
Modelled
Results: Short electron bunch
CLARA operated in a short electron bunch configuration
Bunch duration of 2 ps FWHM
Residual linear chirp of <10 keV/ps
Estimated from beam dynamics simulations
THz pulse
Electron bunch
2.5 ps
Energy
Time
THz off
THz on
f = 0.4 THz
Δf = 100 GHz
Longitudinal phase space
2 ps
“Single-bucket” acceleration
Energy
Time
Modelled
S.P. Jamison, EAAC 2019, September 2019

## Slide 22
Relativistic electron beam acceleration
THz-induced energy and timing stabilization
Energy jitter in electron beam injected into THz structure
Energy modulation more stable – dependent on THz timing, not incoming electron energy.
S.P. Jamison, EAAC 2019, September 2019

## Slide 23
THz-induced energy and timing stabilization
Approximately linear chirp  Ecentral proportional to tarrival
S.P. Jamison, EAAC 2019, September 2019

## Slide 24
THz-induced energy and timing stabilization
S.P. Jamison, EAAC 2019, September 2019
Addition of R56 for compression
Compression : sub-10fs for realistic parameters
Active timing stabilization Micro-bunches locked to THz timing & THz timing locked to laser envelope

## Slide 25
Summary
M.T. Hibberd et al. Acceleration of relativistic beams using laser-generated terahertz pulses. arXiv:1908.04055 (2019)
Demonstrated THz-driven linear acceleration of a 35 MeV relativistic electron beam
  Measurements performed at the CLARA test facility, Daresbury Laboratory
  Generation of narrowband THz pulses with required polarity-inversion
  Dielectric-lined waveguide designed for velocity-matching
  Energy spectra modulation of chirped electron beams,
  Near-singleAcceleration/deceleration of short bunches
S.P. Jamison, EAAC 2019, September 2019
Poster today. Oliver Finlay
Terahertz-Driven Velocity Bunching Experiment
Other research areas: From 100keV to MeV with a THz-driven injector

## Slide 26
With thanks to Cockcroft Institute THz Acceleration Group & STFC Daresbury Laboratory CLARA team
S.P. Jamison, EAAC 2019, September 2019
Postdoc positions available: - THz driven acceleration
(Lancaster University) - Ultrafast electro-optic diagnostics for AWAKE
PhD positions available : THz driven acceleration. (laser/accelerator/simulations)
        Contact: s.jamison@Lancaster.ac.uk