## Slide 1: Status of Steering Module and Future Plans
Eric Raguzin and Sergio Rescia

## Slide 2: Outline
Steering Module Design
Steering Module Future Improvements
Interconnections
Future R&D Items

## Slide 3: Steering Module Overview
Feedthrough
Photodetector Module
Strip Motherboard
Steering Module
Power
High voltage
SPI
Data output (fiber)
Amplified Output
HV3418
HV Switch
HV5523
Amp Enable
SPI In
SiPM Bias
Amp. Power
VEE
SPI Out
VCC
µC
X25 OUTPUTS
Differential to Optical
Optical
Enable
Control
Photodetector Module
Steering Module

## Slide 4
HV3418
HVOUT 1-25
Connected to
SAMTEC
SIPM_01_VBIAS
to
SIPM_25_VBIAS
HV5523
HVOUT 1-25
Connected to
SAMTEC
TIA_EN1
to
TIA_EN_25
100n
100V
VHV
DATA INPUT
HVOUT1
(Outputs 3 to 30 not shown)
Latch
HVOUT2
HVOUT31
HVOUT32
32-Bit
Shift
Register
HV5523
CLK
VDDF
VDDF
DATA OUTPUT
DATA INPUT
CLK
LE
HVOUT2
CLK
POL BL LE
64 bit Static Shift Register
64 Latches
VPP
HVOUT1
DIR
HVOUT64
DIOA
•
•
•
60 Additional
Outputs
•
DIOB
HVOUT63
HV3418
VDDF
VDDF
Latch
Latch
Latch
VDDF
VDDF
L̅E̅
P̅O̅L̅
B̅L̅
VDDF
READ-BACK
Block Diagram

## Slide 5: Steering Module
Steering Module designed, fabricated and tested
Fully functional at liquid nitrogen temperature
Test Input board (takes HV, Amplifier bias, SPI Signals)
Steering Module
Test Output Board

## Slide 6: Switching Testing at Cryogenic Temperature
10 Channels from each chip were monitored in liquid nitrogen for 1 week
HV3418 alternated from 0V to 60V, HV 5523 from 0V to 5V

## Slide 7: Switching Testing at Cryogenic Temperature
Channels were SPI written “on” and “off” every 3 seconds.
Data is as expected (besides gap due to connector).
No indication of long term issues at cryogenic temperatures

## Slide 8
Processes that impact the lifetime of CMOS circuits:
  Electromigration
  Stress migration
  Time-dependent dielectric breakdown
  Thermal cycling
  Hot-Carrier Effect
First three are thermally activated processes (exponential dependence on temperature) and become negligible at cold temperatures.
The process that impacts the lifetime at cold is ONLY Hot-Carrier Effect.
One can perform accelerated lifetime tests on devices to understand the impact of this effect.
LIFETIME OF ELECTRONIC ACTIVE DEVICES

## Slide 9
Hot-Carried Effect deteriorates the performance of devices by creating interface states or trapping charge in the dielectric.
Some hot electrons exceed the energy required to create an electron-hole pair, resulting in impact ionization. Electrons proceed to the drain. The holes drift to the substrate yielding substrate current.
A very small fraction of hot electrons exceeds the energy required to create an interface state at the Si-SiO2 interface: 3.7eV for electrons, ~4.6eV for holes.
Hot Carrier Effect primarily affects performance of NMOS transistors.
LIFETIME OF ELECTRONICS: HOT CARRIER EFFECT
Electric field is the strongest near the drain

## Slide 10
For NMOS:
L=180nm
W=10um
LIFETIME*CURRENT DENSITY vs 1/VDS
EXTRACTED FROM THE STRESS MEASUREMENTS
LIFETIME (AGING) OF THE ELECTRONICS
It was found for 180nm, 130nm and 65nm technologies that reducing the VDS at cryogenic temperature by ~6% makes the lifetime equal to that at 300K (x10 improvement).
Increasing the device length (thus decreasing electric field) also increases the lifetime.

## Slide 11: Steering Module Lifetime: Assured by Design
HV3418 HV push-pull switch ■ HVmax= 180V ➝ VBIAS,max≃70V ■ Vlogic,max= 12V ➝ Operating Logic Voltage ≃4.5V
HV5223 open drain switch:
■ HVmax= 220V ➝ VEN,H=2.5V
■ Vlogic,max=5.5V ➝ Operating Logic Voltage ≃4.5V
HCE for switched logic happen only during transition (no current in steady state). Minimal switching of SM logic, only during configuration

## Slide 12: Steering Module Connectors
Back uses Samtec FTS connectors to mate with strip motherboard CLP (non radiopure)
Want to add ground pins.
Mix-up with connector orientation. It will be fixed in next version
Input uses Mini-D connector for now.
Will look into radiopure connectors and minimizing number of signal lines

## Slide 13: Future improvements (minimizing signal lines)
All signals
Minimizing signals will lower mass of cable, help with radiopurity
29 total lines ★ 22 signal, power ★7 shields
HV3418
HV5523
Return
Shield
Signal
Sense
SPI - CLK
SPI - DATA
SPI - CS
VDD
LV_UC
VCC
VEE
SPI - Readback
HV

## Slide 14
+2.5 V
RET +2.5 V
+ sense
- sense
- 2.5 V
RET -2.5 V
+ sense
- sense
HV
GND- HV
shield
LV- uController
RET - LV –uController
shield
VDD
VDD - RET
Shield
SM control 1 +
SM control 1 -
Shield
SM control 2 +
SM control 2 -
Shield
SM control 3 +
SM control 3 -
Shield
SM control 4 +
SM control 4 -
shield
total of 29 conductors
(22 signals, power & 7 shields )
Connector needs 23 positions min (22 signals, 1 for shields together)
SAMI Cable for DarkSide (mates to MiniD on Steering Module Proto)

## Slide 15: Future improvements (minimizing signal lines)
Linear LTC6820 – takes 4-pin SPI, encodes in bi-directional differential signal
With proper termination resistors, can be designed for up to 100 meters of twisted pair cabling
Low EMI susceptibility/High Noise immunity
For our application, slow data rate is OK

## Slide 16: Future improvements (minimizing signal lines)
Requires matching chip on the warm side of the flange
Would reduce to 19 signals
HV3418
HV5523
Return
Shield
Signal
Sense
IP
LTC6820
IN
SPI - CLK
SPI - DATA
SPI - CS
SPI - Readback
VDD
LV_UC
VCC
VEE
HV

## Slide 17
+2.5 V
RET +2.5 V
+ sense
- sense
- 2.5 V
RET -2.5 V
+ sense
- sense
HV
GND- HV
shield
VDD
RET - VDD
shield
LV- uController
RET - LV –uController
shield
SM control 1 +
SM control 1 -
Shield
SM control 2 +
SM control 2 -
Shield
SM control 3 +
SM control 3 -
Shield
SM control 4-ctrl +
SM control 5-ctrl -
shield
total of 11 conductors (10 signals, power & 1 shields )
Connector needs 11 positions min
SAMI Cable for DarkSide: Minimizing Number of Conductors (Cable Mass)

## Slide 18: Future improvements (minimizing signal lines)
Can achieve similar reduction by using USB-to-Serial chip
Will use 4 pin USB - power and ground from existing lines
HV3418
HV5523
Return
Shield
Signal
Sense
DATA +
FT232H
DATA -
SPI - CLK
SPI - DATA
SPI - CS
SPI - Readback
VDD
LV_UC
VCC
VEE
HV

## Slide 19: Radiopurity
Next (final) version of Steering Module will be made with Pyralux.
Steering Module needs only two copper layers. If solder mask cannot be used, an extra layer of Pyralux may be needed to insulate SM from strip motherboard (blind vias).
Need a radiopure connector between SM and strip motherboard and to connect to input power/signal cable

## Slide 20: Radiopure SM to strip motherboard
An interposer with compression type contacts (eg “Fuzz Button”) allow reliable connectivity at low T with ~10mΩ resistance
Requires external pressure to hold two surfaces together (e.g. screws)
Flexibility with choice of interposer body material

## Slide 21: Radiopure SM to strip motherboard
Similar ideas:
■ Ardent Concepts’ “Stamped Contact” ■ Belfuse (Cinch) “CIN::APSE” contact
Are currently procuring samples, will test connectors/interposers for radiopurity
CIN::APSE
Ardent Concepts “Stamped Contact”

## Slide 22: Radiopure SM to strip motherboard (backup)
Strip Motherboard
Install thru-hole, open-ended metal receptacles on the SM and SMT metal pins on the Strip Motherboard
Steering
Module
Strip Motherboard
SM

## Slide 23: Backup Slides

## Slide 24
General spread of 60V readings