## Slide 1: Computing Status
Emanuele Leonardi
PADME General Meeting - LNF January 8-9th, 2019

## Slide 2: DAQ Status
DAQ working reasonably well
  2 days downtime related to trigger board replacement (see report of Dec 11th)
  1 night of downtime due to an unplugged clock cable
  Inefficiency due to run restart procedure and board resets O(few %)
  Tests to assess effect of BGO thermocouple readout on ADC boards stability are on-going
New version of trigger firmware provides additional functionalities
  Prescaling of individual triggers
  Software triggers (delayed and random)
  Autopass events for individual triggers
  SIn control for synchronized start of run
  TimePix control
  PadmeTrig module with green functionalities ready for installation

## Slide 3: CDR Status
Data are copied from on-line disk servers (l1padme3, l1padme4) to the LNF disk system and from here to tapes at CNAF and KLOE
  Independent processes handle data streams in parallel
  Total throughput >100 MB/s
  Can keep up with current very high (70 MB/s) DAQ rate
  No backlog: CDR is currently idle and waiting for 2019 data
Procedure to setup/start CDR is described in the PADME wiki
  https://github.com/PADME-Experiment/padme-fw/wiki → «The PADME CDR system»
Disk clean up of on-line disk servers is still manual

## Slide 4: Data Storage
Collected ~130 TB of rawdata
MUCH more than expected (>5x) due to “physical noise” in BTF
All data available on LNF Tier2 disks, CNAF tapes and KLOE tapes
Problem: we only “own” 80 TB of disk space at LNF Tier2.
  Asked INFN for more disk space (100 TB) but it will take a long time before we get it
  For the moment Tier2 management is turning a blind eye on this
More tapes at CNAF and KLOE requested to INFN

## Slide 5: Data Availability
All data are available only via GRID protocols
Need correctly configured certificate with PADME VO access
  Procedures described in PADME wiki at
  https://github.com/PADME-Experiment/padme-fw/wiki → «PADME and the Grid»
Files can be accessed using the ROOT protocol:
  root://atlasse.lnf.infn.it:1094//vo.padme.org/daq/2018/rawdata/
  run_0000000_20181219_194140/run_0000000_20181219_194140_lvl1_00_000.root
Or they can be copied to a local area using the GFAL protocol:
  gfal-copy srm://atlasse.lnf.infn.it:8446/srm/managerv2?SFN=/dpm/lnf.infn.it/
  home/vo.padme.org/daq/2018/rawdata/run_0000000_20181219_194140/
  run_0000000_20181219_194140_lvl1_00_000.root
  file:///home/leonardi/ run_0000000_20181219_194140_lvl1_00_000.root

## Slide 6: PadmeRecoProd
An automatic system to systematically run PadmeReco on all rawdata
PadmeReco must be installed under CVMFS
  This still needs some complex manual activities
One PadmeRecoProd process per run
> PadmeRecoProd –r run_0000000_20181219_194140
All files of the run are distributed to many independent jobs
  100 files per job (option to change it)
  Respect time order at file level but not at event level
Jobs are submitted to the GRID
  By default to the LNF Tier2. There is an option to run at CNAF.
Jobs access the rawdata files at LNF using the rootx protocol
  No need to pre-stage or copy the files before starting the job
Each job produces a single root file which is stored on the LNF disk system

## Slide 7: Conclusions
As Venelin puts it: if we have data, then DAQ is OK
All data are copied to LNF Tier2, CNAF and KLOE
Data storage is coping with current throughput and will be expanded in 2019
All rawdata are available via GRID protocols (rootx, gfal)
Systematic PadmeReco production can be started as soon as we have a stable version of the code