## Slide 1: A gamma-ray imaging camera for ambient radioactivity detection
Set-up
4x4 CsI(Tl) Scintillator matrix
Coded mask technique (7x7 Tiles made with Tungsten and PVC)
PMT-based photodetection vs SiPM-based photodetection
CAEN Digitizer V1725 for data acquisition
Energy Resolution SiPM vs PMT
Better resolution for integration gate grater than 0.5 µs
Point Spread Function
PSF of about 20 mrad, corresponding to 2 cm for a source at 1 m
137Cs 662 KeV Line
137Cs Imaging
5 µs integration gate