## Slide 1
A FAST TIMING MICRO-PATTERN GASEOUS DETECTOR FOR TOF-PET
Raffaella Radogna, Piet Verwilligen, Marcello Maggi
INFN- Bari, Italy
A new detector layout, named Fast Timing MPGD (FTM), has been recently proposed. The FTM would combine both the high spatial resolution (100um) and high rate capability (100MHz/cm^2) of the MPGDs with a high time resolution of 100ps. This new technology consists of a stack of several coupled layers where drift and multiplication stages alternate in the structure, yielding a significant improvement in timing properties due to competing ionization processes in the different drift regions. This contribution introduces the FTM technology as an innovative PET imaging device concept
Adapt structure to detect 511 keV γ from PET
GEANT4.10.03 Simulation of 511 keV γ interaction in different materials and thicknesses: PCB (FR4), kapton, glass, lead glass
Photon Conversion
FTM for photons proposals
Scheme A: photon converted in high-Z resistive material + several thin amplification layers
Charged particles ionize the gas in the drift region producing e- multiplied in the gain region
Improve time resolution by reducing distance to the gain region + resistive structure→ split drift volume in N layers, each with own amp.
sub-relativistic e- has high ionization density
Scheme B: photon can convert in each amp. layer (only resistive material allowed)
Electron energy spectra.
Electron production rate.
Electron energy spectra.
arXiv:1503.05330
Fast Timing Micro Pattern Gaseous Detector
Simulation of AMPTEK X-ray (Ag) passing the drift board