## Slide 1
Development of a Highly Selective Muon Trigger Exploiting the High Spatial Resolution of Monitored Drift-Tube Chambers for the ATLAS Experiment at the HL-LHC
Oliver Kortner (MPI for Physics Munich, Germany) on behalf of the ATLAS Collaboration
The interesting electroweak physics is mainly at pT>20 GeV.
The inclusive muon cross section is very steeply rising with decreasing pT.
Muon pretrigger without MDT data accepts a lot of muons with 10 GeV<pT<20 GeV.
→Reduction of the trigger rate due to sharpening of the turn-on curve and
the rejection of accidental pretriggers:
Rate without MDTs Rate with MDTs
Barrel (|η|<1.05) 45-85 kHz ~15 kHz
End caps (1.05<|η|<2.4) 15-20 kHz ~10 kHz
Muon trigger at the HL-LHC
2-level trigger system: Hardware based level 0 (L0), software based high-level trigger (HLT).
L0 muon trigger:
  Pretrigger: Coincidence of RPC or TGC hits.
→ pp collision time (BCID) + η and φ position of the muon
(spatial region of interest (RoI)). pT measurement with low resolution.
  Final trigger: Use of precision hits of monitored drift-tube (MDT) chambers for precise pT measurement.
Sagitta
Reason for MDT trigger
Continuous streams of
Input from pretrigger
BCID
ROI
MDT hits
MDT trigger hardware and data flow
Implementation on ATCA blades.
Data flow:
  Segment reconstruction in each chamber only in the ROI performed on a FPGA with the option of an associative memory chip for pattern recognition.
  Momentum determination from segment positions and segment angles.
Total muon trigger latency < 4.2 µs